## Slide 1: ITU-T Recommendations explained
Greg Jones
ITU Telecommunication Standardization Sector (ITU-T)
greg.jones@itu.int

## Slide 2: Overview
Y.1001 – IP framework
G.990 series – DSL
H.260 series – Video coding
G.720 series – Audio coding
H.323 – Multimedia terminals
V.90 series – Modems

## Slide 3: Y.1001 - IP framework
Identifies a framework to position the telecommunications aspects with respect to IP-based networks
Understanding the issues involved in the provision of seamless services between IP-based and telecommunication networks in a convergence context

## Slide 4: Typical components of an xDSL system
audio/video/data
POTS
Splitter
xDT
=
SN = Service Node
xDSL
xDT
xDSL
Transceiver
DTU-R =
Transceiver Unit- Remote
DTU-C =
xDSL
Transceiver Unit- Central office
U-R
T
CUSTOMER PREMISES
CENTRAL OFFICE
POTS
Splitter
xDT
U-C
SNI
• PSTN/ISDN
SN
• B-ISDN SN
• Non-ATM based SN
(e.g. - video server
- IP router)
(Subscriber line)
xDTU-R
xDTU-C
ADSL
ADSL lite
HDSL
SHDSL
VDSL

## Slide 5: DSL Recommendations
HDSL - G.991.1, High bit rate digital subscriber line transceivers
  Two wire bidirectional transceiver: Three systems:
    Two or three pairs, each 748 kbit/s
    Two pairs, each 1168 kbit/s
    One pair, 2 320 kbit/s
  Code: 2B1Q or CAP (Carrierless Amplitude and Phase modulation)
SHDSL - G.991.2, Single pair high-speed digital subscriber line transceivers
  Duplex (bidirectional) operation on one copper pair:
  Payload 192 kbit/s up to 2.312 Mbit/s.
  Optional 2 pairs: Payload 384 kbit/s up to 4.624 Mbit/s
  Code: TC-PAM (Trellis Coded Pulse Amplitude Modulation).
ADSL - G.992.1, Asymmetric digital subscriber line transceivers
  One twisted pair, payload upstream up to 640 kbit/s, downstream up to 6.144 Mbit/s. Simultaneous Voiceband and N-ISDN possible. Code: DMT (Discrete MultiTone)
ADSL lite - G.992.2, Splitterless asymmetric digital subscriber line transceivers
  One twisted pair, payload downstream up to 1.536 Mbit/s, upstream up to 512 kbit/s. Code: DMT (Discrete MultiTone)
VDSL - G.993.1, Very high bit rate digital subscriber line transceivers.
  One twisted pair, symmetrical operation 6 Mbit/s or 13 Mbit/s up and down, asymmetrical operation down 22 Mbit/s, up 3 Mbit/s, Code: not yet decided

## Slide 6: Related Recommendations
G.994.1 – Handshake procedures for DSL Recs.
G.995.1 – Overview of DSL Recs.
G.996.1 – Test procedures for DSL transceivers
G.997.1 – Physical layer management for DSL transceivers

## Slide 7: H.261 Video Codec for A/V services at p x 64 kbit/s
The first practical video coding standard (1990)
Used today in (ISDN) video conferencing systems
Bit rates commonly 40 kbits/s to 2 Mbits/s

## Slide 8: H.262 Same as MPEG-2/Video (ISO/IEC 13818-2)
Commonly used for entertainment-quality video applications
The first practical standard for interlaced video
Used in digital cable, digital broadcast, satellite, DVD, etc.
Bit rates commonly 4-20 Mbits/s

## Slide 9: H.263 Video Coding for Low Bit Rate Communication
Significantly improved video coding compression performance (esp. at very low rates, but also at higher rates as well)
The first error and packet loss resilient video coding standard
Used in Internet protocol, wireless, and ISDN video conferencing terminals (H.323, H.324, 3GPP, etc.)
“Baseline” core mode interoperable with MPEG4/Video
Very wide range of bit rates and possible applications

## Slide 10: H.264 Advanced Video Coding
Core development work initiated in ITU-T Q.6/16 “Video Coding Experts Group” (VCEG), now being jointly developed with MPEG under the “Joint Video Team” (JVT)
Objective is to have the same performance of H.263 but operating at half H.263’s bit rate
Conclusion expected for late 2002

## Slide 11: Goals of JVT/H.264 project
Simple syntax specification
  Targeting simple and clean solutions
  Avoiding any excessive quantity of optional features or profile configurations
Improved Coding Efficiency
  Average bit rate reduction of 50% given fixed fidelity compared to any other standard
Improved Network Friendliness
  Issues examined in H.263 and MPEG4/Video are further improved
  Major targets are mobile networks and Internet

## Slide 12: Applications of JVT/H.264
Conversational H.32X Services
  H.320 Conversational
  3GPP Conversational (circuit and packet modes)
  H.323 Conversational IP best effort (ex. Netmeeting)
Streaming Services
  3GPP Streaming IP/RTP/RTSP
  Streaming IP/RTP/RTSP
Other Services
  Entertainment Satellite/Cable/VDSL/DVD, 0.5 – 8 Mbit/s
  Digital Cinema Application
  3GPP Multimedia Messaging Services

## Slide 13: JVT/H.264 Layer structure
Video Coding Layer
Data Partitioning
Network Adaptation Layer
H.320
H.324
H.323/IP
H.324M
etc.
Control Data
Macroblock
Slice/Partition

## Slide 14: ITU-T Wideband Speech Coding (F.700’s A1 Audio Quality Level)
G.722
  Coding of 7 kHz speech at 64, 56, and 48 kbit/s
  Sub-band ADPCM
G.722.1
  Coding of 7 kHz speech at 32 and 24 kbit/s
  Transform coding approach
G.722.2
  Coding of 7 kHz speech at 16 kbit/s or lower
  CELP-based; same as 3GPP AMR-WB
  Optimized for speech, works well also with 7kHz music
Just completed

## Slide 15: ITU-T Telephony Speech Coding (F.700’s A0 Audio Quality Level)
G.711 PCM coding (64 kbit/s) late 60’s
G.726 ADPCM coding (32; 40, 24 & 16 kbit/s) 1988
G.728 LD-CELP coding (16; 40, 11.8 &9.6 kbit/s) 1992
G.723.1 Dual-rate coding (5.3 & 6.3 kbit/s) 1995
G.729 CS-ACELP coding (8; 12.8 & 6.4 kbit/s) 1996-2000
G.4kbit/s
G.VBR (Variable bit rate)
Ongoing
New

## Slide 16: H.323 context
AV
Applications
Audio
G.711
G.722
G.723.1
G.729
Video
H.261
H.263
Encryption
RTCP
H.225.0
Terminal
to
Gatekeeper
Signaling
(RAS)
Terminal Control and Management
Data
Applications
Security
Capabilities
Security
Capabilities
T.124
T.125
Unreliable Transport / UDP, IPX
Reliable Transport / TCP, SPX
Network Layer / IP / IPSec
Link Layer /......
Physical Layer / .....
T.123
Scope of H.323
Scope of H.235
TLS/SSL
Multimedia Applications, User Interface
TLS/SSL
Authenti-
cation
RTP
Scope of T.120
H.225.0
Call
Signaling
(Q.931)
H.245
System
Control

## Slide 17: Functional model for H.323 Terminal
Network
Interface
Audio Coding (e.g. G.711, G.729)
Video Coding (e.g. H.261, H.263)
User Data Coding (T.120)
System Control (H.245)
Call Control (H.225.0, Q.931)
MM Mux & Sync
(H.225.0)
User
Interface

## Slide 18: Interoperability
H.324
H.310
H.320
H.323
Audio/Video
User data
User data
User data
User data
Audio/Video
Audio/Video
Audio/Video
Mux
QoS
RTP/
Non-QoS
H.223
H.225.0
H.222.0
H.222.1
H.221
Call Control
(H.245)
Call Control
(H.242/H.243)
Call Control
(H.245)
Call Control
(H.245)
H.223
Anx.A-D
Fixed
Mobile
Scope
for H.246

## Slide 19: Multimedia terminals
H.320: Communications over N-ISDN
H.310: Communications over B-ISDN
H.323: Communications over packet networks (mainly IP)
H.324: Communications using circuit-switched services (fixed and mobile, including 3GPP)
H.246: Multimedia Terminal Interworking
H.248[.x]: Interworking between H.323 packet-based networks and the PSTN

## Slide 20: H.248 Gateway
Gateway converts between 2 networks:
  signaling conversion
  media (bearer) conversion
  service conversion
Gateway
(H.248)
H.323
PSTN
IP based

## Slide 21: Modems
Modem technology using ITU-T standards continues to bring Internet access to the masses. Dial-up remains the most popular method of accessing the web
ITU-T developed the first modem standard to make use of the fact that one end of a modem session has a digital connection (V.90)
ITU-T has been the pre-eminent body responsible for the development of dial-up Internet access
1994 - first global standard for 28.8 kbps modems, V.34
1998 - V.90 standard took modem technology to its theoretical maximum bitrate level in the down stream
2000 - V.92 completes the loop by taking the technology to its theoretical maximum in the downstream

## Slide 22: V.92
V.92: Bringing dial-up up to date
V.92 focuses on giving dial-up users a better Internet experience
The V.92 standard introduces three new features:
  Quick Connect - shortens connection time Typically the modem handshake takes from 25-27 seconds. Quick Connect halves this
  Modem-on-Hold - allows users to receive incoming calls Many households only have one telephone line. Modem-on-hold allows users to make AND receive calls while surfing the net. (User must have subscribed to Call waiting service from telco)
  PCM Upstream - boosts upstream rates A maximum of 48Kbps is supported in V.92 equipment. A significant improvement.

## Slide 23: New Rec V.moip V‑series DCEs over IP-networks
aims to ensure that modems will stay a viable technology into the twenty first century
enable operators to maximize network efficiency and reliability