## Slide 1
ERICSSONF
WBA Solutions
by

## Slide 2: The Importance of FWBA systems in the popularization of Broadband Services
Ulisses Rodrigues da Cunha L. Santos
Product Marketing Manager
Tel: +55 11 6224 1906
E-mail: ulisses.santos@edb.ericsson.se
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001

## Slide 3: The Industry Shift to Infocom
No of bits/day
$; Operator revenue
1999
PSTN/ISDN
Inter-/Intranet IP/Datacom
1999
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001
Notes: 2
The Industry shift to Infocom
One of many predictions about the rapid growth of data communication. One can always argue about how much and how fast this growth will occur. However, most if not all operators agree that data communication is rapidly overtaking voice communication.
The growing demand for more bandwidth in the access network is mainly due to the growth of Internet/Intranet traffic, LAN - LAN interconnect as well as a growing interest in VoIP to provide the small and medium sized businesses with new, more efficient services. Most actually IP traffic that is packet switched and very bursty in it’s nature.
The paradigm shift from circuit switched to packet switched applications opens up new opportunities for operators to attract new customers. They can and should offer an access system satisfying the growing demand for the data and multimedia applications of small and medium sized businesses providing peak data rates, on demand, in the order of 10 Mbit/s or more, in either the up or down link direction. This way providing superior data access services, but also voice services to these companies.
One should question a business case for LMDS providing only existing services like POTS, ISDN and E1/T1 leased lines where there is an existing copper infrastructure. These services can be supported at a lower cost by alternative access technologies. However, in combination with broadband access, narrow band services will be an important source of revenue. The use of ATM provides efficient support for existing applications, e g voice and video, as well as QoS for future IP based applications.

## Slide 4: Product Positioning
XDSL
Capacity
demand
End user
density
Metropolitan
Dense urban
Urban
Suburban
Rural
Individuals
Residentials
(single units)
SOHO’s
(single units)
SME’s
Multi-dwellings
Business
centers
Large
corporations
LMDS
(PMP)
PTP
BWLL
3G
Fiber ?
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001
Notes: 3
Wireless
Product Positioning
This picture shows different access methods and positions them where they are the most cost efficient alternative. The borders between the different technologies are approximate and in some locations two or three alternatives could be equally interesting to the operator and/or end customer. However, some conclusions are fairly easy to make:
1) At very high data rates, >100 Mbit/s, fiber or PTP SONET/SDH radio are the only options. PTP fiber or microwave are typically also the best alternatives for fixed bandwidth demands exceeding ~10 Mbit/s.
2) At modest requirements for bandwidth in densely populated areas xDSL/HFC (Digital Subscriber Line/Hybrid Fiber Coax) or the next generation mobile systems (next generation GSM and W-CDMA) are the most cost efficient alternatives.
3) At very low customer densities, the most cost efficient access methods are PTP microwave links or leased lines.
There is, however, a large opportunity for wireless broadband access or LMDS systems to be the most cost efficient alternative where the requirements for peak data rates are 2-30 Mbit/s.

## Slide 5
Flexible bandwidth (bandwidth-on-demand)
Reliable service integration
Coverage economics
Investment /
Capacity
Unused capacity
Wireline access
Wireless access capacity
matches subscriber growth
Traffic
demand
Wireless equipment
can be uninstalled and
re-deployed as needed
Radio access
Time
Capacity on demand with WBA
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001

## Slide 6
PmP is limited to a few frequency bands
PMP
PTP
Ghz
8
15
18
23
26
38
56-58
7
13
LMDS
BWLL
28
40- 43
MWS
MWS = Multimedia Wireless System
10.5
3.5
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001

## Slide 7: MINI-LINK BAS Hub Radio Nodes
Radio Unit
Radio Shelf
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001
Notes: 12
Hub
The indoor parts of the Radio Nodes (RN) are housed in a radio shelf (R-AAS) that concentrates the traffic and provides local traffic cross-connection within the hub site. The concentration shelf (C-AAS) connects different R-AAS and provides further concentration. Telephony traffic can be flexibly terminated in any shelf or in a dedicated circuit-emulation shelf (CE-AAS).
The user traffic is dynamically allocated among subscribers in a point-to-multipoint configuration, providing efficient use of available spectrum, using statistical multiplexing over the radio interface.
Point-to-point connections are used for high-capacity users or longer distances.
Interconnections between the different units and the core network are made by standard PDH and SDH interfaces.
The radio shelf can house up to 6 radio node controllers each with a 37.5 Mbit/s capacity. Note that since this is a TDMA system there is no need to adjust or add anything at the hub site for the connection of a new customer. This will save time and cost during the build-out of the system. One Radio Node consists of one modem that can support up to 64 different customer. The footprint of the node is thus very small.

## Slide 8: System Build-out / Scalability
Servers
Backbone Network
2-5 km
TDMA
ATM
37.5 Mbit/s
C-QPSK
28 MHz
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001
Notes: 13
System Build-out / Scalability
MINI-LINK BAS follows a cellular deployment structure where multiple sectors cover a geographical area. Each Hub, or base station, can be equipped with multiple Radio Nodes (RN) with integrated sector antennas for Point-to-Multi Point, or directional antennas for Point-to-Point connections.
The Access Terminals (AT) require a Line of Sight path toward the Hub and can be located anywhere within the sector coverage area, typically up to 3 miles or 5 km for Point-to-Multi Point access and 6 miles or 10 km for Point-to-Point access (depending on operational frequency and rain zone etc.).
The initial system supports up to 64 ATs per RN. The ATs utilize TDMA with a F-DCA (Fast Dynamic Capacity Allocation) scheme to connect to the Hub, guaranteeing maximum utilization of the bandwidth. It is possible to allocate the full bandwidth of 37.5 Mbit/s to a single user within 1 to 2 ms. The statistical multiplexing over the air interface between different users will allow the operator to sell data services requiring peak data rates of up to 10 Mbit/s or more. This service will at the same time not cost him more than the cost for 0,5 Mbit/s of average spectrum if the service has a typical peak/average ratio of 20.
The modulation method C-QPSK used is the same as for MINI-LINK E, giving a gross bit rate of 37.5 Mbit/s over a 28 MHz channel.
For a small build out used in the initial deployment of a network it is possible to connect PSTN traffic directly to a C/E (Circuit Emulation) card in the radio shelf with 4 E1/T1 interfaces.
The radio shelf connects the hub traffic to the backbone through ET 34/45 or ET 155 cards.
The system is very easy to build out from a small layout to a large access system with multiple radio nodes, sectors and hubs.
The traffic concentration over the air interface, as well as the additional traffic concentration in the ATM Concentration shelf at the hub, will also minimize the need for transport backhaul and core network resources. This need is further reduced by the unique possibility to set up local connections (as LAN-LAN, PBX-PBX) within a sector, hub or between hubs, without any use of backhaul capacity, core switches or routers.

## Slide 9: System Build-out / Scalability
Up to 64
Terminals per
Radio Node
Servers
Backbone Network
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001
Notes: 14
System Build-out / Scalability

## Slide 10: System Build-out / Scalability
Servers
Backbone Network
Local Cross-connect
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001
Notes: 15
System Build-out / Scalability

## Slide 11: System Build-out / Scalability
Servers
Backbone Network
Local Cross-connect
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001
Notes: 16
System Build-out / Scalability

## Slide 12: Next Generation Network
Backbone Network
Mobile Access
Fixed Access
Wireless
Broadband
(LMDS)
Content
Content
Communicaton
Applications
Broadband Services
Control
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001
Notes: 17
Next generation network
MINI-LINK BAS can have a common backbone network with other access solutions like Mobile Access and Fixed Access.

## Slide 13
Rental of a leased transmission circuit (5 km): 64 kbit/s capacity circuit: 80 Euro/month (excl. VAT)
2 Mbit/s capacity circuit: 350 Euro/month (excl. VAT)
34 Mbit/s capacity circuit: 2600 Euro/month (excl. VAT)
EC Recommendations On LL
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001
Notes: 7
EC Recommendations on LL
The prices for leased line capacity is rapidly going down in countries with a good copper infrastructure. LMDS operators will therefore find it more and more dificult to compete by providing capacity up to 2 Mbit/s with one important exception, ie transmission to radio base stations in dense cellular networks.
The base stations are often located where there is no previous copper or fiber cable. The high cost of digging means the radio is always a more cost efficent alternative. In dense cellular networks, PMP will be more cost efficent that PTP.
Of course, in countries with bad or non-existent copper infrastructure there may be a buiness case also for leased lines with LMDS.

## Slide 14: Broadband Price Components
Service Content
Network Access
Service Performance
Service Functionality
Network Capacity
Revenues
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001
Notes: 9
Broadband Price Components
Most operators and customers are still used to selling and buying dedicated access, ie 512 kit/s FR, 1 T1, 2 Mbit/s CBR ATM, etc. This means a dedicated connection (eg cable) with low peak rate which is for most of the time significantly under utilized making it very cost ineffecient.
Packet switched networks and especially LMDS which brings the statistical multiplexing all the way out into the access network offers large cost savings as the network cost is shared by a large number of customers. For the end customer thare are also large benefits. He will have access to high peak rates, ie 10 Mbit/s when needed (say 95 % of the time) while he may only use 0,5 Mbit/s on average. He will always be guaranteed a certain minimum rate (say 2 Mbit/s).
With more peak bandwidth available all the way to the end customer it will make it much easier for the operator to sell managed services to the end user, ie to manage the LAN and applications for the SME from a remote server. The average cost for LAN management (eg back-up, virus checking etc.) including simple applications (eg Microsoft office) is about 800 $/employee and month (Gartner Group) for an SME. If the operator where to sell this service for 400 $/employee per month to about a 50 people company there is lot of many to be saved (20000 $/month !) for the company and a lot of new opportunity for the operator to make money. Since this managed service is run with a dedicated team at a server centrally located at the operators premises he can of course sell this service to many SMEs within coverage of the LMDS system.
From the centralised node the operator could sell many different SLA for the service performance including eg security (firewall, encryption etc.), guaranteed availability and much more.
To make the service package even more attractive (to the end customer) and lucrative (for the operator), the operator should also offer service content, eg a B2B (B2C) platform, news, advanced application where you pay per minute/Mbyte etc. And of course, the more to be included in the service package and the larger companies (with more money) the operator wants to adress the more bandwidth is needed.

## Slide 15: Business Package – Example
• Telephony and fax
• VPN from 2-10 Mbit/s (dynamical)
• Internet access from 2-10 Mbit/s (dynamical)
• Several e-mail accounts
• Homepage, Domain hosting
• Secure remote LAN access
• VAS Portal
• Network management with on-line access
• 24-hour customer support, 7 days a week
$2,000/month
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001
Notes: 10
Business Package - Example
The SMEs have traditionally been a neglected market segment by the operators. They often need customised services, but their volumes would only motivate the operator to offer them standardised services. At the same time the SMEs represents probably the most profitable segment for the operators since their negotiating power is not strong enough to erode prices like in the corporate segment.
With the increasing competition on the telecommunication market it will be important to understand the situation of the SMEs. As they normally have short-term focus and limited resources, they want to spend their time and money on the core business and need to justify any activity on a strictly financial basis. Most of the SMEs lack internal telecommunication expertise and therefore have a need for packaged solutions and extensive support from their supplier. The needs of the SMEs vary a lot inside the market segment, as well as over time, and therefore it is important to offer them a flexible service.
Small and medium size businesses are a growing market. Although these businesses need high-powered, flexible services just like large businesses, they do not have the economic ability to implement a private network. Multiple line telephony, Internet connectivity, commercial data circuits, and e-commerce are the main services for the SME segment.

## Slide 16: End-user Services
Telephony
Internet/Intranet Access
Video conferencing
LAN/WAN Interconnection
Virtual Engineer
MSP
ASP
VPN
E-commerce
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001
Notes: 8
End-user Services
The services offered today requiries more and more capacity. SMEs with offices in multiple location require LAN - LAN connections with high symmetrical capacity. Normally LANs built today have a capacity of 100 Mbit/s or 1 Gbit/s. Of course they want the same capacity between buildings.
With the introduction of GPRS and UMTS in the cellular networks the capacity required to companies with a lot of employees travelling will increase dramatically. For the expected bandwidth of about 384 kbit/s to be available E2E for a UMTS user downloading a file from his home company, this company would need at least a 384 kbit/s connection to the fixed network. With several employees using their UMTS terminals simultaneously for download or video conferencing a much higher bandwidth should be available from the company in addition to the bandwidth needed for all other services used. In addition to the traditional services there will be a large growth of new services:
Virtual Engineer: The possibility to solve complex problems over a high quality video connection to an expert anywhere in the world.
LAN Management: Virus checking, backup, application problems etc. is all handled by the operator and will not need a dedicated person working with the PC network (LAN).
ASP/VPN: An operator offering to run the applications for SMEs will save a lot of time and money for the SME since all employees don’t need to upgrade their PCs as often as before and the latest version of all applications are always available.
E-commerce: Companies using the Internet for B2B will need high symmetrical capacity. Companies using the Internet for B2C will need high uplink capacity. Companies using the Internet for collecting information need high downlink capacity.

## Slide 17
MINI-LINK - ALL THE POWER YOU NEED FOR WIRELESS BROADBAND ACCESS
Seminar Multimidia in the XXI Century: Systems, Services and Terminals - Porto Seguro/Brazil 2001
Ulisses Rodrigues da Cunha L. Santos
Product Marketing Manager
Tel: +55 11 6224 1906
E-mail: ulisses.santos@edb.ericsson.se
Notes: 1
Speed
At present, the most sufficient technology to meet Small and Medium Enterprises (SME) eager needs for broadband services is Wireless Broadband Access (WBA). This is mainly based on the ease of system rollout, which enables quick and profitable deployments. The modular design within MINI-LINK BAS allows incremental growth, enabling the operator to start up quickly, and continue to build and add customers as they come online.
- No need for time-consuming digging. Once the sites have been secured, wireless system equipment can be installed in a few days.
- No stranded assets - easy to re-deploy equipment if the customer move location or their requirements change.
Profitability
The main target group for MINI-LINK BAS is communication intensive small and medium sized businesses. Their bandwidth requirements are dynamic in nature requiring very high peak rates but relatively low average, still demanding support for real-time services. To satisfy their need of carrier class voice, data and video, it is necessary to provide peak data rates of at least 10 Mbit/s, on demand. The potential in wireless is here enormous, since it allows fiber bandwidth - on demand - without the fiber. The possibilities within MINI-LINK BAS to instantaneously allocate capacity means that the customers don't have to pay for unutilized capacity.
A symmetrical bandwidth of 37 Mbit/s instead of 2 Mbit/s does not only mean that existing services are executed much faster. Above all, it gives the customer an opportunity to use completely new services, which increase competitiveness and sharpen the business focus.