## Slide 1
Jun/2001
Interactive Television
Takashi Tome
Multimedia in the 21st Century

## Slide 2: Interactive Television
Basic concepts
Interactive Television
  Local interactivity
  One-way interactivity
  Two-way interactivity
Some issues
Contents

## Slide 3: Concepts
Interactive service provider
Broadcast
service provider
Return interaction path
(or channel)
Broadcast channel
Interaction
channel
Forward
interaction
path
RDU - receiver decoder unit
STB - set top box,
navigation device,
IRD - integrated receiver decoder
Television set
ITU-T J.110
ITU-R BT.1369
Notes: The ITU, by means of its standard J-110, defines some basic terms.
We have here a broadcast service provider, which sends TV programs to the users through a “broadcast channel”. On the user’s side, such a program is received by means of a set-top-box and displayed in a monitor.
We may have also an interaction channel linking the user to an interactive service provider. This interaction channel, by it turn, may have a forward interaction path and a return interaction path. This latter is usually known as “return channel”.
About the set-top-box, that is a commercial name, not clearly defined, neither unanimously accepted. It is also known as “navigation device” (by F-C-C) or I-R-D (in Europe). Here in Brazil we are calling it U-R-D, or receiver-decoder-unit.

## Slide 4: Concepts
Television set
ITU-T J.110
ITU-R BT.1369
Interface A4
Interface A1
Interface Ax
Interface Ab
Notes: <Slide excluded from presentation>

## Slide 5: Broadcast
Over-the-air broadcasting
6 MHz channel
Return via PSTN or mobile
Notes: In the case of over-the-air broadcasting, the broadcasting channel is 6-megahertz-wide.
The forward interaction path is supposed to be inside the broadcasting channel, that is, it is in-band.
Whereas, the return is out-of-band, through P-S-T-N or even thru mobile network.

## Slide 6: MMDS
MMDS in Brazil
Broadcast channel:
15 to 31 x 6 MHz
Return channel: 2.170-2.182 MHz
Notes: For the M-M-D-S, the broadcast channel comprises 15 to 31 six-megahertz channels in the range 2500 (two-five-hundred) - 2682 (two six eighty-two) mega-hertz.
The return path, in the brazilian case, is between 2.170 (two thousand one hundred seventy) and 2.182 (two thousand one hundred eighty-two) megahertz.

## Slide 7: Cable
Cable TV network
Broadcast channel +
forward path: 54 to 540, 750,
860, 1000 MHz
Return path: 5 to 35~45 MHz
Notes: In the case of cable TV networks, both the forward and return path are inside the main pipe, that is, they are in-band.
The broadcast channel bandwidth depends on the network design and, here in Brazil, common values are 54 to 540, or 750, 860 or 1000 megahertz.
Return path is normally assigned to be between 5 and 45 megahertz.

## Slide 8: Concepts
audio
video
data
program stream
transport stream
Tx
Rx
transmission media
MPEG-2
multiplexer
MPEG-2
demux
A
V
D
A MPEG-2 System
Notes: Whichever the transmission media, be it broadcast, MMDS, cable or even satellite, transmission of digital television uses M-PEG-2 system.
With M-PEG, audio, video and data informations to be transmited are initially packed into MPEG packets and multiplexed to form what we call a “program stream”. One or several such program streams are then multiplexed to form the transport stream, which is then transmitted through one broadcast channel.
At the receiver side, there is a demultiplexer which recovers the original information.
You may have forward interaction path information bound inside a program stream (that we call “embedded data”), and/or have it as an independent program stream.

## Slide 9: Concepts
What is Interactive Television?
Notes: Well, what is Interactive Television, anyway?
According to the famous market forecasting expert NOSTRADAMUS,
Interactive Television is a device that is going to be invented in the 21st Century to solve ALL the problems of people.
(After appearing the woman):
Well, maybe, ALMOST ALL the problems...

## Slide 10: Local interactivity
Interactive service provider
Local Interactivity
(Enhanced broadcasting)
  All information is broadcasted, and the user navigates locally through data stored in the set-top box.
Notes: We will see now some examples of interactivity.
Interactivity may be classified by several criteria. One of them is thru the transmission criteria.
The most simple case is when there is no use of the interaction channel, that we could call as “local interactivity”.
All needed data is transmitted inside the main pipe, broadcasted to all users.
At the user’s side, that information is stored in the set-top-box and whenever the user “navigates” through the interactive information, he or she is in fact navigating through locally stored information.
This level is also known as “enhanced broadcasting”.

## Slide 11: Local interactivity
Nation
World
Economy
Sports
Shows
EPG - Electronic Programming Guide
IPG - Interactive Programming Guide
  Search programs (channels)
  Set preferences and filters
  Program in advance (timer functions)
  Parental control
Navigation through locally stored information
Local processing of keywords
Could send command messages to VCR or TV through STB’s interfaces
Notes: A good example of local interactivity is the E-P-G (Electronic Program Guide).
Some people call it I-P-G, Interactive Program Guide.
EPG is a graphical information which helps user search programs and channels.
You can also set preferences and filters in order to localize programs with a given characteristic or set parental control.

## Slide 12: Local interactivity
Data broadcasting
Data carousel, object carousel, virtual channel
  Weather
  Economic data
  Community interest news
Navigation through locally stored information
Local processing of user commands
www.climatempo.com.br
Notes: Data broadcasting is also known as “object carousel” in Europe, and “virtual channel” in the United States.
Data is broadcasted to the users, as an independent program stream. This data may be a weather bulletin, economic data, community interest news or whatever else.
Data is broadcasted and stored in the set-top-box. The user then navigates through the information locally stored.

## Slide 13: Local interactivity
Personal VCR
ReplayTV (Panasonic), TiVo (Sony, Phillips)*
  Record programs
  On screen menu
  Intelligent functions to search and record programs
* TiVo is more than a simple PVCR; it has, in fact, a 2-way interaction channel
Notes: “Personal VCR” is the nickname of such devices which have a hard-disk and can record programs like a common V-C-R.
But these devices are more smart. For example, you can quickly go back to a scene you have just seen. Meanwhile, it is still recording the program, so that you will miss nothing: you can go back and continue to watch the program normally, as like as the broadcasting have continued exclusively for you.
More than that, as they are digital devices, you can integrate other features, such as an intelligent EPG functions, to program and record preferred shows.

## Slide 14: One-way interactivity
One-way interactivity
(Interactive broadcasting)
  Return path is used to place orders
Return interaction
path (or channel)
Notes: The second level of interactivity is when you add the return channel. With it, user can place orders or send information to the interactive service provider.

## Slide 15: One-way interactivity
Pay-per-view
  User acquires a credit to watch a given amount of programs, or pays after watching
  Users choose programs to pay-per-watch through a TV menu
  The order and credit card number are sent through return path
  Encoded programs are delivered to users with scrambling keys
Program on demand
  Replay of TV programs showed on the same day (or some days before)
  Schedule defined by the rate of orders
  May be paid or free
Notes: As some examples of one-way-interactivity, we have the “pay-per-view” and “program on demand”.
Pay-per-view can work without a interactive channel. For instance, one person could place order via a telephon call and inform its subscriber ID number previously registered at the broadcasting provider. The broadcaster send then, with the encoded P-P-V program, the serial number of the set-top-boxes enabled to decode that program.
The interactive channel eases this process by means:
- the user can choose the desired program directly from a menu;
- all the user must to do is to click and maybe type a password;
- immediately, the set-top-box send all the needed information to the service provider.
In Program on demand, users can choose what they want to watch. It may be a new movie or a replay of a program broadcasted in that day or week. Users choose what will be rebroadcasted sending “votes” electronically.

## Slide 16: Two-way interactivity
Interactive service provider
Two-way interactivity
(Internet access profile)
  A two-way interactive channel
  (in-band or out-of-band) is used for bidirectional communication between user and service provider
Notes: Two-way interaction channel provides you a powerful tool to build interactive applications, internet-like.

## Slide 17: Two-way interactivity
Internet access
e-Mail
Pizza on demand (Home-shopping)
Internet access server
Can provide
full access to the Internet “cloud”, or
emulate a small portal with a handful set of sites (restricted community)
e-mail
Notes: With 2-way interactivity, you can access the internet, send/receive e-mails and order pizzas on demand through your television set.
Through the television interaction channel, you are connected to an internet access server. That server can then connect you to the internet “cloud”, that is, all the pages of the world-wide-web.
Another possibility, more common today, is that the service provider builds a portal within his machines, enabling access to a handful set of e-banking and shopping services, besides the e-mail.
This restriction is done partially due to commercial interests and partially in order to avoid a big amount of traffic.

## Slide 18: Cultural issues
Display definition:
  PC: 640x480 (VGA), 800x600 (SVGA)
  Analog TV: approx. 330x300 (can think as 320x240)
Viewing distance:
  PC: 30~60 cm
  TV: > 1 m
Therefore:
  Don’t use small fonts or details
  Scroll bars also difficult to handle
H
Notes: When the service provider enables access to full internet, another concern must be considered.
With personal computers today, a 800 by 600 point resolution in usual. Even a standard V-G-A monitor works with 640 by 480 point resolution.
Meanwhile, a common analog television set has a resolution of approximately 330 by 300 points, about a ¼ (quarter) of VGA resolution. Therefore, small details don´t show adequately in a television monitor.
Another concern is the viewing distance (sorry, please correct your notes).
Personal computers are used close the person, whereas television set is watched from no less than 1 meter.
Therefore, you cannot use small fonts nor small details.
Aha: scroll bars are also very awkward to use.

## Slide 19: Two-way interactivity
Internet access
Internet access server
<TBODY><TR>
<TD width=45><IMG height=47
src="img20.gif" width=45></TD>
<TD width=29><IMG height=47
src="img21.gif" width=29></TD>
<TD width=35><IMG height=47
src="img22.gif" width=35></TD>
<TR></TBODY>
<TBODY><TR>
<TD width=90><IMG height=95
src="img20.gif" width=90></TD>
<TD width=58><IMG height=95
src="img21.gif" width=58></TD>
<TD width=70><IMG height=95
src="img22.gif" width=70></TD>
</TR></TBODY>
Original page
Modified page
Set top
Ex: Microsoft TV (WebTV),
WorldGate
Notes: Then, when the internet access server enables you access the full internet, it does another job besides bringing you a given page.
You see here upside left the CPqD´s home-page, in 800 by 600 resolution.
On the right side, you see an excerpt of that page´s code.
The internet server crunches such code, in order to get a result presentable in a television set. For example, several details in the right side and bottom of the page are taken off, and the size of objects are changed.
Here, bellow-right, you have the result of such a crunching as it is shown in a television set with lower resolution.
Today, the internet access server must do such a gym (job) because internet sites don´t provide any page suited for exhibition in conventional television sets. But that´s easy to change: in the same way that most of sites do offer animated and plain-H-T-M-L versions of the same content, you could have a TV version of the same page, in the directory www.anything.com/TV.

## Slide 20
Two-way interactivity
TV + PC
Dual window, WebSync
Join a streaming video with internet pages
Notes: <Slide excluded from presentation>

## Slide 21: Two-way interactivity
Video-on-Demand
MPEG-2 “pipes” inside broadcast channel
Video server
Ex: DIVA, SeaChange, Aerocast
Notes: Video-on-demand is that long-awaited service.
For the broadcasting viewers, the wait will last some more time. For Cable TV users, the V-O-D is a bit more near.
You have here a video server system. Users place orders through return channel and the desired movies are sent them through the forward interaction path, inside the broadcasting main pipe.

## Slide 22: Transmission issues
A 6 MHz-channel standard transport stream: 19 Mbit/s
May transport 4 SDTV programs + some data
A VoD program = 1 SDTV (~ 4 Mbit/s)
An internet access:
averaged 50kB per page (400kbit), 1 page change per minute = 6.7 kbit/s
4 Mbit/s 600 users
How many users can you serve simultaneously?
Need to think a better Business Model
Notes: What is the main challenge for the broadcasters?
An over-the-air broadcasting channel, as we have seen, is 6-megahertz-wide. With M-PEG-2, you have a payload of about 19 mega-bits-per-second. You may have then 4 standard definition television programs + some data.
A video-on-demand, as we saw, needs one S-D-TV channel and therefore you can serve only 4 users simultaneously through a 6-megahertz channel.
For the internet access, figures are slightly better. An average internet page has 50 kilobytes – or 400 kilobits – of size. Assuming that an user will download, read something and then change page at a rate of 1 page per minute, the average traffic is about 6.7 kilobits per second. Therefore, in a 4 megabit stream – a ¼ of the total transport stream – you can serve some 600 users simultaneously. Maybe little in a big metropolitan area, but maybe enough in a medium sized towns.
Anyway, although 2-way interactive channel offers a lot of premises, you must think on a better business model.

## Slide 23: Rethinking the way we do it
A non-linear program
Begin
End
A linear program
Begin
End
Notes: Applications we have seen up to now are good examples of “clickable television”. Notwithstanding, they are a sort of linear programs. What is it?
In a linear program, you have a begin, and end and a well-defined path (or story) between them.
On the other hand, in a non-linear program, you may have a lot of beggining points...
...a lot of possible ends...
...and several possible stories between a given begin and an end...
...and even a loop back like a soup opera.
Linear program is today´s paradigm.
For the Interactive Television programs, we must change the way we create stories and programs, in order to have a truly interactive television.

## Slide 24: Two-way interactivity
A truly interactive television program
More about Ibituruna
How to reach
Hotels
Weather
Embedded data
Can choose script
Can see from other views
... can manipulate information
Ex: Wink-i
Notes: Here is Ibituruna, a beautiful natural resort.
Ibituruna? Where is it? How can we go there? Is there any hotel there? Which is the best season of the year to go?
With interactive television, you can click on the image and have any question answered.
You may have embedded data, can choose scripts, can see from other views. In a short, you can choose, get and manipulate the information as you want.

## Slide 25: Software issues: API
HARDWARE and
OS - a
HARDWARE and
OS - b
The same program (application) written (with differences) to HW-a and HW-b.
Games,
e-ciclopaedias,
t-commerce
Notes: There are a lot of issues to build an interactive television. We saw 2 of them: the man-machine interface (or cultural issues) and the transmission issue.
Here´s another one: the software bottleneck, known as A-P-I or application program interface.
Consider that figure as the software and the hardware functions needed to have your set-top-box working.
A big question is that each hardware exposes its own particularities to the software running over it.
Consequently, when you write a software to a given hardware, and want to have it running on other platform, you must rewrite some part of your software – sometimes, the entire software.

## Slide 26: Software issues: API
HARDWARE and
OS - a
HARDWARE and
OS - b
API - Application Program Interface - provides an uniform interface to application programs, hiding hardware specifics.
API for HW/OS-a
API for HW/OS-b
Games,
e-ciclopaedias,
t-commerce
Notes: API is intended to solve such question, hiding the hardware idiosyncrasies from the application software.
API acts like a cushion-layer between the application and the hardware, creating a more or less “flat” interface to the application software.

## Slide 27: Software issues: API
Some APIs:
  OpenTV
  WorldGate
  Mediahighway
  PowerTV
  DTV Navigator
  Betanova
  Microsoft TV
  MHP
Notes: Here we have some A-P-Is for interactive television. Each one has its pros and cons.
But… what catch our attention is that each API has its own way, creating a…
not so flat, not so interoperable interface to the application.

## Slide 28: Software issues: API
Common
internet-style files
API
HW + OS
Any program written in C/C++, Pascal, VisualBasic, etc.
Notes: Almost all API vendors say that its product support H-T-M-L, X-M-L, Java and Flash, the basic building blocks of today´s internet.

## Slide 29: Software issues: API
Common
internet-style files
Code/script interpreters:
internet browser,
Java Virtual Machine,
plug-ins
API
HW + OS
Any program written in C/C++, Pascal, VisualBasic, etc.
HW
Notes: But what´s behind them? To have an HTML page renderized in your computer, you need a browser engine – like such Microsoft´s Internet Explorer or Netscape Navigator. For Java applets, you need a Java Virtual Machine. For the Macromedia Flash, you need a plug-in. And so on.
All such engines are given – for free and for now – from the API manufacturer.
Another problem comes when you create a pure exe (ekze) file by means of, say, C++ code and compiler. The compiler must create a code for a not so predictable API, an old and well known problem for software writers.
Therefore, if we would like to have a booming increase in the interactive television content creation, with rich diversity, then a truly open and public API – such as M-H-P – is needed.

## Slide 30: Hardware issues
Static Processor:
A typical architecture
Main memory
CPU
Cache memory
16 to 64-bit wide bus
Video Accelerator
Video memory
to monitor
Video Adapter
Optimized for
shared multitasking
Notes: <Slide excluded from presentation>
Concerned about Set-Top-Box’s hardware, present PCs and workstations have an architecture which we could call as being “static processor”.
Such architecture has, among other things, a CPU (central processor unit), a main memory and a video accelerator unit. Just before the CPU, there is a buffer memory, known as “cache memory”.
The data bus interconnecting all such elements is a 16 to 64-bit wide bus.
This architecture is optimized for sequential shared multitasking operations, not real time.

## Slide 31: Hardware issues
CPU
Instruction stream
Data stream
Instruction
cache
Data
cache
Cache:
Main memory status:
Some
amount
of data
Instructions
(more or less huge program)
Static Processor:
Ex: a word processor
Notes: <Slide excluded from presentation>
In any kind of processor architecture, we have an instruction stream and a data stream flowing into the CPU. The cache memory exists because recovering data from the main memory is a slow process. Particularly in the static processor architecture, data cache is somewhat big, because processing job is normally done with closely placed data. See for example, when you are typing something in a word processor: the most of time, you are typing characters following one to other. Only sometimes it happens to you to change the page, and then the PC takes a long time going to get that page.
Instruction stream, by it turn, doesn’t need such caching, normally because there is low correlation between two adjacent instructions.
In terms of RAM usage, the program usually takes a huge amount of it, whereas the user data itself occupies a little piece of the cake.

## Slide 32: Hardware issues
Dynamic Processor:
A typical architecture
Cache for time-synchronizing needs only
Main memory
CPU
64 to 128-bit wide bus
Video Accelerator
Video memory
to monitor
Video Adapter
10-channel
DMA controller
Optimized for
Real-Time (image processing) applications
Notes: <Slide excluded from presentation>
In a dynamic processor – like Sony’s PlayStation 2 – things are different.
Although you still have the CPU, a main memory and a video accelerator, they are connected by a much wider bus – usually 128 bit. That wider bus is needed due to the huge traffic of information that composes the real time moving pictures.
You have also a D-M-A – Direct Memory Access controller. With such device, you can pick the background image from an address of memory, the fliying mosquitos from another address, the hero’s image from the third address, and so on, almost simultaneously.

## Slide 33: Hardware issues
CPU
Instruction stream
Data stream
Instruction
cache
Data
cache
Cache:
Main memory status:
Huge
amount
of data
Small amount of
instructions
Dynamic Processor:
Ex: a 3D video-game
Notes: <Slide excluded from presentation>
In the dynamic processor, data stream is huge, and data cache does only perform time-synchronization function.
In contrast, with video-games, you have the same instruction – for example, “move right” – acting over several pixels of the image. Therefore, such instructions are stored in the instruction cache to save time, in a opposite situation to that of a static processor.
The RAM usage shows that the program itself uses only a small piece of the cake, whereas “user” data takes the main piece.
For the new interactive television world, the differencies between those architectures must be taken in account.

## Slide 34: Hardware issues
Typical Set-Top Box:
  Static type processor architecture
  4 ~ 8 MB RAM
  4 to 8-bit graphics overlay capability
High-end Set-Top Box:
  Static type processor architecture
  14 ~ 90 MB RAM
  32 bit graphics overlay (true color)
  64 bit bus
To the Future:
  How to converge today’s PC-like memory-hungry applications (.exe) and huge-amount-of-data type real time ITV applications?
Example of memory usage:
an HTML page: 10 - 100 k
EPG: 300 - 400k
Microsoft platform: 6 M RAM
Notes: Finally, a little word about the set-top-box´s hardware: all such things look interesting, but how many room is there for the interactive television software to perform its acrobat show?
A typical set-top-box has 8 mega-bytes of RAM. That´s enough to accommodate a Microsoft TV API (with its 6 megabytes); an Electronic Programming Guide, with its 300 to 400 kilo-bytes; and maybe an HTML page, with some 10´s of kilo-bytes. And you still have some… 1 megabyte free, maybe?
(If hardware issues were discussed):
Look that both typical set-top-box and the high-end one use static type processor architecture.

## Slide 35
Conclusion
Interactive Television is more than a television with clickable interface and return channel.
We must change the way we think television programs, from linear programs to non-linear ones (technological and cultural issues).
How can we have a boom of interactive television content production similar to that happened in the internet?
Is the current set-top-box’s hardware architecture suited for future interactive television programs?

## Slide 36: Conclusion
With Interactive Television, sky is the limit...
Take this flight !
...and there’s a lot of things to do.
Notes: Like the internet, with interactive television, sky is the limit…
And there´s a lot of things to do.
Take this flight! Thank you!

## Slide 37: Bib & Ref
Some useful references
[1] ITU-R Rec J.110: Basic principles for a worldwide common family of systems for the provision of interactive television services, 1997-1998
[2] ITU-T Rec. J.111: Network independent protocols for interactive systems
[3] ITU-T Rec. J.112: Transmission systems for interactive cable television services
[4] ITU-T Rec. J.90: Electronic programming guides for delivery by digital cable television and similar methods
[5] Advanced TV Enhancement Forum: www.atvef.com
[6] Digital Audio Video Interactive Council: www.davic.org
[7] DVB Multimedia Home Platform, www.dvb.org
[8] Microsoft TV Platform (WebTV): www.microsoft.com/TV
[9] Motorola Broadband (GI): www.motorola.com/broadband
[10] Scientific Atlanta: www.sciatl.com
[11] SeaChange: www.schange.com
[12] CPqD: www.cpqd.com.br/produtos/dotip
[13] Fluckiger, F: Understanding Networked Multimedia, Prentice Hall

## Slide 38
takashi@cpqd.com.br
http://www.cpqd.com.br
MUITO OBRIGADO
Thank you
Merci