## Slide 1: “IPCablecom” Global standardisation of IP communication for cable networks
Richard Catchpole
Study Group 9 Associate Rapporteur
rjc@nortelnetworks .com
IPCablecom/Mediacom 2004
March 12th-15th, 2002

## Slide 2
“IPCablecom”
IPCablecom refers to standards for IP cable communications
IPCablecom defines architecture and interface specs.
IPCablecom builds on SG9’s J.83/J.112 cable modem transport (“DOCSIS/ EuroDOCSIS 1.1”, etc.)
IPCablecom initial market driver is IP telephony

## Slide 3: IPCablecom service vision
Initial Recs
Application services
Client devices
MTA
Set-Top
Box
PC
IPCablecom
Network
Internet
Telephony
Business/SOHO
Voice/Data/Video
Interactive
Gaming/
Entertainment
Notes: The long term objective of IPCablecom is to provide cable subscribers with access to a variety of multimedia IP services over the high-speed cable data infrastructure using varying types of CPE.
The first phase of the project focuses on IP telephony. Future phases are envisioned to enable the architecture to fulfill it’s multimedia potential.

## Slide 4: IPCablecom Service Possibilities
Residential/Business IP Telephony
Video IP telephony
Voice/data/video unified messaging
Enhanced conferencing and media services
Entertainment Services
  Real-time multiplayer interactive gaming

## Slide 5: Basic standards process for IPCablecom
CableLabs
(projects)
ITU-T
SCTE
…
Global SDO level:
Regional
/national
SDO level:
Contributor
Level:
ETSI
Euro operator
e.g. ECCA
(requirements)
TTC
(Japan)
Vend.
Vend.
Vend.
ECCA European Cable Communication Association
ETSI European Telecom Standards Institute
ITU-T International Telecom Union, Telecom sector
SCTE Society of Cable Telecom Engineers
SDO Standards Development Organisation (accredited)
Vend. Vendor
Standards requirements
Standards draft text to IPR terms of recipient

## Slide 6: IPCablecom Components
AN Access Node
CM Cable Modem
HFC Hybrid Fiber Coax network
MTA Multimedia Terminal Adapter
PSTN Public Switched Tel. Network
Embedded MTA
PSTN
PSTN
Gateway
Call
Management
Servers
CM
MTA
Back Office
Servers
Managed IP
Network
AN
CM
HFC

## Slide 7: Interoperability intra-zone and with PSTN using IP
Operator
A Zone
CMS
Gateway
PSTN
Operator C
Zone
CMS
Gateway
PSTN
CMS
Gateway
PSTN
Operator B
Zone
Operator C
Zone
Notes: A zone is the set of all client devices under the control of a single call management server. The baseline recommendations enable calls within the zone and traffic exchange with the PSTN.

## Slide 8: IPCablecom Recs. for interoperability intra-zone and with PSTN
Architecture
J.160 Architecture
Signaling
J.162 Network Call Signaling
J.165 IPCablecom Signaling Transport Protocol
J.171 Trunk Gateway Control Protocol
Quality of Service
J.163 Dynamic QoS
Media/Codecs
  J.161 Audio Codec Requts.
OSS
  J.164 Event Messaging
  J.166 MIB Framework
  J.167 MTA Provisioning
  J.168 MTA MIB
  J.169 NCS MIB
Security
  J.170 Security
A set of recommendations is now approved…

## Slide 9: Interoperability with Local Exchange
Operator
A Zone
IP Access Terminal
Local Exchange
Operator C
Zone
IP Access Terminal
Local Exchange
IP Access Terminal
Local Exchange
Operator B
Zone
Operator C
Zone
Notes: A zone is the set of all client devices under the control of a single call management server. The baseline recommendations enable calls within the zone and traffic exchange with the PSTN.

## Slide 10: IPCablecom Recs. for interoperability with Local Exchange
MTA interfacing
J.162 Network Call Signaling has been extended, including examples for regional application
IP Access Terminal
Under study in North America and Europe (ETSI)

## Slide 11: Interoperability inter-zone and inter-domain directly over managed IP backbones
Operator
A Zone
Operator
B Zone
Operator
C Zone
Managed
IP Network
Operator
A Zone
Border
CMS
Border
CMS
Border
CMS
Gateway
Gateway
Gateway
Local Zones
Administrative Domains
PSTN
PSTN
PSTN

## Slide 12: IPCablecom Recs. for interoperability inter-zone and inter-domain directly over managed IP backbones
Quality of Service
J.174 Inter-domain QoS
Security
J.170 Security
Architecture
  For further study
Signaling
For further study
OSS
  J.164 Event Messaging

## Slide 13: PacketCable™ Testing Program
CableLabs conducts interoperability and certification testing to:
  Measure conformance with interface specifications
  Facilitate multi-vendor interoperability
  Encourage rapid product development
Modeled after highly successful certification program for DOCSIS™ (ITU-T J.112B) cable modems
Four Certification Waves and Interoperability events scheduled for 2002

## Slide 14
PacketCable™ Testing Process
Business
Reqts.
Test
Plans
Specs.
Test Case
Implementation
Execution
& Results
Requirements.
Management
150 people
80 companies
30 documents
20 teams

## Slide 15: PacketCable™ Testing - 2001
23 vendors brought to CableLabs:
  12 MTAs
  4 Call Agents
  1 AN (CMTS)
  3 Billing
  3 Provisioning servers
  1 Security server
  2 Gateway Controllers
  2 Media Gateways
  1 Signaling Gateway

## Slide 16: IPCablecom progress summary
Dec. 1999: PacketCable™ intra-zone VoIP published.
Nov. 2000: PacketCable™ inter-zone VoIP published.
Apr. 2001: European cable operator (ECCA) VoIP requts.
May 2001: SCTE intra-zone set of VoIP standards.
Aug. 2001: ETSI intra-zone set of VoIP standards.
Feb. 2002: ITU-T intra-zone VoIP recommendations, and first inter-zone recommendation

## Slide 17: IPCablecom related presentations to follow in this workshop
ETSI on IPCablecom
IPCablecom architecture
IPCablecom QoS
IPCablecom Security
Cable modem transport platforms

## Slide 18: ITU-T SG9 IPCablecom contacts
Q13/9 Voice/video IP applns. over cable TV networks
  Rapporteur: Ed Miller (edward.miller@terayon .com)
  Assoc. Rapporteur: Volker Leisse (v.leisse@tu-bs.de)
Q10/9 Interconnection of cable networks with public switched network and other delivery systems
  Rapporteur: Ed Miller (neil.olsen@ieee.com)
  Assoc. Rapporteur: Richard Catchpole (rjc@nortelnetworks.com)
Q12/9 Cable TV delivery of multimedia using IP or packets
  Rapporteur: Rouzbeh Yassini (rouzbeh@yas.com)
  Assoc. Rapporteur: Richard Catchpole (rjc@nortelnetworks.com)

## Slide 19: Summary for IPCablecom
The initial focus has been on VoIP
  For a single zone, a set of interfaces has been approved by SCTE, ETSI and ITU-T SG9
  They cover signaling, QoS, codecs, billing, provisioning, security
  They cover POTS capability
  Local Exchange interfacing is the subject of regional work (using GR303 for North America, V5.2 in ETSI)
  For interdomain VoIP over cable networks, QoS is defined
Later there will be enhancements for multimedia
  Telecommuting, videoconferencing, interactive gaming,...