## Slide 1: IPCablecom - Network and Service Architecture
Dipl.-Ing. Volker Leisse
Institute for Communications Technology
Braunschweig Technical University
E-Mail: v.leisse@tu-bs.de
© 2002
ITU-T Workshop on Multimedia Convergence
Geneva, 12-15 March 2002
European
Cable
Communications
Association

## Slide 2: Introduction (1)
IPCablecom is a multimedia architecture
  Overlay network of data-ready broadband cable infrastructure
  Robust, end-to-end architecture
IPCablecom enables broad family of real-time packet-based services
  First phase focused on packetized voice services
  Additional multimedia services like video envisioned for future project phases
  Enhancement of traditional broadcast service by established interactive service
  Exploitation of convergence of data and voice networks with increased load and cost efficiency

## Slide 3: Introduction (2)
IPCablecom utilizes cable network, managed IP backbone and PSTN as transport networks
Open and interoperable interfaces enable horizontal markets
  Signaling, routing, and media transport functions sufficient to enable high quality voice applications
  Mechanisms for effectively managing QoS on cable access network
  Extensive event logging
  Efficient provisioning of Customer Premises Equipment (CPE)
  End-to-end Security Mechanisms

## Slide 4: Architecture (1)
AN ... Access Node
CM ... Cable Modem
CMS ... Call Management Server
MTA ... Multimedia Terminal Adapter
MG ... Media Gateway
MGC ... Media Gateway Controller
SG ... Signaling Gateway
OSS ... Operational Support System
Announcements
Conference Bridge
...
PSTN
Managed IP Backbone
Cable Network
CMS
Cable Network
Stand-alone MTA
AN
MG
SG
MGC
Billing
Provisioning
DHCP Server
TFTP Server
...
Media Server
AN
Private IP Network
CM
MTA
MTA
CM
Embedded MTA
OSS
PSTN Gateway
Notes: MTA:
- interface between user terminal and IPCablecom network
- data encoding and decoding, signaling to CMS, AN
- embedded and stand-alone
Cable communication system AN und CM:
- high-rate, reliable and secure transport connection
CMS:
- call signaling and control
- decomposes into CA to maintain call state and control of MTA and MGC
- and GC to control resource allocation coordination and authorization
PSTN Gateway with MG, SG and MGC:
- MG terminates PSTN trunks, SG to exchange signaling information with SS7
OSS
single IPCablecom zone defined by single CMS and MGC ->
communication scenarii:
- MTA - MTA with single CMS
- MTA - PSTN across MG
- MTA - MTA across multiple CMS => inter-domain architecture

## Slide 5: Architecture (2)
IPCablecom Domain
IPCablecom Domain
AN ... Access Node
CM ... Cable Modem
CMS ... Call Management Server
MTA ... Multimedia Terminal Adapter
IPCablecom Zone
IP Backbone
CMS Border Proxy
Cable Network
MTA
AN
Cable Network
MTA
AN
IP Backbone
IP Backbone
Cable Network
IPCablecom Zone
MTA
AN
Cable Network
MTA
AN
CMS Border Proxy
IP Backbone
Cable Network
IPCablecom Zone
MTA
AN
Cable Network
MTA
AN
CMS Border Proxy
Notes: Border Proxy
- transformation of signaling, routing and security information across zones and domains
- well-defined entry-/exit-point for domain

## Slide 6: Call Signaling Example - Far-end terminal connected to PSTN
PSTN
Managed IP Backbone
Cable
Network
CMS
SG
MG
MGC
AN
Private IP Network
CM
MTA
Signaling Path
Media Path
DS0
Event detection
NCS
under study
ISTP
TGCP
SS7
ISTP ... Internet Signaling Transport Protocol
NCS ... Network Call Signaling
TGCP ... Trunking Gateway Control Protocol
Notes: - MTA detects events at user terminal (off-hook, dialing)
- User data encoded with ITU-T Codecs and encapsulated in RTP, UDP, IP

## Slide 7: Call Signaling Interfaces (1)
Network Based Call Signaling (NCS) - J.162
  Client (MTA) to IPCablecom network (CMS) signaling interface
  Profile of Media Gateway Control Protocol (MGCP) defined by IETF
  Provides functions to set-up and control calls within IPCablecom Zone
  Optimized for specifics of cable access environment
    Supports simple, thin clients
    Integrated protocol support for Quality of Service and Security
  Highly extensible through the addition of event packages

## Slide 8: Call Signaling Interfaces (2)
Trunking Gateway Control Protocol (TGCP) - J.171
  Media Gateway Controller (MGC) to Media Gateway (MG) signaling interface
  Profile of MGCP, future alternative based on H.248 under study
  Provides functions to control bearer connectivity between IPCablecom network and PSTN
Internet Signaling Transport Protocol (ISTP) - J.165
  Signaling interface of IPCablecom call control elements (MGC, CMS) to Signaling Gateway (SG)
  Provides functions to interconnect IPCablecom signaling with Signaling System No. 7 (SS7)
    local variations of SS7 must be accommodated

## Slide 9: Media Interfaces
Media Stream - J.161
  RTP/UDP/IP for real-time transport
  Low (G.729), medium (G.728), and high (G.711) rate codecs (only G.711 required)
  DTMF transmission is in-band in G.711
  DTMF transmission according to RFC 2833 for other codecs

## Slide 10: QoS Interfaces (1)
Interface between MTA and CM - J.112
  Defined only for embedded MTA
  Direct access to MAC control interface
  Services: request for resource reservation, resource commitment, change of resource allocation and release of resources in cable network
Interface between CM and AN - J.112
  QoS interface of cable communication system
  Services: resource reservation, resource commitment, change of resource allocation and release of resources in cable network

## Slide 11: QoS Interfaces (2)
Interface between MTA and AN - J.163
  Resource ReserVation Protocol (RSVP) as defined by IETF with IPCablecom specific extensions
  Services: reservation establishment, reservation change, reservation maintenance, resource commitment
Interface between AN and GC (function of CMS) - J.163
  Profile of Common Open Policy Service (COPS) as defined by IETF
  Services: allocation and authorization of gates (access control entities for QoS), prevention of theft of service
  Gate co-ordination based on RADIUS

## Slide 12: QoS Interfaces (3)
Interface among ANs and between AN and PSTN Gateway across - J.174
  QoS interface in backbone across domain borders
  Based on Integrated Services (IntServ) and Differentiated Services (DiffServ) architectures defined by IETF
  Several approaches to resource reservation specified
  Edge router defines border between network segments  flexible choice of QoS mechanisms in different segments
  Trade-off between level of guaranty and scalability, delay, efficiency

## Slide 13: Security Interfaces - J.170
Security mechanism defined for each protocol interface
Services provided include authorization, integrity maintenance, confidentiality ensurance
Signaling Security
  based on IPSec mechanisms as defined by IETF
Media Security
  end-to-end encryption of media streams using privacy interfaces of J.112
Device authentication
  Kerberos with public key initial authentication
  Internet Key Exchange (IKE) with X.509 digital certificates
Notes: Usage of J.112 provided media privacy on the cable access network
Additional end-to-end media encryption using AES-Rijndael to protect against eavesdropping by IPCablecom
no prevention of lawfully authorized electronic surveillance

## Slide 14: Other Interfaces (1)
Event Messages - J.164
  Events represent information important for billing and session accounting
  Based on RADIUS as defined by IETF
  Initial message set supports event capture and generation for voice services
  Extensible to support additional services
  Events generated by trusted elements - CMS, AN, MGC and received by Record Keeping Server (RKS)
  Correlated Call Detail Records made available to back-office applications

## Slide 15: Other Interfaces (2)
MTA Device Provisioning - J.166 .. J.169
  Standard protocols like DHCP, DNS, SNMPv3, TFTP used to provision client and download MTA configuration file
  Security relationship established between MTA and CMS(s)
  Management Information Bases (MIBs) for MTA and NCS support device provisioning and enable device management
Announcement Services - draft
  Audio Services for automated messages (e.g. incomplete calls)
  Defined as event package for NCS with further option based on H.248 under study

## Slide 16: Interfaces under study
Signaling between call control elements
  CMS-CMS, CMS-MGC
  Intra-domain and inter-domain signaling interface
Line Control Signaling
  Exploit switch capacity of PSTN for call control in IPCablecom
  Possibly based on V5.2 (in Europe) and GR.303 (in U.S.)
Lawful Interception
  Allows law enforcement agencies to intercept call information and call content
  Interface to be provided to collect intercepted data from IPCablecom elements for delivery to law enforcement facilities
  Influence by country-specific regulation
Notes: Under study does not mean under consideration of SG9 but considered by any involved body

## Slide 17: Specific Features
Primary Line Support - J.173
  Requirements for embedded MTA to provide a primary-line capable service using the IPCablecom architecture
  Sufficient reliability to meet consumer’s expectation of high availability (comparable to PSTN service)
  Includes
    power back-up for customer premises’ equipment,
    access to emergency services
    telemetry support
    definition of analog POTS interface

## Slide 18: Conclusion
IPCablecom is a completely defined end-to-end system to support the delivery of a plethora of packet-based interactive services across cable networks
Initial focus is on voice services
Through international (ITU-T) and European standardization (ETSI) IPCablecom becomes a globally accepted communication system for cable networks
Further developments emphasize on support of additional services (beyond voice)

## Slide 19: Thank you for your attention !