## Slide 1: Interoperability in Multimedia and Data Broadcasting
A MediaCom 2004 Presentation by
Shuji Hirakawa Media & Contents Business Division, Toshiba Corporation e-Solution Company
Vice Chairman, ITU-R Working Party 6M
IPCableCom / MediaCom 2004 / Interactive Multimedia Workshop ITU, Geneva, 12 - 15 March 2002

## Slide 2: WP 6M Activities for Multimedia-and-Data Broadcasting
ITU-R Working Party 6M and ITU-T Study Group 9 established Joint Rapporteur Group 1 (JRG-1) as the first joint studying body between ITU-R and ITU-T in March 2001
There are four major SDOs for multimedia and data broadcasting systems;
  ARIB (STD-B.24)
  ATSC (A/65, A/90, DASE) for terrestrial television
  DVB (MHP)
  SCTE (OpenCable/OCAP) for cable television
WP 6M is seeking interoperable mechanisms between these multimedia and data broadcasting systems

## Slide 3: Digital Broadcasting Systems for Fixed Reception and Mobile Reception
 |  | ARIB | North America | DVB/ DAB
Fixed Reception | Terrestrial | System C in BT.1306 | System A in BT.1306 | System B in BT.1306
 | Satellite | System D in BO.1516 | System B, C in BO.1516 | System A in BO.1516
Mobile Reception | Terrestrial | System F in BS.1114 | System C in BS.1114 | System A in BS.1114
 | Satellite | System E in BO.1130 | System DH in BO.1130 | System A in BO.1130
Physical layers of all broadcasting systems are designed to satisfy the different requirements of respective regions |  |  |  | 
Table 1 Physical Layer Specification

## Slide 4: Multimedia-and-Data Broadcasting System for Several Physical Broadcasting Systems
 |  | ARIB | North America | DVB/ DAB
Fixed Reception | Terrestrial | STD-B.24 | ATSC-DASE | DVB-MHP
 | Satellite | STD-B.24 | Proprietary | DVB-MHP
 | Cable | (STD-B.24) | OCAP | DVB-MHP
Mobile Reception | Terrestrial | STD-B.24 | Proprietary | DAB-MOT ETSI EN 301 234
 | Satellite | STD-B.24 | Proprietary | DAB-MOT ETSI EN 301 234
Table 2 Multimedia and Data Broadcasting Specification

## Slide 5: Interoperability between Fixed Terrestrial and Satellite Television
OFDM in VHF/UHF
Front End for System B / C in BT.1306
MPEG-2 Systems
MHP / ARIB B-24 Multimedia / Interactive System
Back End MPEG-2 Video SDTV / HDVT
There is no interoperability between System B and C in BT.1306 or System A and D in BO.1516 regarding physical layer architecture
Front End for System A / D in BO.1516
QPSK / 8 PSK in Ku Band

## Slide 6: Interoperability between Fixed/Mobile and Sound/Television Systems (1/3)
All broadcasting systems for various distribution media such as Satellite Television, Terrestrial Television, Satellite Sound and Terrestrial Sound adopt the same transport mechanism, i.e., MPEG-2 Systems
Terrestrial television signal has 13 segments of its frequency domain format
Each of these segments could have a different physical parameters
Up to three kinds of parameter sets could be selected in order to satisfy different requirements
The centre part of 13 segments could be received by terrestrial sound broadcasting receiver
This segment usually uses QPSK or 16 QAM with high forward error correction capability for mobile reception

## Slide 7: Interoperability between Fixed/Mobile and Sound/Television Systems (2/3)
Table 2 shows the interoperability between the different systems for multimedia and data broadcasting systems
All ARIB broadcasting systems use MPEG-2 Systems for service multiplexing and Standard B.24 for multimedia and data broadcasting
Terrestrial sound broadcasting receiver could handle the centre segment of 13-segmented terrestrial television signal
Both centre segment of terrestrial television broadcasting signal and the whole part of a terrestrial sound broadcasting signal could be received by portable receivers
By adding a front end of BSS (s) signal, a portable receiver could also decode BSS (s) data streams because all broadcasting systems adopt the same multimedia and data broadcasting standard

## Slide 8: Interoperability between Fixed/Mobile and Sound/Television Systems (3/3)
8-PSK 11 GHz
CDM 2.6 GHz
Front End for System E in BO.1130
Back End AAC Audio MPEG-4 Video
ARIB B-24 Common Multimedia/ Interactive System
Back End MPEG-2 Video AAC Audio
OFDM VHF/UHF
Front End for System C in BT.1306
MPEG-2 Systems
0.5/1.5 MHz
ISDB-TSB One / Three Segments
5.6 MHz
One Segment out of ISDB-TW
Front End for System F in BS.1114
Front End for System D in BO.1516
One Segment Reception out of 13 Segments
BSS (s)
BSS

## Slide 9: Interoperability in Multimedia and Data Broadcasting Systems
 | ARIB STD B.24 | DVB MHP/ OCAP | ATSC DASE
Data Transmission | Data Carousel | Object Carousel | Data Carousel
Presentation | BML | X-HTML | X-HTML
Execution | ECMA Script (+ JAVA) | JAVA | JAVA
Currently, JRG-1 is extracting the common parts of these systems

## Slide 10: Interoperability using Transcoding
Video Format Converter
Video Encoder
Video Decoder
??? Transcoding
Data Encoder
Data Decoder
Audio Encoder 1
Language Translation
Audio Encoder 2
Audio Decoder
SI / PSI Re-generator
De multiplex
IBC Contents
Multiplex
Local Contents
The first solution is a transcoding method converting original contents to a local format
It is better to prepare the well-formed original contents considering the limitation of transcoding capabilities if required a smart outputs

## Slide 11: Interoperability using XML
The second solution is the adoption of XML for authoring multimedia and data broadcasting contents
These XML contents may be converted suitable for more than one distribution media by using different CSSs
XML Document
CSS 3
HTML
Internet
X-HTML
CSS 2
Broadcasting B
BML
CSS 1
Broadcasting A

## Slide 12: Interoperability using Multi-Standard Set-Top-Box
The third solution for interoperable multimedia and data broadcasting is the adoption of multi-standard STB
Even in this case, the common core should be maximised for minimising the complexity of STB
VHF/UHF
Front End for Terrestrial
Multimedia decoding for Satellite
MPEG-2 Video and Audio Common Core of Multimedia decoding
Multimedia decoding for Terrestrial
QPSK C/Ku
Front End for Satellite

## Slide 13: UNI for nation wide contribution and primary distribution network
Broadcasters are preparing primarily distribution and contribution networks for digital terrestrial television broadcasting services in three major populated arias from the end of 2003 in Japan
Two types of User Network Interface (UNI) are now considered, non-compressed baseband interface and MPEG-2 Transport Stream (TS) packets interface
Major commercial broadcasters are considering to adopt non-compressed transmission services for 1.45 Gbit/sec HDTV contribution networks between three most populated areas (Tokyo, Nagoya and Osaka)
In this case, UNI is HDTV-SDI for HDTV digital video interface and AES/EBU for digital audio interface
Special signalling mechanism is provided for accommodating cueing information in order to switch from remote to local contents, and vice versa
Another major broadcaster is considering to use packetised video, audio and data transmission systems for primary distribution services
In this case, UNI is DVB-ASI for accommodating MPEG-2 TS packets

## Slide 14: Nation-wide Contribution and Primary Distribution Networks
HDTV baseband transmission
MPEG-2 TS packet transmission
Note: All systems are under consideration

## Slide 15: Contents Distribution over Internet
ITU-R develops a new Question 7/6 for ‘Interface to webcasting and its supporting data services’
Broadcasters should take care of rights of contents when they offer their contents to webcasting
  Internet service could reach to all over the world while a broadcasting service is licensed only in limited areas
  Some contents are produced supposing being broadcast only within limited areas
  These contents may be replaced by ‘safe’ materials when broadcasters offer their contents to Internet
Requirements from broadcasters to ‘interface to webcasting’ may include not only technical aspect but a mechanism for rights management

## Slide 16: Conclusion
In this presentation, interoperability of multimedia and data broadcasting systems are considered
There are several multimedia and data broadcasting systems in order to respond deferent requirements
ITU-R WP 6M and ITU-T SG 9 are jointly working to develop effective methods to exchange multimedia and data broadcasting contents between deferent systems
Other related observations such as UNI between broadcasters and common carriers are discussed
ITU-R WP 6M is now studying the Question for ‘Interface to webcasting and its supporting data services’

## Slide 17: Contact
Shuji Hirakawa Vice Chair of Working Party 6M Shuji.Hirakawa@Toshiba.co.jp
Thank you for your attention

## Slide 18: Electronic Copy
This presentation is available on: http://www.itu.int/ITU-T/ worksem/ipcablecom/program.html
S1PM1-P4.PDF