## Slide 1: Multi-Services Over MPLS
Dr. Ghassem Koleyni
Dr. Khalid Ahmad
March 2002

## Slide 2: Acknowledgements
Contributions of
Bilel Jamousi
Tim Pearson
Mina Azad
to this presentation is acknowledged.

## Slide 3: Outline
Today’s Networks
Evolution Towards MPLS Interworking
Brief MPLS Overview
Interworking Concepts
Interworking Challenges
Conclusions

## Slide 4: Today’s Network Architectures
Multiple, interworked, interdependent networks
Diversity of control and management architectures
Capacity and performance bottlenecks
Each network has its own control plane and management plane
IP/MPLS
Networks
PSTN/ISDN
Radio Access Networks
Ethernet
Networks
DSL- based Access
Frame Relay
Networks
IWF
IWF
IWF
IWF
IWF
IWF
IWF
IWF
ATM Networks
IWF

## Slide 5: Near Term Evolution
ATM Networks
IWF
PSTN/ISDN
Rec. Q.2931, PNNI
Frame Relay Networks
IP-based Networks
PSTN/ISDN OSF & NM, M series Rec.
Rec. Y.1310
IETF RFCs
Q & X series Rec.
IWF
IWF
Rec. I.555
Rec. I.580
Rec. Q.931
ATM OSF & NM, M series Rec.
SNMP based
FR OSF & NM
OSF = Operating Support Function
Prose
Convergence on ATM core networking enables initial stage of unified management and control
Enhanced performance and QoS capabilities for multi-services over common platform
PSTN/ISDN
IWF
SS7 Network
Rec. I.580
Rec. Q.700 series
Cons
Lack of service transparency between IP based services and ATM/PSTN services

## Slide 6: Outline
Today’s Networks
Evolution Towards MPLS Interworking
Brief MPLS Overview
Interworking Concepts
Interworking Challenges
Conclusions

## Slide 7: Mid Term Evolution Network Architecture-Convergence on MPLS Core
MPLS NETWORK
ATM
Networks
Frame Relay
Networks
Frame Relay
Networks
IWF
Ethernet
Networks
Ethernet
Networks
ATM Networks
Label Switching Router (LSR)
Label Switched Path (LSP)
IWF
IWF
IWF
IWF
IWF
Requires well defined interworking mechanism for all services
  Transfer plane functions
  Control plane functions
  Management plane functions

## Slide 8: MPLS Gateway Networking Solution implications
Multiservice Access Networks
Multiservice Access Networks
Core Network
L3 VPN and other IP services
ATM
FR
Ethernet
ATM
FR
Ethernet
L2/L3 VPN services
Traditional L2 services
L3 VPN and other IP services
L2/L3 VPN services
Traditional L2 services
MPLS Core
IP Routing
L2 Access
Networks
IP-based
Networks
IP Routing
L2 Access
Networks
End-to-end SPVC/SVCs
Exploiting label stacking capabilities of MPLS
IWF
PNNI Networking
Stacked LSPs
MPLS Gateway
MPLS Gateway
PNNI
PNNI
IWF
CR-LDP/RSVP-TE
IP-based
Networks

## Slide 9: Why Multi-Services over MPLS?
Operational Expenditure Reduction
  Leveraging existing IP/MPLS packet core
  Scaling all networks across a common transport and control core
Preservation of Existing Layer Two Operational Models
  Existing Layer Two features and functionality (including SLAs) can be maintained by providing OAM interworking
Core Network Scalability
  High speed links in routed core (e.g., potential OC192 forwarding capability)
  QoS/Traffic engineering based on explicit routing
  Aggregation capabilities based on label stacking

## Slide 10: Outline
Today’s Networks
Evolution Towards MPLS Interworking
Brief MPLS Overview
Interworking concepts
Interworking Challenges
Conclusions

## Slide 11: Overview of MPLS Forwarding
Processing of the packet is done at the edge; restricting core to packet forwarding
Forwarding is based solely on the label , not on destination IP address in the packet
Packet forwarded based on destination IP address
IP
Ingress LER adds label to packet
Packet forwarded based on label
Egress LER removes label
IP
Packet forwarded based on destination IP address
IP
IP
IP
20
IP
10

## Slide 12: MPLS combination of routing and switching
IP
ATM
ATM
Control Plane
Label
switching
MPLS
Multiprotocol Label Switching (MPLS) is hybrid model that makes use of the best properties in both Packet routing & label switching.
IP routing
Software
Forwarding
Label
Switching
IP routing
software
MPLS uses the advantages of both packet routing & label switching protocols

## Slide 13: Source Routing in MPLS
Ingress node determines path from ingress to egress based on layer 3 routing protocol
Easier to do policy or QoS based routing
LSR B
LSR C
LSR D
LSR E
LSR A
Forward to
LSR B
LSR C
LSR D
LSR E
LSR=Label Switching Router

## Slide 14: Hop-by-Hop Routing in MPLS
LSR B
LSR C
LSR D
LSR E
LSR A
Forward to
LSR B
Forward to
LSR C
Forward to
LSR D
Forward to
LSR E
Forward to
LSR ...
Each node runs layer 3 routing protocol
Forwarding decisions made independently at each node

## Slide 15: MPLS Protocol Stack
Physical
Layer 2 (PPP, ATM, FR,..)
MPLS
IP or Multi-Service
Application

## Slide 16
Control Plane Diversity in MPLS
Control Plane
PNNI Routing
OSPF, ISIS
Routing
Signaling
PNNI Signaling
N/A
Addressing
NSAP
IP
ATM
OSPF-TE, ISIS-TE
CR-LDP or RSVP-TE
IP
MPLS
IP
MPLS essentially functions as a Connection-oriented service
MPLS uses IP routing and control protocols
MPLS makes use of Layer 2 typical link-layer protocols, e.g. PPP, FR, ATM, Ethernet, etc.

## Slide 17: Outline
Today’s Networks
Evolution Towards MPLS Interworking
Brief MPLS Overview
Interworking concepts
Interworking Challenges
Conclusions

## Slide 18: General Network interworking
MPLS
Core
Network B
Network A
IWF
IWF
IWF=Interworking Function
Networks A and B are similar networks, e.g. both are ATM or Frame Relay, etc.
In Network Interworking, the PCI (Protocol Control Information) of the protocol and the payload information used in two similar networks are transferred transparently by an IWF (Interworking Function) . Typically the IWF encapsulates the information which is transmitted by means of an adaptation function and transfers it transparently to the other network.

## Slide 19: General Service Interworking
Network B
Network A
IWF
IWF=Interworking Function
Networks A and B are NOT similar networks, e.g. one may be ATM and the other Frame Relay or MPLS
In Service Interworking, the IWF between two dissimilar protocols (e.g., ATM & MPLS) terminates the protocol used in one network and translates (i.e. maps) its Protocol Control Information (PCI) to the PCI of the protocol used in other network for User, Control and Management Plane functions to the extent possible.

## Slide 20: Example ATM-MPLS Network Interworking
ATM Network
A
ATM Network
B
LSP “tunnel”
IWF
IWF
IWF=Interworking Function
LSR
In MPLS, network interworking and tunnelling concepts are used interchangeably

## Slide 21: ATM-MPLS Standards Activities
Standards activities in ITU-T, ATM Forum and IETF
Draft Recommendation Y.atmpls in SG13
Extensive discussion in ITU-T on interworking issues
  QoS support
  Transparency of ATM services, e.g., OAM
  Cell and frame encapsulation formats
  Control plane signalling (e.g, PNNI, etc.)
Work in progress in SG11 on signalling requirements and protocols for ATM-MPLS interworking
One approved specification in ATM Forum, af-aic-0178
  Work in progress to enhance the specification
Several drafts under consideration in IETF (PWE3 WG)
  Draft fischer
  Draft koleyni
  Draft brayley
  Draft martini
ITU-T SG13 Lead Study Group for IP related matters and on Multi-protocol and IP-based networks and their internetworking
Q5/13 mandate is to work on General Interworking including IP-based Multi-service Networks

## Slide 22: FR-MPLS Standards Activities
Standards activities in ITU-T SG13,Frame Relay Forum, MPLS Forum and IETF
Discussions are in preliminary stages in ITU-T
No approved specification yet in any Forum
Couple of drafts under consideration in IETF
  Draft kamapabhava
  Draft martini
Convergence on FR-MPLS interworking is progressing rapidly in all forums

## Slide 23: Ethernet/TDM-MPLS Standards Activities
Ethernet
Standards activities only in IETF PWE3 WG
No approved specification yet
Couple of drafts under consideration in IETF
  Draft so
  Draft martini
TDM
Standards activities only in IETF
No approved specification yet
Few drafts under consideration in IETF
Convergence on Ethernet over MPLS specification is progressing in IETF

## Slide 24: Example of Encapsulation Format
Payload
Control Fields and Service Specific Header (SSH)
Interworking Label
Transport Label
Transport label
Interworking label
Control Field & SSH
Payload
MPLS Frame
Label Stacking

## Slide 25: Outline
Today’s Networks
Evolution Towards MPLS Interworking
Brief MPLS Overview
Interworking concepts
Interworking Challenges
Conclusions

## Slide 26: Interworking Challenges-Sharing of LSPs
How to ensure QoS transparency if multiple services share same transport LSP, e.g., bandwidth sharing between ATM & FR?
MPLS Transport LSP
MPLS Transport LSP
ATM
ATM
FR
FR

## Slide 27: Interworking Challenges-QoS
ATM
ATM
MPLS tunnel with QoS x
MPLS tunnel with QoS y
Mapping of ATM services to diffserve classes for preservation of QoS transparency
Should the LSPs be segregated based on QoS classes?
Examples of service mapping
ATM Transfer
Capability
Diffserv Class
DBR
EF
SBR.1
EF
SBR.2/.3
AF1/AF2

## Slide 28: Interworking Challenges- OAM & Fault Management
ATM Network
A
ATM Network
B
LSP “tunnel”
IWF
IWF
= Possible trouble location
I.610
Y.1711
?
OSF/TMN
SNMP
How fault and performance monitoring capabilities between ATM and MPLS networks can be related?
How do the management I/F communicate (I.e., TMN (CMIP) and SNMP)?
How SLA performance management is handled?
?
Q3, M3

## Slide 29: Interworking Challenges -Protection Switching
ATM NWK
ATM
MPLS
working path
MPLS
protection path
ATM
working path
ATM
protection path
MPLS Network
Protection switching by OAM or fast reroute by control plane?
  IETF adopting restoration based on rerouting capabilities (control plane)
Local repair or end-to-end protection?
  Is local repair manageable?
ITU-T working on protection switching model based on extensions of basic SDH (Synchronous Digital Hierarchy) approach

## Slide 30: Interworking Challenges-Traffic Management
ATM Network
B
RSVP providing some flexibilities
Diffserv require substantial enhancement to LSR traffic management capabilities, i.e. CAC, policing
I.371 & TM4.1
Well defined
TM
capabilities
ATM Network
A
LSP “tunnel”
IWF
IWF
= Congestion
RSVP & Diffserv
?

## Slide 31: Outline
Today’s Networks
Evolution Towards MPLS Interworking
Brief MPLS Overview
Interworking Concepts
Interworking Challenges
Conclusions

## Slide 32: Conclusions
This presentation addresses interworking implications towards core networks evolution to MPLS.
Extensive standards activities, aimed at addressing interworking between different technologies and challenges posed by interworking, in ITU-T, ATM Forum and IETF.
The ATM-MPLS interworking is used to highlight approaches being adopted to achieve seamless interworking in the transfer plane, control plane and management plane functions.

## Slide 33: List of acronyms
ATM Asynchronous Transfer Mode
FR Frame Relay
ISDN Integrated Services Digital Network
ISIS Intermediate System to Intermediate System (an Intra- Domain Routing Exchange Protocol for use in Conjunction with the Protocol for Providing the Connectionless-mode Network Service
IWF Interworking Function
LSR Label Switching Router
MPLS Multi-Protocol Label Switching
NM Network Management
NSAP Network Service Access Point
OSPF Open Shortest Path First
PNNI Private Network-to-Network Interface
PSTN Public Switched Telephone Network
QoS Quality of service
RSVP Resource Reservation Protocol
SNMP Simple Network Management Protocol

## Slide 34: Thank you for you attention