## Slide 1: ITU-T SG16 Work on End to End Quality of Service in IP Multimedia Systems Mike Buckley Telchemy Inc

## Slide 2
Inter-relationship of QoS Factors
Codec Performance
Network Factors
Network Delay
Network Packet Loss
Network Jitter
Overall Delay
Application Factors
Overall Packet Loss
Jitter Buffers
Perceived Quality
QoS Service Level

## Slide 3
Max Packet Loss, Max Mean Delay, Max Delay Variation
TRANSPORT
APPLICATION
Codec Performance, VAD, Frames per Packet, Jitter Buffer Size,Codec Delay, FEC (Redundancy)
QoS Parameters
ITU-T SG16/11
ITU-T SG13/IETF
SERVICE
User Perceived QoS
ITU-T SG12/16

## Slide 4
ITU-T SG16 - New QoS Related Recommendations
H.qos.arch - QoS Architecture
H.priority - Procedures for controlling service priority
H.trans.control - QoS signalling to Transport Domains
H.323 Annex N - QoS signalling and control in H.323 systems
H.mmclass - Multimedia QoS Service classification
H.mmcp - Call processing performance in Multimedia Systems

## Slide 5
Network Packet Loss, Mean Delay, Delay Variation
TRANSPORT
Positioning of Q.F/16 Recommendations in relation to QoS Architecture H.qos.arch)
APPLICATION LEVEL
H.323 Annex N, H.mmcp, H.priority, H.policy, H.resilience
SERVICE LEVEL
H.mmclass, H.mmcp, H.priority
MANAG-
EMENT
LEVEL
H.qos.m
H.qos.m
H.qos.m
H.trans.cont, NSIS, RSVP, DIFFSERV, MPLS etc
TRANSPORT LEVEL
H.trans.control

## Slide 6: H.mmclass - Approach to Characterizing Service Level QoS
  QoS is defined subjectively as perceived by the user,
  It is end to end (e.g. mouth to ear for speech),
  A number of QoS Service Classes are defined,
  Classes include guaranteed quality (statistically) and unguaranteed (best effort).

## Slide 7: The TIPHON Speech QoS Classes
Undefined
Better than G.711
Listener Speech Quality
(One-way Non-conversational)
Equivalent or better than GSM-FR
Equivalent or better than G.726 at 32 kbit/s
Class
Wideband
Narrowband
Acceptable
Unguaranteed (Best Effort)
< 400ms*
< 150ms
< 100ms
< 100ms
End-to-end Delay (G.114)
> 50*
> 80
N.A.
Overall Transmission Quality Rating (R)
> 70
Medium
High
< 400ms
> 50
Undefined
* Target

## Slide 8
Network Packet Loss, Mean Delay, Delay Variation
Multimedia QoS Classification (H.mmclass)
APPLICATION
Application Factors (e.g. codec type, jitter buffer etc)
SERVICE
Voice
Video
Data
Voice Classes
Video Classes
Data Classes
Service Components (Classes e.g. G.1010 and TIPHON)
Service (e.g. videoconferencin,
broadcast video etc)
TRANSPORT
Bearer Classes
Bearer Classes
Bearer Classes
Voice Factors
Video Factors
Data Factors
Parametric (e.g. TIPHON) or Class based (e.g. Y.1541)

## Slide 9: The Concept of QoS Budgets

## Slide 10
Call Signalling
Packet Flow
QoS Signalling
Application Plane
Transport Plane
The H.qos.arch - general model
Service Domain 1
Transport Domain 1
Transport Domain 2
Transport Domain 3
Service Domain 1
Application Level QoS Signalling H.323 Annex N
Vertical QoS Signalling (H.trans.cont)
Transport Level QoS Signalling (H.trans.cont or NSIS)
H.323 Annex N
H.323 Annex N

## Slide 11: QoS in H.323 Protocols (Annex N)
    QoS is determined on a per media stream basis so QoS is negotiated per media stream via H.245. New fields in H.245 under development.
    QoS Class may be requested by End User via H.245 or H.225.0. Additions to both protocols under development to enable this.
    QoS characteristics of terminals may be registered with service providers. This involves additions to H.225.0 RAS.
New Annex N of H.323

## Slide 12: New Vertical Protocol (H.trans.cont)
  Used to signal QoS parameters (max delay, max jitter, max packet loss) to each domain
  Typically will be between GK or Media Gateway Controller and Edge Router or Transport Resource Manager
  Will use H.248/Megaco (with new extensions)

## Slide 13: Service Priority (H.priority)
    Defines Service Types (Way in which QoS Services are offered)
    Defines classes of Session Priority
    For H.323 signalled in H.460.3
H.priority provides framework for Emergency Services

## Slide 14
Summary
H.mmclass provides Service level QoS classification for each service component. (Consistent with G.1010)
H.priority defines session priority and service types
New protocol H.trans.cont required for Application to Transport Level signalling
H.323 Annex N - QoS signalling and control in H.323 systems
H.qos.arch defines domain by domain QoS approach allowing QoS signalling at Application and Transport levels