## Slide 1: Cable broadband delivery (Cable modem transport platforms)
Richard Catchpole
ITU-T Study Group 9 Associate Rapporteur
rjc@nortelnetworks.com
ITU-T Workshop on Multimedia Convergence
March 12th-15th, 2002

## Slide 2
“Cable modem”
“Cable modem” is the term used for equipment for “data communications on a cable television system” [Rec. J.112].
ITU-T Rec. J.112 defines inter-operability of this subscriber located equipment with the cable network.
“Cable modem” is also know as “Interactive Interface Module” [DVB], “Multimedia Home equipment” [Japan].

## Slide 3: Services to be supported by cable modems (IPCablecom services, etc.)
Internet access
Residential/Business IP Telephony
Video IP telephony
Voice/data/video unified messaging
Enhanced conferencing and media services
Entertainment Services
  Real-time multiplayer interactive gaming

## Slide 4: Cable modem system
AN Access Node
CM Cable Modem
HFC Hybrid Fiber Coax network
ISP Internet Service Provider
MTA Multimedia Terminal Adapter
PSTN Public Switched Tel. Network
PSTN
CM
MTA
Managed IP
Network
AN
CM
HFC

## Slide 5: Broadcast reference model

## Slide 7: DVB preferred frequency ranges [J.112A]

## Slide 8: Cable modem physical layer
Downstream, Access Node to Cable Modem, uses TDM over the digital broadcast for cable standards [ITU-T Rec. J.83 A, B, C as used in Regions 1, 2, 3 respectively].
Convolutional interleaving
Reed Solomon encoding
QAM modulation
Upstream, Cable Modem to Access Node, uses TDMA
TDMA slots can be reserved or allocated by contention resolution, according to the required QoS
Reed Solomon encoding
QPSK or QAM, with advanced modulation for further study

## Slide 9: Basic standards process for cable modems
CableLabs
ITU-T
SCTE
…
Global SDO level:
Regional
/national
SDO level:
Contributor
Level:
ETSI
TTC
(Japan)
Vend.
Vend.
Vend.
ETSI European Telecom Standards Institute
ITU-T International Telecom Union, Telecom sector
SCTE Society of Cable Telecom Engineers
SDO Standards Development Organisation (accredited)
Vend. Vendor
Standards draft text to IPR terms of recipient
tComLabs

## Slide 10: Cable modem standards progress
Dec. 1996: Internet access versions of DAVIC/DVB and DOCSIS™ specifications published.
Dec. 1998: Above ratified by ITU-T as J.112 A&B respectively, plus a variant of DOCSIS™ as J.112 C for Japan. J.112A ratified by Region 1 SDO [ETSI], J.112B by Region 2 [ANSI/SCTE] and J.112C by Region 3 [Japan].
Oct. 2000: For time critical services, further versions of DAVIC/DVB and DOCSIS™ specifications published.
March 2001: Those further versions ratified by ITU-T by amendment to J.112 A&B, resp. Both ratified by ETSI.
Feb. 2002: Version for time critical services for Japan ratified by ITU-T by amendment of J.112C.

## Slide 11: Cable modem testing program
Inter-operability testing and certification for ITU-T J.112B cable modems is done by:
  CableLabs for main text option within J.112B [DOCSIS™]
  tComLabs for Annex N option within J.112B [ EuroDOCSIS]
Many cable modem vendors have had their products certified in this way already
The consequence has been multi-sourcing of fully inter-operable cable modems, together with the rapid price reduction needed for successful take-up of bi-directional broadband services.
There are already over 10 million worldwide!

## Slide 12
J.112B Testing Process
Business
Reqts.
Test
Plans
Specs.
Test Case
Implementation
Execution
& Results
Requirements.
Management
J.112B “DOCSIS” by CableLabs, USA
J.112B “EuroDOCSIS” by tComLabs, Belgium

## Slide 13: For more information…
ITU-T Q12/9 on cable TV delivery of multimedia using IP or packets:
  Rapporteur: Rouzbeh Yassini (rouzbeh@yas.com)
  Assoc. Rapporteur: Richard Catchpole (rjc@nortelnetworks.com)
ETSI JTC/Broadcast: http://portal.etsi.org, and click on “Broadcast”
  Rapporteur: Richard Catchpole (rjc@nortelnetworks.com)
CableLabs: http://www.cablemodem.com
tComLabs: http://www.tcomlabs.com

## Slide 14: Cable modem summary
Focus
  Initially on internet access
  Then on Voice over IP
  In future on multi-media
This evolution in focus has required the introduction of more sophisticated QoS and security
Rapidly growing deployment, already exceeding 10M