## Slide 1: SG 15 activity on Broadband Delivery and In-Home Networking Andrew Nunn (BT, UK) Chairman ITU-T WP1/15

## Slide 2
Contents
Introduction
Questions under study
Typical Access Network construction
Optical Access Networks
Digital Subscriber Loop (xDSL) &
Home Phoneline Networking
Current/future work
Other SDOs/Bodies
Summary

## Slide 3
Questions Under Study
Q.2/15 - Optical systems for access networks
Rapporteur: Dave Faulkner (BT, UK)
Q.3/15 - Support for Recommendations Specifying Systems Based on ISDN Physical Layers Lead Study Group
Rapporteur: Koji Kikushima (NTT, Japan)
Q.4/15 - Transceivers for customer access and in-premises phone line networking systems on metallic pairs
Rapporteur: Dick Stuart (Aware, USA)

## Slide 4: Typical Access Network Construction
Central Office
(Exchange)
Feeder Network
Street Cabinet
Distribution Network
Overhead
Feed
Underground
Feed
Customer

## Slide 5
Q.2/15 - Optical systems for access networks
Recommendations
G.983.1 + Amendment 1 - High speed optical access systems based on Passive Optical Network (PON) techniques
G.983.2 - ONT Management and Control Interface specification for ATM PON

## Slide 6
Q.2/15 - Optical systems for access networks
Recommendations (continued)
G.983.3 - A broadband optical access system with increased service capability by wavelength allocation
G.983.4 - A broadband optical access system with increased service capability using Dynamic Bandwidth Assignment

## Slide 7
Q.2/15 - Optical systems for access networks
Recommendations (continued)
G.983.5 - A broadband optical access system with enhanced survivability
G.983.7 - ONT Management and Control Interface specification for Dynamic Bandwidth Assignment

## Slide 8
Access Fibre Deployment Scenarios
FTTBasement
Local Exchange
Street Cabinet
DP
Customer
FTTCabinet
FTTKerb
FTTHome
Fibre
Copper
Optical Splitter

## Slide 9
G.983.1 + Amendment 1 - High speed optical access systems based on Passive Optical Network (PON) techniques
ATM-PON
155.520/155.520 Mbit/s, 622.080/155.520 Mbit/s or 622.080/622.080 Mbit/s downstream/upstream
Single or two fibre working
Maximum range of at least 20 Km

## Slide 10
G.983.3 - A broadband optical access system with increased service capability by wavelength allocation
Defines new wavelength allocations to distribute ATM-PON signals and additional service signals simultaneously
Allows distribution of video broadcast services or data services without disturbing basic ATM-PON system

## Slide 11
Q.4/15 - Transceivers for customer access and
in-premises phone line networking systems on metallic pairs
Recommendations
G.991.1 - High bit-rate Digital Subscriber Line
        (HDSL)
G.991.2 - Single-pair High-speed DSL (SHDSL)
G.992.1 - Asymmetrical DSL (ADSL)
G.992.2 - ‘Splitterless’ or ‘lite’ ADSL

## Slide 12
Q.4/15 - Transceivers for customer access and
in-premises phone line networking systems on metallic pairs
Recommendations (continued)
G.993.1 - Very high bit rate DSL (VDSL) – Foundation
G.994.1 - DSL Handshaking procedures
G.995.1 - Overview of DSL Recommendations

## Slide 13
Q.4/15 - Transceivers for customer access and
in-premises phone line networking systems on metallic pairs
Recommendations (continued)
G.996.1 - DSL Testing procedures
G.997.1 - DSL Physical Layer management
G.989.1 - Phone-line Networking - Foundation
G.989.2 - Phone-line Networking - Payload format and Link Layer requirements

## Slide 14
xDSL Deployment Scenarios
Local Exchange
Street Cabinet
DP
Customer
ADSL
VDSL
Fibre
Copper
Copper

## Slide 15
G.992.1 - Asymmetric Digital Subscriber Line transceivers
One twisted pair
Payload upstream up to 640 kbit/s
Downstream up to 6.144 Mbit/s
Simultaneous Voiceband and N-ISDN possible
Line Code - DMT (Discrete MultiTone)

## Slide 16
G.993.1 - Very high bit-rate Digital Subscriber Line transceivers
One twisted pair
Asymmetric and symmetric data rates up to tens of Mbit/s
Frequency Division Duplexing to separate upstream & downstream traffic
Three band plans defined occupying 138kHz up to 12 MHz

## Slide 17
G.989.1/G.989.2 – Home Phoneline Networking Transceivers
In-premises distribution of data over existing phoneline wiring
Nominal effective throughput equal to 10BASE-T Ethernet
Compatibility with other phoneline services such as POTS, V.90/V.92, ISDN and G.992.2
Spectrum notching for compatibility with Amateur Radio services

## Slide 18
Q.2/15 - Optical systems for access networks
Current/future work
Enhancement of G.983.2 to support survivability (G.983.5) and new services
Enhancement of G.983.3 to include 622.080 Mbit/s upstream rate
Gigabit PON (2.48832 Gbit/s ?)

## Slide 19
Q.4/15 - Transceivers for customer access and in-premises phone line networking systems on metallic pairs
Current/future work
Revision of Single-pair High-speed DSL (SHDSL) - G.991.2
Second Generation ADSL
Second Generation‘Splitterless’ ADSL

## Slide 20
Q.4/15 - Transceivers for customer access and in-premises phone line networking systems on metallic pairs
Current/future work (continued)
Very high bit rate DSL (VDSL) – G.vdsl.l
Phone-line Networking - Isolation Filter – G.pnt.if
Voice over DSL
Bonding of DSL systems
Power Line Transmission (in-premises only)?

## Slide 21
Other SDOs/Bodies
FSAN
ETSI/TM6
T1E1.4
DSL Forum
IEEE 802.3 ah EFM
TR30

## Slide 22
Summary
ITU-T SG 15 has produced a comprehensive set of broadband access network standards for both copper and fibre media
B-PONs either alone of in conjunction with VDSL provide a basis for the implementation of a full service access network
On-going activities are focussing on higher bitrates and transport of packet/Ethernet traffic