## Slide 1: Broadband Passive Optical Networks
March 14, 2002
Tim Gyselings, Alcatel
Tim.gyselings@alcatel.be

## Slide 2: Content
PON Characteristics
PON and Standardisation
Standardisation groups
On-going standardisation activities
Conclusion
Existing PON recommendations

## Slide 3: BPON Characteristics
1:32 (64)
0-20 km
DS: 155/622 Mbit/s
US: 155/622 Mbit/s
Access Node
NB
BB
CC
LT
LT
...
ONU
ONU
ONU
...
BPON = Broadband Passive Optical Network
passive optical splitter
BPON is a full service access network :
support for voice, data and video connections
optical fibre

## Slide 4: FTTx with BPON
OLT
ATM NETWORK
LL Network
OTHER
POTS/ISDN
V5
VB5
G.703
ONU
ANT
PS
ADSL ( < 6 KM )
< 8 Mbit/s
FTTEx
ONU
XNT
STB
PS
ADSL/VDSL ( < 1 KM )
< 26 Mbit/s
FTTCab
ONU
XNT
STB
PS
VDSL/DHN ( < 300 M )
< 52 Mbit/s
FTTC
ONU
ONT
STB
PS
< 622 Mbit/s down
< 622 Mbit/s up
FTTH/B
FITL

## Slide 5: Standardisation
ITU-T SG15 generates Recommendations to standardise access technologies (amongst which PON systems)
Recommendations are backed by vendors and operators in industry forum FSAN (Full Service Access Network)
Benefits of wide backing of Recommendation:
  Interoperability between vendors by common system description and performances
  Maximising volumes with common specifications, leading to cost-effective products

## Slide 6: Recommendation: G.982
Access Node
NB
BB
CC
LT
LT
...
ONU
ONU
ONU
...
G.982 : Optical access networks to support services up to the
ISDN primary rate or equivalent bit rates
Optical Distribution Network
ODN class A: 5 - 20 dB loss
ODN class B: 10 - 25 dB loss
ODN class C: 15 - 30 dB loss

## Slide 7: Recommendation: G.983.1
Access Node
NB
BB
CC
LT
ONU
G.983.1 + amendment : Broadband optical access systems based on
passive optical networks
ONU
ONU
1:32 (64)
0-20 km
DS: 155/622 Mbit/s @ 1530 nm ± 50
US: 155/622 Mbit/s @ 1310 nm ± 50
TDMA
TDM

## Slide 8: Recommendation: G.983.2
Access Node
NB
BB
CC
LT
ONU
G.983.2 + amendment : ONT management and control interface
specification for ATM PON
ONU
ONU
TDM
ONUs managed by LT via OMCI
(ONT Management and Control Interface)
TDMA

## Slide 9: Recommendation: G.983.3
G.983.3 : A broadband optical access system with increased service
capability by wavelength allocation
Access Node
NB
BB
CC
LT
ONU
ONU
ONU
G.983.1
US
DS
nm
nm
1260
1360
1480
1580
G.983.3
US
DS
nm
nm
1260
1360
1480-1500
nm
Future Use
1380
1460
EB
FU
1539-1565
?
distributive video (analogue and/or digital)
dedicated wavelength connections (US and/or DS)
Enhancement Band :

## Slide 10: Recommendation: G.983.4
TDMA
Time period 1
TDMA
Time period 2
G.983.4 : A broadband optical access system with increased service
capability using dynamic bandwidth assignment
Access Node
NB
BB
CC
LT
ONU
ONU
ONU
TDMA
Time period 3
SBA: 622 Mbps / 32 users = 20 Mbps / user
DBA: 20 Mbps average; 622 Mbps peak
DBA: statistical multiplexing gain of PON BW
G.983.7 : ONT management and control interface specification for
DBA B-PON system

## Slide 11: Recommendation: G.983.5
G.983.5 : A broadband optical access system with enhanced
survivability
Access Node
NB
BB
CC
LT
ONU
ONU
ONU
LT
ONU
ONU
ONU
Protection against board - network failure
Redundant network can be used to transmit low priority traffic

## Slide 12: On-going standardisation
Access Node
NB
BB
CC
LT
ONU
ONU
ONU
DS: 1.25 / 2.5 / 10 Gbps
US: 0.155 / 0.622 / 1.25 / 2.5 / 10 Gbps
G.GPON: Gigabit Passive Optical Network
Recommendation for Gigabit PON system is under development
Physical Medium layer
  Optical Distribution Network: G.982
  Wavelength plan: G.983.3
  Use of FEC is under discussion
  Optical interface parameters are under discussion
  Speed: DS 1.25 Gbps - 10 Gbps ; US 155 Mbps - 10 Gbps
Transmission Convergence layer
  Frame structure to be defined
  Basic timeslot and US overhead to be defined
  Fixed timeslot or variable timeslot
  Cell oriented or packet oriented
Target: Recommendation approved by end 2003

## Slide 13: Conclusion
ITU-T has approved a well balanced set of recommendations covering all aspects of BPON (G.983.1 has been approved in 1998)
Solid basis for implementation of a full service access network, offering data, voice and video
On-going activities are opening an evolution path by focussing on higher bitrates and packet oriented PON systems
The existing and emerging recommendations are a strong catalyst for the PON market

## Slide 14
Do you have
any
questions ?