## Slide 1
Never stop thinking.
INFINEON
Home Gateway - The Subscriber‘s Choice
14. March 2002
Matthias Kindler
Business Development Manager
Communication Business Group
ITU Workshop on IP Cablecom/ Mediacom 2004/ Interactivity in Multimedia

## Slide 2: AGENDA
Part 1: xDSL Technology
xDSL - Broadband over twisted-pair
xDSL - An Access and In-house Distribution Technology
Infineon’s Position in xDSL
Part 2: The Home Gateway
Home Gateway - The Subscriber’s Choice
Home Gateway - The Value Chain
Home Gateway - Challenges
HG-Processor - The Heart of the Home Gateway
Home Gateway: Example 1
Home Gateway: Example 2
Conclusions

## Slide 3: Part 1: xDSL Technology

## Slide 4: xDSL - Increases The Capacity of Copper Networks
Modem
ISDN
ADSL
SHDSL
1.5 - 8 Mbps
0.3 / 2 Mbps
VDSL
2 - 26 Mbps
2 - 26 Mbps
3 - 4000 feet
12 - 12000 feet
> 15000 feet
160 kbps
56 kbps

## Slide 5: xDSL – Spectral Allocation
Co-exists with legacy services

## Slide 6: The ADSL Market
Source: SalomonSmith Barney, March 2002
16 million ADSL subscribers end of 2001
Expected growth 02/01: 98%
Main growth is expected in Europe and Japan
ADSL is the dominant xDSL Technology today
ADSL is the dominant Broadband Access Technology today

## Slide 7: xDSL - Distributing Broadband Services in the Building
xDSL - Not only an Access Technology, but also for In-house data distribution over twisted-pair
10BaseS is: Ethernet over VDSL
10BaseS Features:
  10 Mbps symmetric Ethernet
  VDSL robust performance
  POTS/ISDN support
  Reach up to 4000ft/1200m
10BaseS Typical Applications
  MTU/MDU, hospitality
  Fiber, Wireless, Cable LAN extension

## Slide 8: Ethernet over VDSL - The Best of Both Worlds
Ethernet
  Mature, low-cost, zero configuration
  Minimal connectivity and service overhead
  Quick roll-out, little provisioning
VDSL
  Robust performance over single copper pair
  Symmetrical and asymmetrical data transmission up to 26Mbps
  Reach up to 4000ft/1200m

## Slide 9: 10BaseS – Ethernet over VDSL from Infineon Modem Board Diagram
10BaseS-D
PEF 22822
MII, RMII SMII
DAC
ADC
Control
Broadband Amplifier
PEF 22810
Line
Filters, Hybrid, Splitter
Telephony Device
10BaseS PHY
10/100
Base-T PHY
Magnetics
10BaseS CPE
Switch
Chipset
Existing telephone wires and service
10BaseS CO
10BaseS
PHY
10BaseS
PHY
10BaseS
PHY
10BaseS
PHY
VDSL-A
PEB 22811

## Slide 10: Part 2: The Home Gateway

## Slide 11: Home Gateway - The Subscriber‘s Choice
xDSL - Access
VDSL, SHDSL, ADSL
Fiber - Access
APON, EPON
Cable - Access
DOCSIS 1.1
Wireless - Access
MMDS, LMDS, Satellite
Wireline
Home- Networks
Ethernet
Twisted Pair
10BaseS
1394
USB
Coax
Wireless
Home Networks
802.11x
HIPERLAN
HomeRF
DECT
Bluetooth
Data
Data + Voice
Data + Voice
+ Video
Notes: Introduction:
The home gateway is the interface between the external access network and the home network
Data and voice services are delivered to the home gateway over ATM or IP protocol
Video is delivered over dedicated channels, ATM or IP channels
External access network technologies can be ADSL, SHDSL, VDSL, APON, wireless ...
Distribution technologies of the different services in the home can be done with a wirebased or wireless interfaces

## Slide 12: Home Gateway - Value Chain
Customer
Service
Provider
System
House
IC
Supplier
Standard
Groups
Customer’s
Choice
Specific
Challenges
for
Service
Providers
The Customer’s choice leads to specific challenges and requirements for all parts of the value chain.
Specific
Challenges
for
System
Houses
Specific
Challenges
for
IC
Supplier
Specific
Challenges
for
Standard
Groups

## Slide 13: The Customer’s Choice leads to challenges...
… for the Service Provider
      Customer has the responsibility for his own home network
      Customer is confused with all the technology options
      Customer wants data, voice and video services
… for the System House
      flexible platform needed to be able to adopt fast to different or changing requirements
… for the IC supplier
      (see next slide)
… for the standardization group
      Time-to-market
      Broad industry consensus required

## Slide 14: The Customer’s Choice leads to challenges...
… for the IC Supplier
  Deal with broad range of Broadband Access Technologies (not all will survive)
  Deal with broad range of Home Networking Technologies (not all will survive)
  Support of different services: Data, Voice or Video
  HW and SW expertise required
  ATM and Ethernet expertise necessary
  More and more customers require security
  Flexible Platform needed

## Slide 15: HG-Processor - Heart of the Home Gateway
Home Gateway
Processor
xDSL
VDSL, SHDSL, ADSL
Fiber
APON
Cable
DOCSIS 1.1
Wireless
MMDS, LMDS, Satellite
Wireline
Home- Networks
Ethernet
Twisted Pair
10BaseS
1394
USB
Coax
Wireless
Home Networks
802.11x
HIPERLAN
HomeRF
DECT
Bluetooth
Notes: Introduction:
The home gateway is the interface between the external access network and the home network
Data and voice services are delivered to the home gateway over ATM or IP protocol
Video is delivered over dedicated channels, ATM or IP channels
External access network technologies can be ADSL, SHDSL, VDSL, APON, wireless ...
Distribution technologies of the different services in the home can be done with a wirebased or wireless interfaces

## Slide 16: Challenges translated into Target Spec (1)

## Slide 17: Challenges translated into Target Spec (2)

## Slide 18: EasyPort - The Heart of the Home Gateway
Packet Engine
32-bit RISC coprocessor 2 Ethernet 10/100 (one PHY integrated) HDLC, USB DES/3DES
Voice Engine
32-bit RISC coprocessor
2 PCM/IOM-2 units
HDLC
Cell Engine
Utopia/Serial ATM
traffic management
AAL2/AAL5
CPU Subsystem
64-bit RISC MIPS 5kc
64 + 64 kByte Caches
SDRAM Controller
Peripherals
External Bus Unit
SSC/SPI/2 UART
Timer Unit….
ISDN
Ethernet
HomePNA
USB
V.35
SDRAM
Flash SRAM Peripherals
APON xDSL
Notes: IAD Processor Family - Highlights
CPU: MIPS 64
  Powerful k5c core, 64-bit architecture, 200 MHz.
  Established, proven and backward compatible core.
Real-time and hardware acceleration:
  Separate 32-bit RISC for voice processing (voice engine)
  Separate 32-bit RISC for data packet processing (packet engine)
  ATM hardware acceleration (cell engine)
  DES/3DES hardware acceleration.
Software:
  Royalty free open source Linux based BSP and reference software.
  Major reuse over the family of IADs.
  Ready for customer specific modules.
Firmware:
  Turnkey firmware for DSPs and RISC accelerators.
  Royalty free.

## Slide 19: Example 1: SHDSL + HG-Processor + Voice
Ethernet
Home
Gateway
Processor
DC/DC
Converter
SLIC
Vinetic-4
VIP
DSP
SBCX-X
SLIC
SLIC
SLIC
SHDSL
Transceiver
ISDN
ISDN
SBCX-X
SDRAM
FLASH
IOM / PCM
t/r
t/r
t/r
t/r
S-IF
S-IF
parallel
µP IF

## Slide 20
Example 2: APON + HG-Processor + 10BaseS
LAN
VDSL NTU
APON ONU with VDSL support
Local Router
Copper UTP
Fiber
Connection
To the CO
APON
Transceiver
HG
Processor
10BaseS PHY
10BaseS PHY
10BaseS
Switch

## Slide 21: Conclusions
ADSL is the dominant Broadband Access Technology today.
The Subscriber’s choice generates the need for a flexible Home Gateway platform solution.
Service Providers, System Houses, IC suppliers and Standardization Groups face their specific challenges and requirements due to the customer’s choice.
A flexible Home Gateway Processor will be the heart of a Home Gateway to connect different kind of Broadband Access Transceivers with different Home Networking Technologies for different kind of services.

## Slide 22
And don‘t forget:
„Never stop Thinking“
Thank you!