## Slide 1: Multicast Delivery of Broadband Multimedia Applications and Services
Seok Joo Koh
ETRI/KOREA
Editor of X.606 in Q.8/17
sjkoh@pec.etri.re.kr

## Slide 2: Table of Contents
Broadband Multimedia & Multicast
  Characteristics & Requirements
Delivery for Broadband Multimedia
  Possible Delivery Schemes
Multicast Technologies for Broadband Multimedia
  Current Status & Outlook
Related Activities in ITU-T
  In Q.8/17 (end-to-end QoS multicast communications)
  Protocols: ECTP, GMP, and RTM
Future Works

## Slide 3: Broadband Multimedia & Multicast
Characteristics of Broadband Multimedia Services
  Broadband: up to 1-2 Mbps per session
    Bandwidth (resource) consuming
  Multimedia: audio/voice, video, data
  Real-time and live broadcasting: time-critical
Characteristics of Multicast Services
  Group Communications
    Many receivers at the same time
    Cooperation & interaction between users
  Multicast delivery is essential for
    Efficient utilization of network bandwidth (resource)
      Compared to multiple unicast connections
  Technological Challenges for Multicast
    Reliable Multicast, QoS management, Group Management, etc

## Slide 4: Multicast Applications
Classification of Multicast Applications
  Collaborative: Teleconferencing
  Message Streaming: Streaming Media Player
  Bulk Data Transfer: Multicast File Dissemination

## Slide 5: Examples of Multicast Services
One-to-Many Multicast
  Internet TV, Webcasting
    Webcasting of Broadband Streaming Media
  Remote Education
  Distribution of Financial Data: Stock-ticker
Many-to-Many Multicast
  Teleconferencing
  Whiteboard
Current Trend
  Most of commercial services are based on
    One-to-Many Multicast Services
  Most of ISPs focus on one-to-many services

## Slide 6: Webcasting of Broadband Multimedia
Typical Webcasting System

## Slide 7: Possible Delivery Schemes
Replicated Unicast
  TCP/IP unicast connection to each receiver
  Multiple unicast connections for a session
Native IP Multicast
  Within multicast-enabled networks
  Multicast forwarding tree between multicast Routers
  IGMP between router and hosts
Hybrid of Unicast and Multicast
  Unicast from Sender and Relay Server:
    Over unicast networks
  Multicast from Relay Server to Recipients
    Within the multicast-enabled networks

## Slide 8: Unicast Delivery for Broadband Multimedia
CP
Local Network
Local Network
Internet

## Slide 9: Multicast Delivery for Broadband Multimedia

## Slide 10: Hybrid Delivery of Unicast and Multicast

## Slide 11: Comparison of delivery schemes
Replicated Unicasts (current & most)
  Easy to employ, but
  Bandwidth Consuming in the network
  Traffic bottleneck at the sender (contents provider)
IP Multicast (ideal & best)
  Most efficient in terms of utilization of network resources
  But, still much technical challenges to solve
  Not fully deployed in commercial Internet
Hybrid of Unicast and Multicast (realistic alternative)
  An realistic alternative delivery scheme
  For migration to IP multicast
    Based on unicast and multicast

## Slide 12: Multicast Technologies for Broadband Multimedia
Multicast Routing in Networks
  Layer 3 forwarding by Routers
  Multicast Routing Protocols
    DVMRP, PIM, CBT, etc
End-to-End Multicast Transport
  Layer 4 multicast management
  Reliable Multicast & QoS Management
    ECTP, IETF RMT, etc
Multicast Group Management
  Application-level Group Management
  Session Management & Membership Management

## Slide 13: Multicast Routing Protocols
Intra-Domain Routing Protocols
  Source tree: DVMRP, PIM-DM, MOSPF, SSM
  Shared tree: PIM-SM, CBT
Inter-Domain Routing Protocols
  MSDP/MBGP/PIM-SM
  BGMP: tree of domains
Status
  Intra-domain routing protocols are stable
    Deployed in private and local Internet
  Inter-domain routing protocols are premature
    Traffic/Policy negotiation issues between ISPs

## Slide 14: End-to-End Multicast Transport
Reliable Multicast
  Issues: Scalability Concerns (error/congestion control)
  IETF RMT WG
    TRACK (Tree-based ACK) protocol
    ALC (Asynchronous Layered Coding) protocol
    NORM (NACK Oriented Reliable Multicast) protocol
  ITU-T Q.8/17
    ECTP (Enhanced Communications Transport Protocol)
QoS Management
  QoS negotiations/monitoring/maintenance issues
  Working in ITU-T Q.8/17 (ECTP)

## Slide 15: Group Management Protocol
Session Management
  Session creation/enrollment
  User registration/authentication
Membership Management
  Active membership monitoring and report
  Support of billing/charging model
Status
  IETF: SDP/SAP, SIP
  ITU-T Q.8/17: GMP (working)

## Slide 16: Activities in ITU-T Q.8/17
Work items of Q.8/17
  ECTP (Enhanced Communications Transport Protocol)
    ECTP-1 (X.606): Reliable Multicast
      Approved (2001.10)
    ECTP-2 (X.606.1): Multicast QoS Management
      To be approved (2002)
  GMP (Group Management Protocol)
    X.gmp: Session/membership Management
  RTM (Relayed Transport for Multicast)
    X.rtm: Hybrid delivery of broadband multicast traffic
      Based on unicast and multicast transports

## Slide 17: ECTP: model

## Slide 18: ECTP: Overview

## Slide 19: ECTP: Features
Interaction with IETF
  Adopt the IETF TRACK approach for error conrol
  Some inputs to Tree BB and TRACK BB
ECTP distinctively provides
  Tight Connection Control (ECTP-1)
    Sender is at the heart of the multicast communications
    Session Creation/termination/pause/resume
    Connection Join via Sender (after authentication)
  QoS-based Session Management (ECTP-2)
    Support of resource reservation (RSVP)
    Session Monitoring & Maintenance
    Rate adaptation based on the monitored QoS status

## Slide 20: ECTP: Tree-based Error Control
ACK packets flow children to Sender via Parents

## Slide 21: ECTP: QoS Negotiation
Negotiation between Sender and Receivers

## Slide 22: ECTP: QoS Monitoring/Maintenance

## Slide 23: GMP: Overview
Group Management Protocol
  Session management: Group Creation/Registrations
  Membership Management (MMP)
Session Management
Application
MMP
TCP/UDP
ECTP
IP

## Slide 24: Relayed Transport for Multicast (RTM)

## Slide 25: Framework of RTM
RTM is based on two-level hierarchy
  Unicast or Multicast from Sender to Relay Agent (RA)
  Unicast or Multicast from Relay Agent (RA) to Receivers
Four possible transports scenarios
  Unicast (S  RA) & Unicast (RA  R)
  Unicast (S  RA) & Multicast (RA  R)
  Multicast (S  RA) & Unicast (RA  R)
  Multicast (S  RA) & Unicast (RA  R)
Extensions of RTM
  More than two levels of hierarchy
  Subnet Multicast in a local LAN: relatively easy to deploy

## Slide 26: Multicast for Broadband: Status
Multicast deployment has been delayed
  Technical aspect: concerns of scalability & traffic control
  Services aspect: lack of multicast killer applications
  Business aspect: uncertainty of multicast business model
Increasing needs of Multicast deployment
  Broadband Multimedia Services
    Webcasting of broadband streaming media
    Remote education, stock-tickers, etc
  Visualized Business model
    High revenue of broadband multimedia industry

## Slide 27: Multicast for Broadband: Outlook
Deployment Scenarios for broadband multimedia
  Stage 1: until 2003
    Unicast only or local multicast only in private networks
    As shown in the current services
  Stage 2: until 2005
    Hybrid delivery of unicast and multicast
    Seamless transport via Relay Agents
      Unicast over non-multicast regions
      Multicast over multicast-enabled regions
  Stage 3: since 2005
    Expansion of multicast-enabled networks

## Slide 28: Multicast for Broadband: Summary
Broadband Multimedia Services
  Critical need of multicast delivery
    For network resource utilization
    For real-time live broadcasting
    For enhanced business model of broadband multimedia
Multicast Technologies
  Basic technologies are stable: multicast routing
  But, still need to improve some more
    QoS management, Group management, etc
  To accelerate multicast deployment,
    Need to develop an alternate solution for multicast
    Relayed Transport based on unicast and multicast

## Slide 29: Future Works
Development of multicast technologies
  Multicast control at transport layer
    ECTP (Enhanced Multicast Transport Protocol)
    GMP (Group Management Protocol)
  Alternative delivery scheme for multicast
    RTM (Relayed Transport for Multicast)
Deployment of multicast services
  Consolidation of business model
    Broadband multimedia services
    Multicast delivery services
  Interaction between service & technologies

## Slide 30: References
ITU-T Recommendations
  X.601: multi-peer commnunications
  X.605: ECTS (Enhanced Communications Transport Services)
  X.606: ECTP-1 (part1)
  X.606.1: ECTP-2 (part 2)
  X.gmp: working document in Q.8/17
  X.rtm: working document in Q.8/17
http://ectp.etri.re.kr
IETF WG
  RMT WG
  MBONED WG