## Slide 1: NORTH AMERICAN PROGRESS IN MULTIMEDIA BROADCASTING
Workshop on IP Cablecom/Mediacom 2004/
Interactivity in Multimedia
Geneva, 12 - 15 March 2002
by
Metin Akgun
Communications Research Centre Canada

## Slide 2: INTRODUCTION
Digital Broadcasting Infrastructure
- Radio Broadcasting
- Television Broadcasting
Multimedia Broadcasting Standards
Multimedia Broadcasting Applications

## Slide 3: DIGITAL BROADCASTING INFRASTRUCTURE
USA
Radio Broadcasting
- Terrestrial
- Satellite
Television Broadcasting
- Terrestrial
- Satellite
- Cable TV

## Slide 4: DIGITAL RADIO BROADCASTING IN THE USA
Terrestrial Radio Broadcasting
- Replacement for AM and FM Radio
- Will use the existing spectrum (IBOC)
- Initially will coexist with AM and FM broadcasting
- Will use System C of ITU-R Rec. BS.1114 in the FM band
- Initially limited spare capacity for multimedia,
increased capacity when FM broadcasting ceases
- Has not yet been implemented
- Similar technology planned for the AM band

## Slide 5: DIGITAL RADIO BROADCASTING IN THE USA (cont’d)
Satellite Radio Broadcasting (S-DARS)
- Operates in the 2.3 GHz band
- There are two service providers
- XM Satellite Radio Inc.
- Operates from two satellites
- System augmented by 1,000 terrestrial repeaters
- Provides 100 different programs
- Sirius (Service launched in 2002)
- Operates from 3 satellites
- System will be augmented by terrestrial repeaters
- Provides 100 different programs

## Slide 6: DIGITAL TELEVISION BROADCASTING IN THE USA
Terrestrial Television Broadcasting
- Uses System A of ITU-R Rec.1309-1 (8-VSB)
- Uses the existing VHF and UHF TV broadcast bands
- Each 6 MHz channel has ~20 Mb/s capacity
- Over 200 digital TV transmitters exist now
- Currently covers 70% of population

## Slide 7: DIGITAL TELEVISION BROADCASTING IN THE USA (cont’d)
Satellite Television Broadcasting
- Operates in the BSS band
- There are two service providers
- Direct TV
- Echo Star
- Technologies are not compatible with each other
- Decoder STB’s provide interactive capability
- Early models provide return link by PSTN
- New models provide high speed satellite return
link
- 17 million subscribers (16% of TV households)

## Slide 8: DIGITAL TELEVISION BROADCASTING IN THE USA (cont’d)
Cable Television
- Digital Cable Standards have been developed by SCTE
and CableLabs
- All STB’s conform to the Open Cable concept
- STB’s provide return interaction channel
- 73 million basic cable subscribers (70% of TV
households)
- 14 million digital cable subscribers (18% of basic cable
subscribers)

## Slide 9: DIGITAL BROADCASTING INFRASTRUCTURE
CANADA
Radio Broadcasting
- Terrestrial
- Satellite
Television Broadcasting
- Terrestrial
- Satellite
- Cable TV

## Slide 10: DIGITAL RADIO BROADCASTING IN CANADA
Terrestrial Radio Broadcasting
- Replacement for AM and FM Radio
- Will operate in the L-Band
- Will use System A (EUREKA 147) of ITU-R Rec. BS.1114 - 20-30% of capacity available for multimedia,
- DBA service started in 1999
- Service available in Montreal, Toronto, Windsor and
Vancouver - covers 35% of population
- Rapid deployment in high population density corridors -
Quebec-Windsor, Edmonton-Calgary, Fraser Valley
- DAB receivers in some 2003 model GM cars

## Slide 11: DIGITAL RADIO BROADCASTING IN CANADA (cont’d)
Satellite Radio Broadcasting (S-DARS)
- Not planned for Canada at this time

## Slide 12: DIGITAL TELEVISION BROADCASTING IN CANADA
Terrestrial Television Broadcasting
- Uses System A of ITU-R Rec.1309-1 (8-VSB)
- Uses the existing VHF and UHF TV broadcast bands
- Each 6 MHz channel has ~20 Mb/s capacity
- Experimental Transmitters exist in Ottawa and
Toronto
- Commercial service expected in 2003

## Slide 13: DIGITAL TELEVISION BROADCASTING IN CANADA (cont’d)
Satellite Television Broadcasting
- There are two service providers
- Bell ExpressVu (Operates in the BSS band)
- Star Choice (Operates in the FSS band)
- Technologies are not compatible with each other
- Decoder STB’s provide interactive capability
- Early models provide return link by PSTN
- Newer models provide high speed return link by
satellite
- 1.4 million subscribers (8% of TV households)

## Slide 14: DIGITAL TELEVISION BROADCASTING IN CANADA (cont’d)
Cable Television
- Uses same standards as the USA cable systems
- All STB’s also conform to the Open Cable concept
- STB’s provide return interaction channel
- 6.6 million basic cable subscribers (77% of TV
households)
- 0.6 million digital cable subscribers (9% of basic cable
subscribers)

## Slide 15: MULTIMEDIA BROADCASTING ISSUES
Interactive Return Channel
Content Protocols and Standards
Note: Most work on these issues in North America is in connection with Digital TV. In Canada some experimental work is being carried out for DAB.

## Slide 16: INTERACTIVE RETURN CHANNEL
Will be provided by terrestrial wired and wireless telecommunications services
- PSTN, DECT, GSM, LMDS
Satellite Return Channel by ITU-R WP-6S
Terrestrial Return Channel in the UHF band
- One system standardized by ETSI
- CRC in Canada is carrying out return channel technical
studies using COFDM for fixed and mobile users
- ATSC has started studies on return channel
requirements in the Transmission Subcommittee T3

## Slide 17: CONTENT PROTOCOLS AND STANDARDS
ATSC Standards for DTV
- ATSC A/65A: Program and System Information Protocol for
Terrestrial Broadcast and Cable (PSIP)
- ATSC A/70: Conditional Access System for Terrestrial
Broadcast
- ATSC A/80: Data Broadcast Standard

## Slide 18: CONTENT PROTOCOLS AND STANDARDS (cont’d)
ATSC Candidate Standards for DTV
DTV Application Software Environment (DASE-1)
- Part 1: Introduction, Architecture and Common Facilities
- Part 2: Declarative Applications Environment
- Part 3: Procedural Applications Environment
- Part 4: Applications Programming Interface
- Part 5: ZIP Archive Resource Format
- Part 6: Security
- Part 7: Application Delivery System - ARM Binding
- Part 8: Conformance

## Slide 19: MULTIMEDIA BROADCASTING APPLICATIONS
Interactive TV Services
- Interactive Program Guide
- Video on Demand
-TV-Based Web Access
-Digital Video Recorders
-Addressable Advertising
-TV Portals
Enhanced TV Services
- Programming Enhancements
- T-Commerce
- Enhanced Advertising
- Personalized Video
- Interactive Game Shows

## Slide 20: MULTIMEDIA BROADCASTING APPLICATIONS (cont’d)
SOME KEY PLAYERS
Gemstar-TV Guide, TVGateway, iSurfTV, DIVA, Concurrent, SeaChange, nCUBE, Intertainer, WebTV, WorldGate, AOLTV, TiVo, Ultimate TV, Navic Networks, SONICblue/Replay TV, SpotOn, Expanse Networks, MbTV, Jovio, LocalSource, MetaTV, WorldGate, iWink, Mixed Signals, Commerce TV, RespondTV, ACTV, Two Way TV, iBlast, etc., etc.

## Slide 21: MULTIMEDIA BROADCASTING APPLICATIONS (cont’d)
EXAMPLE 1: iWink
Founded in 1995
Provides interactivity synchronized to program and advertising
Is usable on analog and digital TV
User can respond to advertisement and order goods
or request additional detail related to program
Is being used on terrestrial broadcasting, DBS and
cable TV systems in the USA, Canada and other
countries

## Slide 22: MULTIMEDIA BROADCASTING APPLICATIONS (cont’d)
EXAMPLE 2: iBlast
Founded in 1999 - Service started in 2001
Is a wireless data distribution network using terrestrial DTV broadcast transmitters
Has agreement with 258 broadcast stations in the USA
Plans minimum 2 stations per market - reach 92% of population
Agreement with many major content providers
75 Gbyte/day per transmitter
Service can be received on equipped TV sets, PC, etc.
User can personalize content to be received.

## Slide 23: MULTIMEDIA BROADCASTING APPLICATIONS (cont’d)
DAB DATACASTING EXPERIMENTS
IN CANADA
Experiments started in 1996 by CRC
Objective: To provide Internet access to mobile receivers
Return interaction channel provided by Mobitex system
Partners: RIM, Globis, PSR Group
Typical services of interest to mobile users
- Up-to-date traffic information
- Weather reports on demand
- Stock market information
- Image and video information to police forces

## Slide 24
DAB MULTIMEDIA SYSTEM

## Slide 25: SUMMARY
Digital Broadcasting infrastructure is rapidly evolving In the USA and Canada
Interaction channels are available through cable, satellite and other wired and wireless telecommunications services
Standards and protocols for data and multimedia broadcasting exist
Many system and content providers are available for various applications

## Slide 26: For more information please contact:
Dr. Metin Akgun
Communications Research Centre Canada
3701 Carling Avenue
P.O. Box 11490, Station H
Ottawa, Ontario K2H 8S2
CANADA
Tel: +1 613 998 2754
Fax: +1 613 990 6488
e-mail: metin.akgun@crc.ca