## Slide 1: Instrumental speech quality measures: market needs and standardisation within the ITU
IP Cablecom and MEDIACOM 2004
Harald Klaus – T-Systems Rapporteur of Q9/12
Harald.Klaus@T-Systems.com
Notes: Introduce self
report is in doc 21 and 22

## Slide 2: Outline
  Introduction
  Instrumental speech quality measures
    Classification and basic principles
    Today’s coverage
    Market needs
  Standardisation within ITU-T Study Group 12
    Acitivies within Question 9/12
    Activities within other Questions
  Conclusions
Notes: Emphasize uniqueness of 12:
methodologies
terminals
user applications
mention relation to 13, 16

## Slide 3: Introduction
Harald Klaus
  Studied electrotechnical engineering at the Technical University of Berlin
  Research assistant for speech recognition applications and speech quality assessment
  Head of quality assessment of tele-services at T-Systems Nova Berkom in Berlin
  Rapporteur in ITU-T Study Group 12 for instrumental speech quality assessment methods
  Rapporteur in ETSI Technical Committee STQ
Notes: Emphasize uniqueness of 12:
methodologies
terminals
user applications
mention relation to 13, 16

## Slide 4: Intro

## Slide 5: Intro

## Slide 6: Instrumental speech quality measures
Classification of models (listening quality)
  Single-ended models
    In-service non-intrusive measurement devices
    Call clarity index
  Models based on signal comparison
    ITU-T Rec. P.862
    TOSQA, PACE, PAMS, PSQM, ...
  Speech quality analysis tools

## Slide 7: Instrumental speech quality measures (2)
Classification of models (others)
  Planning tools
    E-Model
    Other planning models
  Analysis systems for
    Quality of service parameters
    Conversational quality aspects

## Slide 8: Principle of comparison methods

## Slide 9: Today‘s coverage of models
Sufficient (validated!) accuracy for
  Analogue and ISDN connections with INMD
  Performance of known codecs
  Voice over IP with small amount of packet loss and jitter (electrical-electrical network access only!)
  Background noise
  Codec tandemings
  ... (cf. ITU-T Rec. P.862 Table 1)

## Slide 10: Today‘s coverage of models (2)
Insufficient or unknown accuracy for
  End-to-end speech quality including terminals
    Electrical-acoustical or acoustical-electrical access
    Acoustical-acoustical access
  Performance of proprietary codecs
  Voice over IP with high percentage of packet loss
  ... (cf. ITU-T Rec. P.862, Table 2 and 3)

## Slide 11: Market needs
  Instrumental methods that cover end-to-end speech quality including the terminal
  Single-ended speech quality monitoring tools for packet-oriented networks
  Robust speech quality measures for speech quality enhancement effects in the network
  Instrumental models that consider conversational speech quality aspects

## Slide 12: Market needs (2)
  Scalable measurement solutions (for e.g. different classes / profiles of application, price, accuracy, ...)
  Speech quality assessment using knowledge of network parameters and of the psycho-acoustics
  Speech quality analysis systems

## Slide 13: Standardisation within ITU-T SG12
Activities of Question 9/12 until 2004
  Development of new Recommendations for
    End-to-end speech quality including acoustical interfaces
    Non-intrusive measurement
    7 kHz wideband
    Talker quality
  Rapporteur‘s Meeting in Berlin (March 2002) to define requirements and test plans
  Model selection and characterization starting in Summer 2002
  Recommendations to be expected in 2003

## Slide 14: Standardisation within ITU-T SG12 (2)
Activities of other Questions of SG12 related to speech quality assessment
  Q2: Speech Transmission Characteristics and Measurement methods for Terminals and Gateways interfacing Packet-Switched (IP) Networks
  Q6: Analysis methods using complex measurement signals
  Q7: Methods, tools and test plans for the subjective assessment of speech and audio quality
  Q16: In-service non-intrusive assessment of voice transmission performance on non-linear systems

## Slide 15: Conclusions
  Today‘s instrumental speech quality measurement measures
    cover a rather limited range of application
    require an expert knowledge to prevent ill-usage
    Have to be handled with caution for new technologies
  There is a strong demand for
    assessment of a wider range of applications (e.g. end-to-end transmission including acoustical interfaces, wideband speech, talker quality)
    Scalable and flexible solutions for different business models of network providers
    a revised develompent procedure to create new ITU-T Recommendations with low budget and time-to-market

## Slide 16
Thank you!
Phone: +49 30 3497-2382
Harald.Klaus@T-Systems.de