## Slide 1: Audio-Visual Coding in SG 16 and Future Directions
Workshop on Multimedia Convergence (IP Cablecom / Mediacom 2004/ Interactivity in Multimedia)
Session 6 – Voice and Video Coding and Speech Processing
Yushi Naito
Mitsubishi Electric (Japan); Rapporteur, Q.9/16 (VBR voice coding)
Simão F. Campos Neto
Vice-Chair, SG16 (Brazil); Chair WP 3/16 (Media Coding)

## Slide 2: Introduction

## Slide 3: ITU-T Video Coding
H.261: Video Codec for A/V services at p x 64 kbit/s
  The first practical video coding standard (1990)
  Used today in (ISDN) video conferencing systems
  Bit rates commonly 40 kbits/s to 2 Mbits/s
H.262: Same as MPEG-2/Video (ISO/IEC 13818-2)
  Commonly used for entertainment-quality video applications
  The first practical standard for interlaced video
  Used in digital cable, digital broadcast, satellite, DVD, etc.
  Bit rates commonly 4-20 Mbits/s

## Slide 4: ITU-T Video Coding (continued)
H.263: Video Coding for Low Bit Rate Communication
  Significantly improved video coding compression performance (esp. at very low rates, but also at higher rates as well)
  The first error and packet loss resilient video coding standard
  Used in Internet protocol, wireless, and ISDN video conferencing terminals (H.323, H.324, 3GPP, etc.)
  “Baseline” core mode interoperable with MPEG-4/Video
  Rich set of features for many applications
  Very wide range of bit rates and possible applications

## Slide 5: ITU-T Video Coding (continued)
H.26L: Advanced Video Coding
  Core development work initiated in ITU-T Q.6/16 “Video Coding Experts Group” (VCEG), now being jointly developed with MPEG under the “Joint Video Team”
  Objective is to have the same performance of H.263 but operating at half H.263’s bit rate
  Conclusion expected for late 2002/early 2003
  See separate presentation for details 

## Slide 6: Non-ITU-T Video Coding
MPEG-1/Video (ISO/IEC 11172-2)
  The first video coding standard using half-pel motion compensation
  Typical bit rates 1-2 Mbits/s
MPEG-4/Visual (ISO/IEC 14496-2)
  The first video coding standard defining arbitrary object shapes
  Many creative features for synthetic and synthetic-natural hybrid content
  Contains essentially all features of all prior standard codec designs
  Interoperable with ITU-T H.263 “baseline”
  Very wide range of bit rates and possible applications

## Slide 7: Speech Coding Families

## Slide 8: Speech Coding Families

## Slide 9: ITU-T Wideband Speech Coding (F.700’s A1 Audio Quality Level)
G.722
  Coding of 7 kHz speech at 64, 56, and 48 kbit/s
  Sub-band ADPCM
G.722.1
  Coding of 7 kHz speech at 32 and 24 kbit/s
  Transform coding approach
G.722.2
  Coding of 7 kHz speech at 16 kbit/s or lower
  CELP-based; same as 3GPP AMR-WB
  Optimized for speech, works well also with 7kHz music
Just completed

## Slide 10: ITU-T Telephony Speech Coding (F.700’s A0 Audio Quality Level)
G.711 PCM coding (64 kbit/s) late 60’s
G.726 ADPCM coding (32; 40, 24 & 16 kbit/s) 1988
G.728 LD-CELP coding (16; 40, 11.8 &9.6 kbit/s) 1992
G.723.1 Dual-rate coding (5.3 & 6.3 kbit/s) 1995
G.729 CS-ACELP coding (8; 12.8 & 6.4 kbit/s) 1996-2000
G.4kbit/s
G.VBR (Variable bit rate)
Ongoing
New

## Slide 11: Non-ITU Standards
MPEG2/Audio: audio coding > 64 kbit/s (1992) (*)
MPEG4/Audio: audio + speech coding at bit rates between 64 and 2 kbit/s (1998) (*)
ETSI GSM:
  13 kbit/s RPE-LTP (Full rate GSM, 1988)
  6.5 kbit/s VSELP (Half-rate GSM, 1993)
  12.2 kbit/s EFR (Enhanced full-rate GSM, 1996)
  12.2 - 4.75 kbit/s AMR (Adaptive Multi Rate, 1999)
  6.5 - 23.95 kbit/s AMR-WB (Wideband AMR, 2000)(**)
    (*) F.700’s A2/A3 quality levels
    (**) Same as algorithm as G.722.2

## Slide 12: Non-ITU Standards (cont’d)
US TIA (ANSI)
  CDMA
    IS96 8,4,2 kbit/s QCELP (Qualcomm CELP, 1992)
    IS127 8.55, 4, 0.8 kbit/s EVRC (Enhanced Var. Rate Codec, 1996)
    IS733 13.3, 6.2, 2.7, 1 kbit/s VRC (Variable Rate Codec, 1998)
    CDMA2000 9.6,4,2.4,0.8 kbit/s SMV (Selec.Mode Vocoder, 2002)
  TDMA
    IS54 7.95 kbit/s VSELP (Vector-Sum Excitation Lin.Pred., 1990)
    IS641 7.4 kbit/s ACELP (Algebraic CELP, 1997)
  PCS1800 (GSM upbanded to 1800 MHz)
    IS136-410 12.2 kbit/s US1 (1999)

## Slide 13: Non-ITU Standards (cont’d)
ARIB (Japan)
  Full-rate PDC (Personal Digital Communication) 6.7 kbit/s VSELP
  Half-rate PDC 3.45 kbit/s Pitch Synchronous Innovation CELP
IETF
  Internet Low Bit Rate Codec (ILBC) (http://search.ietf.org/internet-drafts/draft-andersen-ilbc-00.txt)
Recently started

## Slide 14: SG 16 Activities

## Slide 15: ITU-T SG 16

## Slide 16: WP 3/16 (Signal Processing)
Q.E/16 Media coding
Q.6/16 Advanced video coding
Q.7/16 Wideband speech coding
Q.8/16 Speech coding at 4 kbit/s
Q.9/16 Variable bit rate speech coding
Q.10/16 Software tools and maintenance of speech coding standards
Q.15/16 Distributed speech recognition/ distributed speaker verification

## Slide 17: Q.E/16 Mr. Simão Campos-Neto
Umbrella media coding question responsible for long-term planning under the MEDIACOM 2004 Project
Address new media coding work by:
  Creating specific ad-hoc experts groups
  Delegating the work to an existing question
  Proposing the creation of a new question

## Slide 18: Q.6/16 Dr. Gary Sullivan (Microsoft, USA) Dr. Thomas Wiegand (Heinrich Hertz Institute, Germany)
Video Coding Experts Group (VCEG), now working in cooperation with MPEG under the “Joint Video Team” (JVT)
Domain over all ITU-T video codec specifications:
  H.261 and H.120 legacy codecs
  H.262 a.k.a. MPEG-2 high bit-rate coding
  H.263 including H.263+ and H.263++ enhanced coding
  Project for development of new “H.26L” video codec
Recent work completed:
  H.263 version 3 "H.263++" Enhancements
  Definition of new normative “profiles” and “levels” for H.263
  Experiment and proposal work in progress for H.26L development
  Annex X containing normative profile and level definitions

## Slide 19: Q.6/16 (Future Work, Cont’d)
“H.26L” Future Video Codec Design
  Goals:
    A new standard beyond the capabilities of incremental enhancements to existing designs
    High compression and high quality capability
    A simple "back to basics" design structure
    Flexible delay characteristics and high error resilience
    Complexity scalability in encoder & decoder
    Full specification of decoding process
    Network friendliness for broad applicability
  Schedule:
    Target approval by late 2002/early 2003

## Slide 20: Q.7/16 Mr. Rosario D. de Iacovo (Telecom Italia Lab, Italy)
Responsible for definition of audio and wideband speech coding algorithms in the ITU
Current work:
  Completing the work in G.722.2 (Adaptive Multi Rate Wideband coding algorithm at around 16 kbit/s)
  Standard aligned with 3GPP wideband service codec specification
  Approved in January 2002; characterization test phase currently underway
  Improved frame erasure performance annex planned for late 2002/early 2003
  Applications include:
    Videotelephony (H.320, H.323, H.324), Audio teleconferencing
    Voice over packet systems (IP networks, ATM, …)
    Indoor wireless, cellular telephony (CDMA, GSM, IMT 2000, etc)
    Store & Forward Systems

## Slide 21: Q.8/16 Mr. Paul Barrett (BT, UK)
Wireline (“toll”) quality 4 kbit/s speech codec
  Primary Applications
    Very low-rate PSTN visual telephony
    Personal communications
    Simultaneous voice and data systems
    Mobile-telephony satellite systems

## Slide 22: Q.8/16 (Cont’d)
  Secondary Applications:
    Digital circuit multiplication equipment
    Packet circuit multiplication equipment
    Low-rate mobile visual telephony
    Message retrieval systems
    Private networks
  Status:
    Selected one technological solution (“Codec A”) for further optimization
    Target for approval: first quarter 2003

## Slide 23: Q.9/16 Mr.Yushi Naito (Mitsubishi, Japan)
Investigate variable rate coding of voice signals
Two technologies are being studied:
  Multi-rate speech coding (“MSC-VBR”)
  Embedded (“EV”)
Currently, terms of reference are being discussed in conjunction with the application areas for each of the two technologies above
Recommendations are expected in the 2003-04 time frame.

## Slide 24: Q.10/16 Mr. Simão Campos-Neto (acting)
Improvement and maintenance of software tools used in the course of defining ITU-T voice coding standards.
  The ITU-T STL has been extensively used in the ITU and outside the ITU for several codec selection activities: ITU-T Wideband, G.729 and extensions, G.723.1; ETSI EFR & AMR; TIA EFR TDMA
Maintenance, update, and improvement of existing ITU-T speech coding recommendations (G.711, G.72x-Series).

## Slide 25: Q.10/16 (Cont’d)
Recent work:
  Publication of the ITU-T Software Tool Library Release 2000 (G.191-2000)
  G.711 Appendices I (Packet-loss concealment) and II (Silence removal)
  Maintenance of G.722.1, G.723.1, G.728, and G.729
Future Work
  Continue update/evolution of the ITU-T STL
  Continue maintenance of ITU-T voice coding Recommendations

## Slide 26: Q.15/16 Mr. Simão Campos-Neto (acting)
Question to deal with distributed speech recognition and distributed speaker verification
Currently in early stages of definition
  Basic principle: avoid any duplication of effort and unnecessary creation of incompatible but technically equivalent systems. Q.15/16 should try to capitalize on advances realized outside SG 16 (including outside the ITU) identifying areas where the ITU-T can provide supplemental facilities not currently available in DSR/DSV standards.

## Slide 27: Q.15/16 (Cont’d)
Desirable features:
  Development of DSR/DSV algorithms that perform well for a wide set of languages, given the wide audience of the ITU-T membership, in particular the needs of developing countries.
  Potential for use of a common front-end for both DSR and DSV applications
  Use of higher bit rates to enable richer feature sets
  Use of an intelligent architecture that can exploit server load distribution, such as delegation of activities to edge elements according to the complexity of the tasks and the edge element capabilities.
  Desire to use common testing tools, e.g. databases for assessing different solutions, including different environments/scenarios, and use of a common back-end.

## Slide 28: Future Directions
Evolving networks, evolving user expectations
  Higher bandwidths available to end-users
  Convergence of broadcasting and telecommunications: users to expect richer experience, quality & multiplicity of services, integrated services, immersive environments
Long lifetime for existing systems force need to accommodate interoperability between existing systems
  Transcoding-free initiatives
  Minimization of quality loss in transcoding scenarios

## Slide 29: Conclusion
WP 3/16 has been very active in this period in supporting and producing state-of-art A-V coding.
Activities are focusing more towards packet systems and wireless network needs, and integration with multimedia terminals
Superior quality is a prime parameter
Some future directions were identified