## Slide 1: Syntax language for the support of PSTN/ISDN services within IP session control protocols
Keith Mainwaring
Cisco Systems
Rapporteur Q.6/11

## Slide 2: New question in SG 11
No intention to develop syntax
Rather a new more flexible representation of narrowband signalling protocol information (initial contributions based on ISUP)
Application of existing description techniques

## Slide 3: New Question 16/11
“Syntax language based mechanism for the support of PSTN/ISDN services within IP session control protocols”

## Slide 4: The “problem”
Mandatory information
Inflexible structure
Support of protocol variants
Compatibility information
Tunnelling protocols

## Slide 5
Generic Transparency Descriptor
A descriptor cf. SDP (Session Description Protocol)
Contains narrowband signalling (call control) information (e.g. derived from ISUP)
Transfer protocol independent (e.g. H.323 or SIP)
Addresses some of the issues associated with “tunnelling” protocols (such as the alignment of tunnelled information with the same semantic information in the protocol containing the tunnel)
What is it?

## Slide 6
Transfer of narrowband signalling information in packet-networks
H.323 System
SIP Proxy
Call Agent
Call Agent
SIP (encapsulated ISUP) “SIP-T”
SIP / H.323 (encapsulated GTD)
BICC
ISUP
ISUP

## Slide 7
Potential solutions
SIP-T (encapsulated ISUP)
GTD (generic IP e.g. H.323 / SIP)
BICC – PSTN / ISDN services only

## Slide 8
Interworking narrowband signalling protocol to IP call control protocol
Map as much information as possible
Tunnel information that cannot be mapped
SIP-T: encapsulate full ISUP message
GTD: encapsulate information that cannot be mapped
BICC: no need for tunnelling as full mapping of narrowband signalling information

## Slide 9
GTD characteristics
Not required to send all parameters derived from source message (cf. SIP-T)
Information accessible within IP network (not unique to GTD but may simplify procedures)

## Slide 10
SIP – ISUP interworking with GTD
Map ISUP parameters to SIP headers and SDP, if possible
Map other parameters to GTD

## Slide 11
Native GTD Parameters
GCI | Global Call Identification
FDC | Known Field Compatibility Information
PRN | Protocol Name
PRV | Protocol Variant
SEG | Segmentation Indicator
TID | Transaction ID
UFC | Unknown Field Compatibility Information
Newly introduced parameters solely for the purpose of GTD & with no
equivalent in ISUP

## Slide 12
Handling of ISUP variants
Generic compatibility mechanisms used to transfer variant-specific information
GTD does not solve the problem of interworking between all variants

## Slide 13
Protocol Name - PRN
Protocol base derivative
Country variant
Operator or vendor variant
Protocol variant

## Slide 14
Protocol base derivative
uknow - unknown
t1113 - ANSI T1.113 (use prv= to distinguish year)
q767* - ITU q767
q761* - ITU q761-4 (use prv= to distinguish year)
etsv1 - ETSI ISUP V1 (ETS 300 121)
etsv2 - ETSI ISUP V2 (ETS 300 356)
dpnss - BT Digital Private Network Signaling System
isdn* - Integrated Services Digital Network
casr1 - Channel associated R1
casr2 - Channel associated R2
casmf - Channel associated Multi frequency
caslp - Channel associated Multi loop disconnect
tup** - Telephony user part
nup** - National user part
gr317 - Bellcore GR-317
gr394 - Bellcore GR-394
gr905 - Bellcore GR-905
dass2 - BT Digital Access Signaling System # 2

## Slide 15
PRN – other fields
Field-02: c - Country Variant
aaa - 3 char string representing the country
e.g., UK* for United Kingdom (use IANA country domains)
[See Appendix C for listing adopted from:
http://www.ics.uci.edu/pub/websoft/wwwstat/country-codes.txt]
Field-03: o - operator or vendor variant
aaaaa - IA5 characters a-z or 0-9 indicating the operator variant
e.g., btnup for British Telecom NUP, ttc** for JT-Q761-4
Field-04: prv -protocol variant
aaaa definition
---- -------------------
0000 - unknown variant
xxxx - IA5 characters a-z or 0-9 indicating version number
e.g., "1993" variant of JT-Q761-4

## Slide 16
Information mapping
Map to direct equivalent GTD parameter and field value
Or
Map to best fit GTD parameter and field value and encode information using a compatibility mechanism

## Slide 17
GTD – Unknown Information
Parameter Types
MCI - Message Compatability
    Encapsulates unknown protocol messages in raw format and indicates how the receiver should handle them
PCI - Parameter Compability
    Encapsulates unknown parameters, and indicates how the receiver should handle them
FDC - Field Compatability
    Encapsulates unknown field values, and indicates how the receiver should handle them

## Slide 18: A personal view on formal definition techniques from a protocol standardiser
Techniques have outrun us
Please think of the users – may not be mathematicians, computing or language experts
Simplify techniques without losing formality?