## Slide 1: ITU-T Study Group 16 and the need for formal description techniques
Simão Ferraz de Campos Neto
Counsellor – ITU-T Study Group 16
Multimedia Services, Systems and Terminals

## Slide 2: Contents
About SG 16
Highlight of SG 16 Recommendations
Description methods in SG 16 Recs
Future perspectives
Conclusion

## Slide 3: About SG 16

## Slide 4: ITU-T Study Group 16
Responsible for studies relating to:
multimedia service definition and multimedia systems, including the associated terminals, modems, protocols and signal processing.
Lead Study Group on
Multimedia Services, Systems and Terminals
e-business and e-commerce
(www.itu.int/ITU-T/studygroups/com16)

## Slide 5: ITU-T Study Group 16 Structure
Study Group 16
Multimedia Services Systems & Terminals
Pierre-André Probst
Working Party 1
Modems and
Facsimile Terminals
Mitsuji Matsumoto
Working Party 2
Multimedia
Platforms and
Interworking
Sakae Okubo
Working Party 3
Media Coding
John Magill
Working Party 4
Multimedia
Framework
John Magill (acting)
ITU-TSB
Counsellor
Simão Ferraz de
Campos Neto

## Slide 6: ITU-T Study Group 16 WPs (1/2)
Working Party 1/16 - Modems and facsimile terminals
H/16 Accessibility to Multimedia Systems and Services
11/16 Voiceband Modems: Specification and Performance Evaluation
12/16 DCE-DCE protocols for the PSTN and ISDN
13/16 DTE-DCE Interfaces and Protocols
14/16 Facsimile terminals
Working Party 2/16 - Multimedia platform and interworking
D/16 Interoperability of Multimedia Systems and Services
F/16 Quality of Service (QoS) and End-to-End Performance in Multimedia Systems
G/16 Security of Multimedia Systems and Services
1/16 Multimedia Systems, Terminals and Data Conferencing
2/16 Multimedia over Packet Networks using H.323 Systems
3/16 Infrastructure and Interoperability for Multimedia over Packet Network Systems
4/16 Video and data conferencing using Internet supported services
5/16 Mobility for Multimedia Systems and Services

## Slide 7: ITU-T Study Group 16 WPs (2/2)
Working Party 3/16 – Media coding
E/16 Media coding
6/16 Advanced video coding
7/16 Wideband coding
8/16 Encoding of speech signals at bit rates around 4 kbit/s
9/16 Variable bit rate coding of speech signals
10/16 Software tools for signal processing standardization activities and maintenance of existing voice coding standards
15/16 Distributed Speech Recognition (DSR) and Distributed Speaker Verification (DSV)
Working Party 4/16 – Multimedia framework
A/16 Mediacom-2004
B/16 Multimedia Architecture
C/16 Multimedia applications and services
I/16 Use of public telecommunication services for emergency and disaster relief operations

## Slide 8: Highlight of Recommendations under SG 16

## Slide 9: Modem & Fax recommendations
V.34 – Two-wire PSTN data at up to 33.6 kbit/s
V.90 – Digital 56 kbit/s upstream / 33.6 kbit/s analogue downstream PSTN modem
V.92 – Enhancements to Recommendation V.90
V.150.1 – Modem-over-IP NEW!
T.30 – Procedures for G3 PSTN facsimile transmission
T.37 – Facsimile via store-and-forward on the Internet
T.38 – Real-time G3 facsimile communication over IP

## Slide 10: Multimedia terminal and systems
H.310 - Broadband audiovisual communication systems and terminals
H.320 - Narrow-band visual telephone systems and terminal equipment
H.323 - Packet-based multimedia communications systems
H.324 - Terminal for low bit-rate multimedia communication
H.246 - Interworking between H-Series terminals & PSTN / ISDN
H.248.x - Media Gateway Protocol sub-series
H.245 - Control Protocol for multimedia communication
H.225.0 - Call signalling & media packetization for packetized MM
H.341 - Multimedia management information base

## Slide 11: Media coding – Video & Image
H.261 - Video coding at p x 64 kbit/s
H.262 - MPEG2/Video
H.263 - Video coding for low bit rate communication
H.264 - Advanced Video Coding Almost finished
T.81 - JPEG
T.82 - JBIG
T.800, T.801,T.803,T.804 - JPEG-2000 New!

## Slide 12: Media coding – Audio
G.726 - ADPCM coding (32; 40, 24 & 16 kbit/s)
G.727 - Embedded ADPCM coding (40-16 kbit/s)
G.728 - LD-CELP coding (16; 40, 11.8 &9.6 kbit/s)
G.723.1 - Dual-rate coding (5.3 & 6.3 kbit/s)
G.729 - CS-ACELP coding (8; 12.8 & 6.4 kbit/s)
G.722 – Wideband speech coding at 64, 56 & 48 kbit/s
G.722.1 – Hands-free WB speech at 32 & 24 kbit/s
G.722.2 - WB speech at ~16 kbit/s (16; 5.5-24 kbit/s)

## Slide 13: Description Methods in SG 16 Recommendations

## Slide 14: Description Techniques in SG 16 Recs
Formal description techniques (FDT)
  ASN.1
  ABNF (RFC 2234)
  SDL
Other description methods
  Pseudo-code (non compilable, C- or Fortran-like)
  ANSI C code
  Ladder and state diagrams
  Call flow diagrams

## Slide 15: FDT in SG 16: ASN.1
Examples:
  H.323
  H.245
  H.248.x
Recent coordination effort with SG 17’s ASN.1 Project

## Slide 16: FDT in SG 16: ABNF
Used for Text encoding in the H.248 Media Gateway Control Protocol sub-series
Examples:
  H.248.1 Annex B
  …???

## Slide 17: FDT in SG 16: SDL
Examples:
  H.245 (Annex C)

## Slide 18: Other methods in SG 16: Pseudo-code
Non-compilable, non-verifiable
Sequencing / ordering of operations in plain language
C-style:
  G.726, G.727, G.722
Fortran-style
  G.728 & Annexes

## Slide 19: Other methods in SG 16: ANSI-C code
Compilable code
Dual use:
  implementation description
  implementation compliance verification
Examples:
  Telephony speech: G.723.1, G.729
  Wideband speech: G.722.1, G.722.2
  Video: H.264 SOON-TO-BE!
  Still image: T.800 (T.804) NEW!

## Slide 20: Other methods in SG 16: Ladder & State Diagrams Call-flow diagrams
Examples:
  Ladder/State in V, T, and some H-series Recs.
  Call flow used in the H.323-related Recs.

## Slide 21: Examples

## Slide 22: Example of ASN.1 in H.248.1 V2 (2002-03)
Initial statements in Annex A
MEDIA-GATEWAY-CONTROL {itu-t(0) recommendation(0) h(8) h248(248) modules(0)
media-gateway-control(0) version2(2)}
DEFINITIONS AUTOMATIC TAGS ::=
BEGIN
MegacoMessage ::= SEQUENCE
{
authHeader AuthenticationHeader OPTIONAL,
mess Message
}
AuthenticationHeader ::= SEQUENCE
{
secParmIndex SecurityParmIndex,
seqNum SequenceNum,
ad AuthData
}
Etc…

## Slide 23: Example of ABNF in H.248.1 V2 (2002-03)
megacoMessage = LWSP [authenticationHeader SEP ] message
authenticationHeader = AuthToken EQUAL SecurityParmIndex COLON
SequenceNum COLON AuthData
SecurityParmIndex = "0x" 8(HEXDIG)
SequenceNum = "0x" 8(HEXDIG)
AuthData = "0x" 24*64(HEXDIG)
message = MegacopToken SLASH Version SEP mId SEP messageBody
; The version of the protocol defined here is equal to 2.
messageBody = ( errorDescriptor / transactionList )
Etc…
Initial statements in Annex B

## Slide 24: Example of SDL in H.245
Figure C.5/H.245 - State transition diagram for sequence of primitives at CESE outgoing

## Slide 25: Example of Pseudo-code in G.726 (C-like)
Block SUBTB used in the G.726 encoder and decoder
SUBTB
Inputs: DL (DLX in decoder), Y Output: DLN (DLNX in decoder) Function: Scale logarithmic version of difference signal by subtracting scale factor.
DLN = (DL + 4096 - (Y >> 2)) & 4095

## Slide 26: Example of Pseudo-code in G.728 (Fortran-like)
WEIGHTING FILTER COEFFICIENT CALCULATOR (block 38)
Input: AWZTMP
Outputs: AWZ, AWP
Function: Calculate the perceptual weighting filter coefficients from the linear predictor coefficients for input speech.
This block is executed once every adaptation cycle. It is done at ICOUNT = 3 after the processing of block 37 has finished.
For I = 2,3,..,LPCW + 1, do the next line |
AWP(I) = WPCFV(I) * AWZTMP(I) | Denominator coefficients
For I = 2,3,..,LPCW + 1, do the next line |
AWZ(I) = WZCFV(I) * AWZTMP(I) | Numerator Coefficients
Weighting filter used in the G.728 encoder and decoder

## Slide 27: Example of C-code in G.729
/* Decode the positions */
i = index & (Word16)7;
pos[0] = add(i, shl(i, 2)); /* pos0 =i*5 */
index = shr(index, 3);
i = index & (Word16)7;
i = add(i, shl(i, 2)); /* pos1 =i*5+1 */
pos[1] = add(i, 1);
index = shr(index, 3);
i = index & (Word16)7;
i = add(i, shl(i, 2)); /* pos2 =i*5+1 */
pos[2] = add(i, 2);
Excerpt of function Decod_ACELP()

## Slide 28: Conclusion
Extensive use of description techniques in SG 16
Most frequent:
  System recommendations: ASN.1
  Coding: ANSI-C code
  Ladder, state & call-flow diagrams
ABNF also used in H.248 (IETF parallel text)
Future: continued use of ASN.1 and ANSI-C code in the specific areas indicated above

## Slide 29: Thank you for your attention!
For further contact, please feel free to contact:
Simão Ferraz de Campos Neto
Counsellor, ITU-T Study Group 16
simao.campos@itu.int
Tel: +41-22-730-6805
Fax: +41-22-730-4345
http://www.itu.int/ITU-T/studygroups/com16

## Slide 30: Acronyms
ABNF - Augmented Backus-Naur Form [for syntax specifications]
ADPCM - Adaptive Differential PCM
FDT - Formal Description Technique
ISDN - Integrated Services for Digital Networks
ITU - International Telecommunication Union
ITU-T - Telecommunication Standardization Sector of ITU
JBIG – Joint Bi-level Image Experts Group
JPEG - Joint Picture Experts Group
LD-CELP – Low-delay Code-Excited Linear Prediction
MM - Multimedia
PCM - Pulse Code Modulation
PSTN - Public Switched Telecommunication System
WB - Wideband