## Slide 1: Use and needs of description techniques in Study Group 4
Knut Johannessen
Rapporteur Q.12/4, Telenor, Norway

## Slide 2: Outline
SG4
  Responsibility and organization
  Reminder of TMN architecture and management paradigms
Review of historic practice
  Specification of interfaces
  TMN
  Exchange of designators
Current practice
Needs
  Evolving technology support
  Common specifications
  Revised methodology

## Slide 3: ITU-T SG 4 Organization
Working Party 1/4 - Designations, performance, and test equipment
  Q 2/4: Designations for interconnections among network operators
  Q 3/4: Transport network and service operations procedures for performance and fault management
  Q 4/4: Test and measurement techniques and instrumentation for use on telecommunication systems and their constituent parts
  Q 5/4: Jitter and wander test and measurement techniques and instrumentation for use on telecommunication systems and their constituent parts
Working Party 2/4: Common telecommunication management capabilities
  Q 7/4: TMN principles and architecture
  Q 8/4: Requirements for the TMN user interfaces
  Q 9/4: Requirements for the TMN X interface
  Q 10/4: Framework for unified management of integrated circuit-switched and packet-based networks (with an initial emphasis on IP-based networks)
  Q 11/4: Principles of the customer network management and network-network management

## Slide 4: ITU-T SG 4 Organization (cont’d)
Working Party 3/4: Telecommunication management information modelling
  Q 12/4: Methodology and generic information models for TMN interfaces
  Q 13/4: Generic network level management of transmission systems
  Q 14/4: Management models for ANT and ATM network elements, including the support of access signalling and IP
  Q 16/4: TMN management support for IMT-2000 and IN
Working Party 4/4: Telecommunication management infrastructure capabilities
  Q 17/4: Open distributed management infrastructure
  Q 18/4: Protocols to support operations, adminstration, and maintenance at the F, Q, and X interfaces
  Q 19/4: Information models for management applications related to switching and generic support services

## Slide 5: Relationship to Telecommunications Networks
OS
Traffic Mgt
OS
Surveillance
OS
Provisioning
Data Communications Network
WS
WS
WS
WS
TMN
Telecommunications Network
TMN Interfaces
Work Station
TMN Interfaces
Access, switching, routing, transport, and server
network elements and networks
Operation System
Other
TMNs
TMN Interfaces
The focus of TMN standards is on the communication of management information

## Slide 6: TMN Functional Architecture (M.3010)
Service
Management
Element
Management
Network
Management
Network
Elements
Business
Management
Enterprise view
Goal setting, finance, budgeting
Product & human resource planning
Contacts with customers & svc providers
Service orders, complaints, & billing
Quality of service
Network support of all services
End-to-end network view of all NEs & links
View of NE subset, individually or
collectively as a subnetwork
Network resource functionality
OSF
OSF
OSF
OSF
NEF
•
•
•
•
q
q
q
q
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Review of historic practice
TMN based on OSI management
  Guidelines for definition of Management information (GDMO)
    Managed objects
    Packages
      Behaviour – specified using natural language
      Attributes and operations on attributes (GET, SET, …)
      Notifications
      Actions
    Name bindings and allowed operations on subordinate objects
  ASN.1 for definition of syntax of management information
Large number of specification based on GDMO/ASN.1 developed by ITU-T
and other standards organizations

## Slide 8: Implicit capabilities – offered by CMIP
”Base object” identify the entry point in the management information tree structure
”Scope” identify the affected sub-tree from ”base”
”Filter” identify criteria for object instance selection within ”scope”.
”Attribute list” identifies in the case of a GET operation which attributes to be returned

## Slide 9: Highlights of TMN evolution
Management technology evolution
  High cost of OSI management (or perceived high cost)
  User acceptance of SNMP for element management
  CORBA as an attractive management technology
  XML for inter-operator communication (X interface)
  XML now also an interesting technology for inter-operator communication (Q interface)
  Java/J2EE/EJB possibly replacing CORBA
    At least J2EE/EJB as an implementation platform
  Also J2EE challenged by other technologies
Management information is a long lived, strategic asset. Need specifications that can be mapped to new management paradigms/technologies

## Slide 10: Current approach
X.780
X.780

## Slide 11: Current practice
Requirements Specification
Paradigm
independent
Paradigm
specific
CMIP-
based
Specification
CORBA-
based
Specification
Other Paradigm-
based
Specification
X.780
X.780
M.3020
M.3030 tML
M.3020

## Slide 12: M.3020 – TMN UTRAD methodology
Unified TMN Requirements, Analysis and Design
Guidelines for the Definition of Management Interface (GDMI)
  Requirements
    Business level requirements
      Actor roles
      Telecommunications resources
      High-level use cases
    Specification level requirements – refinement of high-level use cases
      Actor roles
      Telecommunications resources
      TMN management functions
      Use cases
  Analysis - Implementation independent specification
  Design
    GDMO/ASN.1, IDL, …

## Slide 13: Selected elements of UTRAD analysis
Functional decomposition, information flows, class diagrams (including relationships between classes), sequence diagrams and state charts/tables
The class diagrams may be augmented with details of attributes and allowed operations
Textual description is required to augment the figures.
Detailed descriptions of the Management Functions and interactions between the functions shall be provided.
The information flow associated with each function should generally be captured using simple tables defining the flow.
The analysis may include state models as a result of information flow
The scenarios describing the information flow amongst the entities may be described using the sequence diagrams
Pre- and post-conditions may be used to describe the information flows in the interaction diagrams.

## Slide 14: UTRAD use of UML
TMN concept
UML notation
Comment
user
Actor
A user is modelled as an actor.
management role
Actor
An actor plays a role. It is normally advisable to only model a single role for each actor.
management function
use case
A management function is modelled by one or more use cases.
management function set
use case
A management function set is a composite use case with each management function (potentially) modelled as a separate use case.
management service
use case
A management service is modelled as a high-level use case.
management scenario
sequence diagram
Sequence diagrams are preferred over collaboration diagrams.
telecommunication resource type
Class
The class diagrams depict the property details of the telecommunications resource type, at the level of detail appropriate to the phase of the methodology.
management goals
–
Management goals are captured as textual descriptions as there is no applicable UML notation.

## Slide 15: Methodology evolution and refinement
Requirements Specification
Paradigm Independent Specification
CMIP-
based
Specification
CORBA-
based
Specification
Other Paradigm-
based
Specification
Process,
Notation,
Traceability,
…
Framework,
Guidelines,
Notation,
…
Transformation
Specification
(level of mechanization?)
Transformation
Reuse?
(how)
Rich set of information models

## Slide 16: Cooperation between SG4 and SG17
Requirements specification
  Possible use of URN by SG4
  Application of URN to M.3208.1 would be a good test
    M.3208.1 describes requirements for management of leased lines across an X-interface (between different TMN domains such as between different telecom operators).
Protocol netural specification
  How to best apply UML
Specification transformation
  Language support of mapping between the protocol/paradigm neutral and specific level
Other areas
  What other languages developed by SG17 would add value to the TMN methodology?