## Slide 1: East Bhutan Tele-ECG Project
Agus Subekti, Futoshi Ohyama, M.Athar Sadiq,
Hiroshi Juzoji, Isao Nakajima
Tokai University,
The Institute of Medical Sciences,
Shimokasuya 143, Isehara, Kanagawa,
259-1193 Japan

## Slide 2: Introduction
The Kingdom of Bhutan is an ancient kingdom with unique customs and people, lies in the Central Himalayas, between Tibet to the north, the Indian territories of Assam and West Bengal, to the south and east, and Sikkim to the west.
The Kingdom has a total area of about 47,000 square kilometers, about the size of Switzerland. Located in the heart of the high Himalayan mountain range, Bhutan is a land-locked country surrounded by mountains.

## Slide 3: Demographic Data
620,000 (1997 estimate); Predominantly rural
Population:
47,000 km2; rugged mountains, swiftly-flowing rivers and extreme climate
Area:
2.55 per 1,000
Maternal mortality rates:
60.5 per 1,000 (47.4 years in 1984)
Infant mortality rates:
66.0 years (in 1994)
Life expectancy at birth:
> 39.1%
Population under the age of 15:
2.5% per year
Population growth rate:

## Slide 4: Healthcare Facilities
Medical facilities - a four-tiered health care network: 1.National Referral Hospital: 2.Regional referral hospitals: 3.District hospitals: 4.Basic Health Units (BHUs): Out-Reach Clinics: | 1 (Thimphu) 2 (Mongar and Yebilabcha) 26 (centers of each district) 160 447
Total hospital beds: | 1023 (in 1999)
Population per bed: | 622 (in 1999)
Total medical doctors: | 109 (including 20 specialists)
complicated cases transferred abroad for specialized treatment per year | 140-150

## Slide 5
Condition of Major Routes in Bhutan Creates
difficulty in Transport Patients to Referral Hospitals

## Slide 6: Telecom Infrastructure
Telephone density: 1.04
Digital microwave link between Thimphu and Tashigang with spurs connecting the main population centers
The first and only ISP, DrukNet, launched in 1999 (http://www.druknet.net.bt; 1600 subscribers until Dec. 2001)
> 50 BHUs connected to the national telecom network by single channel, point-to-point VHF systems (primarily for voice communication, but also handle fax)

## Slide 7: 1. ITU Pilot Project - MCT
A Multipurpose Community Telecenter (MCT) was established in Jakar town by the ITU/BDT in 1999.
The objective of the MCT was as follow:
(1)public telephone, fax, email and photocopying
(2)data communication services (file transfer and email) through modem for simple applications: telemedicine, education and research, trade information services, government and community information
Several Previous Pilot Projects
2. ITU Pilot Project- Telemedicine
A teleradiology link was established between Thimphu and Jakar in 2000.
X-ray images and medical data were transmitted as email attachment through a dedicated line at MCT.
System Configuration: Fine laser scanner, 2 laptop computers, software for image capture, compression, encryption and transmission.
Result: The only doctor at Jakar Hospital found it extremely helpful.
3. WHO - Health Telematics Project
On 20 Oct. 2000, Telemedicine Task Force was jointly formed by WHO and the Dept. of Health. A Health Telematics Masterplan has been drafted
JDW National Referral Hospital in Thimphu was connected to Mongar Regional Referral Hospital via a 64 kbps leased line in Sep. 2001
Telemedicine, including teleradiology, teledermatology and remote medical consultation, has been carried out since then. Training and tutorial courses have been delivered by the Short-Term Consultants (STC). Links to districts hospitals via dial-up connection are under studies

## Slide 8: Tokai University - East Bhutan Tele-ECG Project
Objective: To install tele-ECG equipments at district hospitals in remote East Bhutan
Project description:
  Two hospitals, Trashiyangtse Hospital & Lhuntse Hospital, were linked with Thimphu via dial-up connection
  12-lead ECG analyzer with a laptop computer were installed at each hospital
  Training and tutorial course have been given
Benefits:
  Improved medical care for cardiac and emergency patients
  Early detection of pediatric abnormality
  Cost-saving on referral cases
  Reduced isolation and provision of CME for health-care workers through the Internet

## Slide 9: Configuration of e-health Tele-ECG in Bhutan
Tele-ECG with Echo-graphy in Bhutan via dial-up Analog line( PSTN ): for Consultation and second opinion

## Slide 11: Equipment used for this Tele-ECG Project
12 ECG and
Echocardiography

## Slide 12: Operation procedure of Tele-ECG system.
1. Examine Patient and save image data into the memory card

## Slide 13
2. Teleconsulation and Second opinions based on sent patients data

## Slide 14: Training to doctors and nurses in Bhutan how to use ECG, cardiac ultrasonography, phonocardiogram, and telemedicine system via Internet.

## Slide 15: Several Findings from Tele-ECG Project
ECG machine is a new equipment for those 2 hospitals. Although we gave training, the time is not long enough to make them familiar with the equipment as well as operational procedure such as attach file to email.
Healthcare professionals are excited with our project, they want to get further project for other hospitals as well as training program.
Utilization of the equipment is still under studying.
Future Plan of e-health in Bhutan
Tele-ECG will be installed to more hospital, training program should be conducted properly and will be arranged further.
Tele-consultation will be conducted. Since last March 2003, tele-consultation in cardiology have been conducted between Bhutan`s hospitals and Tokai University of Japan.

## Slide 16: APT Second Opinion Center at Tokai University
On the completion of this tele-ECG Projects, connection has been established between Rural Trashi Yantse, Luntshe hospital and National Referral Hospital in Timphu as well as with Tokai University Japan. Second opinian center is held at Tokai University, to help local doctors in Bhutan dealing with cardiology. This second opinion center is supported by Asia Pacific Telecommunity (APT).
Since then, about 12 patients` data have been sent. Second opinion for treatment and medication have been given by specialists at Tokai University. All discussion and patient data are sent by email, which shows that this system operation is very low cost and effective
At the same time, training in ECG are also given to local medical staffs, in other the achieve better technique, especially in Using ECG machine as well as internet.
Interim results seem promising for continuation of this system, and broadening the projects to more hospitals to achieve better service to patients.

## Slide 17: Example of Teleconsulatation for Patient with serious case in Bhutan
Email from Medical Doktor from Bhutan send to Tokai University:
On Wed, 30 Apr 2003 16:47:54 +0600, username dhsoty <dhxxxx@druknet.bt> wrote... dear sir, This is a case of Ms Dxxx 19 yr old student who is having persistant hemoptysis and giddiness for the last two years.She has no other complaints. OE she is avg built.General examination is WNL. She has a weak pulse in the left side and a good volume pulse on the right.BP is 140/90 in the right and only 100/70 in the left.There is no radiofemoral delay. She has a very prominent suprastenal pulsatile swelling which on palpation is likely to be arterial*the suprasternal hollow is is full with the swelling* Chest exam is normal clinically and so is the heart execept the slightly loud second sound.No clinical evidence of heart failure.
Blood esr-75,ASO negative,Chest xray shows promonent aorta. I am sending her 2 D echo, PSL view ins syst and dias and also the suprasternal view.ecg also sent along.
please advise. Dr. P.Bhxxxxxi,DMO Trashiyangtse Hospital +++++++++++++++++++++++++++++++++++++++++++++++++++ Get a free DrukNet e-mail account and stay in touch http://www.druknet.bt
1. Email and Data of Patient

## Slide 18: Data of Patient

## Slide 19: 2. Advise
From: "Futxxx Ohyama(shonan)" <fxxxx@umin.ac.jp>
To: "dxx" <dxxxx@druknet.bt>
Cc: "sxxxx" <sxxx@is.icc.u-tokai.ac.jp>
Sent: Tuesday, May 27, 2003 3:42 PM
Subject: 19-year-old female patient
Dear Dr.Bxxxxxx, Sr.Kxxxxx
Hello,
I am worried about the 19-year-old female patient introduced by you on the other day. (ID:16 aortic
dissection patient) Has she already moved to Thimphu?
I have also cared many aneurysm patients in the past. Such a patient must control blood pressure enough.
And check the blood pressure of both hands, check the Dorsalis artery and Popliteal artery pulse.
The nursing care which softens uneasiness and pain control is also important to such a patient.
Please let me know about her progress.
F.Ohyama R.N.
Tokai/Japan
From: <sxxxx@is.icc.u-tokai.ac.jp>
To: "username dxxxx" <dxxxx@druknet.bt>
Cc: "Futoshi Ohyama(Isehara)" <fxxx@is.icc.u-tokai.ac.jp>
Sent: Thursday, May 01, 2003 6:22 PM
Subject: RE
Dear DR Bxxx!
This looks to be a case of chronic aortic dissection or aneurysmal dissection. Please look for the signs of
Marfan syndrome in this patient. I think it is better if you refer her to some cardiovascular center in india
without much delay. In the meantime control her systolic blood pressure at 130mm Hg or below.
Dr.M.Athar. S (Tokai Univ.)
“Based on Teleconsulation, finally this patient was sent to referral hospital”

## Slide 20: Concluding Remarks
Telemedicine in Bhutan
- very useful
- step-by-step approach
- sustainability
Evaluation from our current project will become feedback to gain better result for the future projects
Government of Bhutan and Health Professionals have high enthusiasms and welcome to this project which shows high potential sustainable of this project.

## Slide 21: Acknowledgement
Thank You
This East-Bhutan Tele-ECG Project is sponsored by Ministry of Foreign Affairs Japan under Scheme of Grant Assistance for Grassroots Projects.
We are very grateful to Ministry of Foreign Affairs Government of Japan and Ministry of Health of Bhutan for the cooperation.