## Slide 1: H.323 for Telemedicine
Paul E. Jones
Rapporteur, ITU-T Q2/16
Cisco Systems, Inc.

## Slide 2: What is H.323?
H.323* is the international standard for multimedia communications over packet-based networks, including the convergence of voice, video, and data communications
* H.323 is “ITU-T Recommendation H.323: Packet-based multimedia communications systems”

## Slide 3: Where did H.323 Come From?
Recommendation H.323 is a standard published by the International Telecommunications Union Telecommunications Sector (ITU-T)
  Formerly known as CCITT
  Refer to http://www.itu.int/ITU-T/
  A permanent organ of the United Nations System (refer to http://www.unsystem.org/)

## Slide 4: A Little About the Origins…
H.323 was originally scoped to be a protocol for the Local Area Network (1996)
Local Area Network
Or was it?

## Slide 5: Origins (cont.)
The first thing people tried to do was use H.323 in wide area networks, large private VoIP networks, and over the Internet
And it worked!!!

## Slide 6: Origins (cont.)
H.323 was an early adopter of such IETF protocols as RTP, which proved its ability to carry real-time audio and video over IP networks that span the globe
Indeed, H.323 was much more than a LAN protocol

## Slide 7: Origins (cont.)
Recognizing that H.323 was much more than a LAN protocol, evolution and improvement of the H.323 protocol continued (and is continuing) within the ITU-T

## Slide 8: H.323 versus H.320
H.320 is similar to the H.323 protocol in that it provides voice, video, and data communications
H.323 differs in that it is designed for communication over a packet-switched network, such as the Internet, an enterprise LAN, or other IP-based network, whereas H.320 is designed for use over ISDN
Why H.323 over H.320?
  “ISDN is inexpensive to own, but expensive to use… The availability of flat-rate pricing for IP videoconferencing, on the other hand, allows calls at bandwidths too expensive for ISDN, including some IP calls up to 2 Mbps and beyond.” – “Frequently Asked Questions About Voice and Video over IP Networks”, Wainhouse Research and Margalla Communications (January 2003)
  An IP network in the enterprise may be utilized for voice, video, and data, thus potentially lowering the overall communications (both capital expenses and operational expenses)
  H.323 equipment can utilize existing IP-based services, including IP-based voicemail services, LDAP directories, DNS, web-based collaborative tools, etc.

## Slide 9: Evolutionary History of H.323
H.323 version 1 was first approved in 1996, with a focus on enterprise voice, video, and data collaboration
H.323 version 2 was approved in 1998, with a focus on “Internet Telephony”
H.323 version 3 was approved in 1999 with incremental improvements
H.323 version 4 was approved in 2000 with major enhancements focused on the requirements of service providers
H.323 version 5 (scheduled for approval in May 2003) focuses on maturity and stability

## Slide 10: Version Interoperability
While H.323 has been revised a number of time, focus has always remained on backward compatibility
Each new major version introduced a number of new features, but did not sacrifice interoperability
Even so, interoperability events have been necessary to ensure vendor interoperability, with output of those meetings going as input into the SG16 process
At every meeting, an updated H.323 Implementers Guide is published to provide corrections and guidance to implementers of the protocol

## Slide 11: A Cry for Stability… Heard
Enterprise and service providers have requested “stability”, citing a real need for a mature protocol that is not a “moving target”
H.323 version 4 introduced a new extension mechanism, referred to as the “Generic Extensibility Framework” (GEF) that facilitates the addition of new features without making changes to the core standards
All new features that are not considered horizontally useful are being added as separate, optional extensions via the GEF mechanism

## Slide 12: H.248: Scalability of the Gateway
Media
Gateway
Controller
(“Softswitch”)
H.323
H.248
SCN
RTP
Media
Gateway
SCN
RTP
Media
Gateway
SCN
RTP
Media
Gateway
SCN
RTP
Media
Gateway
SCN
RTP
Media
Gateway
SCN
RTP
Media
Gateway

## Slide 13: Today’s H.323 Network Topology
Service Provider IP Core Network
GK
Video Terminals
Enterprise
Enterprise
GK
H.323 PSTN Gateways
GK
GK
GK
“Directory” Gatekeepers
GK
GK
H.248 PSTN Gateways
MGC
MGC
Audio and Video Terminals
GK
GK

## Slide 14: Ongoing Work
LDAP schema specifications
Definition of usage of the H.323 URL, allowing the use of DNS and ENUM with H.323
Enhanced third-party call control
Quality of Service
Scalability and robustness enhancements
Short message service

## Slide 15: Voice, Video, and Data Communications from Day 1
H.323 was designed to be a “multimedia communications” protocol from the outset and not limited only to audio
As such, H.323 provides very tight integration of audio, video, and data communications functionality

## Slide 16: Where We are Today
Voice, video, and data conferencing capability
T.38 fax support
Modem over IP support
Many supplementary services defined
Strong interoperability with other H.32x systems, including H.320 (ISDN) and H.323M (3GPP mobile wireless)
Specification of media gateway decomposition (via H.248)
Support for signaling and media security
User, terminal, and service terminal mobility
Support for emergency services signaling

## Slide 17: Where We are Today (cont.)
Extremely wide deployment
Billions of minutes of traffic per month worldwide (counting public networks only)
More than 90% of all voice over IP traffic today is H.323
Nearly 100% of the video over IP traffic today is H.323

## Slide 18: Where is H.323 Used?
Wholesale transit
Calling Card
Voice Conferencing
Voice VPNs
Unified Communications
IP-PBX
PC-to-phone
Video conferencing
Distance Learning
Call center
IP-Centrex
Mobility services
Custom news / info
Voice/Data/Video Collaboration
Broadband residential
More…

## Slide 19: Industry Support
Hundreds of service providers and equipment manufacturers supporting H.323
H.323 market still growing strongly
“Voice over IP” has been the market driver in recent years
“Video over IP” is now becoming more popular than ever, with deployments in several service providers

## Slide 20: H.323 Forum
The H.323 Forum was founded in 2002
Sponsored by the International Multimedia Telecommunications Consortium (IMTC)

## Slide 21: H.323 Forum Activities
Equipment certification requirements
Live conferences (two or three per year)
Video conferences (three or four per year)
Strategic press releases
Organized presentations at other conferences

## Slide 22: Notable H.323 Forum Events
January 2002: IMTC approves the formation of the H.323 Forum as a part of its organization
May 2002: H.323 Forum “kick-off” in Geneva and a web site
June 2002: H.323 Forum at Collaborative East
August 2002: Certification levels 1a/1b defined
September 2002: First worldwide H.323 Forum video conference was held
October 2002: H.323 Forum at VON
October 2002: ETSI and OSP users group support H.323 Forum
November 2002: H.323 Forum at Collaborative West
November 2002: First H.323 Forum industry conference
March 2003: Second worldwide H.323 Forum video conference was held

## Slide 23: Additional Information
Packetizer http://www.packetizer.com/
H.323 Forum http://www.h323forum.org/
OpenH323 http://www.openh323.org/