## Slide 1: Fiber Optics and xDSL last mile access technologies applicable to E-health
Presented by:
Paolo ROSA
Counsellor – ITU-T Study Group 15
Optical and other transport networks

## Slide 2: Theme 8 from the G7 (’94 – ‘95) 10 Pilot Projects for the I.S. “ Global Healthcare Applications “
demonstrate the potential of telematics technologies in the field of telemedicine in the fight against major health scourges;
promote joint approaches to issues such as the use of data cards, standards and other enabling mechanisms.

## Slide 3: Theme 8 Sub-projects
public health,
cancer,
cardiovascular disease,
telemedicine,
harmonization of datacards and medical imaging.

## Slide 4: Theme 8 Project Results (1999 )
Encouraging results including:
  world-wide interoperability of medical images and health cards
  demonstration of services for a second opinion in oncology and treatment of cardiovascular patients irrespective of their geographic location.
Most projects developed are in the pilot implementation phase.
Demonstrated the potential of telematics technologies in telemedicine and common approaches and standards for individual health smartcards
http://www.europa.eu.int/ISPO/intcoop/g8/i_g8pp_matrix.html

## Slide 5: Theme 2 : Global Inter-operability for Broadband High Speed Networks (GIBN) MAIN RESULTS
19 major applications projects,
tested technologies and inter-working performance
realized interconnection of a number of high speed, national and regional broadband research networks
facilitate the establishment of international links between the various high speed networks and testbeds supporting advanced applications.

## Slide 6
ITU-T Study Group 15
Optical and other transport networks
Responsible for studies relating to:
transport networks, systems and equipment for access, metropolitan and long haul sections and relevant G-series Recommendations.
Lead Study Group on
Access Network Transport (ANT)
Optical Technology

## Slide 7
Access technological evolution
Year
9.6 kbit/s
28.8 kbit/s
56.6 kbit/s
128 kbit/s
2 Mbit/s
640 kbit/s
8 Mbit/s
25 Mbit/s
50 Mbit/s
1989
1997
2000
Analog
modems
ISDN
ADSL2+
ADSL2
HDSL/ADSL
VDSL
OPTICAL
ACCESS
622 Mbit/s
G-PON
2.5 Gbit/s
2003
}

## Slide 8
Many a type of access
F.O.
Copper or F.O.
Copper
Broadcast
SAT
Longhaul
Distribution Network
Access Network
Cable
Home Network
UNI
SNI

## Slide 9: Service definition and requirements ITU-T F.700-series: umbrella definitions:
Definition of several MM tasks:
  Conferencing (multipoint, bi-directional, real-time)
  Conversation (point-to-point, bi-directional, real-time)
  Distribution (point-to-multipoint, unidirectional)
  Sending (point-to-point distribution, Tx controlled, UD; info pushing)
  Receiving (point-to-point distribution, Rx controlled, UD; info retrieval)
  Collecting (multipoint-to-point distrib., UD, Rx controlled; info polling)
Media components: audio, video, text, graphics, data and still-pictures
Quality level for media components: {-1, 0, 1, 2, 3, 4}

## Slide 10
The
Copper Wires Access Network
xDSL technique

## Slide 11: xDSL outline
What is xDSL ?
Why xDSL ?
How it works ?
Typical components
xDSL evolution, standards and applications

## Slide 12: What is xDSL
DSL: Digital Subscriber Line
DSL as a transmission technology using the existing copper wires between a central exchange and a customer with a bit rate speed up to 26 Mbit/s
Signals: symmetrical/asymmetrical, digital, text, audio, video
Concepts of local loop, management, handshake, interoperability, scalability, legacy

## Slide 13: Why x-DSL
Faster than analog (56 kbit/s) and ISDN (>128 kbit/s) modems, reasonable cost, reach 3-6 km
Less expensive that E1/T1 systems, 1.5-2.0- Mbit/s, reach 1 km
Use already existing copper pairs (depending on the performance): start as equipments installed.
Alternative Optical access:
  Wait for full availability
  current cost
  better performance

## Slide 14: Why x-DSL
Transforms potential 700 millions copper wires installed worldwide into multimegabit data pipes
Scenario convenient to providers and users immediately available
Enable the management of different providers of different services to different users tipology

## Slide 15: How it works
Remove line components limiting the bandwidth to the voice frequency (4 KHz = 64 Kbit/s)
Use of copper low attenuation frequencies sending more bits x Hertz for longer reach
Use higher bit rate with a low increase of signal rate (baud) in the line
Use of line codes allowing the transmission of 2 to 15 bits x Hertz (up to 1.1, 2.2, 12 MHz)
Adoption of techniques/phylosophies limiting negative effects (crosstalk, echo, spectrum, etc.)

## Slide 16
Typical components of an xDSL system
audio/video/data
POTS
Splitter
xDT
=
SN = Service Node
xDSL
xDT
xDSL
Transceiver
DTU-R =
Transceiver Unit- Remote
DTU-C =
xDSL
Transceiver Unit- Central office
U-R
T
CUSTOMER PREMISES
CENTRAL OFFICE
POTS
Splitter
xDT
U-C
SNI
• PSTN/ISDN
SN
• B-ISDN SN
• Non-ATM based SN
(e.g. - video server
- IP router)
(Subscriber line)
xDTU-R
xDTU-C
ADSL2+
ADSL2
ADSL
ADSL lite
HDSL
SHDSL
VDSL

## Slide 17
ADSL2+ G.992.5 | Video/ voice/ data/copper | 16 – 25 Mb/s Down Up to 800 Kb up Higher-optional | video capabilities. Dist 1.5 km/BW
ADSL2 With and without splitter – G.992.3 / 4 | Video/ voice/ data/copper | 8 Mb/s down 800 Kb/s up Higher-optional | video capab. Dist + 200m ADSL
ADSL With and without splitter – G.992.1 / 2 | Voice/data /copper | Up to 8 Mb/s down Up to 1.5 Mb/s up | Full use existing copper. Web brows/Voice 2.7- 5.4 km
VDSL Symmetric Asymmetric G.993.1 | Video/ voice/ data (V/V/D) over copper | Up to 52 Mb/s down asymm Up to 26 Mb/s Symm. | Broadcast video, VoD, internet TV, 1.5 km - 300m
SHDSL Symmetric G.991.2 | Voice/data/ Video 1/2 pairs | 192 K to 4.6 M Steps 8/16 Kb/s Poss amplif. | V/V/D Services mainly for business appl.
HDSL Symmetric G.991.1 | Voice data and video 1/2/3 pairs | 784 Kbit/s to 2320 Kbit/s | V/V/D Services mainly for business appl.

## Slide 18
ADSL2 versus ADSL (G.992.3 x G.992.1)
2nd generation of ADSL with improvements on:
  Loop-reach increase for equivalent bit rates (300m)
  Higher down/up bit rates
  loop diagnostics
  Adjustable spectrum shaping during operat/initializ
  Power vs traffic control: L0(full),L1, L2
  robustness against loop impairments and RFI
  Improved multivendor interoperability
Improved application support for an all digital mode of operation and voice over ADSL operation;

## Slide 19
ADSL 2+ : G.992.5
Performance
  Increase downstream: to 16 Mbit/s
  Maybe increase in upstream (Oct. 2003)
  Increase reach (1.5 - 3 Km)
ADSL+ doubles the bandwidth (from 1.1 to 2.2 MHz) with a significant increase of data rates on short loops
Backwards compatibility (needs G.992.3)

## Slide 20
OPTICAL - PONs
The
Optical Access Network
G/B-PONs Technique

## Slide 21: Optical access network architecture (G.983.1)
O
N
U
O
N
U
O
N
U
O
L
T
N
T
N
T
Fibre
Fibre
Fibre
Copper
Copper
HOME
Access network
SNI
FTTB/C
FTTCab
FTTH
Optical Distribution Network
xDSL

## Slide 22: PON Access System
NB
BB
Axs Node
O
L
T
C
C
1:32
OPT
Splitter
ONU
ONU
ONU
ONU
 1530 nm
 1310nm
 +/- 50 nm

## Slide 23: Evolution of Standardization for Multigigabit systems Physical Layer
G.692 | 622 Mbit/s – 10 Gbit/s (STM-4 to STM-16) | WDM from 4 to 32 ch Longit. Compat.- Line amplifiers mono/bidirect. | 1996 / 1998
G.959.1 | 2.5 and 10 Gbit/s | Single ch / up to 16 ch WDM Transv. Compat. - Opt Amplif.s | 2000
G.693 | 10 – 40 Gbit/s (STM-64 to STM-256) | Single channel Transv. Compat. Intra office | 2001
G.694.1 G.694.2 | 2.5 / 10 Gbit/s | Dense WDM ≥ 80 Ch/10 Gbit/s Coarse WDM ≤ 18 Ch/2.5 Gbit/s | 2002
G.983 G.984 | 155/622 Mbit/s 155M/2.5 Gbit | B- and G-PON Access WDM, uni & bidirectional | 2002/2003

## Slide 24
Optical systems for access networks
G.983.x- series : B-PON
Systems supported:
  symmetrical line rates of 155.520 Mbit/s
  asymmetrical line rates of 155.520 Mbit/s upstream and 622.080 Mbit/s downstream.
Transmission techniques:
  Bi-directional - 1 fibre - WDM technique (1.3 mm upstream and 1.5 mm downstream) or
  Unidirectional 2 fibres in 1.3 mm region (both down and upstream)
  Reach at least 20 km
  Enhanced bandwidth for WDM
  Dynamic band assignment

## Slide 25: Optical systems for access networks G.984.x -series - G-PON (01-2003)
2.5 Gbit/s capable PON systems
Symmetrical/Asymmetrical
1.244 and 2.488 Gbit/s downstream
155 Mbit/s up to 2.488 Gbit/s upstream
Business and residential users
Convenient support of IP and Ethernet
Same wavelength plan and full-network design principles as in G.983.x-series (B-PON)
New!
Notes: A passive optical network (PON) is a system that brings optical fibre cabling and signals all or most of the way to the end user in residential and new small/medium business networks. Gigabit-capable PONs will offer customers unprecedented data rates enabling applications such as video-on-demand, streaming video, on-line games, voice over IP and other high bandwidth capabilities.
The draft new standard G.gpon.gsr describes the general characteristics of a Gigabit-capable PON system such as architecture, bit rates, reach, signal transfer delay, split ratio, protection and security.
The second draft new standard G.gpon.pmd describes a flexible optical fibre access network capable of supporting the bandwidth requirements of business and residential services. It covers systems with nominal line rates of 1244.160 Mbit/s and 2488.320 Mbit/s in the downstream (Central Office to customer) direction and 155.520 Mbit/s, 622.080 Mbit/s, 1244.160 Mbit/s and 2488.320 Mbit/s in the upstream (customer to Central Office) direction. Both symmetrical and asymmetrical (upstream/downstream) systems are described.
Both draft new standards enhance the existing set of standards (G.983 series) on Passive Optical Network based access systems by providing unprecedented access network capacities that should satisfy any currently foreseeable customer demands.
A further GPON standard will describe the Transmission Convergence (TC) layer and the ranging protocol.

## Slide 26: G-PONs
    Bit Rate: 7 transmission speed combinations as follows:
       155 Mb/s up, 1.2 Gbit/s down
       622 Mb/s up, 1.2 Gbit/s down
       1.2 Gb/s up, 1.2 Gbit/s down
       155Mb/s up, 2.4Gbit/s down
       622 Mb/s up, 2.4 Gbit/s down
       1.2 Gb/s up, 2.4 Gbit/s down
       2.4 Gb/s up, 2.4 Gbit/s down
    Max Reach :
    20 km for less than 1.25 Gbit/s
    10 km for 1.25 Gbit/s and
    Split ratio : up to 1: 32 (64) , optical power implications, operators convenience, bidirectional

## Slide 27: Targets for the e-health
  Executives & Senior Management
  Physicians, Nurses, other Health Professionals
  Educators, Students, Consultants
  CIOs & Information Managers
  Government Employees
  Health Care Organizations and Association
  Health Record Professionals
  Security & Privacy Professionals
  Vendors of Information Technology and Information Management Solutions
  Consumers/citizens

## Slide 28: Health information
Health information includes information for staying well, preventing and managing disease, and making other decisions related to health and health care.
It includes information for making decisions about health products and health services.
It may be in the form of data, text, audio, and/or video.
It may involve enhancements through programming and interactivity.

## Slide 29: Ethics
Honesty
Security - Privacy
Professionality
Ease understanding for e-patients and e-physicians
Up-dated information/services
Respect fundamental ethical obligations to patients and clients.
Inform and educate patients and clients about the limitations of online health care.
Trustworthy organizations

## Slide 30: Thank you for your attention!
For further information, please feel free to contact:
Counsellor for SG 15: Paolo Rosa
Paolo.rosa@itu.int
Tel: +41-22-730-5235 Fax: +41-22-730-5853
http://www.itu.int/ITU-T

## Slide 31
Additional
slides

## Slide 32
ITU-T Study Group 15 Structure http://www.itu.int/ITU-T/studygroups/com15/index.asp
Study Group 15
Optical and other transport networks
Peter Wery
Working Party 3
OTN Structure
Stephen Trowbridge
Working Party 4
OTN Technology
Gastone Bonaventura
ITU-TSB
Counsellor
Paolo Rosa
Working Party 2
Network Signal Proc.
Yushi Naito
Working Party 1
Network Access
Andrew Nunn
Working Party 5
Projects and Promotion
Haruo Okamura

## Slide 33
Source Siemens
There will never be enough! The bandwidth demand will continue to grow.
Fiber to the home will be necessary sooner or later.
ISDN
100
1k
10k
100k
1M
10M
100M
1G
1980
1990
2000
2010
2020
Year
Bit rate per user (
bit/s)
PSTN / Modem
ADSL
SHDSL
FTTH
double in 18
months
double in 24
months
N.B. The technology bars show
the introduction, not the end of
the technology
VDSL,
FTTCab
Capacity, technologies & availability

## Slide 34
Access Network Transport Reference Model for Scenarios
Customer Premise
Core Network
Wireless
Phone
Access
Unit
[X]
Service
Function
Phone
TV
PC
Core
Network
Access
Network
[X]
Access
Network
[Y]
L
XNI
CP1
x
XNI
WI1
SNI
S1
SNI
C1
SNI
yn
XNI
xxn
Q
Access Network (AN)
Network (CPN)
(CN)
XNI
CX1

## Slide 35
Typical Access Network Construction
Central Office
(Exchange)
Feeder Network
Street Cabinet
Distribution Network
Overhead
Feed
Underground
Feed

## Slide 36
Scenario 1
Services
a) Voice/Data over telecom network and Video over cable, radio&DSB
b) Voice/Data/Video over 2- way cable
Core Network
Existing Infrastructure (PSTN/N-ISDN)
Access network
1-way Cable Distribution Network
b) 2-way Cable Distribution Network
DSB/terrestrial broadcasting in 1 a)
CPN
Access Unit TV, PC, Phone
Information Flow
a) Video Distribution over 1-way cable network, return via PSTN/ISDN
Access Scenarios 1 - 2
a) Voice/Data over telecom network and Video over cable
b) Voice/Data/Video over 2-way cable
B-ISDN
Scenario 2

## Slide 37
Access scenarios – 3 - 4
Scenario 3
Scenario 4
Services
Voice/Data & Video over ADSL/VDSL
Voice/Data & Video over Fibre Network
Core Network
B-ISDN
B-ISDN
Access network
ADSL/VDSL
Fibre (Fibre to the curb/home)
CPN
Access Unit TV, PC, Phone
Access Unit TV, PC, Phone
Information Flow

## Slide 38
Access Scenario 5
Scenario 5
Services
a) Wireless Phone Voice/Data over telecom network and Video over cable
b) Voice/Data/Video over Radio
Core Network
N-ISDN or B-ISDN
Access network
Radio/Wireless for Voice/Data - Cable for a) Video
CPN
Access Unit TV, PC, Phone, wireless Phone
Information Flow
2-way wireless

## Slide 39
Access Scenarios 6 - 7
Scenario 6
Scenario 7
Services
B-ISDN, Internet and Mobile Phone via Satellite
a) Data over Internet
Voice/Video and/or Data over Internet
Core Network
B-ISDN or
Existing (N-ISDN)
a) POTS/FR/ATM
b) ATM Backbone
Access network
Satellite
a) ADSL/VDSL
b) PSTN/ISDN, HFC, PON
c) Fixed wireless Access
CPN
Access Unit: TV, PC, Phone
Access Unit: TV, PC, Phone
Information Flow
2-way satellite

## Slide 40
ADSL 2
Performance
  Downstream: 8 Mbit/s to 15 Mbit/s
  Upstream: 800 Kbit/s to 1.5 Mbit/s
  Data rate on long distances
Improved initialization
Fast Start up : 3 seconds
Fast return to L0 status full operation (0.5 s)
Additional 256 Kbit/s upstream data rate
In-line filters for home installation
Backwards/Legacy compatibility

## Slide 41
G.991.1 (G.hdsl) - High bit rate Digital Subscriber Line (HDSL) transmission system on metallic local lines.
G.992.1 (G.dmt) - Asymmetrical Digital Subscriber Line (ADSL) Transceivers.
G.992.2 (G.lite) - Splitterless Asymmetrical Digital Subscriber Line (ADSL) Transceivers.
G.992.3 Asymmetric digital subscriber line transceivers - 2 (ADSL2.dmt)
G.992.4 Splitterless asymmetric digital subscriber line transceivers - 2 (ADSL2.lite)
ITU-T Recommendations on ADSL (1)

## Slide 42
G.992.5 – Asymmetric Digital Subscriber Line (ADSL) Transceivers – Extended Bandwidth ADSL2 (ADSL2plus) (Jan ’03)
G.995.1 - Overview of Digital Subscriber Line (DSL Recommendations).
G.991.2 (G.shdsl) - Single pair High bit rate speed Digital Subscriber Line
G.993.1 (G.vdsl) - Very high bit-rate Digital Subscriber Line
G.994.1, G.996.1 and G.997.1 for tests, management and handshake
ITU-T Recommendations on ADSL (2)

## Slide 43: Optical Systems for Access Networks Market & Business Drivers (1)
Getting PSTN, data and cable TV together on one system at competitive prices
Fibre To The Home (FTTH), to the Curb (HTTC) to the Business (HTTB) are the next step for many operators
The major change is driven by the explosive growth of the Internet usage
Public and private networks evolve from multiple overlay networks to a unified network platform able to carry multiple applications

## Slide 44: Optical Systems for Access Networks Market & Business Drivers (2)
IP routers and ATM switches are providing higher and higher speed optical interfaces
Major carriers are realizing that services at STM-16 (2.5 Gbit/s) optical pipes may well represent more than 50% of the bulk bandwidth entering networks in the near future
The new high speed data requirements are requiring a new category of Wavelength Services
These new services will require new networking functions (performance monitoring, fault localization, network restoration, etc)

## Slide 45: OTN Standardization Work Plan
Global Optical Transport Network
Supporting Today's and Future Services
OTN
IrDI
OTN
IaDI
Carrier Domain A
Carrier Domain B
SDH
STM-N
USER
NE
USER
NE
OTN
IaDI
OTN
IaDI
OTN
IrDI
OTN
NE
OTN
NE
OTN
NE
User/carrier may originate/terminate the OTN framing for any digital payload
(IP, ATM, SDH,,,)
IaDI = Intra-Domain Interface
IrDI = Inter-Domain Interface
NE = Network Element
Interfaces:For single/multichannels with performance monitoring

## Slide 46: Key aspects for optical technologies
IP over optical, business and market aspects
Switched optical networks
Optics in access and metropolitan networks
Optical interfaces
Optical/IP network OAM and protection and restoration
WDM and C&D-WDM
Signalling and routing
Optical fibres, cables and components
Optical network management
Optical switching equipment
Network performance (IP/Optical)
Optical network clients and services
Services and network evaluation
 Making fully-optical networks viable

## Slide 47: OTN Structure and Technology
Optical Transport Network (OTN) structure
  Automatic Switched Optical Network (ASON)
  Architecture and interfaces for the OTN
  Optical Cross-Connect and Switch functions
  Network management and control
OTN technology (terrestrial and submarine)
  Coarse and Dense WDM, 40 Gbit/s signal channels
  Optical components & amplifiers (e.g. tunable filters)
  Fiber characteristics, more channels/fiber
  Transmission technology (Soliton/RZ), long reach

## Slide 48
G.983.3 wavelength allocation
1260
1360
1340
1320
1300
1280
G983.1 Upstream Band
(
unchanged at 100
nm
bandpass
)
1360
1460
1440
1420
1400
1380
Reserved for allocation by ITU
-
T
Guard band
1480
Guard band
1260
1360
1340
1320
1300
1280
G983.1 ATM PON Upstream Band
(unchanged at 100 nm bandpass)
Basic Band (constrained APON band)
For future use
Upstream Window (no change)
Enhancement Band (other uses)
1360
1460
1440
1420
1400
1380
Reserved for allocation by ITU
-
T
Guard band
1480
Guard band
1360
1460
1440
1420
1400
1380
Reserved for allocation by ITU
-
T
Guard band
1480
Guard band
Intermediate wavelength band (Upstream and/or Downstream)
1.5 m wavelength band (Upstream and/or Downstream)
Basic Band
ATM
-
PON
Downstream
Guard band
Guard band
Future L Band
Reserved for
allocation by ITU
-
T


2

4

3

5

6
WDM
Video/Dig
Enhancement Band
Constrained
ATM-PON
Downstream
Guard band
Guard band
Reserved for
allocation by ITU
-
T
1

2

4

3

5

6
G.983.1 downstream
1 – 2 = 1480 – 1500 nm
3 - 4 = 1539 – 1565 nm
(WDM G.959.1 central freq.)
1.3 m wavelength band (Upstream)

## Slide 49
G.983.4 – Dynamic Bandwidth Assignment
Improves efficiency of upstream
Adjust bandwidth among Optical Network Units in response to bursty traffic requirements
More customers to the PON
More efficient utilization
Possibility of enhanced services (BW peaks) beyond the fixed allocation
Symmetrical 155 Mbit/s
Asymmetrical up 155 Mbit/s down 622 Mbit/s

## Slide 50: Optical systems for access networks Broadband PON: G.983.x-series Recs.
Passive Optical Network up to 622 Mbit/s symmetrical / asymmetrical
Supports wide range of narrow- & broadband services like:
  PSTN / ISDN / Multiple Line
  Data / LAN interconnection / High speed Internet (~100 Mbit/s)
  Cable TV / Video on demand (up to 400 TV channels on single wavelength)
  Videoconferencing
Independent from bit rates, signal formats (digital or analogue, SONET/SDH etc.) and protocols (IP, Ethernet, ATM etc.)
Need to deploy only the equipment at the ends of the network as needed to add new services to existing customers or to add new customers.
Notes: Summary of G.983 sub-series of B-PON Recommendations:
G.983.1: Broadband optical access systems based on Passive Optical Networks Specifies an optical access system with symmetrical line rates of 155.520 or 622.080 Mbit/s and asymmetrical line rates of 155.520 Mbit/s upstream and 622.080 Mbit/s downstream.
G.983.2: ONT management and control interface specification for B-PON Specifies requirements for the OMCI, managed entities of a protocol-independent Management Information Base and protocol/detailed messages for the ONT management and control channel.
G.983.3: A broadband optical access system with increased service capability by wavelength allocation Adds an additional wavelength band to a G.983.1 B-PON to enable the distribution of unidirectional or bidirectional video broadcast or data services.
G.983.4: A broadband optical access system with increased service capability using dynamic bandwidth assignment Specifies the enhancements to a G.983.1 B-PON to allow the use of dynamic bandwidth assignment.
G.983.5: A broadband optical access system with enhanced survivability Specifies protection features for a G.983.1 B-PON.
G.983.6: ONT management and control interface specifications for B-PON system with protection features Specifies the OMCI for a B-PON system with protection features.
G.983.7: ONT management and control interface specification for dynamic bandwidth assignment (DBA) B-PON system Specifies the OMCI for a B-PON system using dynamic bandwidth assignment.

## Slide 51
WDM Spectral bands (proposal) definition for classification and not specification purposes
Band | Descriptor | Range (nm)
O-band | Original | 1260 to 1360
E-band | Extended | 1360 to 1460
S-band | Short Wavelength | 1460 to 1530
C-band | Conventional | 1530 to 1565
L-band | Long Wavelength | 1565 to 1625
U-band | Ultra-long wavelength | 1625 to 1675

## Slide 52
Recommendation G.983.3
(Enhancement band)
  Defines new wavelength allocations to distribute WDM and additional service signals simultaneously.
  Allows distribution of video broadcast services or data services without disturbing basic ATM-PON system
  Potentially provides unidirectional and bi-directional services.
  New reference points and optical interface parameters for new WDM and/or optical power splitter/combining functions at OLT and/or ONU sites.
  Full compatibility with the G.982 and G.983.1.
  Central frequencies => Recs. G.959.1 and G.692

## Slide 53: G-PONs (Cont’d)
    Operating wavelengths
    Downstream direction
    single fibre systems shall be 1480 ‑ 1500 nm.
    two fibre systems shall be 1260 ‑ 1360 nm.
    Upstream direction
    The operating wavelength range for the upstream direction shall be 1 260 - 1 360 nm.
    Physical/Optical parameters
    fibres, lasers, detectors, Pin, sensitivity, margins etc, in G.984.2

## Slide 54: G.PONs (cont’d)
    Improved interoperability – One-to-Many
    Symmetric/Asymmetric
    Backward compatibility to G.983.1
    Fast start-up for initialization
    Increased network capacity
    More efficient IP and ethernet handling
    Video-on-demand, streamed video, games, voice over IP, distance learning, telemedicine
    Less expensive, more reliable
    VDSL, other xDSL backhaul

## Slide 55: G.984.1 – General Characteristics of Gigabit-capable PONs
General characteristics of a G-PON such as architecture, bit rates, reach etc.
G.984.2 –Gigabit-capable PONs: Physical media dependent layer specification
Describes flexible optical fibre access networks capable of supporting the bandwidth requirements of business and residential services

## Slide 56: Metropolitan Optical Network
Short to medium length distances in metropolitan areas. That is, typically, within the limits of a single optical span and often less than 200km distance. signal regeneration, in-line amplification and error correction are of lesser importance than in Long Haul Optical Networks
Maximized coverage commensurate with low cost connectivity
Combined with the wider variety of client signals is a key driver for flexible aggregation (e.g., 100Mb-1Gb rate), higher bandwidth interfaces for inter office
Bandwidth-on-demand services, and multiple classes-of-services leading to further topology and technical considerations.