## Slide 1: Session 6 – Telecommunications in support of E-Health Conclusions & Recommendations
P.A.Probst/Swisscom

## Slide 2: Presentations in Session 6 Telecommunications in support of E-health
H.323 MM-Systems for Telemedicine P.E.Jones, Rapporteur for Q2/16 ITU-T SG16
Fiber Optics and xDSL last mile technologies applicable to E-Health P.Rosa, Counselor ITU-T SG15
Connecting the Health Community: the next Dimension for Patient Centered Care J.Zimmermann, Siemens Medical Solutions/USA

## Slide 3: Highlights from Presentation 1: H.323 MM-Systems for Telemedecine P.E.Jones, Rapporteur for Q2/16 ITU-T SG16
H.323 was built from the ground-up as a multimedia conferencing protocol
H.323 gained huge acceptance for VoIP and international recognised standard for multimedia communication over packet based networks (H.323 carries 90%+ of VoIP traffic today)
H.323 is a system standards integrating audio, video and data functionalities
Specific E-Health requirements will need to be analysed

## Slide 4: Highlights from Presentation 2: Fiber Optics and xDSL last mile technologies applicable to E-Health P.Rosa, Counselor ITU-T SG15
Fiber optic and xDSL access systems standards are in the mandate of ITU-T/SG15 as lead SG for Access Network Transport (ANT) and Optical Technology
xDSL Standards allow today the transport of up to 26 Mbit/s from the local exchange to the user on the existing copper wire. The family of standards includes ADSL, VDSL, SHDSL, HDSL
Fiber optic access systems standardized in SG15 are based on the Passive Optical Network concept (PON) using passive optical components and mono/bi-directional WDM techniques
Optical Systems for PON access networks are specified in the G.983.x/ G.984.x series of Recs (symmetric or asymmetric, 155, 622 and 2488 Mbit/s)

## Slide 5: Highlights from presentation 3: Connecting the Health Community: the next Dimension for Patient Centered Care J.Zimmermann, Siemens Medical Solutions/USA
Role of industry to support and add value to the E-Health customers and their communities
Presentation of the IHE Vision for Growth as a model with four dimensions: workflows inside department, common consistent data, vertically integration of department, community
Definition of a rational business framework and analysis of the workflows based on the patient, physician and payers expectations
Focus on areas like privacy/confidentiality, architecture, standards/vocabulary, safety/quality, …
Providing measurable benefits to patients and physicians creates the best chance for lasting success
Choose the sequence of innovation introduction carefully, select for adoption

## Slide 6: Recommendations
Improve the coordination and cooperation among ITU, IEC, ISO, other SDOs and other involved parties (e.g.DICOM) in order to ensure the interoperability of MM-Systems and benefits from the economic advantages of global recognised standards
Adopt a business process oriented approach and set up priorities
In the design for E-Health application, specific characteristics and suitability of the different technologies like copper, optics, satellite, mobile, WLAN, Bluetooth, etc.. have to be considered.
Special attention should be given to the specific need of developing countries
Promote the implementation of wireless and/or fix network infrastructure in developing countries

## Slide 7: Follow-up actions
Action Item | Lead | Other players | Priority
Capabilities of MM-Systems to support E-health applications (Service definitions and description, architecture, coding, LDAP, security, …) | SG16 (ITU-T) | ITU-T, ITU-D, ITU-R, ISO, IEC, CEN,….. | High
Promote E-Health applications and the deployment of suitable access technologies in developing countries (e.g. international pilot projects,…) | SG 2 (ITU-D) BDT | ITU-T, ITU-R, UN-Agencies Industry, Telcos, … | High
Analysis of the need for standards based on the main business processes | ICG, MoU | All players | Middle