## Slide 1: Basic requiremenst to Quality of Service (IP centric)
Jean-Yves Monfort
France Telecom T&I/R&D
ITU-T SG 12 Chair

## Slide 2: QoS and NP activities at ITU-T
SG 12 : End to end quality, as perceived by the users. It is fully addressed to Quality, and WP3/12 is dedicated to QoS for IP.
SG 13 : WP4/13 is dedicated to Network Performance
SG 2 : Mainly on operational aspects of QoS and SLA. New QoS handbook and activities on the impacts of routing on QoS.
  QSDG : 1 forum meeting each year and QSDG Magazine
SG 4 : Management of QoS and SLA.
SG 9 : QoS for cable networks and video assessment.
SG 11 : QoS signalling.
SG 15 : System-specific requirements for network and transport equipment.
SG 16 : QoS Mecanisms for H.323-based multimedia systems. Quality of speech and video coders.
SG 17 : Frame Relay QoS.

## Slide 3: QoS and NP. Definitions
E.800 definitions:
  QoS : “The collective effect of service performance which determines the degree of satisfaction of a user of a service”
  NP :”The ability of a network or network portion to provide the functions related to communications between users.”
New Concept : QoE
(Quality of Experience)
4 viewpoints on QoS Rec. G.1000 (Communications Quality of Service : a framework and definitions)

## Slide 4: A selection of Recommendations approved during the study period
G.1000 «Communications Quality of Service : A framework and definitions »
G.1010 «End-User multimedia QoS categories »
E.860 “Framework for service level agreement”
Y. 1541 “IP Performance objective and allocations”
Revised Y.1540 « IP Packet transfer and availability performance parameter”
M.3341 « Requirements for QoS/SLA management over TMN X-interface for IP-based services
M.2301 IP Network Provisioning & Maintenance

## Slide 5: A selection of works in progress in the ITU-T SGs
On terminal equipments for VOIP (IP Terminals, Gateways)
On Quality parameters, modelling and classes: G.IPP (Transmission performance pameters for IP …), G.MMPerf (Multimedia performance requirements), H.mmclass,
Several Rec. for perceptual Video Quality.
Several Questions on Quality evaluation and Modelling (Subj./Obj.; intrusive or non intrusive)
QoS Handbooks
On Performance: MPLS Perf, Ethernet Perf
On Management : H.QoS.m
On QoS Signalling Draft TRQ “Signalling Requirements for IP-QoS”, E-QSC (Signalling of proposed QoS services classes…)
On QoS Architecture : H.QoSarch End to End QoS Control , Y.qosar

## Slide 6: New activities under progress in SG 12 (related to user)
Subjective Quality Evaluation of Telephone Services Based on Spoken Dialogue Systems
Transaction performance of applications running over IP- and Web-oriented networks
How and to what extent should the ITU deal with standardising definitions of parameters used in SLAs and other performance-related reports?

## Slide 7
Max Packet Loss, Max Mean Delay, Max Delay Variation
TRANSPORT
APPLICATION
Codec Performance, VAD, Frames per Packet, Jitter Buffer Size,Codec Delay, FEC (Redundancy)
QoS Parameters
ITU-T SG16/11
ITU-T SG13/IETF
SERVICE
User Perceived QoS
ITU-T SG12/16

## Slide 8
Network Packet Loss, Mean Delay, Delay Variation
Multimedia QoS Classification
APPLICATION
Application Factors (e.g. codec type, jitter buffer etc)
SERVICE
Voice
Video
Data
Voice Classes
Video Classes
Data Classes
Service Components (Classes G.1010)
Service (e.g. videoconferencin,
broadcast video etc)
TRANSPORT
Bearer Classes
Bearer Classes
Bearer Classes
Voice Factors
Video Factors
Data Factors
Class based (Y.1541)

## Slide 9: QoS Classes
The concept of QoS classes should be preferred to individual parameters for signalling end-to end QoS.
It is important that the parameters that make up a a given QoS class are independent of one another.
Existing Recommendations : G.109 (for VoIP), G.1010, Y.1541
Progress in the use QoS classes:
  signalling for end-to-end QoS
  management of QoS Classes

## Slide 10: Recommendation G.1010
End-User Multimedia QoS Requirements
Performance expressed by parameters
  Focused on user perceivable effects
  Independent of the networks internal design
Parameters
  Delay
  Delay variation
  Information loss (Expressed as PLR -Packet loss Ratio-)
From P. Coverdale, WP 3/12 Chairman

## Slide 11: Performance considerations for different applications
Tolerance to delay for data applications
  Distinguish between "urgent" applications
    E-commerce
    Command/control functions
    Interactive games
  and "less urgent" applications
    File downloads
    Images
    Messaging

## Slide 12: Recommendation G.1010 End-User Multimedia QoS Requirements
Performance expressed by parameters
  Focused on user perceivable effects
  Independent of the networks internal design
Parameters
  Delay; Delay variation; Packet loss Ratio
Model for user-centric performance requirements Mapping can be formalised into model for QoS categories

## Slide 13: Mapping of user-centric QoS requirements
Packet Loss
8 distinct groupings, covering the range of applications
Distinction between applications which can tolerate some information loss and those that cannot
Main distinction in terms of delay

## Slide 14: Benefit of end-user QoS category model
Model is based on end to end user perception of impairments, therefore not dependent on any specific technology for its validity
Provides basis for realistic network QoS classes (eg ITU-T Rec. Y.1541)
Rec. G.1010 provides an indication of the upper and lower boundaries for applications to be perceived as essentially acceptable to the user (A new Recommendation G.Mmperf is under developpment)
Shows how the underlying impairments of information loss and delay can be grouped appropriately, without implying that one class is “better” than another

## Slide 15: Performance targets for audio and video applications
Medium
Application
Degree of symmetry
Typical data rates
Key performance parameters and target values
One-way
delay
Delay
variation
Information loss**
Other
Audio
Conversational voice
Two-way
4-64 kb/s
<150 msec
preferred*
<400 msec limit*
< 1 msec
< 3% packet loss ratio (PLR)
Audio
Voice messaging
Primarily
one-way
4-32 kb/s
< 1 sec for playback
< 2 sec for record
< 1 msec
< 3% PLR
Audio
High quality streaming audio
Primarily one-way
16-128 kb/s
< 10 sec
< 1 msec
< 1% PLR
Video
Videophone
Two-way
16-384 kb/s
< 150 msec preferred
<400 msec limit
< 1% PLR
Lip-synch : < 80 msec
Video
One-way
One-way
16-384 kb/s
< 10 sec
< 1% PLR
* Assumes adequate echo control
** Exact values depend on specific codec, but assumes use of a packet loss concealment algorithm to minimise effect of packet loss
Provisional values

## Slide 16: Performance targets for data applications
Medium
Application
Degree of symmetry
Typical amount of data
Key performance parameters and target values
One-way
delay*
Delay
variation
Information loss
Data
Web-browsing
- HTML
Primarily one-way
~10 kB
Preferred < 2 sec /page
Acceptable < 4 sec/page
N.A
Zero
Data
Transaction services – high priority e.g. e-commerce, ATM
Two-way
< 10 kB
Preferred < 2 sec
Acceptable < 4 sec
N.A
Zero
Data
Command/control
Two-way
~ 1 kB
< 250 msec
N.A
Zero
Data
Interactive games
Two-way
< 1 kB
< 200 msec
N.A
Zero
Data
Telnet
Two-way (asymmetric)
< 1 kB
< 200 msec
N.A
Zero
Data
E-mail (server access)
Primarily one-way
< 10 kB
Preferred < 2 sec
Acceptable < 4 sec
N.A
Zero
* In some cases, it may be more appropriate to consider these values as response times.
Provisional values

## Slide 17: Performance targets for data applications
Medium
Application
Degree of symmetry
Typical amount of data
Key performance parameters and target values
One-way
delay*
Delay
variation
Information loss
Data
Bulk data transfer/retrieval
Primarily one-way
10 kB-10 MB
Preferred < 15 sec
Acceptable < 60 sec
N.A
Zero
Data
Still image
One-way
< 100 kB
Preferred < 15 sec
Acceptable < 60 sec
N.A
Zero
Data
E-mail (server to server transfer)
Primarily one-way
< 10 kB
Can be several minutes
N.A
Zero
Data
Fax (“real-time”)
Primarily one-way
~ 10 kB
< 30 sec/page
N.A
<10-6 BER
Data
Fax (store & forward)
Primarily one-way
~ 10kB
Can be several minutes
N.A
<10-6 BER
Data
Low priority transactions
Primarily one-way
< 10 kB
< 30 sec
N.A
Zero
Data
Usenet
Primarily one-way
Can be 1 MB or more
Can be several minutes
N.A
Zero
* In some cases, it may be more appropriate to consider these values as response times.
Provisional values

## Slide 18
The previous tables (now under reconsiderations) could be reconsidered for telemedecine applications.

## Slide 19: Recommendation Y.1541 QoS Classes: A Basis for IP Network QoS Control
NI-to-NI Reference Path for network QoS Objectives
NOTE : Customer installation equipment is shown for illustrative purposes, only

## Slide 20: Recommendation Y.1541 QoS Classes: A Basis for IP Network QoS Control
A new parameter as been recently included in Y.1540 (the limits are still under study:
IPSLBR : IP Paket Severely Loss Block Ratio
U means « unspecified » or « unbounded »
Note for IPVD : The value of 50ms is dependent on the capacity of inter-networks links. Smaller variations are possible where all the capacities are higher than primary rate, or when competing packet information fields are smaller than 1500 bytes

## Slide 21
Inter-relationship of QoS Factors
Codec Performance
Network Factors
Network Delay
Network Packet Loss
Network Jitter
Overall Delay
Application Factors
Overall Packet Loss
Jitter Buffers
Perceived Speech Quality
QoE

## Slide 22: Future of QoS/NP in ITU-T
The basis for QoS Classes is available. Need to complete and to converge on complete figures (for the different services and layers)
In the future, other mechanisms and protocols may enable dynamic QoS over multiple networks
Emphasis on User’experience (that could be useful for eHealth
To continue the cooperation with other standardization bodies (working on QoS, but also working on specific applications) to communicate our progress, to offer to solve some issues they meet on QoS and to improve the compatibilities of the standards. See the objective of the Workshop (1-3 october 2003, Geneva) on QoS.

## Slide 23: Annex 1: QoS in IP Networks (From M. Buckley)

## Slide 24: General Approach to IP Transmission
IP Network
Information is digitally encoded via Codec
Data is transmitted in packets
IP Networks transmit packets end to end
Codecs reconstitute original signal

## Slide 25: Factors Affecting Quality
IP
Network
Packet Loss, Delay, Jitter
CODEC
type
Local
Loop

## Slide 26
IP NETWORK
10 bytes every 10 ms
Arrivals nor evenly spaced
Effect of Jitter

## Slide 27: Effect of Delay
CODEC
CODEC
Encode
Transmission
Jitter
buffer
Decode

## Slide 28: Effects of overloading network
Problem
Area
Quality depends on traffic level – time varying

## Slide 29: Typical congestion events
LAN
congestion
Access link
congestion

## Slide 30: Impact on packet stream
Packets discarded
by end system

## Slide 31: Effects of Burstiness
Packet Loss Concealment works well for isolated
lost packets
Periods of high packet loss result in audible sound
Quality degradation

## Slide 32: Annex 2 ITU-T Workshop « End to End Quality of Service. What is it? How do we get it?
Geneva 1-3 Ocober 2003
  Economic impacts and stakes of the QoS
  User’s experience
  QoS approach in the different standardization bodies
  Performance metrics and Measurement techniques
  General concepts of QoS Classes. Definitions. Relations between layers. Signalling and Management
  Overall Panel discussions and Action Plan for the future

## Slide 33
Thanks for your attention
Jeanyves.monfort@francetelecom.com
Jean-yves.monfort@ties.itu.int