## Slide 1: E.164 (05/97)
The international public
telecommunication numbering plan
Presented by:
Sverre Isaksen
Telenor Networks
Senior Associated Rapporteur
ITU SG2 Q.1/2 Numbering, naming and addressing

## Slide 2: Scope
E.164 provides the number structure and
functionality for the following three categories
of International Public Telecommunication
numbers (E.164 numbers).
Geographical Global Networks
areas services
+800
+45

## Slide 3: Scope
In addition to these three categories the
following two new categories will hopefully
appear in a revised E.164.
Groups of Trials
countries

## Slide 4: Structures and options
Number structure for geographical areas
CC
NDC
SN
1 to 3
digits
Max 15-n (number of digits in CC) digits
CC: Country Code
NDC: National Destination Code
SN: Subscriber Number

## Slide 5: Structures and options
Numbers for geographical areas, formats
for national use.
Option 1: separated NDC and SN
NDC
SN
SN
CC
NDC
SN

## Slide 6: Structures and options
Numbers for geographical areas, formats
for national use.
Option 1: separated NDC and SN
NDC
SN
SN
CC
NDC
SN
National prefix
International prefix

## Slide 7: Structures and options
Numbers for geographical areas, formats
for national use.
Option 2: connected NDC and SN
NDC
SN
SN
CC
NDC
The leading digits of the national subscriber
numbers indicates services and/or geography.
National subscriber number

## Slide 8: Structures and options
Numbers for geographical areas, formats
for national use.
Option 2: connected NDC and SN
SN
SN
CC
NDC
NDC
International prefix
When NDC and SN are inseparably connected
to form a single dialling sequence, a national
prefix is not necessary.

## Slide 9: Structures and options
Numbers for geographical areas, formats
for national use.
Option 1 and 2 are normally used in parallel,
with option 1 for geographic numbers and
option 2 for national location independent
numbers.
Option 2 can however be used for both type
of numbers nationally.

## Slide 10: Structures and options
Numbers for Global Services
CC
GSN
3 digits
Max 12 digits
CC: Country Code for global service (800, 808, 878, 979)
GSN: Global Subscriber Number
The leading digits of GSN may indicate some
service specific characterics. The global
services have only one international
format, but access to global services ………

## Slide 11: Structures and options
Numbers for Networks. Network is inter-
nationallly interconnected physical nodes
and operational systems operated and
maintained by one or more ROAs to provide
public telecommunication services.
CC1
CC2
CC3
CC4

## Slide 12: Structures and options
Numbers for Networks.
CC
SN
3 digits
Max 15-n (number of digits in CC+IC) digits
CC: Country Code for Networks (882)
IC: Identification Code
SN: Subscriber Number
IC
1 to 4
digits

## Slide 13: Structures and options
Numbers for Networks, optional formats
CC
IC
SN
IC
SN
SN
Network internal
Incoming to Network
Between Networks
To use the three formats for the mentioned
purposes each Network would have to create
their own Network internal prefixes.

## Slide 14: Structures and options
Numbers for Groups of countries
CC
GIC
SN
3 digits
Max 11 digits
CC: Country Code for Groups of countries (tbd)
GIC: Group Identification Code
SN: Subscriber Number
1 digit

## Slide 15: Structures and options
Numbers for Trials
CC
TIC
SN
3 digits
Max 9 digits
CC: Country Code for Trials (991)
TIC: Trial Identification Code
SN: Subscriber Number
3 digits

## Slide 16: Numbering for geographic areas
Prefixes are not part of the E.164 number
and are not signalled over international
boundaries.
E.164 indicates preference for the use of digit
0 as national prefix.
The digit analysis should not be more than 7
digits to determine the country of destination,
the most appropriate routeing and the proper
charging.

## Slide 17: Planning advices for geographic areas
The national numbering plans should be designed:
a) to allow for generous provision of future growth;
b) so that the national networks be accessible to subscribers in other countries by means of international dialling procedures.
c) so that subscribers would always be called by the same national number regardless of where the call is originated from within a national numbering plan.
It is recommended that notification of national
numbering changes be submitted at least 2 years in
advance.

## Slide 18: International prefix
E.164 recommends that Administrations
that are revising their numbering plans
adopt 00 as an international prefix.
CC1
CC2
CC3
CC4
00 + E.164 numbers

## Slide 19: Frequently asked question
When is a number an E.164 number?
When it satisfies the following:
1. It has to be part of an ITU defined fixed international hierarchical structure.
2. It has to be maximum 15 digits.
3. It has to be unique in its international format.