## Slide 1: Directories
Erik Andersen
Consultant, Andersen's L-Service

## Slide 2: What is a directory?
white pages paper telephone directory
yellow pages paper telephone directory
price list
department store catalogue
e-mail directory
other electronic directories
etc.
A repository for information about objects of particular interest!
Examples:

## Slide 3: Existing Recommendations
The X.500 series: The OSI Directory
F.500: International public directory services
E.115: Computerized directory assistance
F.510: Automated directory assistance, white page service definition

## Slide 4: Work in progress
X.500 extensions
F.511: Directory Profile for the support of the ITU-T F.510 Requirements
Unified Directory Specification E.115 replacement

## Slide 5: IETF activity
Originally developed as simple X.500 access protocol
  Solely base on TCP/IP
  Text oriented
Maps closely to DAP
  Assumes X.500 model
  Low cost entry
Has evolved to be a specification of an LDAP server not being X.500 compatible
LDAP = Lightweight Directory Access Protocol

## Slide 6: IETF activity (cont.)
Several versions:
  University of Michigan implementation
  RFC-1777 - Version 2
  RFC-2251 - Version 3
An API has been developed aiding implementations
LDAP = Lightweight Directory Access Protocol

## Slide 7: The X.500 Directory Specification
An X.500 Directory is a general purpose directory
Gives a set of specifications for:
  how objects are represented by entries in the Directory
  how objects represented in the Directory are named
  how information about objects is created, organised, interrogated, updated and deleted

## Slide 8: The X.500 Directory Specification (cont.)
An X.500 Directory is distributed allowing:
  the establishment of a global Directory
  information to be maintained by the owner of information
  a separation between public and private domains
  possibility for replication of information

## Slide 9: The X.500 Directory Specification (cont.)
Developed jointly by ISO/IEC and ITU-T as
  ISO/IEC 9594 multi-part International Standard
  ITU-T X.500 Series of Recommendations

## Slide 10: The X.500 Directory Specification (cont.)
Available in several editions:
  1988: ISO/IEC 9594 : 1990 CCITT Rec. X.500 (1988)
  1993: ISO/IEC 9594 : 1995 ITU-T Rec. X.500 (1993)
  1997: ISO/IEC 9594 : 1998 ITU-T Rec. X.500 (1997)
  2001: ISO/IEC 9594 : 2001 ITU-T Rec. X.500 (2001)

## Slide 11: X.500 Document Structure
ISO/IEC 9594-1 | X.500 Overview of Concepts, Models, and Services
ISO/IEC 9594-2 | X.501 Models
ISO/IEC 9594-3 | X.511 Abstract Service Definition
ISO/IEC 9594-4 | X.518 Procedures for Distributed Operation
ISO/IEC 9594-5 | X.519 Protocol Specifications
ISO/IEC 9594-6 | X.520 Selected Attribute Types
ISO/IEC 9594-7 | X.521 Selected Object Classes
ISO/IEC 9594-8 | X.509 Public-Key and Attribute Certificate Frameworks
ISO/IEC 9594-9 | X.525 Replication (post-1988)
ISO/IEC 9594-10 | X.530 Use of Systems Management for Administration of the Directory (post-1993)

## Slide 12: Directory Information Tree - DIT
cn=Ole
Jensen
Root
c=DK
c=GB
o=Fallit A/S
ou=Salg
o=Broke Ltd
ou=
Udvikling
Name = < cn=Ole Jensen, ou=Salg, o=Fallit A/S, c=DK >
Entry representing
an object
o=ALS
cn=Per
Yde
cn=Ole
Jensen

## Slide 13: X.500 extension work
Support of Distributed Paged Results within ITU-T Rec. X.500 | ISO/IEC 9594
Support of Friend Attributes within ITU-T Rec. X.500 | ISO/IEC 9594
Enhancements to Public-key and Attribute Certificates
LDAP Alignment
Related Entries in the Directory

## Slide 14: F.500 - International public directory services
Developed based on the 1988 edition of X.500
Service description for a global directory infrastructure
Was never materialised

## Slide 15: E.115 - Computerized directory assistance
Operator
User
Local server
International server
E.115 protocol

## Slide 16: E.115 - Computerized directory assistance
Very simple protocol based on OSI
Very efficient databases behind
Have had little publicity
Widely implemented
Limited to a single application
Does not specify a naming structure
Difficult to extend to meet future requirements

## Slide 17: F.510 - Automated directory assistance, white page service definition
Description of a service to replace the E.115 service
Not an implementation specification
A snapshot of the requirements at the time of development
Basis for considerable extensions to X.500 as provided by edition 4

## Slide 18: F.511 - Directory Profile for the support of the ITU-T F.510 Requirements
Identified the subset of X.500 required for the support of F.510
Defines additional information types for the support of F.510

## Slide 19: Unified Directory Specification (UDS)
Developed for "Association for European Interworking of Directory Inquiry Services" (EIDQ Association)
To become ITU-T Recommendation (hopefully)
Replacement of E.115 instead of X.500

## Slide 20: X.500 seen as being complex
Originally developed for other environment
Resource demanding
Requires skilled personnel
Has many functions not needed
Migration from current E.115 systems difficult
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Approach taken for first draft of UDS
X.500
with EIDQ goodies
E.115
Functions
Cut-down version of X.500 access protocol (“UDAP”)
UDS

## Slide 22: UDS Characteristics
Uses X.500 model and concepts
Unified Directory Access Protocol (UDAS) encoded in ASN.1 and XML
XML Schema used for the specifications
Imports attribute types from X.500 and F.511

## Slide 23: UDS Characteristics (cont.)
Can be used to access E.115 systems
Is general in nature and usable for other applications (e.g. Electronic Commerce)
Does not require, but supports naming of entries
Extensibility is built into the protocol

## Slide 24
END
UDS
X.500