## Slide 1: IETF
Overview of the
Sub-IP AREA
Blurring the Lines Between Circuits and Protocols
Bert Wijnen, bwijnen@lucent.com
Scott Bradner, sob@harvard.edu
Co-ADs for IETF SUB-IP Area

## Slide 2: Above and below
traditionally the IETF has been:
  “above the wire and below the application”
  not (often) defining user interfaces
  not defining physical wire types
while doing “IP over foo”
  “foo” has been types of networks
  Ethernet, Token Ring, ATM, SONET/SDH, ...
  but foo has been changing

## Slide 3: IP over “trails”, “circuits”, “paths” …
what looks like wires to IP:
  may not be physical wires
  may instead be something where paths can be configured
  where a path looks like a wire to IP
    e.g. ATM VCs
  might also be routed datagrams another layer down
    e.g. IPsec tunnels
and then there is MPLS
  a progressively more important “foo”

## Slide 4: Layer Violations
there is an extra complexity when the sub-IP technology is configurable
  e.g. MPLS, ATM, Frame Relay, ...
  Namely:
how to control the sub-IP technology:
  what information should be taken into account?
  the question may be “could a new path exist with certain characteristics”
  not just “can (or does) a path exist?”

## Slide 5: SUB-IP, a (new) area in the IETF
a systematic/co-ordinated approach to sub-IP issues would be nice
  but exact scope is not clear
IESG created a temporary area for sub-IP
  like what was done for IPng
  created in March 2001
to be short lived (1-2 years)
  2 current ADs have been appointed to run the area

## Slide 6: SUB-IP Area - Non-Objectives
the IETF is not expanding into standards for physical or virtual circuit technologies
  no new circuit switch architecture from IETF
  leave them to others
  But/So:
We need to communicate (more) with other standards organizations on what we are actually doing
significant overlap with some other SDOs like OIF, ITU-T, etc

## Slide 7: SUB-IP Area Objectives/Work-items
“Layer 2.5” protocol: MPLS
Protocols that monitor, manage or effect logical circuit technology
  e.g. IP Over Optical, Traffic Engineering, Common Control and Management Protocols
Protocols that create logical circuits over IP:
  e.g. Provider Provisioned VPNs
Protocols that interface to forwarding hardware
  e.g. General Switch Management Protocol

## Slide 8: SUB-IP Area Working Groups/WGs
Common Control and Management Protocols (ccamp)
  measurement & control planes for ISP core tunnels
  info collection via link state or management protocols
    e.g. OSPF, IS-IS, SNMP
  protocol independent metrics to describe sub-IP links
  signaling mechanisms for path protection
  Design team preparing docs for Protection and Restoration (based on TEWG requirements document)
  GMPLS docs (inherited from MPLS WG) finished and in IESG queue.

## Slide 9: SUB-IP Area WGs, contd.
Internet Traffic Engineering (tewg)
  principles, techniques, and mechanisms for traffic engineering in the internet
  current operational aspects and deployment
  Requirements for Network Hierarchy and Multilayer Survivability
    draft-ietf-tewg-restore-hierarchy-00.txt
    Input to CCAMP

## Slide 10: SUB-IP Area WGs, contd.
Multiprotocol Label Switching (mpls)
  label switching technology
  RSVP & CR-LDP signaling to establish LS paths
  MPLS-specific recovery mechanisms
Provider Provisioned Virtual Private Networks (ppvpn)
  detail requirements for ppvpn technologies
  define the common components and pieces that are needed to build and deploy a PPVPN
  BGP-VPNs, virtual router VPNs, port-based VPNs
  security

## Slide 11: SUB-IP Area WGs, contd.
IP over Optical (ipo)
  framing methods for IP over optical data plane and control channels
  identify characteristics of the optical transport network
  define use of ccamp protocols for optical networks
IP over Resilient Packet Rings (iporpr)
  input to the IEEE RPR SG to help it formulate its requirements – has moved to the INT Area
General Switch Management Protocol (gsmp)
  label switch configuration control and reporting

## Slide 12: SUB-IP Area -What’s In and Out?
boundaries of IETF work have been blurry
  the sub-IP area will not help clarify this
basic concept:
  the IETF works on IP-related technology
  if something does not have a relationship to IP networks then the work should be done elsewhere
  But:
since many networks (e.g. all-optical) carry IP, control of those networks may be IP-related
But: MPLS support for power distribution is out of bounds
  see RFC 3251

## Slide 13: SUB-IP Area - Summary
IESG created temp area to coordinate IETF sub-IP work
  area to last a year or two
will re-evaluate experience/status soon
most work of the sub-IP WGs should be done by the time the area is closed
any remaining working groups will be distributed to existing IETF areas

## Slide 14: SUB-IP Area Additional Information
SUB-IP Area web page, with ptrs to WG charters
  http://www.ietf.org/html.charters/wg-dir.html - Sub-IP Area
SUB-IP mailing list archives
  http://www.ietf.org/html.charters/SUB-IP.html
Generic IETF information
  http://www.ietf.org