## Slide 1: Network Protection and Restoration Session 5 - Optical/IP Network OAM & Protection and Restoration
Presented by: Malcolm Betts
Date: 2002 07 10

## Slide 2: Outline
Definition of Recovery, Protection and Restoration
Causes of client connection unavailability
Types of Network Protection
Interworking
Potential ASON applications
ITU-T Recommendations

## Slide 3: Client connection Protection or Restoration (Recovery)
A client connection is supported by a concatenation of link connections and sub network connections selected by a connection management process
Protection and Restoration are mechanisms that allow the network to recover a client connection when a network resource fails or becomes unavailable.
  From the perspective of the client the end points of the connection remain constant across network failures
Connection recovery is invoked:
  Autonomously for failures
  Manually by a network operator to allow “engineering works”

## Slide 4: Restoration
Replacement of a failed resource by a connection management process that selects alternate resources from spare capacity within the network
  The end points of the connections used inside the network are changed
Typical recovery times range from 100’s of ms to 10’s of minutes

## Slide 5: Protection
A property of the resource being used
A failed resource is replaced without changing the connection end points selected by the connection management process
Typical recovery times are in the range of 10’s of ms
This example uses trail protection

## Slide 6: Causes of Recovery failure
Multiple failures
  Backup resources in use due to a previous event
  With protection mitigated by breaking a long connection into shorter connections with independent protection resources
  With restoration mitigated by allocating adequate spare resources and network connectivity

## Slide 7: Causes of Recovery failure (cont’d)
Single point of failure
  At one point in the network the active and all potential backup paths rely on a single resource at any layer
    e.g. fiber cable, single physical location
  Mitigated by network design
  At the expense of increased network cost and complexity

## Slide 8: Causes of Recovery failure (cont’d)
Silent failures
  Failure of backup resource that is only detected when an attempt is made to use it for an “active” connection
  Failure of an active connection that is only visible to the client
  Mitigated by equipment design
Operational errors
  Incorrect configuration
  Wrong unit removed during maintenance activities
  Avoid complexity!

## Slide 9: Types of Network Protection
Subnetwork connection protection
Trail protection
Equipment protection
  Normally used to protect against the failure of common equipment e.g. Power supply, crossconnect matrix
  Scope is limited to a single network element,
  Not subject to standardization

## Slide 10: Protection configurations
1+1
  Dedicated protection, the client signal is placed on two connections (one active one standby) i.e. bridged at the head end, the “better” signal is selected at the tail end.
Head end
Bridge
Tail end
Selector
Only one direction of transmission is shown

## Slide 11: Protection configurations
1:n
  A single protection channel is shared between n working channels
  Requires a protection switch signaling scheme to coordinate activities between the head end bridge and the tail end selector
m:n
  m protection channels are shared between n working channels
  Has the potential to provide high availability with reasonable network cost
  Not commonly used due to complexity

## Slide 12: Protection configurations (cont’d)
Linear
  Used in point to point physical networks to provide protection against equipment failures (e.g. Optical Amplifiers)
  Commonly working and protection channels share the same fiber cable
Ring
  A collection of interconnected NE’s that form a loop
  Ring may be physical or logical
  Provides protection against equipment failures and cable cuts
Mesh
  Protection and working channels are routed over an arbitrary topology
  Normally working and protection are routed diversely
  Provides protection against equipment failures and cable cuts

## Slide 13: Connection recovery behaviour
Unidirectional
  Only the direction of the connection affected by the failure is replaced
  Commonly used with subnetwork connection protection
Bi-directional
  Both directions of the connection are replaced even if the failure only affected one direction
  Requires a protection switch signaling scheme to coordinate activities between the directions
  Commonly used with trail protection and restoration

## Slide 14: Connection recovery behaviour (cont’d)
Non-revertive Operation
  The client connection continues to use the replacement resources (after the original resources have recovered)
  Commonly used with subnetwork connection protection
Revertive Operation
  When the resources initially allocated to the client connection become available the connection is placed back onto those original resources
  Commonly used with shared trail protection

## Slide 15: Subnetwork connection protection
Subnetwork Connection Protection (SNC-P) is a dedicated protection mechanism (1+1)
  Can be used across any server layer topology structure
    e.g. Physical Ring (UPSR) or mesh
  The active and backup connections are normally diversely routed, this is not a requirement of the mechanism
  Can be used to protect a portion of a path or end to end
  Unidirectional operation; no APS signaling
Switch Initiation
  Client layer information (using non-intrusive monitoring)
  Server failures (using inherent monitoring)
    Used if client layer information is not available
    Imposes a restriction that the server layer trail is coincident with the SNC protection domain

## Slide 16: SNC-P example
Active
Bridge
Selector
Standby
Standby
Active
Client
Layer
Server
Layer
Protection Matrix
SNC Protection Function
SNC Protection with non-intrusive monitoring
Client signal monitor

## Slide 17: Establishing client connection across a region using SNC-P
Compute and activate (independent) active and backup paths
  With the degree of diversity required to support the connection availability requirements
  Simple with a physical ring, more complex with a mesh topology
Configure and activate the SNC-P function at the end points
  End points must support SNC-P function

## Slide 18: Trail protection
Provides protected link connections to a client layer network
  Commonly application is in the MS layer of SDH, OTU or ODUk layers of OTN
Common configurations
  Linear 1:n
  Ring
  Bi-directional operation with an APS signaling scheme

## Slide 19: Trail Protection
Adaptation and Trail Termination Functions are expanded to include a Protection Matrix
Protected Trail
Protected
Link Connection
Protection Matrix
Protection Matrix
APS signaling and server layer monitor

## Slide 20: 4 fiber MS-SPR example - Span switch
1
2
3
4
5
6
7
Protection
Working
Connection between nodes 2 & 6 on timeslot 9
Connection between nodes 2 & 4 on timeslot 9

## Slide 21: 4 fiber MS-SPR example - Ring switch
1
2
3
4
5
6
7
Protection
Working
Connection between nodes 2 & 6 on timeslot 9
Connection between nodes 2 & 4 on timeslot 9

## Slide 22: 4 fiber MS-SPR example - Node failure
1
2
3
4
5
6
7
Protection
Working
Connection between nodes 2 & 6 on timeslot 9
Connection between nodes 2 & 4 on timeslot 9
Traffic misconnected between nodes 4 & 6
Ring node maps and Connection tables allow Nodes 3 & 7 to squelch the traffic on timeslot 9 thus preventing the misconnection
Connection between nodes 1 & 3

## Slide 23: Establishing client connection across a region using protected trails (link connections)
Note that the equipment must be configured to support the protection mechanism
  e.g. provision ring node maps
Select and activate the protected link connection
Update all NEs involved in the protection mechanism
  e.g. update connection maps

## Slide 24: Interlayer interworking
Single failure events may cause multiple protection switch events
  Mitigated by using hold off timers in the client layer to allow the server layer to complete any recovery action before client layer initiates action
The use of protection in multiple layers requires careful consideration
  e.g. use of protected link connections (in the server layer) for connections that use SNC-P in the client layer
  Need to weigh the improvement in client connection availability against the cost of additional network resources

## Slide 25: Intra layer interworking
Allows a large network to be segmented into a number of independent regions
  Improves network availability by providing independent recovery resources in each region
  Allows different recovery mechanisms within and between regions
    For example an end to end client connection could use, SNC-P, MS-SPR and Mesh restoration in different regions
  Allows independent maintenance or engineering activities in different regions

## Slide 26: Potential ASON applications
Mesh restoration
  Rapid redial to reestablish failed connections
SNC-P active and standby connection selection and activation
For ultra high availability replacement of a failed (active or standby) connection

## Slide 27: Potential ASON applications (cont’d)
Nested protection and restoration
  Protection provides rapid recovery for most failure cases
  Redial provides recovery against failure of the gateway between networks

## Slide 28: Recommendations in ITU-T SG 15
Approved
  G.841 Types and Characteristics of SDH Network Protection Architectures
Under development
  G.gps-1 Generic Linear Protection Schemes (01-2003)
  G.gps-2 Generic Ring Protection Schemes (07-2004)
  G.otnprot-1 ODUk SNC Linear Protection (01-2003)
  G.otnprot-2 ODUk Ring Protection (10-2003)
  G.8080 v2 Architecture for the Automatically Switched Optical Network (ASON) - additional details on Protection and Restoration (01-2003)