## Slide 1: Call & Connection control Signalling : the ITU-T SG11 status and perspectives for “New Network control Architectures and Protocols”
Alain LE ROUX
ITU-T SG11 Vice-chairman
email: alainxavier.leroux@rd.francetelecom.com

## Slide 2: Presentation Layout
  Scope of ITU-T Study Group 11 current activities
  Overview and status of Signalling Systems/SS7
  Overview of Legacy Signalling Systems
  Bearer (ATM, IP) Independent Call Control: BICC
  Signalling Enhancements for Convergence to pure IP environment: SS7/BICC-SIP interworking
  Addressing Call, Connection & Resource/Policy control protocols for new network architectures (NGNs)
  From Legacy Signalling to new generation signalling Protocols
  Summary/Concluding remarks
Notes: This presentation material and slides are prepared by:
Alain LE ROUX (France Telecom), ITU-T SG11 Vice-chairman and WP3/11 chairman
email: alainxavier.leroux@rd.francetelecom.com
And
Arshey ODEDRA (ITU), ITU-T SG11 Counsellor/Engineer
email: arshey.odedra@itu.int
Presenter: Arshey ODEDRA (ITU)

## Slide 3: Scope of ITU-T Study Group 11 activities
Define Signalling requirements and protocols for:
  enhancements to existing Recommendations on access (UNI) and (inter)-network (NNI) signalling protocols for PSTN, ISDN and Packet (ATM and IP)-based networks
  Some Mobility & Nomadic related functions (in relation with SSG)
  the support of voice, data and Multi-media communications and services
  emerging NGN architectures, including Internet Protocol (IP) related control functions
Lead Study Group for Intelligent Networks (and emerging Services & applications control platforms):
  Architectures, signalling requirements, and
  control Protocols

## Slide 4: How is ITU-T Study Group 11 structured
SG 11 is organised in 4 Working Parties:
  WP 1 - Intelligent Network (IN) and Services/Applications control
  WP 2 – Requirements for IP and Advanced network applications
  WP 3 – Engineering of emerging (e.g. BICC) and ‘legacy’ signalling protocols
  WP 4 – Engineering of ATM AAL2 signalling and common Signalling (transport) Protocols
SG11 Home page at:
http://www.itu.int/ITU-T/studygroups/com11/index.html

## Slide 5: ITU-T SG11 products
Develops Recommendations in the Q-series, e.g.:
  Q.700-series for Signalling System n° 7 (SS7), signalling transport and call/connection control protocols in TDM-based networks
  Q.900-series for ISDN DSS1, access signalling
  Q.1200-series, IN architecture and protocols
  Q.2100-series, B-ISDN ATM-based networks signalling transport
  Q.2700-series, B-ISDN ATM-based (inter-)network (NNI) signalling
  Q.2900-series, B-ISDN DSS2 (UNI) access signalling
Produces informative documents, as Supplements to Q-series of Recommendations, e.g.:
  Q.Supplement n°1 – SS7, Testing and Planning tools
  Q.Supplement n°3 - Number Portability, Scope and Capability Set 1 architecture

## Slide 6: ITU-T SG11 Current work focus:
Interactions between IN and IP-based networks:
  Question 1/11: Signalling requirements for signalling support for new, value added, IP based and IN based services
  Question 4/11: API/object interface and architecture for signalling
IP-related signalling protocols:
  Question 6/11: Signalling requirements for signalling support for service inter-working of both dialup Internet access and Voice, Data and Multimedia Communications over IP-based networks
  Question 8/11: Signalling requirements for flexible management of dynamic bandwidth and QoS demands in connection control (e.g. MPLS-ATM)
Bearer (ATM, IP) Independent Call Control (i.e. BICC):
  Question 9/11: Signalling requirements for the support of BICC applications
  Question 11/11:Protocols for the support of BICC applications
Signalling transport over IP:
  Question 13/11: Common signalling transport protocols, including over IP
  Question 15/11: ATM AAL2 signalling, interworking with IP
Notes: The other Questions currently addressed by the ITU-T Study Group 11 are:
Question 2/11 - Network signalling requirements for the support of Virtual Home Environment (VHE) in the fixed network
Question 3/11 - Network signalling protocols to support mobility in the fixed network
Question 4/11 - API/object interface and architecture for signalling
Question 5/11 - Protocols for further evolution of IN capability sets
Question 7/11 - Signalling requirements for signalling to efficiently identify and direct traffic destined for Internet Service Provider (ISPs)
Question 10/11 - Signalling requirements for control of signal processing equipment and of remote transmission nodes
Question 12/11 – Access and network signalling for advanced narrow-band and broadband services
Question 14/11 - Protocol (conformance) testing specifications
Question 15/11 – (Control) Protocols for the support of ATM AAL Type 2 bearers

## Slide 7: Signalling techniques evolution:
Initially “in-band” signalling (in analog networks):
  DTMF on analog lines and Multi-Frequency over circuits
  also used in X.25 Packet networks (Virtual Circuit control packets and user data packets carried over the same logical channel)
Common Channel Signalling (CCS) in digital networks:
  Signalling messages carried over dedicated signalling links (typically 64 kbs circuits): SS7 (Q.700 series) widely deployed
  Integrated Call and Bearer connection control: initially designed for 64 kbs circuit switched networks, also adopted for ATM (VP, VC) switched networks
  Has enabled the emergence of Intelligent Network (IN) services from Service Control Points (SCP) separated from Switching Functions
Separated Call and Connection control in Packet-based Networks:
  The Bearer Independent Call Control protocol (BICC)
  applicable to control narrowband calls and services (typically voice) in ATM and IP-based transport networks
Notes: The other Questions currently addressed by the ITU-T Study Group 11 are:
Question 2/11 - Network signalling requirements for the support of Virtual Home Environment (VHE) in the fixed network
Question 3/11 - Network signalling protocols to support mobility in the fixed network
Question 4/11 - API/object interface and architecture for signalling
Question 5/11 - Protocols for further evolution of IN capability sets
Question 7/11 - Signalling requirements for signalling to efficiently identify and direct traffic destined for Internet Service Provider (ISPs)
Question 10/11 - Signalling requirements for control of signal processing equipment and of remote transmission nodes
Question 12/11 – Access and network signalling for advanced narrow-band and broadband services
Question 14/11 - Protocol (conformance) testing specifications
Question 15/11 – (Control) Protocols for the support of ATM AAL Type 2 bearers

## Slide 8: Overview of legacy Signalling Systems
For TDM narrow-band (PSTN, ISDN) networks
  Access (UNI) signalling
    DTMF (PSTN)
    DSS1 (ISDN BA and PRI)
  Inter and Intra Network (NNI) signalling
    SS7 MTP, SCCP (control protocol transport), TC
    SS7 ISUP (call control)
    SS7 INAP (IN service control)
For ATM networks
  Access signalling: DSS2, UNI
  Network signalling: B-ISUP, PNNI, AINI
IN SCP
SS7 INAP
SCF
SSF
CCF
PSTN/
ISDN
SSP
Network (NNI) signalling
Access (UNI) signalling
Notes: TDM Time Division Multiplexing PSTN Public Switched Telephony Network
ISDN Integrated Services Digital Network ISDN BA ISDN Basic Access
ISDN PRI ISDN Primary Rate Interface DTMF Dial Tone Multifrequency (signalling)
DSS1 Digital subscriber Signalling System number One SS7 Signalling System number Seven
MTP (SS7) Message Transfer Part SCCP (SS7) Signalling Connection Control Part
TC Transaction capability ISUP (SS7) ISDN Signalling User Part
INAP (SS7) Intelligent Network Application Part ATM Asynchronous transfer Mode
DSS2 Digital subscriber Signalling System number Two UNI User-Network Interface (ATM Forum specification)
B-ISUP (SS7) Broadband ISUP PNNI Private Network Node Interface (ATM Forum specification)
AINI ATM Inter-Network Interface (ATM Forum spec.)

## Slide 9: SS7 and IN Convergence towards Packet based Networks (1)
Inter-working between Legacy and IP-based transport networks
Application of IN to IP network services
SCP
SS7 INAP
SCF
SSF
CCF
PSTN/ ISDN
SSP
INAP over IP (or via SGW for SS7 over IP)
Must contain (or have access to) user profile data
Statefull mode of operation
SSF
IP
Proxy
SS7 INAP
Media Gateway
Call Server
Notes: SSP Service Switching Point
SSF Service Switching Function
CCF Call Control Function
SCP Service Control Point
SCF Service Control function
SGW Signalling Gateway

## Slide 10: SS7 Convergence towards Packet based Networks (2)
Intelligent Network architecture and protocols enhanced to support the IETF PINT & SPIRITS services
  IN Capability Set 4 (CS4) Recommendations approved in May 2001, using a fast track approval process (i.e. AAP)
    Q.1241 – Introduction to IN CS4
    Q.1244 – Distributed Functional Plane for IN CS4
    Q.1248.1-7 – Interface Protocols for IN CS4
  IN CS4 Recommendations include support for the IETF
    PINT (PSTN and InterNetworking for Telephony), e.g. Click-to-dial, &
    SPIRIT (Services in the PSTN/IN Requesting InTernet) Services, e.g. Internet Call Waiting
    (i.e. the requirements and architectures are in alignment).
Notes: IETF = Internet Engineering Task Force; IN = Intelligent Network;
PINT = PSTN and Internet Internetworking (a former IETF WG, closed-2001); SPIRIT = Service in the PSTN/IN Requesting InTernet Service (IETF WG)

## Slide 11: SS7 Convergence towards Packet based Networks (3)
For Call control signalling, Bearer Independent Call Control (BICC) protocols have been defined to apply over Packet (ATM or IP) based transport networks
  BICC Capability Set 1 applicable to ATM (AAL1 or AAL2) transport: Recommendations have been approved in year 2000
  BICC CS2 applicable to ATM and IP transport: a set of 15 Recommendations have been approved in June 2001.
  A BICC CS3 release with various enhancements (including interworking with SIP) is currently under development. Scope and requirements being finalized. Protocols documents approval planned in 2003.

## Slide 12: BICC signalling protocol
The high level requirements
  BICC is a Signalling protocol to ease PSTN/ISDN evolution towards (NGN) Next Generation Network (packet-based transport) architectures
  Usable to control calls over any packet (ATM, IP) -based transport network
  Simplifies the signalling interworking between legacy networks and NGN architectures
The solution developed in ITU-T SG11:
  The Bearer Independent Call Control (BICC) protocol
  Based on SS7 ISUP: quicker to define and to implement, easier ISUP-BICC inter-working
  Multiple Capability Sets (or releases), enabling phased deployment and smooth evolution towards NGN architectures

## Slide 13: BICC overview
What is BICC ?
  an architecture that provides a means of supporting narrowband (PSTN, ISDN) services across a Packet-based backbone network without impacting the existing network interfaces and end-to-end services
  a call control protocol that is unaware of the actual bearer transport being employed. Binding information identifies the bearer used for each communication instance
  a call control protocol that is based on SS7 ISUP signalling protocol commonly used in legacy networks for PSTN/ISDN intra- and inter-networking
  bearer (connection) control signalling protocols depend on the underlying bearer technology used (e.g., DSS2/UNI for ATM AAL type 1 and ATM AAL type 2, IP and/or MPLS related signalling protocols)

## Slide 14: BICC application
As a call control protocol between Call Servers
    Where it inter-acts with SS7 ISUP signalling
    And ensures NB-networks end-to-end services, unaffected
PSTN/ ISDN
LE
PSTN/ ISDN
LE
Call Server
Media
Gateway
ATM, IP backbone
BICC
Call Server
Media
Gateway
SS7 ISUP
SS7 ISUP

## Slide 15
Call & Service Functions
Call & Service Functions
Call Mediation Node (opt.)
Bearer Control Function
Bearer Function
Bearer Control Function
Packet (ATM, IP) Transport
Network
Bearer Function
Serving Node
Serving Node
BICC
BICC
SS7 ISUP
SS7 ISUP
TDM Trunks
TDM Trunks
Bearer Signalling
Bearer Signalling
      Functional separation of Call/service Functions, Bearer Control Functions and Bearer (Media) Functions.
BICC underlying architecture

## Slide 16: How the ITU BICC approach fits with that in IETF (1/4)
BICC is a pragmatic solution to enable evolution from legacy networks towards NGN architectures (using ATM and/or IP-based transport technologies)
It inter-acts easily with legacy signalling protocols (as it is very much based on SS7 ISUP)
But it is not the only candidate protocol for call and service control in emerging networks:
  SIP and SIP-T are also under consideration for adoption by the ITU-T, for use between Call Servers (often referred to as Call Agent or “Softswitches”)
As such, the approaches are complementary

## Slide 17: How BICC approach fits with that in IETF (2/4)
Interworking with SIP & SIP-T is required. Cases being considered within ITU SG11 are:
      SIP-ISUP (over a TDM insfrastructure) SIP-BICC (over ATM infrastructure) as shown below SIP-BICC (over IP infrastructure) SIP-T – ISUP SIP-T BICC (over ATM infrastructure) SIP-T – BICC (over IP infrastructure)
SIP
IP
BICC
ATM
SIP ‘phone
Interworking
Call Agent
Media Gateway or Integrated Access Device
Phone
Call Server

## Slide 18: How BICC approach fits with that in IETF (3/4)
SIP is being considered as a candidate signalling protocol for emerging public telecom networks:
  As an access protocol (UNI)
  As a network protocol (NNI)
  Possibly as a service and application control protocol (towards services and application control platforms)
Which means that various SIP profiles are needed to be developed, e.g.
  SIP UNI (access) profile
  SIP NNI (Network interface) profile
  SIP with enhancements to fully support PSTN/ISDN legacy services
Interworking requirements between the various SIP profiles and BICC (and SS7 ISUP) are being addressed in ITU-T SG11.

## Slide 19: How BICC approach fits with that in IETF (4/4)
SIP-BICC-CS-3 (IP-to-IP network transport) interworking case
MMSF
(Media Mapping/ Switching Function)
BCF**
BCF
CSF
CSF
SIP
RTP/IP
SDP
(carried via H.248/SIP)
BICC (over IP)
RTP/IP
H.248/Megaco
Q.1950 (BICC CS2)
IP BCP
(carried via Q.1950/BICC)
BCF*
Call Server (or Agent)
Media Gateway
From ‘Data’
From ‘Legacy’
Notes: CSF Call & Service Functions
BCF Bearer Control Functions
MMSF Media Mapping and switching Functions
RTP Real Time Protocol
SDP Session Description Protocol

## Slide 20: BICC Enhancements for Convergence to pure IP environment (1/2)
Various enhancements to BICC are currently under consideration (in Capability Set 3) to enable smooth interaction with and evolution towards NGN architectures. These include:
  QoS aspects
  Addressing and routing (ENUM impacts on BICC)
  Signalling (and inter-working) requirements for the support of new generation (audio and multi-media) services

## Slide 21: BICC Enhancements for Convergence to pure IP environment (2/2)
To enable simultaneous support of BICC and SIP by Call servers (=Softswitches)
  BICC used for legacy voice (between A-B legacy phones) services and between A to IP-phone
  SIP used for IP-phone to B, VoIP (IP-phone-IP-phone) and for multi-media services
PSTN/ ISDN
LE
PSTN/ ISDN
LE
Call Server = SoftSwitch
Media Gateway
IP Network(s)
Call Server = SoftSwitch
Media Gateway
SS7 ISUP
SS7 ISUP
BICC
SIP
IP -phone
IP-phone
Megaco
A
B

## Slide 22: Role of BICC in emerging Telecom Networks
A pragmatic solution to evolve smoothly legacy networks towards more effective and more flexible network architectures
  To support legacy services,
  Offering an opportunity to share the same core network services and transport resources between legacy & IP-based networks users
  With minimal investments (for enabling TDM->ATM->IP/MPLS switch-routing network evolutions)
Does not preclude the additional support of a more open and extensible signalling protocols such as SIP
  For advanced multi-media and Internet oriented services
  Either BICC or SIP being used on a per call/session basis

## Slide 23: Current status of the BICC use
By some fixed network operators, for TDM trunking replacement with ATM or IP transport technologies in core networks
In emerging 3G mobile networks, to support voice traffic in the UTRAN (voice over ATM AAL type 2)
  BICC is retained in 3GPP R99 and R4 specifications
Some Call Servers (or Softswitches) start supporting BICC (CS1 or CS2)
  And usually also support primarily SIP (for VoIP and multimedia communication services)

## Slide 24: Call Control summary
BICC defined in ITU-T is seen as a pragmatic solution to ease transition from legacy to emerging packet-based (ATM, IP) network solutions
  BICC-CS1 and CS2 are limited to the support of legacy services
  CS3 (under study) is expected to enable additional services
Other signalling protocols, such as SIP, are also expected to emerge in NGN architectures
  To support more advanced (multi-media and IP based) services
Smooth Inter-action and interworking between both is seen as an ultimate requirement
  Both are likely to co-exist in public networks for an interim period
NGN should ideally implement both to satisfy legacy network operators expectations
  To enable both legacy and new generation services offering

## Slide 25: Example of emerging architectures
Customer
Premises
Integrated
Access
Devices
IP/MPLS Backbone
Optical Core
DWDM
Legacy Applications
IP Applications
IN
PSTN/ISDN
SS7
Directory / Policy
Server
Appl / Feature Server
Service Operations
Service Access Control
Network & Subscriber Services
Service Operations Management
V5.2
Network Mgmt.
Packet-Based
Optimized for the Internet Protocol
Enabled by….
  Multi-Protocol Label Switching (MPLS & GMPLS)
  Distributed Call-Agent (e.g. SoftSwitch) Services
Drive IP/MPLS to the Access
where b/w is constrained
IP
IP
IP
Access Gateway
IP Access Network
‘SoftSwitch’

## Slide 26: Emerging Network Control Architectures and Protocols
Bearer (connection)
control (Switch/Routers)
Session (or call)
control (Call Agents)
Service & Application
Control (Servers)
1
2
2
3
e.g. Megaco
3
4
Per Session Control Protocols:
Session (call): 1
Service/Application: 2
Resources allocation & traffic policy control: 2, 3
Transport resource control:
Bearer/Connection control: 4
Backbone resource control: 5
Backbone Transport
(SDH/DWDM/Optical)
5 (NNI)
Scope ITU-T SG11
E.g. BICC, SIP, SIP-T
E.g. ATM sig, MPLS ...
E.g. GMPLS with RSVP-TE
or CR-LDP, or Optical-PNNI
5 (UNI)
5 (UNI)

## Slide 27: Signalling protocols summary (SG11view)
Trend to increasingly separate Call/session control, Bearer/connection control and Services/application control protocols:
  IN architecture was a first step
  BICC is another step, enabling Legacy signalling and IP convergence
  Need to well specify the interactions between the functional areas
Emerging NGN architectures need to be defined functionally
  To identify the interfaces that require standardization
  New signalling/control protocols, IP oriented and optimized
Resource and Bearer/connection control significant evolutions:
  IP as the service convergence layer, (G)MPLS as the networking convergence ?
  SG11 and SG15 coordination required in the area of Call & Bearer Control ?
OTN
(G)MPLS
IP ...
WDM
To ?
OTN
MPLS
IP
WDM
ATM
SDH
From

## Slide 28
Thank You for your attention
N2CAP ?
towards NGN

## Slide 29: Session 7 presentations:
1. Overview on Optical Service and Network Architecture Requirements
by Masahiro Goshima, NTT Network Service Systems Labs
2. Call & Connection control Signalling : the ITU-T SG11 status and perspectives for “New Network control Architectures and Protocols”
by Alain Le Roux, France Telecom R&D
3. CR-LDP for ASON Signalling
by Stephen Shew, Nortel Networks
4. GMPLS RSVP-TE for ASON Signalling
by Dimitrios Pendarakis, Tellium