## Slide 1: CR-LDP for ASON Signalling Session 7 – Signalling and Routing
Presented by: Stephen Shew
Date: 2002 07 10

## Slide 2: What is CR-LDP?
“CR-LDP” stands for “Constraint-based Label Distribution Protocol”
  Developed in the IETF in the MPLS WG
  Built from the Label Distribution Protocol (LDP) also developed in the IETF
CR-LDP is a signalling protocol used to set up Label Switched Paths in an IP/MPLS network.

## Slide 3: What is CR-LDP for ASON?
G.7713 describes detailed requirements for Distributed Call and Connection Management
  It conforms to the G.8080 architecture (ASON).
  It is protocol-neutral.
G.7713.3 “Distributed call and connection management signalling using GMPLS CR-LDP”
  Is a protocol specification that will comply with G.7713.
  Based on CR-LDP.
  Progressing in Q14/15.

## Slide 4: CR-LDP Development History
Dec. 1997:
First LDP draft at
IETF
Dec. 1998:
First “separate”CR-LDP draft at IETF
June 2000:
OIF Starts working on CR-LDP extensions for optical UNI
Jan. 2001:
LDP becomes an RFC (3036) at IETF
Oct. 2001:
OIF UNI 1.0 approved
Jan. 2002:
CR-LDP becomes an RFC (3212) at IETF
March 2002:
ITU starts CR-LDP for G.7713 (7713.3)
Jan 2000:
GMPLS work starts
At IETF

## Slide 5: CR-LDP Details
CR-LDP is an extension to LDP
  Uses existing LDP messages, but defines additional TLVs for the messages.
  CR-LDP adds TE capability to LDP
    Explicit route capability
    QoS capability
Like LDP, runs over TCP
  Hard state that requires explicit request for state removal
  TCP provides reliable transport and flow control
Employs the same signalling model as ATM PNNI and Q.2931
  Sender-initiated setup of resource reservations
  Suits connection oriented networks and services
Recognized as a method of transporting IP over ATM in Recommendation Y.1310.
Notes: TLV = Type, Length, Value
TE = Traffic Engineering
TCP = Transmission Control Protocol, an IETF protocol that runs over IP for correcting packet loss
ATM PNNI = Asynchronous Transfer Mode Private Network-Network Interface, this is a signalling and routing specification of the ATM Forum
TLVs are encodings of information within protocol specific messages

## Slide 6: CR-LDP Messages and Categories
Message
Category
Function
LDP Messages
Discovery
Announce and maintain the presence of NEs in a network
Hello (using UDP)
Session
Used to establish, maintain, and terminate sessions between LDP peers
Initialization, and Keepalive
Advertisement
Used to create, change and delete Label mappings (connections)
Label Request, Label Mapping, Label Abort, Label Withdraw, Label Release, Address, and Address withdraw
Notification
To provide advisory information and to signal error information
Notification

## Slide 7: LDP Message Format
U
Message Type
Message Length
Message ID
Mandatory Parameters
Optional Parameters
U bit: defines the action to be taken upon receipt of unknown message
U = 0 a notification is returned to the originator of the message
U = 1 the unknown message is silently ignored

## Slide 8: CR-LDP details: Example
10.1.1.2
10.1.1.6
10.1.1.3
10.1.1.7
10.1.1.4
10.1.1.5
10.1.1.1
12.0.0.1
POP
* Message contains: Explicit route TLV 10.1.1.5 strict 10.1.1.3 loose
Preemption TLV setup priority: 4 holding priority: 4
Traffic parameters TLV CDR: 10M
(other stuff) LSPID TLV ingress router: 10.1.1.4 local id: 100
• • •
Request *
Request
Mapping
Mapping
Request
Mapping
Notes: This example shows CR-LDP use in an IP network. The connection request is required to use intermediate point 10.1.1.5 and has freedom to choose how to get to 10.1.1.3.

## Slide 9: CR-LDP details: Example
10.1.1.2
10.1.1.6
10.1.1.3
10.1.1.7
10.1.1.4
10.1.1.5
10.1.1.1
12.0.0.1
POP
* Message contains: Explicit route TLV 10.1.1.5 strict 10.1.1.3 loose
Preemption TLU setup priority: 4 holding priority: 4
Traffic parameters TLV CDR: 10M
(other stuff) LSP ID TLV ingress router: 10.1.1.4 local id: 100
• • •

## Slide 10: CR-LDP Extensions for GMPLS: what is GMPLS?
GMPLS generalizes the concept of label to include:
  Packet-switch capable (PSC) interfaces
  Time-division multiplex capable (TDM) interfaces
  Lambda switch capable (LSC) interfaces
  Fiber switch capable (FSC) interfaces
CR-LDP in its original form (RFC3212) handles only the PSC cases
  Extensions are being worked out to cover TDM, LSC, and FSC cases
    Draft-ietf-mpls-generalized-cr-ldp-06.txt

## Slide 11: CR-LDP Extensions for GMPLS: Details
Uses the same set of messages as in LDP
Introduces new TLVs for the generalized label operation
  Generalized Label Request TLV
  Generalized Label TLV
  Label Set TLV
  Suggested Label TLV
  Acceptable Label TLV
  Admin Status TLV
Introduces technology specific TLVs
  For Sonet/SDH

## Slide 12: CR-LDP Progression
CR-LDP extends LDP but does not use some LDP functions
GMPLS extends CR-LDP
OIF UNI 1.0 uses a derivative of GMPLS CR-LDP
LDP
(RFC3036)
CR-LDP
(RFC 3212)
GMPLS
CR-LDP
OIF UNI 1.0
CR-LDP
Notes: CR-LDP does not use all of the modes of LDP and hence is not a superset of LDP.
GMPLS CR-LDP is a superset of CR-LDP.
OIF UNI 1.0 uses either a derivative of GMPLS RSVP-TE or GMPLS CR-LDP. It does not use all of GMPLS CR-LDP but does introduce extensions.

## Slide 13: CR-LDP Extensions for OIF UNI 1.0
Borrows from GMPLS
  It is common to say that OIF UNI 1.0 is “GMPLS based” or “GMPLS Compliant”
Two new messages are introduced for use across the UNI
  Status Enquiry and Status messages
Introduces new TLVs necessary for UNI operation
  User identification TLV (related to Transport Network Assigned (TNA) address).
CR-LDP (signaling) messages could be transported out of band over IP control channel (IPCC)

## Slide 14: CR-LDP Operation at the UNI: AN Example
Label Request
Label Request
Label Mapping
Label Mapping
Client
Client
Network
Network
Network
Connection is available
Notification
Notification
UNI
UNI

## Slide 15: ASON Signalling Requirements
Separation between control and bearer
  Unlike a traditional IP network, ASON cannot use the state of the bearer to infer any useful information about the health of the control channel.
  Bearer connections must not be disrupted as a result of control channel failure.
Call and connection control separation
  Support of multiple connections associated with the same call.
  Useful to differentiate between call parameters and connection parameters.
  Useful to define “call/bearer coordination points” that usually reside at the network boundaries (at UNI and E-NNI).
Notes: Detailed requirements for ASON signalling are contained in recommendation G.7713 “Distributed Call and Connection Management”.
Specific protocols are being developed from G.7713 and are G.7713.1, G.7713.2, and G.7713.3.

## Slide 16: CR-LDP Progression
CR-LDP for ASON Signalling is being developed in G.7713.3. It is derived from GMPLS CR-LDP and OIF UNI 1.0.
LDP
(RFC3036)
CR-LDP
(RFC 3212)
GMPLS
CR-LDP
OIF UNI 1.0
CR-LDP
G.7713.3

## Slide 17: CR-LDP Extensions for ASON
CR-LDP already doesn’t rely on bearer to check the health of the control channel
  A keepalive mechanism has always been a part of LDP
Introduces new messages related to call control
  Call Setup message
    Only used for cases where the call setup is not accompanied by a connection setup
  Call Release message
    Triggers the release of all connections associated to the call (using the normal CR-LDP procedure for connection release)
Introduces new TLVs related to call operation
  Call ID TLV
  Call Capability TLV
ITU-T G.7713.3 draft capturing these
  “Distributed call and connection management signalling using GMPLS CR-LDP “

## Slide 18: CR-LDP Extensions for ASON: An Example
Call Request
Connection Request
Call
State
Call
State
Initial Call Request may or may not be accompanied by a connection Request
A mechanism is needed to associate connections to Calls (use of Call Id)
Call Release MUST terminate all active connections associated with that call
Notes: In this example, a call is setup with zero connections. Then, a connection is established followed by two other connections. All three connections are associated with the same call.

## Slide 19: Next Steps
March 2002:
ITU starts CR-LDP for G.7713 (7713.3)
July 2002:
Introduces G.7713.3 extensions to IETF CCAMP WG
Jan. 2003:
G.7713.3 for consent
Near Future
Everyone uses G.7713.3 for ASON Signaling 

## Slide 20: Conclusions
CR-LDP originated with a connection oriented signalling model.
CR-LDP has evolved for IETF GMPLS and OIF UNI
CR-LDP can be successfully extended to meeting ASON signalling requirements.

## Slide 21: Acknowledgements
Material originally developed by various Nortel Networks authors, noteably Osama Aboul-Magd, was used in this presentation.