## Slide 1: Practical Issues In Managing Optical Networks by Wesam Alanqar and Tammy Ferris
ITU-T Workshop IP/Optical (Chitose, Japan, 9-11 July 2002)
Wesam.Alanqar@mail.sprint.com

## Slide 2: Abstract
This paper discusses practical issues with respect to optical network management from a network and service provider perspective. It provides a background for the optical network by describing optical network services and optical network transport architecture then discusses management issues service and network providers face in deploying such networks.

## Slide 3: Overview
Optical Network Service Types
Optical Network Transport Architecture
Optical Network Deployment
  Transition to OTN Transport Networks
  Transition to Switched Connections
  Management System Integration
Summary and Recommendations

## Slide 4: Optical Network Service Types
OTN
  ODU1 (i.e. 2.5 Gbps), ODU2 (i.e. 10 Gbps)
  When Fully Standardized, ODU3 (i.e. 40 Gbps)
SONET/SDH
  VT1.5 SPE/VC-11, VT2 SPE/VC-12, VT3 SPE,VT6 SPE/VC-2,
  STS-1 SPE/VC-3,STS-3c SPE/VC-4,STS-12c SPE/VC-4-4c ,
  STS-48c SPE/VC-4-16c, STS-192c SPE/VC-4-64c
  Subrate Services
  Transparent Services
Gigabit Ethernet
  1 Gig, 10 Gig
  10Gig WAN Transparent Service
    Transparency via adaptation into ODUk (& SONET/SDH when fully standardized)
Additionally Impact Service Type
  Agreements (e.g., QoS, Protection / Restoration, Connection Monitoring)
  UNI Signaling and Constraints
  Virtual Concatenation (E.g., VC-n-Xv (n=11,12,3,4), ODUk-Xv)

## Slide 5: Optical Network Transport Architecture
Standardized Layered Transport Networks
  SONET/SDH Services over OTN Networks
  OTN Services over OTN and SONET/SDH Networks
  Ethernet Services over OTN and SONET/SDH Networks
Legacy Pre-OTN DWDM Transport Networks
  Client Signal (e.g. STM-N, GbE) Direct on Wavelength
  No Fabric
  Point to Point
DCN Networks for Transport of Management Plane Messages
  Transport Network Overhead
  Additional External Network
DCN Networks for Transport of Control Plane Messages
  Transport Network Payload Channel
  Transport Network Overhead
  Additional External Network

## Slide 6: Optical Network Transport Architecture DCN Networks
OSS-Management Plane
Administrative Area
Control
Domain
Control
Domain
Management
Communications (out of band)
ECC: Embedded Communications Channel CCI: Connection Controller Interface
EMF: Equipment Management Function SNCr: SubNetwork Controller
OXC
OTN layer-Vendor domain 1
EMF
Signaling
Communications (in band)
CCI
CCI
NNI
ECC
ECC
OXC
OXC
OXC
OTN layer-Vendor domain 2
EMF
SNCr
Signaling
Communications (in band)
EMF
EMF
CCI
SNCr
SNCr
SNCr
Not all interfaces are shown for simplicity
Control Plane layer
Management Plane Layer
Out of band Data Communication Network (DCN)
Signaling
Communications (out of band)

## Slide 7: Optical Network Deployment
Transition to OTN Transport Networks
  OTN Services Over Fully OTN Network
  OTN Services Over OTN Overlay Network
  OTN Services Carried over SONET/SDH Transport Networks
  OTN Transport In Place of DWDM
  OTN XC Equipment In Place of DWDM ADMs
Transition to Switched Connections
  SONET/SDH and OTN Transport Networks (ASON)
Management System Integration
  Additional Support Needed
  New Services Maintenance Issues
  New Services Policy Issues
  Management Applications Issues
  ASON Issues

## Slide 8: Transition to OTN Transport Networks Some Scenarios
OTN Services Over Fully OTN Network
  Complete Changes In Carrier’s Back Office Infrastructure
    New operations training and all new test equipment
OTN Services Over OTN Overlay Network
  OTN Network Sharing Fibres with SONET/SDH Networks
  Deployment of OTN Line Systems and Cross Connects
OTN Services Carried over SONET/SDH Transport Networks
  ODU1 (2.5 Gbps), ODU2 (10 Gbps)
    Some attractive features: transparency (e.g. transparent STM-16 over ODU1 over VC-4-17v, STM-64 over ODU2 over VC-4-68v), multiple TCM, etc.
OTN Transport In Place of DWDM
  Deployment of OTN Line Systems Only
    Limited to point-point connections
OTN XC Equipment In Place of DWDM ADMs
  Deployment of Cross-connects in Central Locations
    Future proof some expenses when upgrading equipment but not ready for transition

## Slide 9: Transition to Switched Connections See Session 2, “Switched Optical Networks” Paper for Details
Integration With Legacy Systems
  Also applies to incomplete or not completely interoperable automatically switched systems
Allocation of Functions Between Control Plane and Management Plane
  Only Routing and Link Management Done via Management Plane
  Routing and Link Management, Call Processing, and Connection Processing All via Control Plane
Mix of Automatically Switched and Not Automatically Switched Within Different Transport Network Layers
  Client Layer Switched and Server Layer Not Switched
  Server Layer Switched and Client Layer Not Switched
Mix of Automatically Switched and Not Automatically Switched Within Transport Network Partitions
  UNI
  E-NNI
  I-NNI
  Sub-networks
Combinations and Permutations of Above

## Slide 10: Management System Integration Additional Support Needed
Ethernet, OTN, & Concatenated Services over Existing Networks
  SONET/SDH
  Legacy DWDM
OTN Transport Networks & Network Elements
  Vendor Specific Network Elements
  Vendor Specific Element Management Systems
  Vendor Specific and Vendor Independent Networks
OTN Management DCN
  Connectivity Between OTN Elements
  Connectivity For OTN Client Layer Elements
ASON DCN
  Connectivity Between Control Elements
Control Plane
  Vendor Specific Control Elements
  Vendor Specific Control Element Management Systems
  Vendor Specific and Vendor Independent Networks

## Slide 11: Management System Integration With Control Plane
OSS-Management Plane
Control Domain2
Control
Domain1
EMF: Equipment Management Function SNCr: SubNetwork Controller (Vendor Specific Control Elements,
Managed through EMF)
OXC
OTN layer-Vendor domain 1
EMF
OXC
OXC
OXC
OTN layer-Vendor domain 2
EMF
SNCr
EMF
EMF
SNCr
SNCr
SNCr
Not all interfaces are shown for simplicity
Control Domain
Vendor Specific Control Element Management System
Vendor Specific Networks
Vendor Specific Control Element Management System
Management Plane Layer
Vendor Independent Network

## Slide 12: Management System Integration New Services Maintenance Issues
Monitoring Concatenated Services & ASON Services
  Correlation between Connection(s) and the Service
    Concatenated services have multiple connections
    ASON services have dynamic relationship between connections and services
Fault Isolation for ASON Services
  Isolating Faults with Connections based on Trouble Tickets
    Associations between calls and connections are dynamic

## Slide 13: Management System Integration New Services Policy Issues
Coordinating Service Requests from Multiple Sources
  Sources
     - Phone call from customer
     - CNM interface via web
    - Service contract
    - Internal work order
    UNI
  Policy Issues Examples
    If UNI, does this imply customer cannot also request connections or releases of connections via phone call or CNM interface?
    If UNI is not used to set up a connection can UNI be used to request the release of the connection?
Use of GCC1 & 2 (General Communications Channel) for OTN Services
  Clear Channel for Customer
  Interface for Requesting Service (e.g. CNM interface or UNI)
  Transport for Management Plane Messages between Management Systems and ODU Terminating or Monitoring Devices
Use of TCM (Tandem Connection Monitoring) Levels for OTN Services
  TCM Level Agreements
  Adequate Enforcement to Prevent Others Use of Agreed Levels

## Slide 14: Management System Integration ASON Issues
Management Plane and Control Plane DCN Independence
  Management Plane DCN Topology
    Typically single management system talking to many NE (and now also CE (Control plane Element), if separate from NE)
    Cascaded/hierarchical paths
  Control Plane DCN Topology
    May require many paths from CE (if communication with many CE)
Bridge-n-Roll for Unprotected & Restored Connections in ASON
  In-service Moves for Maintenance Activities
(Re)Grooming in ASON
  In Response to Architectural Changes in Optical Network
  To Optimize Existing Connections
Interoperability Between Multi-vendor Control Plane Interfaces
  Interfaces Between Control Plane Entities

## Slide 15: Management System Integration Management Application Issues
Integration with Control Plane
  Data Replication between Management Plane and Control Plane
  Resolution/Correlation of Multiple “Names” for a Resource
    Name used by control plane (e.g. local addresses and global addresses)
    Name used by management plane (e.g. Local Distinguished Name, Label)
  Function Allocations between Control Plane and Management Plane
  Partitioning Resource Control Among Control Plane & Management Plane Instances
  Interfaces Between Management Plane and Control Plane Entities
Harmonization of Demands & Capacity at Each Transport Layer
  Dynamic Identification of Services Available
    Reachability
    Service parameters (such as service type, resiliency, QOS)
  Dynamic Identification of Demands
    Usage, call requests, and call blocks
  Dynamic Identification of Capacity
    Capacity (available, used, or under maintenance)

## Slide 16: Summary and Recommendations
There are many optical service types and multiple optical network transport architectures that need management support.
There are many issues to be resolved in migrating to the OTN and ASON.
There is a need for migration strategies and integration strategies for inter-working with existing environments.
Some issues potentially resolved by further standards work:
  Monitoring Concatenated Services & ASON Services
  Fault Isolation for ASON Services
  Bridge-N-Roll for Unprotected & Restored Connections in ASON
  (Re)Grooming in ASON
  Data Replication between Management Plane and Control Plane
  Resolution/Correlation of Multiple “Names” for a Resource
  Function Allocations between Control Plane and Management Plane
  Partitioning Resource Control Among Control Plane & Management Plane Instances
  Interfaces Between Management Plane and Control Plane Entities
  Harmonization of Demands & Capacity at Each Transport Layer