## Slide 1: Services Optical access introduction Drivers and hindrances Carrier activities Multi Service PON solution Market research Financial aspects
Kalt
Warm
Dr. Helmut Schink, Johann Wurzenberger
Optical Access

## Slide 2: Optical Access: Services
a) VPN service with bandwidth guarantees
b) RLA e.g. for home offices
Internet access:
a) “always on”, guaranteed bandwidth
b) statistically shared bandwidth
Legacy services:
a) Leased Line service with STM1 / OC3 (155 Mbps)
b) E1/T1 (2 Mbps)
Analog and digital broadcast
Switched video - VoD
Internet access
p t p
leased line
LAN to LAN
Ethernet P2MP
Broadcast
Telephony
ISDN/POTS via TDM channel
voice over IP/ voice over ATM

## Slide 3: Adoption of Broadband Technology
Innovators: Techies try it
Early Adopters: Visionaries get a head of the herd
Early Majority: Pragmatists stick with the herd
Late Majority: Conservatives hold on
Laggards: Skeptics no way
2.5%
13.5%
34%
34%
16%
Chasm
Providers have to
cross the chasm to
fuel market growth
Customer segmentation and profiling
Market segmentation
Customer profiling and identification of service demand
Service offering strategy
Alliance with Content providers
Marketing and service roll-out
5%
16%
27%
52%
Willingness to pay
for broadband access
Dial-up user
Broadband user
Willingness to pay
for broadband services
5%
26%
27%
40%
Marco Motivator to switch to
broadband
50% dial-up was to slow
58% always-on service
67% fast download of video and audio
37% of German inhabitants are online. 1.6’ DSL broadband access lines are installed.
With 2.3 users per DSL line 3.7’ broadbanders (4.5%) have adopted broadband technology..

## Slide 4: Optical Access Principles
Dedicated fiber
Active switched access
passive optical network
ATM
SDH
Enet
PPP/IP
IP/SRP
Enet/RPR
ATM
MPLS
SDH
WDM
TDM/TDMA
FDM
Fiber drop or hybrid
Transport method:
switching method:
MAC principle:
Aggregation
switch
Aggregation
switch
Aggregation
switch
Rings,
Dedicated fiber,
PON

## Slide 5: Options for Hybrid Fiber
DSL copper
(SHDSL, VDSL,
ADSL, MDSL,
HS-SDSL)
coax
radio
drop
service
Internet,
Phone
VoD, AoD
IP-VPN, L2L
Internet,
Phone
Broadcast a/d
VoD, AoD
IP-VPN, L2L
Phone
Internet
IP-VPN, L2L
interfaces
Enet 10BT
ISDN BA, a/b
VoIP/Enet
MPEG
Enet 10/BT
ISDN BA, a/b
VoIP/Enet
DVB/MPEG TS
Enet 802.11
modem
OLT
feeder

## Slide 6: Arguments for PON and xDSL
Large coverage area (PON/DSL)
Reduced fiber deployment/rental costs (PON/DSL)
Multicast and broadcast capabilities (PON)
Reduced costs for maintenance no active elements (PON)
Ease of upgrades to higher bit rate (PON/DSL)
No additional infrastructure costs (DSL)
Dedicated fiber
Active optical access
passive optical access
1 fiber
14 tranceivers
1 multiplexer
6 fibers
12 tranceivers
1 fiber
7 tranceivers
Fiber drop or hybrid
Question to be answered:
Which argument is valid in a specific environment?

## Slide 7: 64Kbps is Enough for all Applications?
Similar to the “famous last words” of Bill Gates 1981 “640KB ought to be enough for anybody.”
There will never be enough! The bandwidth demand will continue to grow.
Fiber to the home will be necessary sooner or later.
Kalt
Warm
ISDN
100
1k
10k
100k
1M
10M
100M
1G
1980
1990
2000
2010
2020
Year
Bit rate per user (bit/s)
PSTN / Modem
ADSL
SDSL
FTTH
double in 18 mon.
double in 24 mon.
N.B. The technology bars show the introduction, not the end of the technology
VDSL, FTTCab

## Slide 8: Overcoming the Cost Trap of Optical Access
Example: 4000 subscribers in 2 sq.km., ducted main cable, buried distribution cable
Line Termination (LE)
Network Unit
Termination
Fibre
Twisted Pair
Civil works
0
500
1.000
1.500
1. ADSL (Ref.)
2. P2P VDSL
3. APON VDSL
4. P2P Ethernet
5. FTTH APON
greenfield
upgrade
Make civil works irrelevant
Alternate access
New developing areas
Replacements of copper
„We did our due-diligence with all the various wireline solutions, and we kept coming back to fiber-to-the-home. We figured if we’re going to open the trench anyway, it doesn’t make sense to put in an infrastucture that has limited, short-term bandwidth capacity.“
Steve Sackrider, Wamego Telecommunications (ILEC Kansas)
Reduce system cost
Ethernet I/O
PON
Cheap optical components
Increase revenue
Universal access
Any service
Every customer
(SME, buildings, private user)
Cost per user (€)

## Slide 9: Cases for Operators
Lease fiber
Provide transport solution
(Enet, SDH, ATM, FR)
Provide end user services
Telephony, broadcast, VPN, ..
Example: City of Stockholm (one connection point each block in 2002)
Milano (20% of households in reach of fiber)
Example: BT, Palo Alto CA
Colt
France- 230‘ + 1,5“ fund by CDC – Caisse des Depots et Consignations
Example: Hamburg-Norderstedt,
Bredbandsbolaget (video and transport) in Sweden, Norway, Denmark
Kalt
Warm

## Slide 10: Concept for Optical Access Solution
Metro Access/Core
Residential users
Business users
Kalt
Warm
LME
SME
Business parks
PON
MTU
Broadcast
entertainment
Telephony
MM-
communication
Internet
Access
Information
retrieval
FTTC
FTTB
Dedicated fiber
FTTB
FTTB
FTTB
Telephony
MM-
communication
Internet
Information
Retrieval
RLA
VPN,
Lan2Lan
DLC
xDSL
FTTH

## Slide 11: MS-PON: Principal Concept
ONU
CWDM
PON Splitter
WDM Splitter
TDMA upstream
TDM downstream
<=10 Km
xDSL
Fiber to the curb
<=10 Km
DLC/
DSLAM
Fiber to the
Home, business, building
CO
CO
OLT
Metro core/
WAN
TDMA
Time slots
VC 4/12 frame
ATM cells
Ethernet frames
IP packets
broadcast

## Slide 12: Performance Examples – Enough for High Density Areas
Bandwidth
allocation
STM1 units
Total
Gbps
Number of VC4 units
Max.
Users
per OLT
Users
per ONU
wire speed
Number of ONUs
4
8
20
20
128
128
1280
Enet
16
GEnet
40
Enet
1
GEnet
2
20
128
1280
Enet
20
Enet
64
32
16
Up to 1280 users per fiber pair with 10 Mbps guaranteed bandwidth are possible. Statistical multiplexing would even further increase the bandwidth per user or the number of users.

## Slide 13: Optical Access Growth
Source: Siemens, Status: May, 2002
„ The residential market offers the largest potential volume for termination units, but is more expensive to enter on a per end-user basis. The SME market offers the largest portion of equipment revenue.“ Japan and Korea are in the forefront. The regulatory picture in US remains clouded, it doesn't encourage outside plant investments.
(source RHK)

## Slide 14: DSL Technologies and Services
with IMA
Services/
Bandwidth
Technology
ADSL
1M
6M
10M
14M
2M
SHDSL
VDSL
Fast Internet
E-learning
Gaming
Multimedia Home
Broadcast TV
High Speed VPN
Streaming Media
Video Conferencing
Virtual Private Networks

## Slide 15: Longterm Price Decrease Mfg Port ASP ($) ADSL
Source: Dell’Oro Report 4Q01 21.02.2002
Price Decrease ~ 30 – 40 % / y

## Slide 16: Network Cashflow and NPV ( 10% discount rate)
For the same number of subscribers and sites, the 3 year roll-out gives sensible better results than the 5 year roll-out. The NPV break even occurs in 3 years against 5 years for the slower one.
Also, the faster roll-out anticipate the EBITDA

## Slide 17: Conclusion
Optics in the Access is there and growing
Termination point will migrate towards end-user
Current and near term: dedicated fiber in combination with xDSL
early adopters for FTTH: green fields like new construction areas, high rise buildings
PON in combination with Ethernet for high density residentials (MTUs) and SME
Large enterprises will continue to use dedicated fiber