## Slide 1: Session 10: Optical Switching and Equipment ITU-T Study Group 15, Q12
Michael Mayer
Nortel Networks

## Slide 2: Q12/15: Network architecture
Overview:
  Scope of work in Question 12/15
  Principles of architectural specification
  Q12 work on the Optical Control plane (ASON)
  Relationship of control and management planes
  Control plane component overview
  Relationship to other SG-15 work

## Slide 3: Optical Switching and Equipment ITU-T Q12.15
Q12/15 “Technology Specific Transport Network Architectures”:
  Responsible for the study and specification of various transport network architectures.
  Network architecture:
    is developed by examining the overall functions required of the network and developing specific components that can be interconnected to represent networks.
    Interactions of these components can then be studied and specific equipment and related recommendations can be developed
    Allows reference points (interfaces) to be clearly defined
    Specifies high level requirement for OAM
  Architecture specification methodology:
    uses a common “language” and well defined interconnection rules as specified in G.805
    Can be made technology independent
    Provides a certain degree of recursion

## Slide 4: G.805 architectural principles
TCP
AP
Trail
Termination
TCP
S
N
C
C
P
T
r
a
i
l
t
e
r
m
i
n
a
t
i
o
n
T
r
a
i
l
t
e
r
m
i
n
a
t
i
o
n
T
C
P
S
N
C
C
P
L
C
C
P
C
P
LC
C
P
S
N
C
T
C
P
LC
Server
Layer
Adaptation
Client
Layer
Network
Client to
Server
Adaptation
Client to
Server
Adaptation
AP
AP
Network Connection
AP
Trail
Link Connection
Trail
Termination
Trail
AP: Access Point CP:Connection point
LC: Link Connection SNC: Sub-network connection

## Slide 5: Why Architecture?
Architecture Recommendations form the base documents describing the overall requirements and capabilities of specific networks
  Additional recommendations are developed guided by the architecture for example:
    Equipment
    Management
    Rates and formats
    Protocols
  Examples of network architectures developed under Q12/15:
    Transport Networks
      ATM transport (I.436)
      SDH (G.803)
      OTN (G.872)
    Transport Network Control Plan (ASON)
      Architecture for the Automatically Switched Optical Network (ASON) (G.8080)

## Slide 6: Architecture of the Optical Control Plane
Began in previous study period in SG-13
  G.807, Requirements for the Automatically Switched Transport Network (ASTN)
  New approach to connection set-up in Optical and other transport networks
    Rapid connection set-up
    Signaled connection set-up
  Connection control (Soft permanent and switched connections) over existing layer networks
  Related to work in :
    OIF (e.g. UNI, NNI)
    IETF (Protocols)
    ATMF (Protocols)
    Other Questions within SG-15
      Q14 (Protocols and Management)
      Q9, Q11 (Equipment)

## Slide 7: Control plane vs. Management plane Provisioned connections
NE
NE
NE
Transport Plane
Connection
End point
Connection
End point
A
B
Management Plane
Provisioning
Request
Provisioning
Request
Provisioning
Request
Provisioned connection
Provisioning
Request
Provisioning
Request
Provisioning
Request

## Slide 8: Control plane vs. Management plane Soft permanent connections (SPC)
NE
NE
NE
Transport Plane
Connection
End point
Connection
End point
A
B
Management Plane
Control Plane
Connection
Request
Connection
Request
Connection
Request
Connection
Request
Soft permanent connection
Switched connection
Permanent
connection
Permanent
connection

## Slide 9: Control plane vs. Management plane Switched connections (SC)
NE
NE
NE
Transport Plane
Connection
End point
Connection
End point
A
B
Management Plane
Control Plane
Connection
Request
UNI
Connection
Request
Connection
Request
Connection
Request
Connection
Request
UNI
Switched connection

## Slide 10: ASON control plane relative to network equipment
Switch
Switch
Switch
Clients
e.g. IP, ATM, TDM
Clients
e.g. IP, ATM, TDM
OCC
OCC
OCC
CCI
I-NNI
UNIcontrol
User
signaling
E-NNI
IrDI
OCC
ASON control plane
Optical Transport Network
UNIData
Network
Management
System
NMI

## Slide 11: ASON control plane components
ASON control plane performs many functions
  Neighbor (adjacency) discovery
  Protocol control
  Link Resource Management
  Routing control
  Signalling
  Connection control
  Call control
Individual functions form the basic components of the architecture
Described in UML-like language

## Slide 12: ASON architecture: UML like descriptors
UML-like descriptors defined for individual components
  Defined for all basic components in the ASON control plane architecture
  Allows interactions to be studied in similar manner to decomposition of transport network architecture
  Can be used to define specific details of protocols

## Slide 13: Example of application of ASON architecture
CCI
Calling Party
Call Controller
Network Call
Controller
(NCC)
In
Out
In
In
Out
In
Out
Policy
Connection
Request
Call Teardown
Call Request
Call Teardown
Call Accept
Policy
Manager
Directory
Manager
Directory
Request
Out
Out
Connection
Controller
(CC)
In
Out
Out
Out
In
Out
In
Peer Coordination
Out
Route Table
Query
Routing
Controller
(RC)
Link
Resource
Manager
(LRM)
Link Connection Request
Out
In
Local Topology
In
Local Topology
Out
In
Out
Network Topo
Network Topo
Protocol
Controller
(PC)
Protocol
Controller
(PC)
SNP Negotiation
Out
SNP Release
Out
Topology
Configuration
Translation
In
Out
In
Out
In
Connection Request
Transport Plane
Called Party
Call Controller
In
Out
Call Request
Call Teardown
Call Request
Call Indication
Client Side
Network Side
Out
Network Call Coordinator
Network Call Coordinator
Call Teardown
Call Indication
Peer Coordination
NNI
UNI
Out
Link Connection Teardown
Out
In
Connection
Teardown
Out
In

## Slide 14: G.8080 relationships
Q9/15
  G.783, G.798, G.841 Equipment and protection
Q11/15
  G.707, G.709, G.7041 SDH, OTN, VCAT, GFP, LCAS
  G.7042
Q12/15
  G.803, G.872, G.etna SDH, OTN, Ethernet architecture
Q14/15
  G.7712, G.7713, DCN, DCM,
  G.7713.x (1,2,3) DCM(PNNI, RSVP ,CRLDP)
  G.7714, G.7714.1 Discovery, Protocol for auto discovery
  G.7715, G.7716 Routing, Link management
  G.7717 Connection admission control