## Slide 1: Optical Control Plane - The realization of distributed control for optical switches Siva Sankaranarayanan ITU-T Workshop on IP/Optical Chitose, Japan July 2002

## Slide 2: Outline
Motivation
  What is the Optical Control Plane?
  Optical Control Plane - Value Proposition
Fundamentals
  Reference Points
  Optical Control Plane Requirements & Architecture
Relationship between ITU-T and other SDO work
  Domains of application of each
Protocol Neutral Work - Q14/15
  Connection Management
  Routing
  Discovery
Protocol specific work - Q14/15, OIF, IETF CCAMP WG
Conclusions

## Slide 3: Outline
Motivation
  What is the Optical Control Plane?
  Optical Control Plane - Value Proposition
Fundamentals
  Reference Points
  Optical Control Plane Requirements & Architecture
Relationship between ITU-T and other SDO work
  Domains of application of each
Protocol Neutral Work - Q14/15
  Connection Management
  Routing
  Discovery
Protocol specific work - Q14/15, OIF, IETF CCAMP WG
Conclusions

## Slide 4: What is the Optical Control Plane?
Traditionally networks employ manual provisioning of long duration services based on a management system
The optical control plane enables a paradigm shift towards automatic distributed approaches to end-to-end service provisioning
  Supports intelligence that enables transport networks to be “self-managed” with regard to topology discovery, routing, and connection set-up
  Enables a new networking platform that will create tremendous business opportunities for network operators and service providers to offer new services to the market.
  Improves accuracy in inventory information and resource optimization through “self-aware” network
Ultimate goal is multi-vendor, multi-carrier interoperable networking that enables end-to-end services on a global scale
The optical control plane enabler - Industry-Standard ASTN signaling, discovery and routing

## Slide 5: Optical Control Plane Value Proposition
Improved speed of service provisioning
  Provisioning occurs within seconds rather than days or weeks
Infrastructure that supports managed bandwidth services
  Ability to offer a variety of services and different levels of granularity
Enhanced survivability
  Distributed mesh restoration
Lower operational costs
  Enabled by auto provisioning and scalable maintenance solutions
Improved inventory and service offerings
  Enabled by auto-discovery of resources and service capability discovery
Ease of integration across different layers
  Common control architecture between service and transport layers

## Slide 6: Outline
Motivation
  What is the Optical Control Plane?
  Optical Control Plane - Value Proposition
Fundamentals
  Reference Points
  Optical Control Plane Requirements & Architecture
Relationship between ITU-T and other SDO work
  Domains of application of each
Protocol Neutral Work - Q14/15
  Connection Management
  Routing
  Discovery
Protocol specific work - Q14/15, OIF, IETF CCAMP WG
Conclusions

## Slide 7: Fundamentals - Reference Points
Service Provider A
Admin Domain
UNI
E-NNI
Service Provider B
Admin Domain
Domain A1
Domain A2
E-NNI
I-NNI
I-NNI
I-NNI
Provider A has divided network into multiple control domains (e.g., vendor, geographic, technology, managerial, etc.)
Provider B’s network is a single control domain
User
Domain
User-Network Interface (UNI):
operations between user and provider control domains
Exterior Network-to-Network Interface (E-NNI):
inter-control domain operation
Interior Network-to-Network Interface (I-NNI):
intra-control domain operation
Network-to-Management Interface (NMI):
operations between management systems and service provider administrative domains
Notes: The control plane (and the transport plane) in ASTN is subdivided into domains that match the administrative domains of the network. Within an administrative domain the control plane may be further subdivided, e.g., by actions from the management plane. This allows the separation of resources into, for example, domains for geographic regions, that can be further divided into domains that contain different types of equipment. Within each domain, the control plane may be further sub divided into routing areas for scalability, which may also be further subdivided into sets of control components. The transport plane resources used by ASTN will be partitioned to match the sub divisions created within the control plane
To provide network services for connection management requires clearly defined interfaces. The interconnection between domains, routing areas and, where required, sets of control components is described in terms of reference points. Four specific abstract interfaces are of particular interest in ASTN -- UNI, E-NNI, I-NNI and NMI. Multiple abstract interfaces may be multiplexed over a single physical interface. The reference point between an administrative domain and an end user is the UNI. The reference point between domains is the E-NNI. The reference point within a domain between routing areas and, where required, between sets of control components within routing areas is the I-NNI. The reference point between an administrative domain and a management system the NMI.
More on these later.

## Slide 8: ASTN Requirements and Architecture
ITU-T Rec. G.807/Y.1301, Requirements for Automatic Switched Transport Networks (ASTN)
  Scope and requirements largely driven by operators
  Provides network level requirements for control plane, identifying and describing
    UNI, E-NNI and I-NNI reference points
    Supportable connection types (permanent, soft-permanent, and switched)
    High-level control plane functions and requirements
ITU-T Rec. G.8080/Y.1304, Architecture for the Automatic Switched Optical Network (ASON), Approved Nov. ‘01
  Based upon G.807, provides canonical architecture for the control plane
  Architecture described in terms of components with well- defined interfaces
    Components derived from G.85x distributed management specifications
    Separates Call and Connection Control (Intelligent Networking - switching experience)
  Applicable to any transport technology (e.g., SDH, OTN, etc.)
  Separates protocol dependent parts from invariant parts

## Slide 9: Outline
Motivation
  What is the Optical Control Plane?
  Optical Control Plane - Value Proposition
Fundamentals
  Reference Points
  Optical Control Plane Requirements & Architecture
Relationship between ITU-T and other SDO work
  Domains of application of each
Protocol Neutral Work - Q14/15
  Connection Management
  Routing
  Discovery
Protocol specific work - Q14/15, OIF, IETF CCAMP WG
Conclusions

## Slide 10: Optical Control Plane Relationship between ITU-T and other SDO
OIF
UNI 1.0, 2.0
NNI 1.0
Distributed Call & Connection Management
(
(G.7713/Y.1704)
Discovery Techniques
Data & Signaling
(G.7712/Y.1703)
ITU-T ASTN Umbrella
Protocol for Automatic Discovery
in SDH & OTN Networks
(G.7714.1)
Distributed Connection Mgmt.
Protocols
(G.7713.1, G.7713.2, G.7713.3)
Automatically Switched Optical
Network Architecture
(G.8080/Y.1304)
Generalized Automatic
Discovery Techniques
(G.7714/Y.1705)
Date Communications Network Arch.
(G.7712)
Automatically Switched
Transport Network Reqts.
(G.807/Y.1301)
Architecture & Requirements
for Routing
(G.7715)
IETF GMPLS Umbrella
  Signaling Functional Description
  RSVP-TE Extensions
  CR-LDP Extensions
  SONET-SDH Extensions
  G.709 Extensions
  Link Management
  (LMP, LMP-WDM)
  Routing
  OSPF-TE/IS-IS Extensions
ATM
Forum
PNNI signaling and
routing extensions
converged ASTN
Requirements
Protocols

## Slide 11: Optical Control Plane Application Domain of ITU-T, OIF and IETF CCAMP
Control
Domain A1
I-NNI
IETF GMPLS
Control
Domain A1
I-NNI
IETF GMPLS
Control
Domain A1
I-NNI
IETF GMPLS
Control
Domain A1
I-NNI
IETF GMPLS
User
Domain
User
Domain
Provider C
Admin Domain
UNI
I-NNI
OIF
Control Domain A
(e.g., vendor 1, metro)
E-NNI
Control Domain B
(e.g., vendor 2, core)
Intra-Carrier
Admin Domain
E-NNI
Provider A
Admin Domain
Provider C
Admin Domain
Domain A2
E-NNI
Domain A1
I-NNI
ITU-T
View in slide show mode
Notes: Network Navigator advanced distributed control plane based upon ASTN/GMPLS
  Provides control for multiple transport technologies (SONET/SDH, OTN)
  Enables different customer business models and network scenarios
High level Network Navigator features
  Connection Management
    End-to-end connection services with only start/end points specified by requester
  Restoration Management
    Mesh restoration, 1+1, and shared protection options
  Network Topology Management
    Auto-discovery of physical neighbor connections and ports
  User and Management Interfaces
Phased evolution based upon evolution of open industry standards
  Phase 1 - Open UNI to support user service requests (e.g., IP/MPLS routers, ATM switches) from day one
  Phase 2 - Adds Open Exterior NNI (E-NNI) for multi-domain operation
  Phase 3 - Adds Open Interior NNI (I-NNI) for multi-vendor operation in a single domain

## Slide 12: Outline
Motivation
  What is the Optical Control Plane?
  Optical Control Plane - Value Proposition
Fundamentals
  Reference Points
  Optical Control Plane Requirements & Architecture
Relationship between ITU-T and other SDO work
  Domains of application of each
Protocol Neutral Work - Q14/15
  Connection Management
  Routing
  Discovery
Protocol specific work - Q14/15, OIF, IETF CCAMP WG
Conclusions

## Slide 13: Protocol Neutral Work - Q14/15 Call and Connection Management
ITU-T Rec. G.7713, Call and Connection Management
  Provides protocol neutral control plane signaling requirements
    Functionally specifies control plane on a per layer basis, allowing for implementation flexibility
    Supports both soft-permanent and switched connections
    Provides for enhanced signaling robustness, considering several rainy-day scenarios
    Considers control/management plane interactions
    First version supports basic connection management
  Basis for mapping to specific protocol solutions (G.7713.x series)
    Detailed information enables protocol compliance assessment
      Attributes list and messages
      State machines
      Signal flows and exception cases

## Slide 14: Protocol Neutral Work - Q14/15 Routing
ITU-T Rec. G.7715, Architecture and Requirements for Routing in ASON
  Provides a foundation for routing related work in Q14/15
  Employs a consistent and self-contained terminology based on fundamental ODP principles
  Enunciates an invariant architecture for routing involving G.8080 based components
  Enlists a common set of architectural, protocol and path computation requirements for routing
  Forms a basis for routing protocol related work by providing
    Basic routing attributes, abstract routing messages and state machines
    Different configurations of routing adjacencies and relationship to transport topology

## Slide 15: Protocol Neutral Work - Q14/15 Discovery Techniques
ITU-T Rec. G.7714, Generalized Automatic Discovery Techniques
  Describes the auto-discovery requirements, attributes and methods in a protocol-neutral fashion
    Supports features that enable auto-discovery in the context of switched transport connections
    Covers various aspects of auto-discovery
      Association between physical ports on cross-connects
      Associations affecting routing of transport connections (building topology knowledge at the layer of flexibility)
      Identification and association between control plane entities to enable communications
    Addresses service capability exchange
      Exchange of service capability sets between identified control entities
    Discusses methods for discovery, and relative advantages of each
  Basis for examining specific protocol solutions
    Provides discovery attributes, messages, and process flow/state diagram

## Slide 16: Outline
Motivation
  What is the Optical Control Plane?
  Optical Control Plane - Value Proposition
Fundamentals
  Reference Points
  Optical Control Plane Requirements & Architecture
Relationship between ITU-T and other SDO work
  Domains of application of each
Protocol Neutral Work - Q14/15
  Connection Management
  Routing
  Discovery
Signaling Protocol Work - Q14/15, OIF, IETF CCAMP WG
Conclusions

## Slide 17: Signaling Protocol Specifications
OIF UNI GMPLS
  Addresses the client/user signaling – i.e., this is the call management portion
  OIF used base GMPLS signaling and extended/modified to support UNI 1.0
    Supports both RSVP-TE and CR-LDP based signaling protocol options
  Enhancements expected to support further functions in UNI 2.0 (e.g., bandwidth modification, support for Ethernet signal types)
OIF E-NNI GMPLS
  Work is starting in specifying an implementation agreement for E-NNI signaling specifications (close linkage between ITU-T Rec. G.7713.x series expected)
  Carrier/network requirements to serve as a foundation
IETF GMPLS
  GMPLS continuing to evolve as requirements impacts are felt
    “Toolkit” approach with various options; not tailored according to interface type
    Provide RSVP-TE and CR-LDP based signaling protocols
  Continuing to discuss technology specific extensions (e.g., SONET/SDH, G.709)
ITU-T ASTN
  Work moving quickly on G.7713.1, G.7713.2, G.7713.3 addressing PNNI, GMPLS RSVP-TE-based and GMPLS CR-LDP-based signaling, respectively

## Slide 18: Back Up Slides

## Slide 19: Optical Control Plane Key Benefits to Operators & Service Providers
Operators can optimize their network operations to their criteria, e.g.,
  Some operators choose to subdivide the network into several domains based on different criteria, e.g., geographic, vendor, administrative, etc.
  Some operator additionally choose to employ hierarchical network organization
Definition of proper reference points (e.g., UNI, E-NNI, I-NNI) enables end-to-end service offerings consistent with existing business practices
Ability to apply different types of policies at the reference points consistent with their network practices
Ease of operation by offering a consistent set of protocols across the reference points
Allows for reorganization of domains, e.g., segmentation, mergers, etc.