## Slide 1: Relating Optical Layer and IP Client Performance
Peter Huckett, Chairman ITU-T WP 1/4
Acterna Director International Standards
Tel: +44 1245 401 329
Fax: +44 1245 401 334
GSM: +44 7768 104663
Email: peter.huckett@acterna.com

## Slide 2: Agenda
IP client mapping into the OTN
Monitoring OTN performance
Challenges to evaluating OTN performance
Optical domain measurements
Benefits of new measurement techniques
Relating optical and IP client performance
Wavelength services and role of SLAs
Relationship of SG4 work to SG13 & SG15

## Slide 3: Optical Transport Networks
OFA
OFA
n
OADM
GigE
Metro
SONET/SDH
Voice
Switch
ATM Data
or VoIP
Switch
Terabit
Router
Optical Switch
Ultra Long-haul
DWDM
Optical
Switch
Node
Gigabit
Router
OC-192c STM-64c
GigE
OC-48 STM-16
Optical Core
Optical Edge
Switched optical network
Regional optical network
Linear DWDM Backbone Spur
OC-48/12 STM-16/4
DWDM Mux
DWDM Mux
OC-192c STM-64c
TP
TP
TP
TP
TP
TP
OC-192 STM-64

## Slide 4: Presentation Focus

## Slide 5
client
OH
OH
OH
FEC
client
OPU
ODU
Optical Channel
Optical Multiplex Section
Optical Transmission Section

Non-associated overhead Optical Supervisory Channel
OPU
ODU
OTU
OCh
OMS
OTS
Optical Multiplex Section:
intended to support the connection monitoring and assist service providers in troubleshooting and fault isolation
describes optical DWDM connection between two components with multiplex functions e.g. OXC, OADM
Optical Transmission Section:
describes transport on an optical link between two components
it is used for maintenance and operational function
it allows the network operator to perform monitoring and maintenance tasks between NEs
Optical Transport Structure
Optical Transport Module
Courtesy of Lucent Technologies
OCh = Optical Channel
ODU = Optical Data Unit
OPU = Optical Payload Unit
OTU = Optical Transport Unit

## Slide 6: OTN Layer Trails
Example of OTSn, OMSn, OCh, OTUk, ODUk, OPS0 trails
  Transport of STM-N signal via OTM-0, OTM-n & STM-N lines
DXC
3R
3R
3R
OTSn
OTSn
OTSn
OTSn
OTSn
OMSn
OMSn
OMSn
STM-N
ODU
k
Client
Client
3R
DXC
OPS0
OSn
OTM-0
OTM-n
STM-N
OCXC
OCADM
LT
R
R
LT
DXC: Digital Cross-Connect
OCADM: Optical Channel Add-Drop Multiplexer
OCh: Optical Channel
OCXC Optical Channel Cross-Connect
ODUk: Optical Data Unit k
OMSn: Optical Multiplex Section n
OPSn: Optical Physical Section n
OTM-n: Optical Transport Module n
OTSn: Optical Transport Section n
OTUk: Optical Transport Unit k
R: Repeater
3R: Reamplification, Reshaping & Retiming
STM-N: Synchronous Transport Module n
OCh, OTU
k
OCh, OTU
k
OCh, OTUk
Courtesy of Lucent Technologies
Notes: <number>
<footer>
<header>
<date/time>
This slide shows the OTN layer network trails and example use of the transport entities in the OTN. In this example, the client signal is an STM-N transported between the terminating DXCs. This STM-N is carried on the concatenation of an SDH section (Osn) and the end-to-end connection in the OTN, the ODUk. The ODUk itself is carried on a concatenation of OTUks, each delimited by a 3R regeneration point. Each ODUk is assocaited with an optical wavelength by means of the OCh. A number of Ochs are multiplexed into an OSMn, which spans the distance between the line-terminating equipment – LTs, OCADMs, OCXCs.
Although G.709 and G.optperf defines ODUk and OTUk as bidirectional entities and their error performance objectives, BIS and Maintenance treats these as independent entities in each direction.

## Slide 7: Monitored Layer Signals
ODUkP – ODUk Path
  End-to-end connection in the OTN
  Performance as perceived by the client
  Uses BIP-8 EDC, BDI and BEI
ODUkT – ODUk Tandem Connection
  Performance of part of a path
  Transport service by a sub-contractor to SLA
OTUk – Connection between 3R points
  O-E-O conversion
  Support of 3R regeneration spans
  Uses BIP-8 EDC and optional FEC

## Slide 8: M.24otn Network Reference Model
TOD
TOD
BOD = Backbone Operator Domain
ROD = Regional Operator Domain
TOD = Terminating Operator Domain
BOD
ROD
ROD
BOD
ODUk Hypothetical Reference Path (HRP) -
an M km length path spanning six domains
Error performance events – BBE and SES
Error performance parameters – BBER and SESR
Note: ES and ESR not very useful since every second in high-speed systems may be errored before correction by FEC

## Slide 9: Performance Evaluation Challenges
Manufacturing/qualification of OTN equipment
Efficient DWDM/SDH/SONET installation
System integration of OTN equipment
Commissioning OTN systems and paths
Access to the optical domain in-service
Detecting optical signal degradation
Fault location within the optical domain
Pure wavelength services

## Slide 10: Optical Transmission Impairments - welcome to the real world!
A certain amount of
3R Regeneration will be needed:
O-E-O conversions
Next step in bit rate per channel?
10G -> 40G?
Shorter pulsewidth (1/4)
Requires higher power per channel (x4)
Causes stronger nonlinear effects (x16)
Worse BER, no alarm indication at optical layer!

## Slide 11: Fibre Transmission Effects
linear
non - linear
Parametric Effects
Dispersion Effects
Scattering Effects
Attenuation Noise
SPM
FWM
Raman
Brillouin
P M D
Chromatic
XPM

## Slide 12: Optical Domain Measurements
Impairments:
  Attenuation and optical multiplexer crosstalk
  Polarization Mode Dispersion (PMD)
  Chromatic dispersion
  EDFA noise and transmit laser chirp
  Non-linear effects e.g. four-wave mixing, XPM, Raman crosstalk
  Scattering
All impact digital error performance of client signal!
Measurement tools:
  Power meter
  Fast optical spectrum analyzer
  Q-factor meter

## Slide 13: DWDM Provisioning Example
ONT-50
3
BERT
1
1
1
Power
2
OSNR
Step 1 Optical power level measurements
    Check the overall power level at the far end
    Tune the power levels at test points according to the budget
Step 2 Optical wavelength measurements
    Check the optical spectrum and tune the OSNR
    Check max. OSNR difference at each lambda (e.g. < 4 dB)
Step 3 BER measurements
    OC-N/STM-N loop/daisy-chain test
    0 bit errors over 24 – 72 hours

## Slide 14: DWDM Spectrum

## Slide 15: Business Need in Ultra-high Bandwidth Networks
Multiple dominant impairments
Migration towards analogue network behaviour
P, , OSNR is no longer enough
-factor measurement
10
Gbit
/s
TDM
Attenuation
Dispersion + nonlinear Effects
DWDM
TDM
Notes: Today transmission systems working at data rates up to 10Gbit/s are mainly limited by linear impairments like attenuation and noise.
Increasing data rates above 10Gbit/s or migrating towards multi channel dense WDM systems with more than 32 channels nonlinear effects like
  FWM (four wave mixing)
  XPM (Cross phase mixing)
  SPM (Self phase modulation)
  SBS and SRS (Brillouin and Raman Scattering)
become dominant leading to signal quality degradation.
To guarantee a certain QoS measurements of Power, Wavelength and OSNR is no longer sufficient.
Beside the time consuming method of BER testing Q factor shows an excellent solution for signal quality analysis within short measurement time.

## Slide 16
BER
-30
-28
-26
-24
-22
-20
-18
-16
-14
-12
-10
Second
Year
Millennium
Earth
Human Race
Hour
6
7
8
9
10
11
Cannot measure bit errors
=> „Error-free Region“
Bit
Errors
Time for 1 error at 10 Gbit/s
Measurement of Very Low BER
Notes: Under the assumption of stochastically distributed signal impairments there is a way of relating the measured Q-factor and the bit error rate.
In contrast to a traditional BER tester the Q-factor meter only can measure a Q value which can be related to a bit error rate.
We do not talk about a BER measurement but a BER estimation.
The relation between Q and BER shows a nonlinear behaviour for high Q values / low bit error rates.
As Q factor is a calculation of statistical distribution functions Q will always have a certain confidence interval. For high Q values this leads to an ‘estimation’ of bit error rates which may cover a range of several decades.

## Slide 17
Bit
Errors
- factor measurement < 1 Minute
Testing Challenge
Optimization of DWDM systems in a timely manner, which covers all impairments (e.g. dispersion)
Requires accelerated measurement principle!
Notes: Bellcore GR-2918 and ITU-T G. 692 spezify maximum bit error rates of 10^-12 meaning no bit error in 7 minutes at 2.5 Gbit/s data rates.
More and more system manufacturers and service providers are looking for bit error rates in the range of 10^-14.
Acceptance tests with traditional BER testers need very long measurement times up to 11hours for 10^-14 at OC-48/STM-16.
Customers using ultra high speed links are looking for even lower BER values down to 10^-16. This results in test times of several days.
Here Q-measurement is a way to cut down measurement times to less than 1 minute.

## Slide 18: Optical -factor
Reflects quality of optical communications signal
  “Q-factor” doesn’t stand for quality
  Standard maths symbol for Gaussian error integral
  Property of signal, not of the communications system
Monitors amplitude & noise of analog signal
Statistical techniques determine Q-factor
Fundamentally different to BER test
Estimates BER given certain assumptions
  Stochastic distribution of white amplitude & phase noise
  Gaussian tail extrapolation with applicability check
Quick check of very low operating BER in < 1min.
  Still need BER for end-to-end performance

## Slide 19
Measurement Principle: -factor
Principle: Indirect BER Monitoring
Measurement of electrical signal to noise ratio performed at the input of a reference receiver (like BER measurements)











0
1
0
1
|
|
Q




stat. distribution
Different methods – Histogram and Pseudo-BER synchronous / asynchronous sampling
Calculation of -factor based on statistical PDF distribution of logic „0“ and „1“
µ1
µ0
 1
 0
optical eye
Standard deviation
Mean value

µ

## Slide 20: Key Benefits of - factor
Complete performance analysis
  including effects of dispersion and non-linearities
Fast measurement time
  independent of bit rate and BER in < 1 minute
Rate-transparent quality testing
  bit rates: 622M, 2.5G, 10G, GigE
  including bit rate with 7% FEC
In-service performance monitoring
  small modular design used at key points
  measures lowest BER

## Slide 21: Compare BERT versus -factor
Test time slashed by
Example: Evaluating the BER 10-14 of a OC-48/STM-16 line
Bit Error Ratio Test Q-Factor
11 hours <1 minute
700
Notes: You need to measure 100 bit errors to get a confidence of 85 % for your BER result.
Q-Factor slashes test time to 1 minute!

## Slide 22: System Optimization
ONT-30
Optical Q-factor Meter
Verification of dispersion management
Optimization of DWDM system settings for best signal quality => channel power, gain, dispersion compensation
n
OFA
OFA
OFA
DWDM Mux
Tx
Tx
Tx
Tx
Rx
Rx
Rx
Rx
DWDM Mux
OFA
DCM
DCM: dispersion compensation module
IMPAIRMENTS dispersion, non-linearities, (FWM, XPM ...)
Notes: Quick BER approximation < 1 min down to 10-7 ...10-40

## Slide 23: Multi-layer Transport Networks
Optical Layer Network
Optical Channel Layer
Optical Multiplex Section Layer
Optical Transmission Section Layer
Physical Medium
Digital Clients
„3++“ Optical LayerNetwork
Fibre
NBT
(The Next Big Thing!)
IP
ATM
SDH

## Slide 24: IP Packet Transfer Errors
OTN Trail
Transmission Errors
Client / OTN Adaptation
Successful Packets
Discarded Packets
Lost Packets
Discarded Packets
Errored Packet
OTN Client

## Slide 25: Relating IP & OTN Performance
IP performance depends on supporting network technology performance
Network complexity is a major factor
Distance does play a part, especially on delay
Care needed with protection and restoration
QoS classes at different network technology layers need to be matched

## Slide 26: QoS Classes
Recognise supporting technologies may differ
In principle, entrance-to-exit node NP and capacity information may be available
IP QoS Class (Y.1541/M.2301) | ATM QoS Class (I.356/M.2201) | SDH/OTN “QoS Class” (note)
0 | 1 | 10-16 and Q=8
1 | 1 | 10-14 and Q=7.5
2 | FFS | 10-16 and Q=8
3 | FFS | 10-14 and Q=7.5
4 | FFS | 10-14 and Q=7.5
5 | 4 | 10-10 and Q=6
Note: item for discussion!

## Slide 27: Wavelength Services & SLAs
Operators are offering wavelength services
Should these have QoS classes?
TM Forum SLA Management Handbook GB917
  Focus on Customer-SP and SP-SP interfaces
  Customer-driven requirements
  SLA parameter framework
  Defines service life cycle
  SLA drives operator business processes and QoS
  Covers all network technologies
  Relates NP to end-to-end QoS

## Slide 28: Validation of Connection Attributes
Optical sub-networks
3R
3R
3R
OTN
Client
OTN
Client
OCh Trail
OCh Trail
OCh Trail
3R
OTN Connection
OCC
OADM
OCh Link Connection
Digital Transmission Analyser
OSA,Q-Factor
OSC, OTDR
Analysis of signal quality in ‘sub-networks’
Check network sections (passed / failed)
Trouble shooting and monitoring in sub-networks
Notes: Quick BER approximation < 1 min down to 10-7 ...10-40

## Slide 29: Selected Optical Standards
Selected ITU-T optical standards (short titles):
G.671 Transmission characteristics of optical components and subsystems
G.681 Functional characteristics of inter-office and long-haul systems
G.691 Optical interfaces for single-channel systems with optical amplifiers
G.692 Optical interfaces for multi-channel systems with optical amplifiers
G.709 Network node interface for the Optical Transport Network (OTN)
G.807 Architecture for Automatic Switched Transport Network (ASTN)
G.959.1 OTN physical layer interfaces
G.976 Test methods applicable to optical fibre submarine cable systems
G.8080 Architecture for Automatic Switched Optical Networks (ASON)
G.optperf Error and availability performance parameters and objectives for OTN
M.24otn Error performance objectives and BIS/Maintenance procedures for OTNs
O.qfm Q-factor test equipment for measuring optical transmission performance
Some other relevant optical standards:
IEC Definition of principal test method and parameters (under study by SC86C WG1)
OIF Electrical Interface and Very Short Reach Interface Implementation Agreements
OIF UNI 1.0 Signalling Specification
TIA/EIA-526-12 Q-factor measurement procedure for optical transmission systems

## Slide 30: Network QoS & Application QoS
Network QoS (bearer Network Performance) must support a range of application services
  Point-to-point telephony
  Multimedia conferencing
  Interactive data transfer
  Streaming video
  Bulk data transfer
Network QoS equals service QoS for pure IP
Transport capacity and traffic statistics are fundamental to QoS
  Defined in traffic contract
  Signalled or agreed between user and/or network

## Slide 31: Role of M.2301 vs Y.1541
M.2301 specifies practical operational performance values for IP Operator Domains (IPODs), based on Y.1540 metrics
M.2301 takes end-to-end performance of Y.1541 and allocates it between IPODs
M.2301 also defines operational procedures for provisioning and maintenance
  Intrusive tests using test packets
  Non-intrusive performance monitoring using MIB data
  Recommends which method to use when
Like Y.1541, MPLS performance is FFS

## Slide 32: Role of M.24otn vs G.optperf
M.24otn specifies practical operational performance values for optical paths, links and systems based on G.optperf metrics
M.24otn takes end-to-end performance of G.optperf and allocates it between domains
M.24otn also defines operational procedures for provisioning and maintenance:
  Multi-operator international ODUk and OTUk
  Non-intrusive performance monitoring
  Unidirectional vs bidirectional availability
  General introduction to maintenance of the OTN
Use of the OTN for analog clients is outside the scope

## Slide 33: Role of O.qfm vs G.optmon
O.qfm specifies Q-factor measurement
Estimates BER of digital clients
Q-factor measurement includes dispersion and non-linear effects
Supports need for optical monitoring
Could be applied at key monitoring points
  Future inclusion in NEs is
  technically possible, but is
  not intended at present

## Slide 34: Possible Discussion Topics
Performance model for ASON/IP client interactions
  Interfaces, reference events, functions, parameters
  service classes, Service Level Agreements (SLAs)
  Are the performance needs of IP and Ethernet different?
Allocation of performance limits among Providers
Performance monitoring (in- and out-of-service)
Mechanisms for providing assured-quality services
Localization of optical network failures

## Slide 35
Thank you. Come surf the optical wave !
OTN Standards in ITU-T