## Slide 1: Network Performance (IP/Optical) IP/Optical Performance Management
Prepared For:
ITU-T Workshop On IP/Optical
Chitose, Japan, 9-11 July 2002
Tobey Trygar
ttrygar@telcordia.com
+1 732 758-5399

## Slide 2: Outline
Definitions and Classifications
Networks and Technologies
Optical Transport Network (OTN), Layers and Interfaces
OTN Performance Parameters
OTN Client Signals
Automatic Switched Optical Network (ASON)
ASON Signalling
IP As ASON Client
IP/OTN Performance

## Slide 3: Performance Management
Per X.700, Performance Management enables the behaviour of resources in the network and the effectiveness of communications activities to be evaluated. This entails:
  Collecting statistical information,
  Maintaining and analyzing logs of system state histories,
  Determining system performance under natural and artificial conditions,
  Altering the modes of system operation to conduct performance management activities.
This presentation considers performance management topics from the optical transport network and the IP network layer.

## Slide 4: Trouble Event Taxonomy
Trouble Events
Non-Alarmed
Defects
Anomalies
Fault Event
Alarmed
Critical
Major
Minor
Performance Event
Warning

## Slide 5: Physical Network Topology
Collector
Ring
HUB
CO
CO
CO
Metro Network
HUB
CO
HUB
CO
HUB
CO
O
N
U
xDSL
xDSL
LAN
IP, GbE
Business
Access
Ring
Access
Inter-Office Facilities
DSLAM
DLC
DLC
CO
VIP
VIP
POS
ONT
ONT
•••
PON
ADM
Core Network
ISP
ISP
CO = Central Office
DLC = Digital Loop Carrier
DSLAM = DSL Access Multiplexer
ISP = Internet Service Provider
ONU = Optical Network Unit
ONT = Optical Network Termination
POS = Passive Optical Splitter
PON = Passive Optical Network
VIP = Video Information Provider

## Slide 6: Taxonomy Of Physical IP And Optical Networks
Enterprise
Access
Access
Metro
Core
Layer 3
Layer 2
Physical
Metro WDM
Long Haul
DWDM
ULH
DWDM
Core
OXC
Grooming
OXC
Core Routers
MPLS/ATM/FR
Core Switches
Edge/Aggregation Routers
Aggregation/Distribution
Networks
Regional
Networks
Residential
Access
MSPP/RPR
Core OADM
Metro/Regional
OADM
GbE/ATM/MPLS
Access Switches
MSPP = Multi-service Provisioning Platform
OADM = Optical Add-drop Multiplexer
OXC = Optical Cross-connect
RPR = Resilient Packet Ring
ULH = Ultra-long Haul

## Slide 7: The Optical Transport Network
The Optical Transport Network (OTN)
  Is specified primarily in G.872, G.707, G.798, G.9591, and G.874,
  Is currently limited to the transport of digital signals
  Provides transport, multiplexing, routing, supervision and survivability of client signals
It is composed of the following digital layers:
  Optical Channel Data Unit (ODU), Path and Tandem Connection
  Optical Channel Transport Unit (OTU)
It is composed of the following photonic layers:
  Optical Channel (OCh) Layer, OCh Reduced (OChr)
  Optical Multiplex Section (OMS) Layer
  Optical Transmission Section (OTS) Layer
  Optical Physical Section (OPS) Layer

## Slide 8: OTN Survivability Mechanisms
The two fundamental survivability mechanisms supported in the OTN are protection and restoration schemes.
Protection schemes are:
  Autonomous and make use of pre-established backup resources
  Optical Multiplex Section (OMS) resilience - all channels in a fiber (or fiber bundle) protected as a whole,
  Optical Channel (OCh) resilience - each optical channel is protected individually.
Restoration schemes are:
  Reactive and make use of dynamically identified backup,
  Management system or signalling system based,
  Require network state information.

## Slide 9: Structure Of The OTN Interfaces
OMSn
OTSn
Full Functionality
OCh
OTU-V
OTU-V
OTU
ODU
Clients (e.g. STM-N, ATM, GFP, Ethernet)
Optical Channel Payload Unit
ODU-P
ODU-T
OPSn
Reduced Functionality
OChr
OCh
Substructure
OTU
ODU = Optical Channel Data Unit
OTU = Optical Channel Transport Unit
Och = Optical Channel
OMS = Optical Multiplex Section
OTS = Optical Transmission Section
OPS = Optical Physical Section

## Slide 10: Physical View Of A Linear OTN
ODU
OCh/OTU
OCh/OTU
OTS
OMS
OMS
OMS
OTS
OTS
OTS
OTS
OTN Client Signal
OTN Client Signal
ONE
ONE
ONE
ONE
ONE
ONE
Physical
Layer
Physical
Layer
Physical
Layer
Physical
Layer
Physical
Layer
Physical
Layer
OTS Termination
OTS Termination
OTS Termination
OTS Termination
OTS Termination
OTS Termination
OMS Termination
OMS Termination
OMS Termination
OMS Termination
OCh/OTU
Termination
OCh/OTU
Termination
OCh/OTU
Termination
ODU
Termination
ODU
Termination
ONE = Optical Network Element

## Slide 11: Fundamental Performance Parameters
Physical Media
Layer Network
Measurement
Apparatus
Analog
Parameters
Digital Parameters
Background Block Errors
Performance Threshold
Dispersion
OSNR
Power
Jitter
Q

SNR
Bit rate
X-talk
NL Distortion
Ext. Ratio
Chirp
Protocol
Mod Format
Phase
OSA
Wavemeter
Rx
DSP
Power Meter
BERT
Other
OTN Client
Layer Network

## Slide 12: IP Over OTN
ATM
HDLC
Ethernet MAC
RPR MAC
10GbE
LAN PHY
10GbE
WAN PHY
GFP
SONET / SDH
G.709 OCh digital wrapper/ optical channel
Optical fibre / G.652, G.653 etc.
IEEE 802.2 LLC
PPP
AAL5
GbE
PHY
IEEE 802.2 LLC
RPR PHY
IP

## Slide 13: ASON Architectural Components
LN1
LN2
LN3
Control Plane
LN1
LN2
LN3
Transport Plane
Management Plane
Data Communications Network

## Slide 14: Distributed Connection Management Reference Model
ARA – A-end requester agent
AUSN – A-end user sub-network
ZRA – Z-end requester agent
ZUSN – Z-end user sub-network
ASC-1 – A-end sub-network controller – domain 1 (CC)
ANSN-1 – A-end network sub-network – domain 1
ISC-1 – Intermediate sub-network controller – domain 1 (CC)
INSN-1 – Intermediate network sub-network – domain 1
ZSC-1 – Z-end sub-network controller – domain 1 (CC)
ZNSN-1 – Z-end network sub-network – domain 1
ASC-n – A-end sub-network controller – domain n (CC)
ANSN-n – A-end network sub-network – domain n
ZSC-n – Z-end sub-network controller – domain n (CC)
ZNSN-n – Z-end network sub-network – domain n
AUSN
ARA
ZRA
ZUSN
ASC-1
ANSN-1
ZSC-1
ZNSN-1
ASC-n
ANSN-n
ZSC-n
ZNSN-n
ISC-1
INSN-1
Domain 1
Domain n
UNI
I-NNI
E-NNI

## Slide 15: Connections Types And Policy Attributes For ASON Signalling
UNI = User Network Interface
E-NNI = External Network Node Interface
I-NNI = Internal Network Node Interface

## Slide 16: IP/OTN Performance
Both technologies support unique performance mechanisms with IP predominately uni-directional and OTN bi-directional.
Depending on the OTN survivability mechanisms, the IP layer may assume OTN performance to be predictable.
Survivability speeds within the OTN may interact with IP routing convergence.
IP routers as ASON clients, may change OTN performance characteristics, e.g., error rates, bandwidth, and link creation.
To provide support for an Emergency Service per E.106, F.706 and Y.roec, special consideration must be given to the IP - OTN interactions.
End-to-end IP client performance will require consideration of both the IP layer and the OTN layers.

## Slide 17: References
E.106, Description of an International Emergency Preference Scheme (IEPS)
F.706, (Draft), International Emergency Multimedia Service
G.709, Network Node Interface For The Optical Transport Network (OTN)
G.798, Characteristics of Optical Transport Network Hierarchy Equipment Functional Blocks
G.805, Generic Functional Architecture Of Transport Networks
G.806, Characteristics of Transport Equipment - Description Methodology and Generic Functionality
G.872, Architecture Of Optical Transport Networks
G.874, Management Aspects Of Optical Transport Network Elements
G.959.1, Optical Transport Network Physical Layer Interfaces
G.7041, Generic Framing Procedure
G.7710, Common Equipment Management Function Requirements
G.7712, Architecture And Specification Of Data Communication Network

## Slide 18: References
G.7713, Distributed Call and Connection Management
G.7713.1 (Draft), Distributed Call and Connection Management (DCM) Based on PNNI
G.7713.2 (Draft), DCM Signalling Mechanism Using GMPLS RSVP-TE
G.7713.3 (Draft), Distributed Call and Connection Management Signalling Using GMPLS CR-LDP
G.8080, Architecture for the Automatic Switched Optical Network (ASON)
M.20, Maintenance Philosophy for Telecommunications Networks
M.3010, Principles For A Telecommunications Management Network
X.700, Management Framework for Open Systems Interconnection (OSI) for CCITT Applications
Y.roec, (Draft), Framework(s) on Network Requirements and Capabilities to Support Emergency Communications Over Evolving Circuit Switched and Packet Switched Networks