## Slide 1: Data over Transport with ASON Session 12 – Optical Network Clients and Services
Presented by: Stephen Shew
Date: 2002 07 11
Notes: Abstract:
In response to an increasing amount of data traffic in transport networks, a new set of capabilities has been standardized in transport technology that address the needs of packet traffic. There are two broad categories of these capabilities: packet adaptations, and transport bearer flexibility. Packet adaptation capabilities include 10GE WAN (IEEE 802.3ae), and Generic Framing Procedure. In the transport network new flexible capabilities include virtual concatenation and link capacity adjustment scheme (LCAS). The combination of the packet adaptations with flexible transport offers benefits to both packet clients and transport network efficiency.
ASON describes a control plane architecture that enables dynamic connection setup, release, and maintainance in transport networks. Further recommendations in progress are developing protocols compliant with the ASON architecture.This paper describes the enhancements an ASON control plane could bring to the new data over transport capabilities. These include interaction with LCAS control, management of virtually concatenated connections, and enabling of packet adaptation interworking service. IP/Optical services are a key beneficiary of this interaction.

## Slide 2: Outline
Optimization of Transport for Data
New Standardized Capabilities
ASON Architecture
Enhanced Services with ASON

## Slide 3: Optimization of Transport for Data
Bandwidth Granularity Issues
  Ethernet rates are 10 Mbit/s, 100 Mbit/s, 1Gbit/s, 10Gbit/s
  Common private line rates are:
    North America DS-1 (1.5M), DS-3 (45M),
    Europe, E1 (2M) E4 (140M)
    Global, OC-3/STM-1 (150M), STM-4 (600M), STM-16 (2.5G)
Other Issues in WAN Data Transport
  Frame Relay does not scale to higher speeds (DS3)
  Proprietary solutions not interoperable
Need for more efficient transport of data traffic (packet) in SONET/SDH and OTN networks.
Notes: Ethernet is a PHY and a service (MAC frames). Supporting Ethernet service in an optical network is a problem because the Ethernet PHY rates don’t match transport service rates very well. The growing desire for Ethernet services over transport networks makes this a more pressing problem.

## Slide 4: New Standardized Capabilities
Bandwidth Granularity Issues addressed by:
  Virtual Concatenation (VCat) [1]
    Provides flexible channel capacities in transport networks
    Defined for SONET/SDH and OTN.
  Link Capacity Adjustment Scheme (LCAS) [2]
    Procedures that enable concatenated payloads to be changed dynamically and non-disruptively.
    Builds on Virtual Concatenation capabilities.
Generic Framing Procedure (GFP) [3] to replace proprietary mappings
  Simple and robust encapsulation method for packet traffic
  Standardized mappings to SONET/SDH and OTN.
  Reduces need for diversity of mappings
VCat+LCAS+GFP = New transport plane capabilities
Notes: The units of granularity needed for data traffic include Ethernet, Fiber Channel, and storage network protocols like ESCON.
GFP is more efficient mapping than ATM and more robust than POS.

## Slide 5: Bandwidth Granularity Example
Table 2 from [6]
VC-3
VC-3
100Mbit/s
Notes: Virtual concatenation allows fine bandwidth granularity that minimizes stranded transport bandwidth for clients whose native rates don’t match classical transport network path capacities. Virtual concatenation creates synchronous payloads of flexible sizes using SONET/SDH standard payload sizes. In effect, it is inverse multiplexing.
For this example, sizes are (from [6]):
VC-12 = 2.176 Mbit/s
VC-3 = 48.384 Mbit/s
VC-4 = 149.760 Mbit/s
VC-4-4c = 599.040 Mbit/s
VC-4-16c = 2,396.160 Mbit/s
VC-4-64c = 9,584.640 Mbit/s
Another example is ESCON which at 160Mbit/s can be carried in a VC-4-4c at 27% efficiency or VC-3-4v at 83% efficiency.

## Slide 6: VCat +LCAS+GFP Example
VC-3
50 Mbit/s
100 Mbit/s Ethernet PHY
50Mbit/s MAC service
GFP Mapping to SDH
Virtual Concatenation
Independent paths
VC-3
VC-3
100 Mbit/s Ethernet PHY
100 Mbit/s
Resize to 100Mbit/s MAC service
Setup 2nd VC-3
LCAS signalling to add to Virtual Concatenation Group
Notes: GFP reduces the need for a variety of existing mappings (ATM, POS, proprietary). It can be used for PDU oriented signals like IP/PPP or Ethernet MAC frames, as well as block-code oriented constant bit rate streams like Fibre Channel.
The Link Capacity Adjustment Scheme (LCAS) provides a way to add or subtract members to or from a Virtually Concatenated Group (VCG) without introducing errors. LCAS uses STS Path / OTN ODUk overhead to convey the messages required to co-ordinate these changes. When the capabilities of the Link Capacity Adjustment Scheme (LCAS) are added to Virtual Concatenation, the possibility of dynamic, hitless bandwidth adjustment is introduced. LCAS is part of the Data Plane and not part of the Control Plane. LCAS cannot initiate requests for VCG changes, it simply co-ordinates the response such that the requested changes do not disrupt the client traffic

## Slide 7: How to Manage the Service?
Desirable to match more dynamic timeframes for packet volume changes.
Resizing bandwidth of packet service bounded by:
  Time required for bandwidth service change request process.
  Time required for connection management
  Time required for LCAS & GFP configuration.
Leverage ASON to control new transport plane capabilities
Notes: Traffic flow in IP networks is difficult to engineer. It is accomplished with topology modification and other traffic engineering techniques such as MultiProtocol Label Switching (MPLS). The frequency of topology change can be in the order of every several days (e.g., bandwidth addition). In contrast, creation of private lines in transport networks can take weeks. Improving the speed of private line deployment will make the transport network more responsive to IP network topology needs.

## Slide 8: Switched Optical Networks - ASON [4]
A switched optical network is an optical network (e.g., SDH, OTN, WDM) in which connections can be created using switching control technology.
ASON describes that control plane
Call Request
Connection Request
Call Accept
Call Accept
Connection Indication
Notes: G.8080 is the ASON architecture document that follows from the requirements of G.807. Extending G.805 constructs, the ASON architecture describes the relationship between the control plane and the transport plane, what the components of the control plane are, and the relationship between those components.
Operational and business boundaries can be realized from the UNI, INNI and ENNI reference points described in G.8080

## Slide 9: ASON Call/Connection Components
B
Connection End Point
NE
NE
NE
Control Plane
A
Connection End Point
Connection Request
Connection Request
UNI
UNI
Setup Request
Setup Request
Setup Request
Call Ctl
Connection Ctl
Call Ctl
Connection Ctl
Transport Plane
Call/Connection Separation  multiple connections per call
Notes: A call is a relationship between parties that enables the negotiation, maintenance, monitoring, and accounting of their communication. In G.8080 and other connection oriented service architectures (e.g., Q.2931 and Q.2982), a call has an association with zero or more connections. Each connection is a means of traffic transfer between the parties involved in the same call.
A typical transport service involving 1+1 protection from an ingress line side to an egress line side fits well into this model. Here one call contains two connections and those connections are visible only to the network, not the users.

## Slide 10: ASON+VCat+LCAS+GFP
Current transport service has:
  Fixed sized trails
  Multiple adaptations
  Protection: all or none
ASON+VCat+LCAS+GFP has:
  Flexible sized trails
  Streamlined adaptations
  Protection: range of services
ASON Control Plane
UNI
Static
Dynamic
Mgmt Plane
POS
Eth
ATM
FR
FC
Energizing Transport Transformation:
  ASON
  Virtual Concatenation
  LCAS
  GFP
Transport Service Reality: Diversity
Multiplicity of Adaptations
Dedicated, Static, Coarse Pipes
Shareable, Flexible, Fine-grain Pipes
POS
Eth
ATM
FR
FC
Streamlined Adaptation
Dealing with Diversity
Transport Network Pre/Post Transformation

## Slide 11: Transforming Packet Service
Automate setup/take-down of right-sized layer 1 pipes.
  Not bound to SONET/SDH interface rates
Automate resizing of pipes.
  E.g., provide flexibility in layer 1 pipes to better match packet traffic variation (day-of-week, time-of-day).
Efficient protection schemes
  E.g., two unprotected diverse paths that are virtually concatenated. When one fails, the service throughput falls in half.
  E.g., load-spreading with pruning of failed members.
Packet friendly transport services are applicable to a multiplicity of packet clients including ATM, IP, FR, FC
Simplify/enhance packet-friendly transport for real-world service diversity.

## Slide 12: ASON Interaction
POS
Eth
ATM
FR
FC
Call Request from packet client received over UNI.
ASON selects GFP mapping, sets up paths in VCat Group (VCG), service starts.
Client requests change via UNI.
ASON adds/removes paths, triggers LCAS to add/remove from VCG.
  This changes the number of connections associated with the single call.
ASON Control Plane
Transport Plane
LCAS
Call Ctl
Connection Ctl
VCat
L1 Adaptation
UNI
POS
Eth
ATM
FR
FC
Notes: UNI-N Call Controller can select adaptation e.g., GFP-T for FC, GFP-F for Ethernet.
UNI could signal change in call parameters. E.g., change in bandwidth.
Call Controller in UNI-N adds/removes connections.
Connection Controllers are told to make connection changes. Connections can be independently routed from each other.
When connections are in place, Call Controller triggers hitless addition/removal of members via LCAS.
LCAS adds/removes members to/from virtual concatenation group.
LCAS awareness not required at intermediate NEs (protocol operates end to end).
Connection Controllers are aware of individual members, not aggregate.

## Slide 13: ASON+VCat +LCAS+GFP Example
50 Mbit/s
VC-3
VC-3
100 Mbit/s Ethernet PHY
100 Mbit/s
Control Plane
Call Ctl
Connection Ctl
UNI Call modification request
Trigger LCAS to add connection to VCG
Signalling new VC-3 path
Connection confirmation
Single call now has two connections associated with it

## Slide 14: Ethernet Protected Private Line Example
Service Characteristics
  MAC service offered to client over ASON UNI with Ethernet PHY.
  MAC bit rate requested up to Ethernet PHY rate.
  If there is a failure in the network, MAC service bit rate will be reduced in half. Service is revertive on recovery.
Network Solution
  Single Ethernet port mapped via T-GFP or F-GFP into a VCG. VCG members (route A and B) can be diversely routed.
  Client call request received over ASON UNI.
  Call Controller invokes Connection Control for each diverse route.
  Two paths combined into same Virtual Concatenation Group (VCG).
  Traffic can be shifted using LCAS to accommodate failure of either path.
  After restoration of failed route, it can be added back to the VCG using, and traffic added hitlessly.
Notes: In the case that both SDH paths are functioning and one fails, there will be a traffic hit due to a sudden drop in bandwidth. LCAS will shift all traffic to the remaining link. LCAS is needed in this case to inform a traffic sending end that a failure occurred.

## Slide 15: Multiple VCG Example
Multiple VCGs could be used to support a single packet service instance.
  Each VCG would follow same equipment path
  ASON Call Control tracks VCG members
Transport Plane
GFP Adaptation
UNI
Eth
LCAS
ASON Control Plane
Call Ctl
Connection Ctl
VCG 1 - path A
VCG 2 - path B

## Slide 16: Conclusion
VCat+LCAS+GFP = flexible transport capabilities for data traffic.
Service management of VCat+LCAS+GFP can benefit from a control plane (esp. timescales).
ASON control plane for VCat+LCAS+GFP
  Adds value to service management.
  Architecture fits with multiple connections per call.
  Enables range of protection services.

## Slide 17: Acknowledgements
Material originally developed by Tim Armstrong (Nortel Networks) was used in this presentation.

## Slide 18: References
ITU-T Rec. G.707, Network Node Interface for the Synchronous Digital Hierarchy, Oct. 2000
ITU-T Rec. G.7041/Y.1303, Generic Framing Procedure (GFP), Dec. 2001
ITU-T Rec. G.7042/Y.1305, Link Capacity Adjustment Scheme (LCAS) for Virtually Concatenated Signals, Nov. 2001
ITU-T Rec. G.8080/Y.1304, Architecture for the Automatically Switched Optical Network (ASON)
P. Bonefant, A. Rodriguez-Moral, “Generic Framing Procedure, the Catalyst for Efficient Data over Transport”, IEEE Comm. Magazine, May 2002.
N. Jones, C. Murton, “Extending Point-to-Point Protocol (PPP) over Synchronous Optical Network/Synchronous Digital Hierarchy (SONET/SDH) with virtual concatenation, high order and low order payloads”, IETF RFC 3255, April 2002