## Slide 1: Carrier Motivations and Requirements for Automatically Switched Optical Network (ASON) by Wesam Alanqar and Tammy Ferris ITU-T Workshop IP/Optical (Chitose, Japan, 9-11 July 2002)

## Slide 2: Abstract
This paper discusses business motivations and network requirements for automatically switched optical networks from a service provider perspective. The paper identifies potential automatically switched optical network services, identifies optical network functions needed to support those services, and compares advantages of control vs. management planes for overlapping functions. Different migration scenarios from legacy management systems to optical control planes will be addressed taking into consideration the implications per deployment scenario.

## Slide 3: Overview
Business Motivations for ASON Deployment
Optical Network Functions Needed
Management vs. Control Plane
Possible Deployment Scenarios
ASON Challenges and Future Research Areas
Summary

## Slide 4: Business Motivations for ASON Deployment New Services
Differentiated Private Line SLAs
  Additional Protection/Restoration Mechanisms
Bandwidth on Demand
  Long-term Coarse Grained Pipes for Average Steady State Bandwidth
  Short-term Finer Grained Pipes for Hitless Bandwidth Adjustment
    Charging customers sooner for the service
    Increase customer satisfaction
Partitioned Network Management View
  More Configuration Flexibility
    Closed membership
    Additional security
    O-VPN standardization under study in IETF and ITU

## Slide 5: Business Motivations for ASON Deployment Cost Savings and Improved Operations
Reduce Current Operations Cost
  Reuse of Protocols at Different Layers
  Common Terminology
  Interface Integration Across Layers
  Packet Network and Circuit Network Integration
Improved Network Utilization
  Shared Protection Paths Using Mesh Architectures
  Opportunity for Concentration
Near Real-time Self Healing Capability Within Layer
  Occurrence of Fault
    Need for SLA manager to prioritize restoration of service
  Recovery from Fault

## Slide 6: Optical Network Functions Needed Automatic Switching Functions
Call Processing
  Allows Multiple Connections Per Call
  Allows Calls with No Connections (e.g., short lived condition for restoration)
  Connection Modifications without Call Tearing Down (e.g., equipment protection)
Routing and Link Management
  Need for Constraint Shortest Path First (CSPF) Paths
  Rapid Convergence of Network Topology Updates
  Isolation of Topology or Resources Across Routing Areas
  Link State Aggregation
Connection Processing
  Management and Supervision of Connection:
    Set-ups, Releases, and Modifications of Parameters for Existing Connections

## Slide 7: Optical Network Functions Needed Administrative Functions
Fault Management
  Fault Isolation & Localization
  Link Connectivity Verification
Address Configuration
  Scalable Naming and Addressing Scheme
  Addressing Independence
  Provisionable Addressing
Traffic Management
  Race limit (or pace) call and connection setup attempts into the network
  Load balance across call and connection processes
    Dual homed scenario for call processors
    Alternate connection paths for connection processors
  Record call/connection setup attempts and blockages, and usage
    Data made available to management plane for analysis and long term storage

## Slide 8: Optical Network Functions Needed Resiliency
Integrity and Reliability of Control Plane
  Reliable Message Transfer of Optical Control Plane Messages
  Control Plane Link Failure Capabilities
  Control Plane Node and Node Component Failure Capabilities
    Node Component is a field replaceable software or hardware entity
Protection of Data Plane Connections
  Protection Options
    1+1, 1:n, no protection
    Revertive and non-revertive
  Protection Route Selection Options
    Least cost, least delay, greatest diversity, alternate destination

## Slide 9: Optical Network Functions Needed Security
Admission Control
  Authentication of Client, Verification of Services, and Control of Access to Network Resources
    Carrier E-NNI, I-NNI, UNI policies related to the above may vary
Prevention of Misconnection
  For Data Plane Security
    It may be helpful to support scrambling of data at layer 2 or encryption of data at a higher layer.
  In the Event of Restoration
    Event sequencing may be required.
Reporting of Security Violations
  Generation of Alarm Notifications about Security Related Events
    Ability to send to the management plane in an adjustable and selectable fashion

## Slide 10: Optical Network Functions Needed Other Supporting Functions
Auto Discovery
  Allows Peer Communication of Relationships
  Allows Peers to Communicate Capabilities and Provisioning Information
  Allows Peer Validation of Connectivity
    Test connections not be used for new data connections.
    Degree of validation required will vary
      Integrity of information provided by the transport plane
      Integrity of information provided by the management plane
      Integrity of the processes used to establish relationships

## Slide 11: Management vs. Control Plane
Control Plane Introduces Notion of a Call to an Optical Network
Control Plane May Add Need for Call Records
  Information Necessary for Billing
Control Plane Adds Need for Demand and Capacity Statistics
  Demand Statistics
    Usage provides aggregate usage information
    Attempts provides aggregate call attempts
    Blockages provides aggregate call blockages
  Capacity Statistics
    Capacity (available, used or under maintenance)
Other CP Functions Redundant with MP Functions
  Control Plane Offers an Alternative Approach with Emphasis Toward Maximum Functional Distribution
    Control plane functions can be contained in an NE
    Make neighbor NEs collaborative, communicating peers

## Slide 12: Possible Deployment Scenarios
Integration With Legacy Systems and Incomplete New Systems
    Also applies to incomplete or incompatible automatically switched systems
Allocation of Functions Between Control Plane and Management Plane
  Only Routing and Link Management Done via Management Plane
  Routing and Link Management, Call Processing, and Connection Processing All via Control Plane
Mix of Switched and Not Switched Within Different Transport Network Layers
  Client Layer Switched and Server Layer Not Switched
  Server Layer Switched and Client Layer Not Switched
Mix of Switched and Not Switched Within Transport Network Partitions
  UNI, E-NNI, I-NNI, Sub-networks
Combinations and Permutations of Above

## Slide 13: Possible Deployment Scenarios Integration With Legacy Systems and Incomplete New Systems
Management Based Solution with In-house Development
  Carrier-specific control plane
  Expensive to maintain under dynamic market business requirements
  Integration scope is broader (multiple complex interfaces required)
Provide a Thin Layer Above Multiple Vendor Control Domains
  Carrier-independent control plane
  Less expensive to maintain under dynamic market business requirements
  Integration scope is narrower (control-management interface required)
Control
Domain 1
Control
Domain 2
Control
Domain 3
Control Plane-Administrative Area
I-NNI ?
Carrier-independent integrated common control plane
Control-Management Interface
API
API
API
OSS-Management Plane
Administrative Area
I-NNI ?
Control
Domain 1
Control
Domain 2
Control
Domain 3
Control Plane-Administrative Area
I-NNI ?
Carriers-specific integrated control plane
API
API
API
OSS-Management Plane
Administrative Area
I-NNI ?
I-NNI ?: Possible no standardized multi-vendor control domains

## Slide 14: Possible Deployment Scenarios Mix of ASTN and Not ASTN Within Transport Network Partitions
Control
Domain 1
Optical Transport-Service Provider
OXC
OXC
OXC
OXC
Vendor
domain 1
Vendor
domain 2
Transport - Control Interface
Control-Management Interface
OSS-Management Plane
Administrative Area
Transport-Management Interface
One Domain ASTN, another Domain Not ASTN
Control Plane-Administrative Area

## Slide 15: Possible Deployment Scenarios Mix of ASON and Not ASON Within Transport Network Partitions
E-NNI Supported as Interface to other Providers, but not Fully Automatically Switched within Provider Network
    Control and management planes need to collaborate for E-NNI requested connections
    Routing and link management is done by the management plane
    E-NNI call / connection processing is done by the control plane
Optical Transport-Service Provider 2
OXC
OXC
OXC
OXC
Vendor
domain 1
Vendor
domain 2
Transport -Management Interface
OSS-Management Plane
Administrative Area
OSS-Management Plane
Administrative Area
Optical Transport-Service Provider 1
OXC
OXC
OXC
OXC
Vendor
domain 1
Vendor
domain 2
Transport -Management Interface
E-NNI
Control
Domain
Control
Domain
Administrative Area 1
Administrative Area 2
Management-Control Interface
Management-Control Interface

## Slide 16: ASON Challenges and Future Research Areas Per Functional Area
Automatic Switching
  Routing Optimality with Long Holding Time Connections
    Grooming of existing connections
    Large overhead of message processing when little or no changes to network
Administrative
  Role of Control Plane vs Management Plane
    Alarm filtering and root cause analysis and fault isolation
    Data replication and synchronization
Resiliency
  Signaling, Routing, and Link Management Message Storms
  Detection Of Dropped Calls
  Monitoring Call Performance when Connections are A Moving Target
Security
  Keeping the ASON DCN Secure
Other Supporting Functions
  Communicating Discovery Processes Need to be managed and scaleable
  Must Accept Input when no Automatic Discovery Between Peers

## Slide 17: ASON Challenges and Future Research Areas Vendor Interoperability
Control
Domain 1
Optical Transport-Service Provider 1
Optical Transport-Service Provider 2
OXC
OXC
OXC
OXC
OXC
OXC
OXC
OXC
OXC
OXC
OXC
OXC
ET-NNI
Vendor
domain 1
Vendor
domain 2
Vendor
domain 3
Vendor
domain 3
Vendor
domain 1
Vendor
domain 2
IT-NNI
DCS
ATM
ADM
Router
DCS
ATM
ADM
Router
O-UNI
EC -NNI
Control
Domain 2
Control
Domain 3
Control
Domain 1
Control
Domain 2
Control
Domain 3
IT-NNI
IT-NNI
IT-NNI
C C3
C C3
C C2
C C2
C C1
C C1
C C1
C C1
C C2
C C2
C C3
C C3
Third-Party or Sprint-Specific common control
Control-Management Interface
Control-Management Interface
OSS-Management Plane
Administrative Area 2
Control Plane-Administrative Area 2
OSS-Management Plane
Administrative Area 1
API
API
API
Control Plane-Administrative Area 1
All management interfaces not even shown
I-NNI ?
I-NNI ?
I-NNI
I-NNI
I-NNI ?: Possible no standardized multi-vendor control domains

## Slide 18: Summary
Historical Industry Expressed Need for ASON
  Enhanced Support of Packet Services (e.g., IP, ATM, FR)
    Harmony between demand and capacity
  Improved “Provisioning Speeds” over Management Systems (I.e. increased dynamicity of a connection)
    Introduces call concept to optical network
Assumptions
  Available Network Capacity Can be More Efficiently Utilized
    Dynamic control mechanism
  At Least Some Connections Have Short Hold Times
Value Propositions for ASON
  Combination of NNI and UNI for New Services
  NNI for Cost Savings
    Trunk lines (NNI) became automatically switched before access lines (UNI)
    A desire to find ways to best utilize optical networks

## Slide 19: Summary: Packet & Optical Convergence Example Future Integrated Network
Overlay “Layered” model is the best fit for: transport layer and packet layer in different business units, topology isolation, security, scalability, upgradeable , and interoperability
MPLS can be used in forwarding & control planes
Forwarding: Tunneling L2 cells/frames into MPLS labels
Control: GMPLS or other control plane
O-UNI between packet and transport layers and O-NNI within the transport layer
Fiber
Optical Transport
MPLS
T
D
M
A
T
M
I
P
V
O
I
C
E
F
R
Possible Layered
Approach
Optical
Switch
Optical
Switch
Optical
Switch
O-UNI
O-UNI
IP
Sprint LD
O-NNI
A
S
O
N
Packet layer
Converged network
Interfaces are (SONET,SDH, or OTN) framed
G
M
P
L
S