## Slide 1: ITU-T Solutions Session 2 – Switched Optical Networks
Presented by: Stephen Shew
Date: 2002 07 09

## Slide 2: Outline
Switched optical network definition
Impact on Current Architecture
Role of ITU-T in switched optical networks
ITU-T Solution Framework
  Architecture and Requirements
  Protocols

## Slide 3: Switched Optical Networks
A switched optical network is an optical network (e.g., SDH, OTN, WDM) in which connections can be created using switching control technology.
Call Request
Connection Request
Call Accept
Call Accept
Connection Indication
Notes: A user makes a call request over a UNI to the network. Processing of the call request includes determining where the destination of the call and initiating a connection to that destination. The call is usually carried in the connection setup procedure. At the destination UNI, the call request is forwarded to the destination user. If accepted, the connection is completed including a notification to the source user.

## Slide 4: Relationship to Current Architecture
A control plane is introduced with a switched optical network to gain many improvements.
The control plane alters the relationship between the following planes:
  Network Management Plane
  Transport Plane
Control plane communication uses the Data Communication Network (DCN)
Functional changes for the Control Plane
  Some functions move from the Network Management Plane to the Control Plane.
  New functions are needed in the Transport Plane.
  Use of DCN for communications within the Control Plane
Notes: Switched optical networks utilize a control plane to establish and teardown connections. The control plane is configured and managed by applications in the network management plane. It also directly interacts with the transport (data) plane to manage connections. Calls are maintained by control plane and are used as a demarcation of the service between the user and network.
Components within a control plane communicate over the DCN. This is in addition to network management use of the DCN.
To enable routing in the control plane, a discovery function is required in the transport plane to learn of the association between subnetworks that are connected by common link resources.

## Slide 5: Relationship to Current Architecture
LN3
LN2
LN1
Transport Plane
Management Plane
Control Plane
Data Communication Network
Service
Management
Billing
Maintenance
Connection
Management
Routing
Connection
Management
Routing
Autodiscovery

## Slide 6: Role of ITU-T
Main body progressing standards related to transport and optical networks.
  “Study Group 15 is the focal point in ITU-T for studies on optical and other transport networks, systems and equipment. This encompasses the development of transmission layer related standards for the access, metropolitan and long haul sections of communication networks.”
ITU-T Role for Switched Optical Networks
  Develop standards for what a switched optical network should do and specifications for how interoperable networks can be built/deployed.
  Build on existing transport and optical standards, and understanding of optical technology and service.
Standards for service and technology evolution

## Slide 7: ITU-T Solution Framework
Requirements
Architecture
Protocols
Network Management
Notes: ITU-T recommendations have proceeded from broad requirements to comprehensive architecture, and is now developing protocol specifications compliant with detailed requirements and architecture.

## Slide 8: Why not just re-use PSTN, ATM, or GMPLS?
Valuable precedents but …
Transport is different in many ways including:
  Resources are much more expensive
  Network is not over engineered
  Traffic plane is separated from control and management planes
  Traffic needs vary from connection to connection
  Obtaining connectivity and usage views is difficult
Transport Services have distinct requirements including:
  Protection and restoration
  Importance of connection relative to control functions
There is no layer beneath the physical layers!
Notes: Existing (telephony, ATM) and new (GMPLS) connection oriented services have developed their own protocols. These provide useful lessons in the development of switched optical services. They cannot be reused completely as there are some unique aspects of optical services.
Unlike telephony, the transport network has varying granularities (e.g., STM-1, STM64) and layers (e.g., VC3, STM-1).
Unlike ATM, the transport network has fixed bandwidth services only with no equivalent to ATM UBR or VBR.
Unlike GMPLS, transport services need to be offered in a call model with public addresses (a public switched service vs an enterprise connection service).
In transport services, once a connection is established and the service enabled, control functions are secondary in importance to the connection. Control functions such as the DCN could change state (e.g., degrade or fail) without affecting the connection.

## Slide 9: Requirements
G.807/Y.1301 “Requirements for the Automatic Switched Transport Network”
  Network level requirements for the Control Plane
  Describes functions for switched services – establishment, teardown, maintenance
Requirements categories
  Connection services, Connection control
  Reference points (UNI, INNI, ENNI)
  Routing, Connection Admission Control
  Naming and Addressing
  Signalling network
  Resource Management
  Support for Transport Network Survivability
Evolving leased line services with control functions
Notes: G.807 specifies the high level requirements for a switched optical network and was consented May 2001. Services such as switched connections and soft permanent connections are described.

## Slide 10: Switched Connection Example
Fig. 2/G.807
B
Connection End Point
NE
NE
NE
Switched Connection
Transport Plane
Control Plane
A
Connection End Point
Connection Request
Connection Request
UNI
UNI
Setup Request
Setup Request
Setup Request
Notes: In G.807, it is required that a control plane for the transport network be able to accept a call/connection request and then interact with the transport network to set it a connection.

## Slide 11: Architecture - ASON
G.8080/Y.1304 “Architecture of the Automatically Switched Optical Network”
  Reference architecture for switched optical networks that supports G.807.
  “Describes the set of control plane components that are used to manipulate transport network resources in order to provide the functionality of setting up, maintaining, and releasing connections”.
  Develops G.805 (Generic Functional Architecture of Transport Networks) constructs for routing function in switched optical networks.
  Is applicable to all layer networks including SDH and OTN (G.709).
Key Advancements
  Describes for the first time the relationship between a transport subnetwork and control plane artifacts like a routing domain.
  A transport centric view of the control plane components that are described terms of subnetwork points (which represent G.805 control points).
  Defines control plane components that can follow the G.805 recursive subnetwork definition.
Notes: G.8080 is the ASON architecture document that follows from the requirements of G.807. Extending G.805 constructs, the ASON architecture describes the relationship between the control plane and the transport plane, what the components of the control plane are, and the relationship between those components.
Operational and business boundaries can be realized from the UNI, INNI and ENNI reference points described in G.8080.
As an architecture, ASON does not impose a particular distribution of functions into equipment nor does it specify protocols that accomplish those functions.

## Slide 12: Architecture – Subnetwork Organization
Adaptation  multiple layer
layer
CTP organization
SNPP organization
Routing areas
Partitioned CTPs  VPNs
Single layer network
SNPP organization  subnetworks
Notes: G.8080 defines SNPPs to be pools of SNPs. These are the resources between subnetworks and are commonly known as links/trunks. G.805 subnetworks are defined by how SNPs are organized and G.8080 follows this definition.
Within the same layer network, subnetworks can be partitioned recursively. The control plane can follow this subdivision by dividing the routing function into routing areas that may also be organized into hierarchical levels. Subnetworks can also be separated from one another in which case there are distinct routing domains that may not interact. This is a flexible private network (or VPN) concept.
SNP – Subnetwork Point, from G.8080 “The SNP is an abstraction that represents an actual or potential underlying CP (or CTP) or an actual or potential TCP (or TTP). Several SNPs (in different subnetwork partitions) may represent the same TCP or CP.”
SNPP – Subnetwork Point Pool, from G.8080 “A set of subnetwork points that are grouped together for the purposes of routing. An SNP pool has a strong relationship to Link Ends (See Recommendation G.852.2)”
CP – Connection Point, from G.8080 “For the purposes of this Recommendation, a Connection Point represents the North input port of an Adaptation function”
TCP – Termination Connection Point, from G.8080 “… a Termination Connection Point represents the output of a Trail Termination function or the input to a trail termination sink function”
CTP – Connection Termination Point, from G.8080 “See Recommendation M3100, amendment 1. A connection Termination point represents the signal state at the CP”

## Slide 13: Architecture – Components
From contribution D.348 Q12/15
(PDP)
UNI
NNI
NMI
(PEP)
CCI
Calling Party
Call Controller
Called Party
Call Controller
Protocol
Controller
Network
Call Controller
Protocol
Controller
Directory
Manager
Policy
Manager
OSS
Connection
Controller
Routing
Controller
Link Resource
Manager
NE Fabric
Controller
Protocol
Controller
Notes: Protocol Controllers are the protocol specific implementation of the abstract components. For example, communication over the UNI between a calling party call controller and a network call controller could be via a PNNI based UNI (G.7713.1).
The Connection Controller is responsible for establishing a connection in the network. It uses the services of the routing controller to determine a path.
Call Controllers are responsible for establishing a call between parties in the transport network. They invoke the Connection Controller to setup a connection or connections for a call.
PEP – Policy Enforcement Point
PDP – Policy Decision Point
CCI – Connection Control Interface
UNI – User Network Interface
NNI – Network Network Interface
NMI – Network Management Interface

## Slide 14: Architecture – Example Instance
Clients
e.g. IP, ATM, TDM
Clients
e.g. IP, ATM, TDM
OCC
OCC
OCC
CCI
NNI
UNI
ASON: Automatic Switched Optical Network
OCC: Optical Connection Controller
ENNI External network network interface
Interfaces:
UNI: User Network Interface
CCI: Connection Control Interface
NNI: ASON control Node Node Interface
User
signaling
ENNI
Inter
Carrier fibre
OCC
ASON control plane
Transport Network
Integrated
Management
Notes: In this example instantiation of a G.8080 network, the OCC contains the Network Call Controller, Connection Controller, Routing Controller, Link Resource Manager, and all associated Protocol Controllers. Functions within the OCCs co-operate to provide connection management and routing over the transport plane. This is a distributed instantiation of G.8080.

## Slide 15: Recommendation Framework
G.807/Y.1301
High level requirements
G.7713/Y.1704
G.7715/Y.1706
G.7712/Y.1703
G.7714/Y.1705
Detailed Requirements
G.8080/Y.1304
Architecture
Protocols
G.7713.1
G.7713.2
G.7713.3
G.7714.1
??

## Slide 16: Framework Details
Requirements & Architecture
  G.807 – Requirements for the Automatic Switched Transport Network
  G.8080 – Architecture for the Automatic Switched Optical Network
Detailed Requirements and Protocols
  G.7712 - Architecture and Specification of Data Communication Network
  G.7713 - Distributed Call and Connection Management
    G.7713.1 – PNNI based
    G.7713.2 – RSVP-TE based
    G.7713.3 – CR-LDP based
  G.7714 - Generalized Automatic Discovery Techniques
    G.7714.1 – Protocol for Automatic Discovery in SDH and OTN Networks
  G.7715 – Architecture and Requirements for the Automatically Switched Optical Network
    Substantial interest in starting a protocol specification

## Slide 17: Routing Architecture
G.7715 refines the architecture of routing and provides detailed requirements.
  G.7715 is protocol neutral.
  Independence of bearer topology from routing control topology.
  Enables subdivision of the network into routing areas, where areas can contain smaller areas. This creates routing levels.
  Adjacent routing levels may be implemented by different routing protocols.
  Path computation can encompass step-by-step, source, and hierarchical routing paradigms.
Influences from IP routing, telephony routing, ATM routing
Independence of routing function from established connections.
Notes: Multi-level hierarchies are defined in the G.7715 architecture. It is required that the routing protocol at a given level not be dependent on a routing protocol at another level. In other words, the same routing protocol is not required to be run at adjacent levels. A limited example this is concept is the use of BGP between IP networks that internally run OSPF.
Path computation is dependent on the information that the routing protocol learns and maintains. Different routing protocols have different degrees of information gathering.
Routing paradigms for path computation are seen in:
IP routing which has step-by-step
2. ATM PNNI which supports source routing and
3. Telephony routing which uses hierarchical routing
Connection management uses results from path computation to establish a connection. After the connection is in service, the routing function is no longer needed to maintain the connection. In fact, the routing function could terminate without effect on the connections in service. This differs from IP routing where the forwarding of packets using a shortest path method is always dependent on the functioning and integrity of the routing function.

## Slide 18: Routing Levels
Level 1
Level 2
Level 3
A
B
top
A.1
A.2
A.3
Step-by-step routing
Hierarchical routing
Source routing
Notes: Different routing paradigms may be present between levels. Information passed from lower to higher levels includes reachable addresses and topology (summarized subnetwork and link information).
In this example, the top routing area is subdivided into two areas, A and B. Routing area A is further subdivided into 3 areas. This forms three routing levels, all within the same layer network. It is possible to have different routing paradigms at each level.

## Slide 19: Protocols
Protocols are specific mechanisms that can be implemented to perform a function between two or more entities.
Protocols supporting switched optical networks include those for routing, connection management (signalling), and discovery.
SG15 working with other standards bodies in adapting their protocols for switched optical networks.
Protocols must conform to architecture and requirements

## Slide 20: Signalling Protocols
Connection Management function
  Currently a network management application
  Can be implemented in a signalling protocol
Detailed Requirements in G.7713 being instantiated in three protocols.
  G.7713.1 – PNNI based – ATM Forum
  G.7713.2 – GMPLS RSVP-TE based - IETF
  G.7713.3 – GMPLS CR-LDP based - IETF
Additions
  Soft Permanent Connection Support
  Call model, separation of call and connection
  Connection modification while maintaining a call
Notes: G.7713.1, G.7713.2, and G.7713.3 are recommendations in progress within Q14 of SG15.

## Slide 21: Signalling Example
From G.7713.3 – Distributed Call and Connection Management Using GMPLS CR-LDP
Message sequence for single call with two connections
UNI
NNI
NNI
UNI
Label Request
Label Request
Label Request
Label Mapping
Label Mapping
Label Mapping
Label Mapping
Notification
Notes: Here the call protocol is carried inside the connection control protocol. Two connections are being setup with the same call. This could be used for example to support a 1+1 path request. Each of the connections would be routed over a different set of NNIs (not shown) in order to be diverse.

## Slide 22: Routing and Signalling Example
Call Request
Connection Request
Call Accept
Connection Indication
Centralized RC with Source Routed Path Computation
NCC
CC
CC
CC
NCC
Call Accept
Notes: RC – routing controller
NCC – network call controller
CC – connection controller
Here the NCC receives a call request from a user. It requests a route from the path computation function in the routing controller (via the route query interface). Using the path obtained, the NCC makes a connection request to a connection controller. Both the call and the connection are progressed to the destination NCC. Upon acceptance from the destination user, the connection request is completed and the bearer path is established.

## Slide 23: Conclusion
ITU-T is developing standards for the switched optical network that:
Builds on existing layer network recommendations and service.
Understands requirements unique to transport networks.
Encompasses architecture and protocols.