## Slide 1
First-Mile Broadband Access:
Strategic Planning Meets Pragmatism in the Outside Plant
Or
An Expanded Role for Passive Optical Networks
Lowell D. Lamb, Director, PON Networks
Terawave Communications, Inc.
30680 Huntwood Avenue Hayward, Ca 94544 USA
+1 510 401 6532 (voice) +1 510 401 6511 (fax)
llamb@terawave.com

## Slide 2: Outline
 What Problem are We Trying to Solve?
Where are the Customers,
 or
What is an Access Network?
 How do We get There?

## Slide 3: What’s the Problem?
http://www.runco.com/Products/CWPlasma/CWDefault.htm
http://www.sandman.com/images/oldmonarchwall.jpg
Today’s
Customer Premises Equipment (CPE)
4 kHz 20 Mb/s
Tomorrow’s
Customer Premises Equipment (CPE)

## Slide 4: What are Broadband Services?
Original Bell System Definition
“A broadband channel is a communications channel having a bandwidth greater than a voice-grade channel, and therefore capable of higher-speed data transmission.”
1996 US Telecom Reform Act
Broadband services are capable of carrying “high-quality” voice, data, graphics, & video
Available to “all Americans”
Practical Definitions
Residential
  Currently means DSL, cable modem, or high-speed wireless
  Today’s services are web access, work-at-home, & streaming audio (Napster, etc.)
  Tomorrow, next-generation video will be the “killer app” (Son of Napster?)
Business
  Data, data, & data
    Today – Generally 1.5 Mb/s and up
    Tomorrow – MUCH MORE than 1.5 Mb/s ( 100Mb/s? )
  Notes
“Broadband” is a moving target.
Don’t forget multi-service wireless!

## Slide 5: Broadband Wireless
Youth Let Their Thumbs Do the Talking in Japan New York Times April 30, 2002
ABSTRACT - Young Japanese in a quiet, technology-driven change are developing hyper-agile thumbs, the fruit of childhoods spent furiously thumbing hand-held computer games and young adulthoods thumbing out e-mail messages on cell-phone key pads; a study of cell-phone habits of people in eight major world cities finds Japan's 'thumb generation' is the most advanced in the world.
100 Words / Minute
80 Emails / Day
Cell Phones With Cameras
…

## Slide 6: Where are the customers?
Typical North American Central Office
70k pairs terminated
65% residential, 35% business
20k residences (2+ pair per home)
SAI : Serving Area Interface
DLC: Digital Loop Carrier
Central
Office
SAI
.
.
.
.
SAI
.
.
.
.
Design Area
(400-600 homes)
Feeder
DLC
Lateral
(1200 pr)
Distribution
(2400 pr)
Drop
(5 pr)
Man
Hole

## Slide 7: Passive Optical Network Cheat Sheet
Specified by ITU-T & IEEE
  155& 622 Mbps currently, 1.2 & 2.5 Gbps in preparation;
ITU-T Systems
  Protection switching,
  Dynamic bandwidth allocation,
  WDM overlay,
  Encryption used to insure security;
  Data-rate, QOS, etc. provisionable on a per-customer basis;
  Systems in deployment (tens of thousands of customers turned up)
Central Office
OC-n/STM-n
TDM
Network
Splitter
Optical
Line
Terminal
(OLT)
OC-nc/GbE
Data
Network
Customer Premises
Service
Interfaces
Optical
Network
Terminal
(ONT)
20 km Max
@ 32-Way Split (155 Mbps)
15xx nm
1310 nm

## Slide 8: Example: Verizon Access Lines
Switched access lines in service (3 Months Ended 3/31/02)
Residence 39,347,000
Business 21,296,000
Public 584,000
Total 61,227,000
Special DS0 Equivalents (Data) 72,537,000
Total voice grade equivalents 133,764,000
Resale & UNE-P lines (000)* 3,679,000
* N.B. Unbundled lines are not uniformly distributed!
http://investor.verizon.com/financial/quarterly/VZ/1Q2002/1Q02Bulletin.pdf

## Slide 9: DSL: Who’s Connected?

## Slide 10: Some Examples: Broadband Customers, Prices & Costs
North America
  Cable Modem: 13 M by 2002E, $50 / month
  DSL: 7M by 2002E, $50 / month
Japan
  DSL: 3 M by 2002E, $21 / month (incl. ISP, POTS)
  Fiber-fed 100BaseT: $51-92 / month (incl. ISP)
Sweden
  DSL, Cable Modem, etc.: $20 per month (incl. ISP)
Korea
  DSL: 7 M by 2002E, $25 per month (incl. ISP)
  Sources include Outside Plant, February 2002

## Slide 11: A Distressing Case – US Rural Broadband Access
9.5 M Rural Lines
DSL-ready Lines by 2002 6.2 M
Un-equipped lines ( < 18 kft) 1.6 M ($493 per)
Un-equipped lines ( > 18 kft) 1.1 M ($4,121 per)
Un-equipped lines (“Remote”) 0.6 M ($9,328 per)
www.neca.org

## Slide 12: A Distressing Case – In English
NECA's Middle Mile Broadband Study shows that … even at a very significant 15 percent penetration rate, the total cost for an average high-speed [1.5 Mb/s] circuit is $63.50 per month, which is above the $50 per month retail rate for this service in urban areas. Consequently, this service loses money in most rural areas, due in large part to the high "middle mile” * costs. "Revenue shortfalls won't end as the market grows, they'll actually increase … This sobering conclusion suggests that high-speed Internet service may not be sustainable in many rural areas, based on pure economics."
* “Middle Mile” refers to the distance from the rural CO to the nearest Internet Backbone Provider node.
www.neca.org

## Slide 13: How Do Japan, Sweden, & Korea Do It?
Central Office
COs often are smaller and more closely spaced than US COs;
Loops are short (2-3 km);
Multi-tenant structures dominate;
Zoning regulations allow co-location of businesses and residences;
Governmental guidance.
Commercial
Customers
Residential
Customers
Short-Reach,
Well-Behaved
Outside Plant

## Slide 14: The Hard Truth
In general, broadband economics are dominated by the outside plant (cables, conduit, distances, etc), by labor costs, and by regulatory constraints,
NOT
by details of the telecom equipment.
(Recommended Reading: Outside Plant Magazine.)

## Slide 15: So how do we get there?
What are our choices?
What will it cost?
How long will it take?
See Next Slides …

## Slide 16
FTTC:Fiber To The Curb
FTTCab
:Fiber To The Cabinet
FTTH :Fiber To The Home
FTTB :Fiber To The Building
Figure adapted from image on www.fsanet.net
Fiber “As Close As You Can Get It” (FTTx)
“Soon”
Service Node
ONU
FTTH
FTTB
FTTC
FTTCab
Optical Fiber
PON
xDSL
OLT
ONU
NT
NT
Internet
Leased Line
Frame/Cell
Relay
Telephone
Interactive
Video
Twisted Pair
ONT
ONT
$$$
*FTTB costs compared to traditional solutions
**Depends on the service set
“Soon”
“Later”
“Later”
$*
$$$
$-$$*

## Slide 17: Cocktail Napkin Calculation Suppose Equipment Were Free… Suppose Infrastructure Were Free… Suppose Money Were Free… How Long Would it Take?
Labor per Subscriber 7.5 Hours 29.2 Hours 196 Hours
Years to Convert Network 9.4 Years 36.5 Years 245 Years
CO
2
1
SAI
RT
5
3
4
6
ONU /
RDSLAM
5
3
6
.
ONT
5
3
4
6
OLT
4
.
NT
.
NT
Model Parameters
(1) CO
(2) Feeder Fiber
(3) Lateral Fiber
(4) RT
(5) Distribution/Drop
(6) NT
Assumptions
North American Telco
50% Aerial / 50% Buried
Full-service platforms
Work performed by 20% of total Telco workforce
100% Coverage
FTTCab FTTC FTTH

## Slide 18
CO
STM-1c
PT-to-Pt
STM-1c Trunk
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSL
DSL
DSL
DSL
DSL
DSL
DSLAM
DSLAM
DSLAM
DSLAM
DSLAM
DSLAM
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
ATM
SW
PON’s Role 1
Yesterday’s Backhaul Solution

## Slide 19
CO
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSLAM
DSLAM
DSLAM
DSLAM
DSLAM
STM-1c Trunk
DSL
DSLAM
ONT
ONT
ONT
ONT
ONT
ONT
OLT
DSLAM
DSL
ONT
ONT
ONT
ONT
ONT
ONT
622MB Symmetrical
ONT
ONT
ONT
ONT
ONT
ONT
ONT
ONT
DSL
DSL
DSL
DSL
DSLAM
DSLAM
DSLAM
DSL
DSL
DSL
DSL
DSL
DSL
DSL
DSL
DSL
DSL
DSLAM
ONT
ONT
ONT
ONT
ONT
ONT
ONT
ONT
ONT
ONT
DSLAM
DSLAM
DSLAM
DSLAM
ONT
ONT
ONT
ONT
ONT
ONT
ONT
ONT
ONT
ONT
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
DSLAM
DSL
PON’s Role 2
Tomorrow’s Backhaul Solution

## Slide 20: Summary What is PON good for?
Small Business Deployments
  As 10/100BaseT grows in popularity, PON will be the only viable solution
MDU Applications
  Large market (especially internationally) for ONTs with many 10/100BaseT ports
RT-Backhaul (Full-Service VDSL, wireless, etc.)
FTTH
  Next-generation video will drive this
Leased Line Services (DS1/E1, DS3)
  FSAN spec matches SONET/SDH service features (protection switching, jitter, wander, etc.)
  Allows deployment of data-capable access network for legacy services
High-End Video Services
  SDI (270 Mb/s), PAL, NTSC, etc.
  Note: many video customers also have substantial data and/or leased-line needs!
GbE (Gigabit PONs in preparation)
  On a lightly loaded PON, customer can burst at line-rate
  On a congested PON, BW is distributed fairly (enforce SLAs)
  Collapse core transport requirements (no more pt-to-pt fiber)
1 Gb/s
1 Gb/s
ONT
#N
OLT
ONT
#1
ONT
#n
…
…
Idle
Idle
Notes: Our mission is:
Pioneer the Intelligent Wave Division Multiplexing (IWDM)
equipment market and be the leading supplier of optical networking
solutions for fiber-based metropolitan networks.
IWDM refers to the access network intelligently utilizing WDM to:
1.) deliver multiple service types on a flexible basis to customers.
2.) provision bandwidth on demand.
3.) provide QOS on a customer by customer basis.
The first two generations of WDM are focused on solving the fiber exhaust problem through bigger pipes. They are strictly a transport solution. We are focused on the flexible delivery of services over fiber in an efficient, cost effective manner.