## Slide 1: NTT’s Broadband Access Services and Deployment Experiences in Japan
July 10, 2002
NTT Access Service Systems Laboratories
Yoichi Maeda
maeda@ansl.ntt.co.jp
Workshop on IP/Optical : Session 3

## Slide 2
Outline
1. Current Network Services in Japan
Access services and Metro services
2. Standardization Trend of Optical Access System
B-PON and G-PON
3. B-PON Trial and Deployment in NTT
4. Future issues and Conclusions

## Slide 3
1. Current Network Services in Japan
Access services and Metro services
2. Standardization Trend of Optical Access System
B-PON and G-PON
3. B-PON Trial and Deployment in NTT
4. Future issues and Conclusions

## Slide 4
Mar.,
94
Mar.,
95
Mar.,
96
Mar.,
97
Mar.,
98
Mar.,
99
Mar.,
00
Mar.,
01
Mar.,
02
Mar.,
03
Mar.,
04
Mar.,
05
Mar.,
06
20
40
60
80
(2000.3)
PSTN
Mobile Telephone
Broadband
(FTTH/B + DSL + CATV)
Internet
(Fixed & Mobile Access)
ISDN
(Million Users)
Telecommunication Service Trend
(Estimated)

## Slide 5
Broadband Access (FTTH, ADSL, CATV)
2001/3
2002/3
(Million Users)
(Year/Month)
ADSL
Optical
0.1
10
CATV
2003/3
2004/3
2005/3
2006/3
1
(Estimated by Ministry of Public Management;
http://www.soumu.go.jp/joho_tsusin/eng/index.html)
ADSL : 695 Million
CATV : 429 Million
Optical: 773 Million
0.01
Estimated broadband users
at March, 2006 in e-Japan Strategy

## Slide 6: Architecture for IP Access Service in NTT
FLET’S ISDN
POTS/ISDN
FLET’S ADSL
Fiber
POTS/ISDN
Local
IP network
Content, Application
Always ON connection
Content, Application
Content, Application
Dial-up connection
B-FLET’S
Time-dependent charge
Call congestion at
switching system
Fixed charge
Avoiding
congestion
Selection of
multiple ISPs
ISP
Access Networks
RAS
NTE
Local Node
Local Networks
ISP
ISP
The Internet

## Slide 7: Competition in IP Access Mass Service
0
5,000
10,000
FLET’S ISDN
(JPY/month)
L Mode
Metallic
Optical Fiber
Basic Type
Condominium Type
1G
100M
100k
10M
10k
(bps)
1M
1k
ADSL (Yahoo! BB)
FTTH (Usen)
FTTH
(Tokyo Electric
Power Co.)
FLET’S ADSL
Family Type
: NTT FLET’S services
: Other operators
(including ISP charge)
B FLET’s
series

## Slide 8: Service Lineup for Business Users in NTT
100k
1M
10M
100M
1G
(bps)
6
5
0.1
1
0
0.5
High Speed Digital
(64k - 6M)
DA64
ATM Megalink
(0.5M - 135M)
ATM Megalink (600M)
Mega Data Nets
(PVC : 64k - 10M)
Metro Ether (1G)
Metro Ether (100M)
DA128
DA1500
DA6000
Metro High Link
(45M,150M,600M)
Super High speed
(50M,150M)
Analog
(2400bps)
Monthly charge (million JPY)
(Connection distance between two points is 15km.)

## Slide 9
Intensive office
Metro Area Services for Business Users
Intensive office
GbE-SW
GbE-SW
Central
office
GbE-SW
Central
office
MC
MC
MC
MC
User
MC
User
MC
User
User
ISP
Core Router
100Mb/s
100Mb/s
100Mb/s
1Gb/s
Metro Ether
(Ether Network)
SDH-Node
Central
Office
Central
Office
User
User
Metro High Link
(SDH Network)
SDH-Node
SDH-Node
SDH Ring
45/155/622 Mb/s

## Slide 10
1. Current Network Services in Japan
Access services and Metro services
2. Standardization Trend of Optical Access System
B-PON and G-PON
3. B-PON Trial and Deployment in NTT
4. Future issues and Conclusions

## Slide 11
TE
To
Core Network
Scope of Q2/SG15
Optical
Splitter
UNI
NNI
ONT
ONT
ONT
TE
TE
OLT
ODN
OSS
Scope of
Q14/SG4
155Mb/s 155Mb/s
622Mb/s 622Mb/s
1.244Gb/s 1.244Gb/s
2.488Gb/s 2.488Gb/s
Upstream
Downstream
Broadband-PON
Gigabit-PON
PON bit rate
lineup
Upstream Downstream
ONT : Optical Network Terminal OLT : Optical Line Terminal
TE : User terminal ODN : Optical Distribution Network
PON : Passive Optical Network
B-PON Standardization in ITU-T

## Slide 12
Business Requirements for B-PON
Business factors
B-PON Requirements | ITU-T Standards
International standards compliances and multi-vendor interoperability | G.983.1 G.983.2
Video signal overlay with 3-waves multiplexing | G.983.3 G.983.3.a
DBA (Dynamic Bandwidth Assignment) to improve transmission efficiency of upstream signals | G.983.4 G.983.7
Access line protection and survivability | G.983.5 G.983.6
Enhanced OMCI (ONT Management and Control Interface) for new services | G.983.2.a
Adding 622Mb/s upstream Future upgrade to 1.2Gb/s and higher | G.983.1.a G-PON
Competition with CLEC’s ADSL
Competition with Long Haul operators
Competition with CATV providers
Low-cost and
reliable products

## Slide 13
Relationship in B-PON Standardization
Contributions
Communication
Members
SG4 (Q14)
TMN
SG15 (Q2)
Optical access
SG9 (Q16)
Video overlay
SG15(Q16)
CWDM
ITU-T
802.3.EFM
GE-PON
IEEE
ATM-F
ETSI
Liaison
Liaison
IEC
FSAN (Full Service Access Networks) Initiative
(21 operators + 20 vendors)

## Slide 14
FSAN (Full Service Access Network) Members
21 Operators and 20 vendors as of June 2002
Agere Alcatel Broadcom BroadLight Ericsson
FlexLight Fujitsu Hitachi Iamba Infineon
INOVIA/ECI Lucent Marconi Mitsubishi / Paceon
NEC/eLuminant Oki Optical Solutions Quantum Bridge
Terawave Zonu
NTT
KT
SingTel
Telstra
BellSouth
Bell Canada
SBC
Verizon
Qwest
Chunghwa
Bezeq
FT
BT
DTAG
TI
Eirecom
KPN
Telia
Malta
Telefonica
SwissCom

## Slide 15
New G-PON Standardization in ITU-T
GSR (G-PON service requirements)
Target Date : 1 / 2003 to be consented
GTC (G-PON Transmission Convergence layer)
Target Date : 10 / 2003 to be consented
GPM (G-PON Physical Medium Dependent layer)
Target Date : 1 / 2003 to be consented
- Full services and Ethernet supporting
- Same ODN requirements as B-PON
Maximum commonality in the lower layer specifications between ITU-T and IEEE is expected to reduce the G-PON components cost.

## Slide 16
Service Requirements for G-PON
Items | Target descriptions
Services and QoS performances | Full Services (e.g. 10/100Base-T, Voice, Leased lines, )
Bit rates | 1.25Gbit/s symmetric and higher.
Physical reach | Max 20 km or Max 10 km
Logical reach | Max 60 km (for ranging protocol)
Branch number | Max 64 in physical layer Max 128 in TC layer
Wavelength allocation | Downstream: 1480 – 1500nm Upstream: 1260 – 1360nm
ODN classes | Class A, B and C ( Existing ODN requirements )
Video overlay in the downstream is considered

## Slide 17
G-PON TC Layer Options
ATM frame
base
Generic frame
base
Ethernet frame
base
AAL1/AAL2
AAL5
TCP+UDP etc.
IP
Ethernet
Layer 2
Layer 3
Layer 4
Layer 5
or more
Layer 1
ATM cell
PON-PHY
T1/E1
TDM
POTS
Video
Data
TCP+UDP etc.
IP
Ethernet
Generic frame
T1/E1
TDM
POTS
Video
Data
TCP+UDP etc.
Ethernet frame
T1/E1
TDM
Video
Data
IP
Now being discussed in PWE3 WG in IETF
POTS
VoIP
VoIP
VoIP
Comparative analysis will be made by the FSAN members
One of the best solutions will be proposed to ITU-T from
the members in FSAN
G.983 base
IEEE802.3 base
G.707 base

## Slide 18
Harmonization in G-PON Standards
Operators
Communication
IEEE
802.3EFM
GSR
GTC
GPM
G-PON
(FSAN)
P-MP
sub track
PMD
sub track
GE-PON
Liaison person in SG15;
Dr.Frank Effenberger
(Quantum Bridge)
ITU-T
Q.2/SG15
Common specs for PMD
Down stream wavelength allocation
Physical layer specifications
(except for line code and bit-rates)
Operators requirements
(ODN, Services)

## Slide 19
1. Current Network Services in Japan
Access services and Metro services
2. Standardization Trend of Optical Access System
B-PON and G-PON
3. B-PON Trial and Deployment in NTT
4. Future issues and Conclusions

## Slide 20
B-PON Deployment for ATM Services
Mar.,
98
Mar.,
99
0
Circuits
Mar.,
02
Mar.,
01
10,000
20,000
Mar.,
00
30,000
ATM Mega-Link (SS and PON)
0.5 – 135 Mb/s, CBR
ATM Share-Link
64kb/s – 2Mb/s, CBR
0.5 – 10 Mb/s, GFR
Mega Data Nets
64kb/s – 2Mb/s, CBR with CUG
0.5 – 10 Mb/s, GFR with CUG
(CUG: Closed User Group)
ATM Mega-Link
ATM Share-Link
Mega Data Nets
Mar.,
97
Notes: This graph shows the growth of ATM services circuits provided by B-PON system.
Demands for ATM services have been rapidly increased since June 1999 and NTT provided about 10,000 (ten-thousand) circuits by June 2000. FSAN B-PON system is used for 25% of these circuits.

## Slide 21
Local
IP NW
Basic Type
For SOHO & heavy users
NTT CO
ISP
-A
(9,000JPY/Month)
Network Terminal Equipment
ISP
-B
100Mbps
100Mbps
E/O
Business Type
For Business users
(40,000JPY/Month)
E/O
O/E
O/E
Access Configuration of B-FLET’S service
Network Terminal Equipment
(3,500JPY/Month)
100Mbps
Shared use by the group
E/O
O/E
Condominium Type
Family Type
(10Mbps) ---(5,000JPY/Month)
(100Mbps) ---
(4,300JPY/Month) (NTT West)
(5,800JPY/Month) (NTT East)
10Mbps or
100Mbps
E/O
O/E
For mass users
BRAS
-
-
-
-
-
-
BRAS
BRAS
BRAS

## Slide 22
To OpS
Server
PC: WEB
Browser
155/622M Broadband IP Access System
OLT
MAX:
32 Branches
100BASE-TX
PDS/
Ether-IF
…
100BASE-TX or Gb-E
…
ONU
ONU
DCN
155/622M B-PON
(G.983.1 & G.983.2)
Shared access of
upstream band using
DBA function (G.983.4)
NE-OpS
…
Optimize for
Ether-LC
Single ASIC
for PON
termination
・SNMP for NE-OpS
・2000 units of NE
is controlled.
Service separation
and multiplex function
VLAN tagging
function
Guaranteed
bandwidth and
priority control
functions
DCN:Data Communications Network
EMDX
100BASE-TX
Local IP NW
Contents
Delivery NW
PDS/
Ether-IF

## Slide 23
Joint Trial of NTT and Sky PerfecTV!
The Internet
Each user
: Equipment installed by NTT
: Equipment installed by SPTV
Apartment equipped
with broadband access
SKY PerfecTV!
(CS Broadcasting)
Video
Transmitting
Equipment
Single Optical Fiber
Meguro
Media Center
High-speed Internet (Max.100Mbps)
STB
100Mb/s Data Communication
500 channels Video Distribution
Central Office
B-OLT
B-ONT
Objective: Verification of video signal overlay on B-PON
Terms: March 2002 to February 2003 in Yotsuya, Tokyo
CS
Broadcasting
ISP

## Slide 24
1. Current Network Services in Japan
Access services and Metro services
2. Standardization Trend of Optical Access System
B-PON and G-PON
3. B-PON Trial and Deployment in NTT
4. Future issues and Conclusions

## Slide 25
100k
1M
10M
100M
1G
600M
B-PON
G-PON
Year
ADSL
2000
2001
1998
Bit Rate
(bps)
Developed
Developed
IEEE802.3
FSAN, ITU-T
FSAN, ITU-T
2003
150M
B-PON
100M-Ether
MC
GbE-MC
10M-Ether
MC
Carrier grading ?
LAN(SS)
STM
PON
Developing
FSAN, ITU-T
Trend of Broadband Access Studies
WDM-PON
2002
2004

## Slide 26: NTT’s approach for G-PON
FSAN
Initiative holder Carriers
Main companies
NTT, SBC, BellSouth,
BT, FT, TI, etc.
IEEE
- Initiative holder Vendors
- Main companies
Cisco, Nortel, Intel,
Lucent etc.
NTT
NTT contributes to FSAN & ITU-T.
Task forces
for G-PON
established in April, 2001.
EFM Study Group
For GE-PON
established in Jan., 2001.
Input of carrier’s
requirements
- ODN
- Target services
- OAM
EFMA supports the EFM study group
EFMA
(EFM Alliance)
established in Dec., 2001.
NTT joined EFMA as the first
alliance members.
ITU-T

## Slide 27
Features of CWDM Access System
- Multiplexes all kinds of services (SDH,Ethernet,FC)
- Wide wavelength band
- Cost effective un-cooled DFB module
- Low cost WDM filter
- Flexible and high reliable system
CWDM
Wavelength spacing (nm)
Wavelength (um)
0.8
1.0
1.2
1.4
1.6
1.8
0.6
1
10
100
1000
0.1
4 - 16 wave
DWDM
(G.694.1)
1.3/1.5-WDM
CWDM
(G.694.2)
- 1000 wave
2 wave
20
CWDM:
Coarse WDM
DWDM:
Dense WDM

## Slide 28
Conclusions
Competitive IP access services for mass users in Japan
Broadband access services based on optical fibers
Future service integration of communication and broadcasting on an optical fiber using B-PON
Maximum commonality in G-PON specifications between ITU-T and IEEE
Future access systems using CWDM

## Slide 29
Thank you
The beckoning cat, Maneki Neko,
brings Luck.

## Slide 30
Appendix
ITU-T B-PON Standards and the outlines

## Slide 31
Number | Title | Date
G.983.1 | Broadband optical access systems based on Passive Optical Networks (PON) | 10 / 1998
G.983.1.amd1 | Broadband optical access systems based on Passive Optical Networks (PON) amendment 1 | 12 / 2001
G.983.2 G.983.2r | The ONT Management and Control Interface Specification for ATM-PON | 4 / 2000 5 / 2002
G.983.3 | A broadband optical access system with increased service capability by wavelength allocation | 4 / 2001
G.983.3.amd1 | A broadband optical access system with increased service capability by wavelength allocation amendment 1 | 5/ 2002
G.983.4 | A Broadband Optical Access System with increased service capability using Dynamic Bandwidth Assignment | 12 / 2001
G.983.5 | A broadband optical access system with enhanced survivability | 1 /2002
G.983.6 | ONT management and control interface specification for B-PON system with protection features | 5 / 2002
G.983.7 | ONT management and control interface specification for DBA B-PON system | 12 / 2001
Q.834.1 | ATM-PON requirements and managed entities for the network element view | 4 / 2001
Q.834.2 | ATM-PON requirements and managed entities for the network view | 4 / 2001
Q.834.3 | A UML description for management interface requirements for broadband passive optical networks | 12 / 2001
List of ITU-T Recommendations on B-PON

## Slide 32
B-PON Basic Recommendations
G.982 (PON requirements and ODN definition)
Date : 11 /1996 approved
G.983.1 (Physical layer specifications)
Editor : B. Ford (BellSouth) Date : 10 /1998 approved
G.983.1.amd1 (Add 622Mbit/s upstream)
Editor : F. Effenberger (Quantum Bridge) Date : 12 /2001 approved
ONT
ONT
ONT
OLT
Physical Interface specifications between OLT and ONT
Service and functional requirements for B-PON system
Physical Medium Dependent layer specs. (e.g. Optical parameters)
Transmission Convergence layer specs (e.g. Frame structure and protocol)
ODN
Multi-vendors
interoperability

## Slide 33
B-PON OMCI Recommendations
G.983.2 (Basic OMCI specifications)
Editor : Y. Maeda (NTT) Date : 4 / 2000 approved
G.983.2 amendments and revision
Editor : J. Lorentzen (SBC)
Date : 12 / 2001 approved for amendments
5 / 2002 consented for revised Recommendations
1 / 2003 to be consented for additional new services
ONT
ONT
ONT
OLT
OMCI : ONT Management and Control Interface
Commands
Responses or alarms

## Slide 34
B-PON WDM Recommendations
G.983.3 (Wavelength allocation for additional services)
Editor : T. Sato (NTT) Date : 4 /2001 approved
G.983.3.amd1 (Adjustment for 622Mbit/s upstream)
Editor : K. Nakanishi (NTT) Date : 5 /2002 consented
1200
1300
1400
1500
1600
Upstream
Enhancement
Band
Downstream
Future
Band
Future
Band
for Video Use
(1550-1560)
for Digital Use
(1539-1565)
1260
1360
1480
1260-1360 nm for upstream and 1480–1500 nm downstream wavelength allocation becomes a common PON standard

## Slide 35
B-PON DBA Recommendations
G.983.4 (Dynamic bandwidth assignment protocol)
Editor : B. Ford (BellSouth) Date : 12 /2001 approved
G.983.7 (OMCI for DBA )
Editor : S. Karasawa (Oki) Date : 12 /2001 approved
OLT
ONT-A
ONT-B
ONT-C
ONT-D
Dynamic granting
Sharing
Bandwidth
Occupying
Bandwidth

## Slide 36
B-PON survivability Recommendations
G.983.5 (Survivability mechanism)
Editor : H. Ichibangase (Mitsubishi) Date : 1 /2002 approved
G.983.6 (OMCI for survivability)
Editor : J. Lorentzen (SBC) Date : 5 /2002 consented
LT
LT
LT
LT
LT
OLT
ONT#1
ONT#2
ONT#n
LT
LT
LT
LT
LT
LT
LT
LT
OLT
ONT#1
ONT#2
ONT#n
Type B
(Duplicated OLT)
Type C
(Duplicated PON)
・
・
・
・