## Slide 1: OTN Equipment and Deployment in Today’s Transport Networks
Session 5
Dr. Ghani Abbas Q9/15 Rapporteur
Dr. Stephen Trowbridge Chairman WP 3/15
10/7/2002

## Slide 2: Topics
Today’s Transport Networks
Types of OTN Equipment
Interworking with other transport networks
ITU Recommendations

## Slide 3: Today’s Transport Networks
Metro Access
  SDH metro ring applications
  Multi-Service Provisioning Nodes - combining data and SDH
Metro Core
  SDH ADM metro ring and mesh application
  Optical add/drop multiplexers (proprietary)
Long Haul/Ultra Long haul
  SDH ADM rings and line systems
  DWDM line systems (proprietary)

## Slide 4: OTN Requirements
Functionality as that offered by SDH or better
Transparent transport of SDH and other payloads
Stronger FEC
G.709 is the answer
G.709 defines the interfaces for the OTN

## Slide 5: Applicability of SDH and OTN Standards
SONET and SDH technology evolved with fully standardized external interfaces.
While many of the features of Optical Transport Networks (OTNs) are standardized, many of the external interfaces are highly proprietary, trying to maximize:
  bit-rate
  density of packing of wavelengths
  total number of wavelengths carried
  distance that can be spanned without requiring O-E-O (Optical to Electrical to Optical) regeneration.

## Slide 6: Strategy for Standardization of Optical Transport Networks
Standardize around digital frame formats supporting (initially) client bit rates of 2.5, 10, and 40 Gbps
Develop layered network architecture (as for SDH) to support in-service monitoring, fault detection, and isolation.
Monitoring occurs at “3R” points in the network.
Fully standardize “path” layers to support end to end transport of client signals
Partially standardize line and section type layers to allow interconnect at handoff points in the network without limiting the ability of vendors and operators to take advantage of new technologies.

## Slide 7: Network Evolution - Transport
X
X
X
X
X
X
Long Haul/Ultra Long Haul
X
X
X
X
X
DWDM mesh
Metro Core
STM 64/256
Rings or Mesh
X
OADM Rings or Mesh
X
X
Metro Access
ISP
Business
user
Campus/MTB site
E3
STM 16/64
Rings
Metro
DWDM
E1
E2
STM 1/4
Rings
X
Network Management
Increase in IP/Ethernet transport
Overlay Data Networks - Public LANs/WANs
New services/providers
Optical metro supports ring/mesh router networks
Overlay IP Networks - Routers with integrated optics
GMPLS routing and restoration
All-optical (DWDM) networks
Optical switching nodes
Support for meshed router networks
Flatter feeder networks
Fast provision & High Churn Rate - volatile
Building on existing SDH infrastructure
Lowering transport costs
Lowering provisioning costs
Delivering multi-services
Volatilty reflected from access
Increasing capacity
SDH consolidation & grooming
Optical rings for capacity build
Direct access for wavelength service
More stable - long haul transport
High capacity DWDM for lowest cost per bit
Managed Optical Networking
Common management across layers and domains
Integrated technology layers - for data and transport
Layer & vendor interworking
Common control interface - GMPLS

## Slide 8
Types of OTN Equipment
Metro OADM using CWDM or DWDM
OADM for core applications using DWDM
Optical Line systems
Cross-connect : OEO and OOO
Mixed fabric switch OEO and OOO

## Slide 9
Metro ADM and Core OADM are very similar in network
function to the SDH ADM
DWDM Line Systems are terminating line equipment
similar to SDH line systems
Two types of OTN cross-connects are envisaged
- ODU(Optical Data Unit)
- Optical Channel (OCh) (ie. wavelength)
The ODU cross-connect is a digital cross-connect
with O-E-O while the OCh cross-connect is an
all optical cross-connect.
Types of OTN Equipment - continue

## Slide 10: Mixed Fabric Switch
OEO and OOO Cross-connect Node
Transparent OOO Switch
SDH/PDH/Data
Interfaces
Local IP Router
or ATM switch
Transparent OOO Switch
ODU switching
+
SDH/SONET switching
SDH Optical
Interfaces
DWDM Optical
Interfaces

## Slide 11: Example of nested and cascaded ODUk monitored connections

## Slide 12: TDM Multiplexing in the OTN New Addition to G.709, October 2001
ODUk multiplexing, allowing multiplexing of 4x2.5G clients into 10G wavelengths, 4x10G clients into 40G wavelengths, and combinations of 2.5 and 10G clients into 40G wavelengths.
Virtual concatenation of Optical Channel Payloads to allow inverse multiplexing of larger payloads into OTNs:
  May be used to invese multiplex 40G payloads to carry over only 10G capable fibers.
  May carry future services at greater than 40G rates

## Slide 13: OTN Multiplexing Hierarchy

## Slide 14: SDH Standardization
Network Architecture (G.803, G.805)
Structures and Mappings (G.707)
Physical Layer (G.957, G.691)
Equipment Functional Spec. (G.783, G.806)
Equipment Management (G.784, G.7710)
Information Model (G.774 Series)
Protection Switching (G.gps, G.841, G.842)
Laser Safety (G.664)
Data and Signaling Communications Network (G.7712)
Jitter and Wander Perf. (G.825)
Error Performance (G.826-829)
Notes: Italicized Recommendations are Not Yet Complete
Red Recommendations are Common between SDH and OTN

## Slide 15: Optical Transport Network (OTN) Standardization
Network Architecture (G.872)
Structures and Mappings (G.709)
Physical Layer (G.692, G.959.1, G.694.x)
Equipment Functional Spec. (G.798, G.806)
Equipment Management (G.874, G.7710)
Information Model (G.874.1, G.875)
Protection Switching (G.gps, G.otnprot)
Laser Safety (G.664)
Data and Signaling Communications Network (G.7712)
Jitter and Wander Perf. (G.8251)
Error Performance (G.optperf)
Notes: Italicized Recommendations are Not Yet Complete
Red Recommendations are Common between SDH and OTN

## Slide 16: ITU OTN Equipment Recommendations
G.798 Characteristics of OTN Hierarchy Equipment Functional Blocks
G.709 Interfaces for OTN
G.8251 The Control of Jitter and Wander within the OTN
G.872 Architecture of OTN
G.959.1 OTN Physical Layer Interfaces
G.694.1 Spectral Grid for WDM Applications : DWDM Frequency Grid
G.694.2 Spectral Grid for WDM Applications : CWDM Frequency Grid

## Slide 17: Re-use in the development of OTN Standards
Optical Fiber Recommendations (G.651, G.652, G.653, G.654, G.655)
Laser Safety Recommendation G.664.
Generic Equipment Functionality G.806.
Generic Protection Switching G.gps (under development).
Common Equipment Management Requirements, G.7710.
Data Communication Network (DCN), G.7712.
Approach is to separate generic aspects from SDH Recommendations to avoid “reinventing the wheel” for OTN.

## Slide 18: Summary
  OTN technology introduces a number of new equipment:-
  Metro OADM
  Core OADM
  Cross-connect - OEO and OOO
  Line Systems
  TDM Multiplexing