## Slide 1: General Principles and Requirements for OAM Functions
July 10, 2002
Hiroshi Ohta (NTT, Q.3/13 rapporteur)

## Slide 2: Contents
Purposes, principles and requirements of OAM functions
OAM functions for SDH-based ATM networks
OAM functions for emerging networks (MPLS and Ethernet)
Study issues

## Slide 3: Purposes, principles and requirements of OAM functions

## Slide 4: Purpose of the OAM functions
OAM (Operation and Maintenance) functions are used to detect defects and performance degradation and localize them in order to maintain and guarantee the service performance
  When an operator receives complaints from a customer, they need to
    Localize the defect and report it to the customer
    Arrange corrective action
  When a defect or performance degradation occurs, they should be reported to the operator automatically and recovered automatically extent possible.
  When a service is released to a user, it should be tested beforehand to ensure its availability and QoS

## Slide 5: OAM principles
OAM functions are designed to meet the following objectives
Defect detection
Defect localization
Defect information (reporting to OSS/NMS)
Performance monitoring
System protection (protection switching, redundancy of network elements)

## Slide 6: Defects and performance degradation
Examples of defects and performance degradation
Defects
  Fiber/wire cut
  Defect in equipment
  mis-connection
  swapped connection
  Loop
Performance degradation
  Bit errors
  Packet/Cell/Frame losses
  Delay and its variation
Although there are several technologies to build a network, problems are similar

## Slide 7: Requirements to OAM functions
On-demand diagnosis and continuous monitoring
Defect should be automatically detected, localized and reported to OSS/NMS.
Customers should not be used as a defect detector
Availability and QoS should be able to be measured
OAM functions should not be dependent of the dynamic behavior of customer traffic
The OAM function should perform reliably even under degraded link conditions
Requirements are similar regardless of the technology (OTN, SDH, ATM, MPLS, etc.)

## Slide 8: Methods to realize OAM functions
Hierarchical maintenance entity (ME)
Fault management and performance management functions for each ME/layer
  SDH
  ATM
  MPLS … under standardization
  Ethernet … under study/standardization
OAM functions are categorized into:
  Continous surveillance for detection of defects and performance degradation (e.g., CC, AIS/RDI, PM for ATM)
  On-demand diagnosis test for defect localization (e.g., Loopback and on-demand non-intrusive monitoring for ATM)
Methods are also similar regardless of the technology (OTN, SDH, ATM, MPLS, etc.)

## Slide 9: Situation of standardization
For ATM
  OAM for ATM: Rec. I.610
  Protection switching for ATM: Rec. I.630
For MPLS
  OAM requirements for MPLS: Rec. Y.1710
  OAM mechanisms for MPLS: Draft Rec. Y.1711
  Protection switching for MPLS: Draft Rec. Y.1720
For Ethernet
  Under standardization within IEEE/EFM for OAM for Ethernet access networks
  Under study within ITU-T SG13/15

## Slide 10: OAM functions for SDH-based ATM networks

## Slide 11: Protocol stack
Regenerator Section
Multiplex Section
Transmission Path (TP)
Virtual Path (VP)
Virtual Channel (VC)
Segment VC
End-to-end VC
End-to-end VC
Segment VC

## Slide 12: Hierarchical maintenance entity
VPH
VCH
VCH
VCH
VCH
VPH
VPH
VPH
VPH
VPH
VC
VP
Transmission Path
Multiplex Section
Regenerator Section
VPH
VPH
TPH
TPH
Rep
Rep
Rep
Rep
Rep
Rep
Transmission Path
*VCH: VC Handler, VPH: VP Handler, TPH: Transmission Path Handler, Rep: Repeater/regenerator

## Slide 13: Defect detection
VPH
VPH
TPH
TPH
Rep
Rep
Rep
Rep
Rep
Rep
LOS is detected
MS-AIS
P-AIS
VPH
VCH
VCH
VCH
VCH
VPH
VPH
VPH
VPH
VPH
VP-AIS
VC-AIS
*VCH: VC Handler, VPH: VP Handler, TPH: Transmission Path Handler, Rep: Repeater/regenerator
MS: Multiplex Section

## Slide 14: Defect detection and performance monitoring method
Regenerator Section
Multiplex Section
Transmission Path
Virtual Path (VP)
Virtual Channel (VC)
Detection of LOS/LOF at a regenerator
Detection of LOS/LOF/LOP
Reception of MS-AIS
Path trace (J1)
Signal Label (C2)
(Seg/EE) VP Continuity Check (CC)
(Seg/EE) VC Continuity Check (CC)
Layer
Methods for defect detection
Methods for performance monitoring
(Seg/EE) VC Performance Monitoring (PM)
(Seg/EE) VP Performance Monitoring (PM)
Bit error monitoring (B3)
Bit error monitoring (B2)
Bit error monitoring (B1)

## Slide 15: Reports to OSS (1) – Physical layer defect
OSS (Operation Support System)
VPH
VCH
VPH
VPH
VPH
VPH
VPH
VCH
VCH
VCH
Report (LOS)
VP-AIS
VP-CC
Detection of Loss of VP-CC (LOC)
But it is not reported because VP-AIS is received
VC-AIS
Detection of Loss of VC-CC (LOC)
But it is not reported because VC-AIS is received
VC-CC
*LOS: Loss of Signal

## Slide 16: Reports to OSS (2) – VP layer defect
OSS (Operation Support System)
VPH
VCH
VPH
VPH
VPH
VPH
VPH
VCH
VCH
VCH
Report (LOC)
VP-CC
Detection of Loss of VP-CC (LOC)
It is reported because VP-AIS is NOT received.
VC-AIS
Detection of Loss of VC-CC (LOC)
But it is not reported because VC-AIS is received
VC-CC
VP layer defect (e.g., table corruption)
*LOC: Loss of Continuity

## Slide 17: Multi-operator environment – VP layer defect
OSS (Operation Support System)
VPH
VCH
VPH
VPH
VPH
VPH
VPH
VCH
VCH
VCH
Report (LOC)
VP-CC
Detection of Loss of VP-CC (LOC)
VC-AIS
Detection of Loss of VC-CC (LOC)
VC-CC
VP layer defect (e.g., table corruption)
Operator A
Operator B
OSS (Operation Support System)
Operator A
Detects VP-LOC defect at the VP terminating point.
Understands it is the root-cause because there is no AIS.
Operator A is responsible to handle this defect.
Operator B
Detects VC-LOC at the VC terminating point.
Understands that the cause of this defect is already detected in upstream because there is VC-AIS.
Operator B is not responsible for this defect.
*LOC: Loss of Continuity

## Slide 18: OAM functions for emerging networks

## Slide 19: OAM aspects for MPLS and Ethernet
MPLS and Ethernet are widely used recently for providing services for corporate users such as:
  MPLS based IP-VPN
  Transparent LAN Service (TLS) / Ethernet based on optical pure Ethernet or MPLS
There services are replacing leased line services based on SDH and ATM because they are cheaper in terms of the cost per bandwidth
However, although services for corporate users require high reliability in general, OAM functions for MPLS and Ethernet have not been fully developed yet.

## Slide 20: OAM for MPLS networks (1)
Functions below are specified in Draft Rec. Y.1711
Defect detection: Connectivity Verification (CV)
  Verify connectivity by sending CV packet periodically
  Verify TTSI (Trail Termination Source Identifier) at the sink of an LSP to detect the following defects
    Misconnection, swapped connection, unintended replication, loop
Alarm signal transfer: Forward Defect Indication (FDI) and Backward Defect Indication (BDI)
  Notify defects downstream and upstream
  Suppress unnecessary reporting to OpS (because it has been already reported by the NE generating FDI)

## Slide 21: OAM for MPLS networks (2)
Functions below are under study
Performance monitoring
Loopback
LSP trace

## Slide 22: OAM for Ethernet (1)
OAM for access network is under study (IEEE/EFM, SG13/15)
No OAM functions which cover entire network
Link up/down can be reported by L2 switches to OSS but (for example) it does not cover the cases where:
  there are regenerators between L2 switches
  there are WDM systems between L2 switches
There is no OAM functions to indicate defects to other operators in multi-operator case
Link up at all L2 switches does not mean defect-free end-to-end connectivity because switches can have defects such as VLAN table corruption.

## Slide 23: OAM for Ethernet (2)
Ethernet is a connectionless mesh network. Ethernet OAM functions must be applied to this.
Following OAM functions are envisaged:
  connectivity verification
  alarm signal transfer (forward/backward)
  performance monitoring
  Loopback
  Trace
Ethernet OAM functions should be coordinated with lower layer OAM functions (e.g., OAM for WDM, regenerator spans) so that operator can grasp all the defects in the network.

## Slide 24: Ethernet over MPLS, SDH/SONET, ATM
Ethernet services can be provided by emulations such as:
  MPLS (Ethernet over MPLS … several Internet-Drafts)
  SDH/SONET (Ethernet over SDH/SONET with GFP … G.7041)
  ATM (Multiprotocol Encapsulation over AAL5 … RFC2684)
If the paths (LSPs, Transmission paths, VPs/VCs) spans UNI to UNI or edge to edge, OAMs for these lower layer can be used as OAM for Ethernet services.

## Slide 25: Study issues

## Slide 26: Study issues
Clarification of the requirements to OAM functions, in particular, for emerging networks such as MPLS and Ethernet
  Defect detection and localization
  Performance monitoring
Development of the standard methods to realize necessary OAM functions
Clarification of the trade-off between cost/complexity and OAM functions
Clarification of what OAM functions should be performed by what layer