## Slide 1: Session 6 – WDM and DWDM 10th July, 2002 Chitose ANA Hotel Session Coordinator Masahito Tomizawa (NTT) Editor, SG15

## Slide 2: Trends in Technologies & Standardization (1)
Technological progress is so fast, that standardization-organizations should be aware of the latest LAB result.
  LAB tests - (short period) - getting into the market
DWDM is one of the most progressing technologies.
  Minimum channel spacing - At present, 12.5GHz grid is standardized in G.694.1
    G.694.1,”Spectral Grids for WDM applications 1: DWDM Frequency Grid”, May, 2002

## Slide 3: Trends in Technologies & Standardization (2)
High-speed channel technology is also progressing.
  Maximum channel bit-rate - At present, optical parameters of 40Gbit/s/ch are going to be standardized in G.959.1
    G.959.1, “OTN Physical Layer Interfaces”, to be consented in Jan. 2003.
Optical amplification is the key to enable the technologies in the system.
  Distributed Raman amplification is under discussion.

## Slide 4: Scope of session 6
Initial input of new technologies such as Super-DWDM (< 12.5GHz spacing), ultra-fast TDM (e.g., 160Gbit/s), and new optical amplification (e.g., Raman) into ITU-T.
To find out the direction and new study items in ITU-T
To cope with IEC on some study items (e.g., Raman amp.)
To increase awareness of ITU-T, also attract new members
Objectives

## Slide 5: Invited Speaker (1)
Mr. Franko Kueppers
  T-Systems NOVA, Deutsche Telekom, Germany
    Head of Group
Key words: 40G-WDM, 160G
  Abstract: Experiences from pilot trials of commercial 40 Gbit/s/ WDM systems in the backbone network will be reported and an outlook to 160 Gbit/s TDM will be given - both with respect to relevant effects (e.g. chromatic and polarization mode dispersion), the handling of these effects in future systems, and the relation to standardization.

## Slide 6: Invited Speaker (2)
Mr. Toshio Morioka
  NTT Network Innovation Labs., NTT, Japan
    Group leader
Key words; SDWDM, OTDM, Light-source
  Abstract: Recent progress in broadband OTDM and DWDM technologies is presented including over Tbit/s OTDM transmission and processing, 1000 channel DWDM source, and over 100 nm-bandwidth seamless transmission.

## Slide 7: Invited Speaker (3)
Mr. Haruo Okamura,
  Corning International K. K, Corning, Japan
    ITU-T SG15 Vice-chairman, IEC TC86 Convenor
Key words; Raman amplification, 40G-WDM.
  Abstract: Trends in standards discussions at ITU-TSG15 and IECTC86 on the emerging broad-band optical transmission technologies/systems are reviewed from the viewpoints of technologies as well as businesses. The key words include 40Gb/s, WDM transmission and Raman amplification.

## Slide 8: Discussion (1)
Why Standard?
  Benefits
    <12.5GHz spacing
    160Gbit/s
    Raman amplification
  Compatibility (Longitudinal or transverse)
    <12.5GHz spacing
    160Gbit/s
    Raman amplification

## Slide 9: Longitudinal vs Transverse compatibility
Longitudinal compatibility
Single vendor configuration
Target distance compatible
Small set of specifications
Major WDM spec., G.692, G.IaDI
Transverse compatibility
Multi-vendor configuration
Interface compatible
Full set of specifications
Only G.959.1 for WDM

## Slide 10: Discussion (2)
When standardization?
  Study items for the near future.
  Study items for far future.