## Slide 1
Haruo Okamura
Corning International, Japan
Standardization of Optical Technologies
at ITU-T and IEC
40 Gb/s, WDM and Raman Amplification

## Slide 2
- International standards overview
History, where, what, why, who,,,
- ITU-T SG15
Overview, WDM, 40Gb/s
- IECTC86
Overview, OFA reliability, Raman
- Summary
Contents

## Slide 3
History of International standardization
Standards has been
“must” in Europe for 500 years
OTTOMAN
Standard of Bread
Under global economy,
it is also “must” in Asia !!
500 years ago

## Slide 4
OIF
IETF
Optical
User Interface
Operator B
Operator C
Internet Architecture Operation
International Standards Bodies
Optical Networks
Operator A
IEC
Definitions
Test methods
Architecture, Interface, System Requirements
ITU-T
Data
Data

## Slide 5
Use of International Standards
An example in a “System Supply Contract”
Purchaser's specification requirement
“The following documents shall form part of this specification”
ITU-T Recommendations
G. 650, 652, 653, 654, 661, Draft 662, Draft 663, 701,
702, 703, 707, 712, 772, 773, 774, 783, 784, 801, 811,
812, 813, 823, 824, 825, 826, 841, 911, 957, 958,
971, 972, 975,,,,
IEC Standards
IEC6297, 6617, 6721, 6825,
ISO Standards
ISO8402, 9001, 9004
Even Drafts are included !!

## Slide 6
Europe: Adjust / Harmonize Technologies/Markets
(standards since 500 years ago)
North America: Lead / Grow the Market
(standards as a strategic marketing tool)
Asia：Smell / Know / Meet the Global Market
(standards to join the Global markets)
Motivation of standards activities
personal view

## Slide 7
By Proposing
Current technologies：
Focus in / Grow / Stabilize the market
Promote constructive/effective competition
New technologies
Clarify requirements, Quickly create the market
Future technologies
Prioritize Targets & Technologies
By Contributing / Supporting
Catch the Market Trends / Technology Trends
Enhance the Presence of Your Company
Develop company networks / human networks
Be prepared for the future lead of standards
What are expected from standards activities
（From the viewpoint of SG15 promotion）

## Slide 8
ITU-T

## Slide 9
ITU (International Telecommunication Union)
United Nations
WTO UNESCO ITU WHO ILO WIPO ,,,,,,,
Since 135 Ys ago
7 Study Groups 13 Study Groups Study Group
ITU-R ITU-T ITU-D

## Slide 10
Subscribers to
SG Web sites
ITU-T Work Areas
IP
Optical
    SG2 (Operational aspects of service ...) 480
    SG3 (Tariff and accounting...) 331
    SG4 (Telecommunication management,,) 541
    SG5 (Protection against electromagnetic ,,) 256
    SG6 (Outside plant) 209
    SG7 (Data networks and ,,) 365
    SG8 (Characteristics of telematic systems) 168
    SG9 (Integrated cable networks and television...) 328
    SG10 (Languages and software...) 248
    SG11 (Signaling and protocols) 993
    SG12 (transmission performance of networks...) 357
SG13 (Multi-protocol and IP-based networks) 905
SG15 (Optical and other transport networks) 1443
SG16 (Multimedia services, ,,) 817
SG17 (Data networks and telecom software) 446

## Slide 11
SG15, Responsibility and Mandate
Access / Metro / Long Haul Networks / Equipment
Lead Study Group on
  Access Network Transport (ANT)
  Optical Technology
WP 1 - Network access
WP 2 - Network signal processing
WP 3 - Multiplexing and switching
WP 4 - Transmission
WP 5 - Projects and Promotion
Q.15 Fibres, Cables
Q.16 Long-haul terrestrial systems
Q.17 Active/passive components
Q.18 Submarine systems
Q. 1 Access Transport Networks
Q.19 Optical Transport Networks
SG15

## Slide 12
Europe Nokia, Ericsson Telecom, Ericsson Comp., Telia, Sonera, Teledanmark, Lucent Nederlands, BT, Marconi, Nortel Networks(Euro), Siemens, Swisscom, France Telecom, ＩＳＣＴＩ，Italtel, Telecom Italia, Alcatel SEL, Alcatel Italy, Pirelli, Telecom Italia, CSELT, Ukraine, Marconi
North America AT&T, Corning, Ciena, EXFO, Elisa, Fujitsu Networks(US), JDS, Lucent(US), Hitachi Telecom(US), Motorola, NEC(US), Nortel, Networks(US, Canada), MCI Worldcom, Sprint, Telcordia, Tycom, Ciena, Cisco
Asia China Telecom, China Unicom, CLPAJ, Corning Int. DDI, ETRI, Fujitsu, Hitachi, Huawei Technol., Japan Telecom, Korea Telecom, KDDI, Mitsubishi, NEC, NTT, Oki, Shanghai Bell, Sumitomo, Sumsung, Toshiba
Participants
SG15 WP4 Optical Transport Network Technology

## Slide 13
  ATM Forum Traffic & network management
  DSL Forum Access network
  TM Forum Network management
  ATIS T1 Access, SONET/SDH, OTN
  ETSI Access network, SDH
  ISO/IEC Optical fibers, components
  ISOC/IETF Optical transport network
  Network signal processing
  TIA, OIF Optical networks & technology
  IEEE Ethernet
Standards bodies recognized by ITU-T(SG15)
Exchanging information and /or Reference documents

## Slide 14
History of “ITU Grid” for WDM (SG15)
Absolute Channel allocation
not agreed (96.5)
Giving up “Transversely compatible” standards
“ITU-Grid” with 100GH-spacing
agreed with anchor
G. 692 (98.10)
Compromise
200 GHz absolute allocation
for < 40km, 16 ch, Systems
G. 959.1 (99.7)
195.1 THz
Anchor
193.10 THz
192.1 THz
CWDM Grid
100, 50, 25, 12.5 GHz spacing
DWDM Grid
20 nm specing
G. 694 (02, 5)
DWDM≦1000GHz
CWDM＜ 50nm
WWDM≧ 50nm
G. 671 (02, 5)

## Slide 15
Applications
Very short reach
Metropolitan
Long/Ultra-long Haul
Fibres
PMD (0.1-0.5 ps/km), PMD compensation
Low Dispersion Slope
Use of Installed/New Fibre
Systems/Comps.
Worst‐case approach Statistical approach
Optical amps. including Raman
Line coding (NRZ, RZ, CSRZ,,), RZ Duty ratio,
Source linewidth,
Discussions of Optical Technologies (SG15)
40 Gbit/s/ch, WDM
G.693（G.vsr)
Optical interfaces for intra-office systems
-Single channel
-NRZ 10/40 Gbit/s, 0.6 and 2 km
-Single-mode fibers
Agreed
G. SCL
Wide band NZDSF
Discussing

## Slide 16
IEC

## Slide 17
TC 01 Terminology
-
TC 31 Electrical Apparatus For Explosive Atmospheres
-
TC 47 Semiconductor Devices
-
-
TC 76 Optical Radiation Safety And Laser Equipment
-
-
TC 86 Fibre Optics
-
TC 100 Audio, Video And Multimedia Systems And Equipment
-
TC 109 Insulation Co-ordination For Low-voltage Equipment
International Electrotechnical Commission(IEC)
95 Technical Committees

## Slide 18
WG 1: Fibre Optic Systems & Sub-Systems
WG 3: Optical Amplifiers
WG 4: Fibre Optic Active Devices/Components
SC 86A Fibres & Cables
SC 86B Passive Components incl. Connectors
SC 86C Fibre Optic Systems & Active Devices
Specification parameters
Definitions
Test methods
Referred to
by ITU-T
IEC, TC 86 (Fibre Optics)
Keeping Close Liaison
with ITU-T

## Slide 19
- Requirements and standard method for the OFA
reliability assessment
- Guidance on testing, use of failure criteria
during the testing, reliability predictions
- Assistance for purchasers in selecting OFAs
- Means to determine the failure distribution
(equipment failure rates) for specified end-of-life criteria
OFA reliability standard IEC61291-5-2
Provides:
IEC developed this standard
with
CENELEC(Europe)

## Slide 20
Definitions
Effective Gain (for a Distributed Amplifier)
Effective Noise Figure(for a Distributed Amplifier)
Double Raleigh Scattering Figure of Merit” ,
Distributed Amplification
Discrete Fibre Raman Amplifier
Test Methods Effective Gain/Noise
Raman Amp. Sources
Degree of Polarisation
Pump Spectral Power Distribution
“Reference” Test Fibre
Raman Amplifier (Descrete)
Applicability of Existing Test Methods for EDFAs
.
Raman Amplification Discussions
IECSC86CWG3 (Optical Amplifiers)
Under discussions

## Slide 21
that
identifies the direction of technologies / markets
focuses in / grows /stabilizes the market
through discussing
- need for IP transport in access, metropolitan and backbone
- OTN toward an “all optical” networking capability
- intra-office, inter-office and long distance WDM networks,
including OTN up to or above 40 Gbit/s for e.g. IP
- what is necessary to be compatible with Ethernet?
at ITU‐T，IEC，IETF，OIF,,,,
Summary
International Standards discussions are important
( particularly to recover from the recession )
Optical Technologies