## Slide 1: G.7713.2: DCM Signaling Mechanism Using GMPLS RSVP-TE
ITU-T Workshop on IP-Optical, Chitose, Japan
7/11/2002
Dimitrios Pendarakis, Tellium, Inc.

## Slide 2: Presentation Overview
Scope of G.7713.2 specification
Main architectural assumptions
Evaluation of GMPLS RSVP-TE against requirements specified in G.7713
Proposed resolution for requirements that are not satisfied

## Slide 3: Example Control Plane Partition
User Admin
Domain
Provider A
Admin Domain
Provider C
Admin Domain
UNI
E-NNI
Provider B
Admin Domain
firewall
firewall
L2/L3
L2/L3
Load
Balancer
Load
Balancer
firewall
firewall
L2/L3
L2/L3
Load
Balancer
Load
Balancer
Domain A1
Domain A2
I-NNI
I-NNI
I-NNI
Provider A has divided its
network into multiple control
domains (e.g., based on
vendor, geographic,
technology, business unit, etc.)
Provider B’s network is a single control domain
User Admin
Domain
UNI
E-NNI
E-NNI

## Slide 4: Scope of G.7713.2
Distributed call and connection management for automatic switched optical network (ASON) based on GMPLS RSVP-TE
Applicable on interfaces between control domains
Focus on UNI and E-NNI (Exterior Network-Node Interface)
  But could be applicable to I-NNI as well
Primary focus on E-NNI interfaces within a single carrier

## Slide 5: Required Signaling Functionality
Need to support two types of connection services
Switched: initiated by clients over a UNI interface
  Requires translation of UNI requests & parameters into NNI end-to-end
Soft permanent: initiated by the management plane (EMS or NMS), without involving client signaling
  Requires appropriate EMS/NE I/F
  Should allow EMS/NMS to specify complete path, including all ports and timeslots

## Slide 6: Soft Permanent Connections: Example
CORE
METRO 2
METRO 1
Client B
Client A
Client C
EMS
E-NNI
Connection Set-Up
Request (SPC)
UNI
Scope of Signaling Messages
End-to-end connection
Both source and destination user-to-network connection segments are provisioned (e.g. via EMS/NMS)
The network connection segment is set up via the control plane.

## Slide 7: NNI Signaling: Support of Explicit Routes
Path typically known at the source
  Computed at or provided to ingress node
Required for diversity and protection
Explicit routes may be either strict or loose
  Strict if node computing path has complete topology of all (abstract) nodes and links in the connection
  Loose if some, not all, topology information is available
    More consistent with overlay model
Dependency on routing mechanisms

## Slide 8: Additional Requirements for GMPLS RSVP-TE
Derived from “protocol neutral” G.7713 specification
Identified in Q14/15 meeting
  Call/connection separation
  Support for soft permanent connections
  Support for crankback
  Additional error codes
  (Potentially) additional control plane resilience & recovery mechanisms
    Based on RSVP “restart” mechanism

## Slide 9: Call & Connection Separation
Comes in two “flavors”:
  Logical separation – call and connection signaled within the same message
    supports one or more connections per call
    Signals a call as part of a connection
    This model implies UNI has a call controller – all changes to a call are considered modifications
  Complete separation – call signaled separately from connection
    supports zero or more connections per call
    Signals a call separate from a connection
    This model implies UNI has both separate call and connection controllers

## Slide 10: Call & Connection Separation (2)
Proposed resolution:
  Focus on logical separation, for now (significantly simpler)
  Re-use existing messages
  Adds two new objects: call_id, call_ops (call capability)
Issues currently under consideration
  Modification in RSVP-TE procedures
  Backwards compatibility

## Slide 11: Soft Permanent Connection
SPC connection assumes that the UNI-C to UNI-N signaling does not exist or is not exercised; instead it is provisioned
Signaling occurs only within the network
Request from EMS/NMS
E-NNI
User
A Interface/ Label identified by EMS/NMS
I-NNI
Z Interface/ Label identified by EMS/NMS
User

## Slide 12: Soft Permanent Connection (2)
Information needed is the ingress interface/label into the network, and egress interface/label exiting the network
Ingress already provided by the external initiator (NMS/EMS) -- non-standard interface
Egress info needs to be handled and carried across
  New sub-object of GENERALIZED_UNI defined: SPC_LABEL
    G_UNI defined in OIF UNI 1.0
    Assumes G_UNI is always used -- may require TNA configuration
  SPC_LABEL also serves to indicate the request is a SPC request
  Alternative proposal relies on ERO processing to identify egress port/label

## Slide 13: Soft Permanent Connection (3)
SPC_LABEL provides the method for carrying the information
7713.2 specification does not provide discuss how the information is obtained
An SPC may span multiple control or administrative domains
  It is assumed that the entity initiating the SPC (EMS/NMS) knows this information

## Slide 14: UNI-NNI Inter-working
Path
Path
Resv
Resv
+ MESSAGE_ID_ACK
ACK
NNI Transport Connection Established
Source NNI may start transmitting
ACK
Source UNI-C
Destination UNI-C
UNI-N  I-NNI
ResvConf
ResvConf
+ MESSAGE_ID_ACK
ACK
Destination NNI may start transmitting
Path
ACK
ACK
Resv
ACK
ResvConf
I-NNI  E-NNI
E-NNI  I-NNI
I-NNI  UNI-N

## Slide 15: Open Issues
Reducing dependency on routing protocols
Multiple protocols – need for translation?
Alignment with OIF E-NNI and UNI 1.0 work
Interaction with restoration signaling?
Management & OAM&P interfaces
  Configuration of control plane parameters (timers, features), monitoring, state information retrieval
  Network element to EMS interfaces
    SNMP MIBs, TL1, CORBA?
  EMS to NMS extensions for integration with a multi-domain, multi-technology network

## Slide 16: Alignment Issues
Alignment with IETF & OIF desirable
Key contributors same across all bodies
IETF more focused on “peer” model
  Hence, less inclined to introduce changes to GMPLS
  Also, does not formally recognize OIF, yet!
OIF focused on overlay model also, so coordination with E-NNI effort expected to be easier
First alignment draft submitted to IETF
  draft-lin-ccamp-gmpls-ason-rsvpte-00.txt