## Slide 1: ITU-T Workshop on IP/Optical Optical amplifiers and their standardization in ITU-T & IEC
Akira Hirano
NTT Network Innovation Labs, NTT Corporation

## Slide 2: Outline
Standardization activities in optical amplifiers
Trends in optical amplifiers
Current standardization issues

## Slide 3: Outline
Standardization activities in optical amplifiers
Trends in optical amplifiers
Current standardization issues

## Slide 4: Optical amplifiers - Transparency of physical layer -
Specific parameters:
Output power, Gain, Noise figure, …
- Independent on signal formats, bit rate, etc -
NRZ, RZ, duobinary, …
OTU1, OTU2, …

## Slide 5: Cooperation with IEC
IEC role
Selection of specific parameters
Definition of the parameters
Test method of the parameters
optical power, gain, noise figure, etc..
ITU-T role
Requirement from the viewpoint of optical systems based on IEC definition and test method

## Slide 6: Cooperation with IEC-SC86C-WG3 in Rec. G. 661
Table 1/G.661 – Recommended test methods for parameters defined in clause 4
Group of test parameters | Parameters of clause 4 involved | Test Method (TM) – IEC Basic Specification number
Gain parameters | 4.1 to 4.8, 4.10, 4.32, 4.39, 4.40 | 61290-1-1: Optical spectrum analyser TM 61290-1-2: Electrical spectrum analyser TM 61290-1-3: Optical power meter TM
Optical power parameters | 4.9, 4.11, 4.12, 4.25, 4.28, 4.29 | 61290-2-1: Optical spectrum analyser TM 61290-2-2: Electrical spectrum analyser TM 61290-2-3: Optical power meter TM
Noise parameters | 4.13 to 4.15, 4.33 to 4.36 | 61290-3-1: Optical spectrum analyser TM 61290-3-2: Electrical spectrum analyser TM 61290-3-3: Pulse optical TM (under study)
Reflectance parameters | 4.16 to 4.19, 4.38 | 61290-5-1: Optical spectrum analyser TM 61290-5-2: Electrical spectrum analyser TM 61290-5-3: Electrical spectrum analyser TM (for reflectance tolerance)
Pump leakage parameters | 4.20, 4.21 | 61290-6-1: Optical demultiplexer TM
Insertion loss parameters | 4.22, 4.23, 4.37 | 61290-7-1: Filtered optical power meter TM

## Slide 7: Recommendations and publications for optical amplifiers
ITU-T SG15 Recommendations
G. 661: Definition and test methods for the relevant generic parameters of Optical Amplifiers
G. 662: Generic characteristics of Optical Amplifier devices and sub-systems
G. 663: Application-related aspects of Optical Amplifier devices and sub-systems and comprehensive Appendix on transmission-related aspects
IEC TC86 SC86C Publications
Generic specification
Test method
Performance specification template

## Slide 8: Outline
Standardization activities in optical amplifiers
Trends in optical amplifiers
Current standardization issues

## Slide 9: Trends in optical amplifiers - EDFA vs. Raman -
EDFA: Mature technology
New materials (Fluoride, Tellurite)
New dopant (Pr, Tm) ~PDFA, TDFA
to exhibit broader and flatter gain
Raman amplifier: Advantage in long-haul (LH) space
SN improvement by distributed Raman
Flat gain by multiple pump wavelength
>> Efficiency merit of EDFA is offset by required gain flattening.
>> Raman systems are challenging EDFA stronghold in LH applications.

## Slide 10: Optical amplifier type
Rare earth-Doped Fiber Amplifiers
Erbium-Doped Fiber Amplifiers (EDFA) : C, L-Band
Thulium-Doped Fiber Amplifiers (TDFA) : S-Band
Praseodymium-Doped Fiber Amplifiers (PDFA) : O-Band
Fiber Raman Amplifiers
Discrete Raman Amplifiers
Distributed Raman Amplifiers (DRA)
Semiconductor Optical Amplifiers (SOA)
conventional SOA
GC-SOA (Gain-Clamped SOA)
LOA (Linear Optical Amplifier)

## Slide 11: Rare earth (Er, Tm, Pr) -Doped Fiber Amplifiers
Gain band:
Er (C, L-Band), Tm (S-Band), Pr (O-Band)
76 nm (1532-1608 nm) record gain bandwidth in single band configuration [M. Yamada et al.,OFC’98PD].
- Flat gain: 21 dB, Noise figure: 7 dB
- Gain equalizer: two MZ filters with FSR of 32 and 120 nm

## Slide 12: Semiconductor Optical Amplifiers
Gain band:
1.3~1.7 um (tunable by InGaAsP composition)
Maximum gain bandwidth: ~100 nm
Conventional SOA
Suffering from gain ripple and XGM-induced cross talk originated from gain dynamics (relaxation oscillation etc.)
-> Not applicable to high-speed or wide-band signals
GC-SOA (Gain-clamped SOA):
Gain stabilization by an additional lasing oscillation which locks the carrier density.
> Excellent linearity (low XGM)
>> high-speed or wide-band applications

## Slide 13: Fiber Raman Amplifiers
Gain band: 1.3~1.7 um (tunable by pump wavelength)
132 nm record gain bandwidth in double band configuration has been achieved [H. Masuda et al., ECOC’99].
- Combination of Distributed Raman amplifiers (DRA) and discrete Raman
- Two-gain-band Raman amplifier

## Slide 14: Gain profile of hybrid DRA
- 132 nm Record Gain Bandwidth in Double-Band Configuration -
25
20
15
10
5
0
-5
-10
Gain (dB)
1650
1600
1550
1500
Wavelength (nm)
91 nm
distributed gain
discrete gain
total gain
fiber loss
41 nm

## Slide 15: Gain bandwidth of optical amplifiers

## Slide 16: Optical amplifier classifications (G. 662) - Functional blocks -
The Booster power Amplifier (BA):
a high saturation-power OA device to be used directly after the optical transmitter to increase its signal power level.
The Pre-Amplifier (PA):
a very low noise OA device to be used directly before an optical receiver to improve its sensitivity.
The Line Amplifier (LA):
a low noise OA device to be used between passive fibre sections to increase the regeneration lengths or in correspondence of a point-multipoint connection to compensate for branching losses in the optical access network.

## Slide 17: Applications in each functional blocks - Implementation example -
Pre-Amplifier
Booster power
Amplifier
Line Amplifier
S
O
A
D
i
s
t
r
i
b
u
t
e
d
R
a
m
a
n
E
D
F
A
T
D
F
A
D
i
s
c
r
e
t
e
R
a
m
a
n
O
A
T
x
N
T
x
3
T
x
2
T
x
1
A
W
G
O
A
O
A
A
W
G
R
a
m
a
n
p
u
m
p
L
D
R
x
N
R
x
3
R
x
2
R
x
1
R
a
m
a
n
p
u
m
p
L
D
R
a
m
a
n
p
u
m
p
L
D
O
A

## Slide 18: Current standardization topics for optical amplifiers
Raman amplifier
Safety issues
G. 664 APR procedure
Sup.dsn Safety in operation
Sup.Raman Under discussion
Definition of relevant parameters
Proposals are invited
in IEC TC86 SC86C WG3

## Slide 19: Conclusion
Increase of available optical bandwidth
EDFA (RDFA), Raman, SOA
Spectrally efficient transmission formats
Duobinary, CS-RZ, DCS-RZ, CRZ, NRZ, RZ, DPSK-RZ,…
↓
Standardization of specific parameters
↓
Cost effective use of available bandwidth by sophisticated combination OAs of different vendors and manufacturers.