## Slide 1: Optical Network Management Fault Management And Service Recovery
Prepared For:
ITU-T Workshop On IP/Optical
Chitose, Japan, 9-11 July 2002
Tobey Trygar
ttrygar@telcordia.com
+1 732 758-5399

## Slide 2: Outline
Definition of Fault Management
Scope of Fault Management
Transmission Fault Event Classes
Generic Layer Networks
Optical Transport Network (OTN) Layers
OTN Supervision and Fault Management Processes
Key Aspects of Service Recovery

## Slide 3: Fault Management
Fault Management is the process of
    detecting,
    isolating, and
    correcting
the abnormal operation of a telecommunications network and its environment.
M.3010 defines a management structure that contains five layers, namely the business management, the service management, the network management, the element management and the network element layer.
This presentation addresses the network element layer and the functions that are supported within optical network elements.

## Slide 4: Trouble Event Taxonomy
Trouble Events
Non-Alarmed
Defects
Anomalies
Fault Event
Alarmed
Critical
Major
Minor
Performance Event
Warning

## Slide 5: Fault Management Scope
In general, Fault Management addresses the following five classes of trouble events:
  Events related to the received Transmission signal content and structure
  Events related to severe Quality of Service degradations
  Events related to software Processing
  Events related to network Equipment replaceable modules
  Events related to the Environment in which the equipment resides
The remainder of the presentation will focus on transmission signal related events.

## Slide 6: Fault Management Transmission Events
Continuity supervision to detect loss of the transmission signal
Connectivity supervision to detect misconnections
Signal quality supervision to detect signal degradation
Payload type supervision to detect inconsistencies between the transmitted signal and the expected received signal
Multiplex structure supervision to detect inconsistencies between the transmitted and expected received signal
Alignment supervision to detect framing problems
Protocol supervision to detect inconsistent or unexpected protocol exchanges

## Slide 7: G.805 Network Classes
There are two broad classes of transport layer networks - Path Layer Networks and Transmission Media Layer Networks.
Path Layer Networks
  Independent of the physical media which supports the communications signal, e.g., STM-1 electrical section or an STM-1 in an optical section, or via a microwave radio link.
  Defined in terms of signal hierarchies, SDH, PDH, ATM VC-VP.
Transmission Media Layer Networks are divided into
  Section Layer Networks which are related to the technology implementing the transmission system. They are based on the multiplexers, cross-connects, and regenerators.
  Physical Media Layer Networks which contain the collection of interconnected media, e.g., twisted pairs, optical fibers, coaxial cables, waveguides etc., that carry the communication signals.

## Slide 8: G.805 View Of Layer Relationships - Bi-directional Transmission
AP
AP
TCP
TCP
CP
CP
Link Connection
Trail
Server Layer Network
Client Layer Network
Subnetwork
Connection
= Adaptation Function
= Trail Termination Function
= Subnetwork Connection
Link Connection
Network Connection
CP = Connection Point
TCP = Termination Connection Point
AP = Access Point

## Slide 9: Supervision And Management Processes Within An Adaptation Function
Supervision Processes
(G.806, G.798)
Access Point
Connection Point
Management Points (MP)
Data and Maintenance Signals
Layer-Descriptor_Adaptation_Sink_Function
Fault Management Processes
(G.7710, G.874)
Management Application Functions
(M Series)

## Slide 10: Layers Defined For The Optical Transport Network1
Digital Optical Transport Network (OTN) Layers
  Optical Channel Data Unit (ODU), Path and Tandem Connection
  Optical Channel Transport Unit (OTU)
Original OTN Layers
  Optical Channel (OCh) Layer, OCh Reduced (OChr)
  Optical Multiplex Section (OMS) Layer
  Optical Transmission Section (OTS) Layer
  Optical Physical Section (OPS) Layer
Fault Management is concerned with received transmission signals as contrasted with transmitted signals.
1 See Recommendation G.872

## Slide 11: Physical View Of A Linear OTN
ODU
OCh/OTU
OCh/OTU
OTS
OMS
OMS
OMS
OTS
OTS
OTS
OTS
OTN Client Signal
OTN Client Signal
ONE
ONE
ONE
ONE
ONE
ONE
Physical
Layer
Physical
Layer
Physical
Layer
Physical
Layer
Physical
Layer
Physical
Layer
OTS Termination
OTS Termination
OTS Termination
OTS Termination
OTS Termination
OTS Termination
OMS Termination
OMS Termination
OMS Termination
OMS Termination
OCh/OTU
Termination
OCh/OTU
Termination
OCh/OTU
Termination
ODU
Termination
ODU
Termination
ONE = Optical Network Element

## Slide 12: Information Flow Across A Management Point At A Given Atomic Function (Sink)
PRS
Network Element
Alarms
Unit Alarms
Station Alarms
Alarm
Synchronization
Report
TMN alarm event
notifications
ARC information
Alarm Severity Assignment Profile
Current Problem List
Alarm Status
Operational State
Failure
fZZZ-value
fZZZ-severity
SEV
fZZZ-value
fZZZ-severity
fZZZ-arc
Reportable Failure
ARC
REP
TEP
UNA
NEA
STA
ASY
LOG
TAN
CPL
AST
OPS
fZZZ-value
rZZZ-value
rZZZ-severity
rZZZ-value
rZZZ-severity
Query
Management Application Functions
Supervision Processes
MP
Fault Management Processes
cZZZ-value
Fault cause

## Slide 13: OTN Fault Indicators
G.798/G.874 specify 21 supervision processes for the OTN layers.
These 21 processes generate 69 fault cause indicators.
The fault cause indicators that an optical network element may generate depend on the number of trail termination and adaptation sink functions it contains.
ODUkPath_Trail-Termination_Sink Supervision Process
Open Connection Indication
Trace Identifier Mismatch
Signal Degrade
Backward Defect Indications
Server Signal Fail
Locked Signal
Fault Management Process
Management Point

## Slide 14: Alarm Report Control
NALM
-
QI
do: Alarm Reporting Inhibited
CD
entry: reset timer (1)
NALM-
entry: reset timer (1)
NALM-NR
Qualified
Problem
Free
Modify Interval
ALM
do: Alarm Reporting Allowed
NALM
do: Alarm Reporting Inhibited
NALM-TI
entry: reset timer
do: Alarm Reporting Inhibited
Modify Interval
Management Request or
Qualified Problem Free
or Timer Expired
Qualified
Problem
Free
Management Request
Management
Request
Management Request
Management Request
or Timer Expired
Qualified
Problem
Raised
Timer
Expired
Management
Request
Management
Request
Management
Request
Management
Request
Management
Request
ALM = Alarmed
NALM = Not Alarmed
TI = Timed Inhibit
QI = Qualified Inhibit
NR = Not Ready
CD = Count Down

## Slide 15: Key Aspects Of Service Recovery
For protected services, recovery may be accomplished via protection schemes if the failure event is not too extreme.
Re-routing, (restoration), can recover services again provided that the failure event is not too extreme.
Assuming that conventional methods succeed, the network may be vulnerable to future failure events.
To provide support for an Emergency Service per E.106, F.706 and Y.roec, special consideration must be given to the assignment of alarm severity levels.
Given the extensive capacity of the OTN, e.g., from 2.5 to 40 gigabits per second per channel, enhanced OTN services such as emergency service, are best provided via Service Level Agreements.

## Slide 16: References
E.106, Description of an International Emergency Preference Scheme (IEPS)
F.706, (Draft), International Emergency Multimedia Service
G.709, Network Node Interface For The Optical Transport Network (OTN)
G.798, Characteristics of Optical Transport Network Hierarchy Equipment Functional Blocks
G.805, Generic Functional Architecture Of Transport Networks
G.806, Characteristics of Transport Equipment - Description Methodology and Generic Functionality
G.872, Architecture Of Optical Transport Networks
G.874, Management Aspects Of Optical Transport Network Elements
G.7710, Common Equipment Management Function Requirements
G.7712, Architecture And Specification Of Data Communication Network
M.3010, Principles For A Telecommunications Management Network
M.3013, Considerations For A Telecommunications Management Network
M.3100, Generic Network Information Model
Y.roec, (Draft), Framework(s) on Network Requirements and Capabilities to Support Emergency Communications Over Evolving Circuit Switched and Packet Switched Networks