## Slide 1: ITU-T Security Workshop Session 2 – Security in IP-based networks and services 13-14 May 2002, Seoul/Korea
Multimedia Security within Study Group 16
Past, Presence and Future
Pierre-André Probst Chair ITU-T SG 16 Martin Euchner Rapporteur Q.G/16

## Slide 2: Outline of Presentation
Study Group 16 Overview
    Question G “Multimedia Security”
Examples of past, present and future MM-security in SG16
    Secure H.323-based IP Telephony
    H.235 and associated security profiles
    H.248 Media Gateway Decomposition Security
    Secure H.320 Audio/Video and T.120 Data Conferencing
    Emergency Telecommunications Services Security

## Slide 3: ITU-T Study Group 16 Question G “Security of MM Systems & Services“
Part I


## Slide 4: Study Group 16 - Security-related Questions in the MediaCom2004 project
Q.C - MM Applications & Services F.706
Q.D - Interoperability of MM Systems & Services
Q.G - Security of MM Systems & Services H.233, H.234, H.235
Q.1
MM Systems, Terminals & Data Conferencing
H.320
H.324
T.120
Q.2
MM over Packet Networks using H.323 systems
H.225.0
H.323
H.450
H.460
Q.3
Infrastructure & Interoperability for MM over Packet Network Systems
H.245
H.246
H.248
Q.4
Video and Data conferencing using Internet supported Services
Q.5
Mobility for MM Systems & Services
H.501
H.510
H.530
Q.F - MM Quality of Service & E-2-E Performance in MM Systems


## Slide 5: Question G Security of MM Systems & Services
A horizontal question with broad focus
General Responsibilities:
  Perform threat analysis, analyze security requirements; recommend security services/mechanism for MM applications
  Build sound security architecture and interface with security infrastructure
  Realize multimedia communications security, engineer MM security protocols with real-time, group-communication, mobility and scalability constraints
  Address interdomain security and security interworking
  Maintain H.233, H.234; progress H.235
For further details on Q.G terms of reference, please see Annex G of the Mediacom2004 project description
http://www.itu.int/ITU-T/studygroups/com16/mediacom2004/index.html


## Slide 6: Multimedia Communications Security Some questions to address
Secure the signaling for MM applications
Secure data transport and MM streams
Protect MM content (authorship, IPR, copy-protection)
Efficiently integrate key management into MM protocols; interface with security infrastructures (e.g., PKI)
Negotiate security capabilities securely
Interact with security gateways and firewalls
Enable MM security across heterogeneous networks
Provide scalable security (small groups, medium sized enterprises, large carrier environments)
Build future-proof security (simple and sophisticated security techniques)
Address the performance and system constraints (SW/HW crypto, smart-cards,...)
….


## Slide 7: Q.G Work and Study Items Some Highlights
Investigate confidentiality and privacy of all signaling
Address the concept of a centralized key management for MM systems
Security for MM Mobility, MM Presence, MM Instant Messaging
Optimize voice encryption, develop video encryption, consider sophisticated crypto algorithms
MM security support for emergency services
Consolidate or develop new security profiles
Clarify the impact due to lawful interception
Architect secure, de-composed systems
Security interworking H.323-SIP
Interaction with e-commerce and network security
...


## Slide 8: Target Multimedia Applications with Security Needs
Voice/Video Conferencing
Data Conferencing
IP Telephony (Voice over IP)
Media Gateway Decomposition
Instant Messaging and MM-Presence


## Slide 9: Threats to Multimedia Communication
Internet PC
PDA
Notebook
PC
Telephone
TV
Kiosk
Terminal
Online-Services
e.g. WWW,
Compuserve
Radio/Television Data
Telephone
Data
Video
WAN
Internet
Private
Network
LAN
Intranet
Public
Network
Unauthorized Access to Resources and Services
Intrusion
Repudiation (Data, Service)
Eavesdropping, Disclosure
Billing Fraud
Masquerade
Manipulation of Data
Replay
Misuse of Data
Misuse of Services
Denial of Service
Traffic Analysis
Insider Threats

## Slide 10: Part II
Secure IP Telephony H.235 H.235 Annex D H.235 Annex E H.235 Annex F H.235 Version 3 H.530


## Slide 11: General H.323 Scenario
H.323 Intranet Client
Gatekeeper
H.323 Internet Client
Firewall
H.323 Client via PPP
Gateway
(Access Server)
Gateway
(H.323/ISDN/H.320)
Intranet (LAN)
IP Phone (SET)
PSTN
Multicast Unit
Internet
PBX
IP
Analog and Digital Phones
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: IP Telephony - Security Issues
User authentication:
  Who is using the service? (Who am I phoning with?)
Call authorization:
  Is the user/terminal permitted to use the service resources?
Terminal and server authentication:
  Am I talking with the proper server, MCU, provider? Mobility ...
Signaling security protection;
  Protection of signaling protocols against manipulation, misuse, confidentiality & privacy
Voice confidentiality:
  Encryption of the RTP voice payload
Key management:
  Secure key distribution and key management among the parties
Interdomain security:
  Security profile & capability negotiation, firewall traversal


## Slide 13: Specific IP Telephony Security Challenges
IP Telephony is real-time, point-2-point or multi-point
  secure fast setup/connect
  real-time security processing of media data
  real-time certificate processing
  IKE security handshakes take too long
Security measures must be integrated in proprietary platforms and in VoIP stacks
  security can best be added at application layer
  tight interaction with voice CODECs and DSPs
  low overhead for security: small code size, high performance,...
  “Windows 5000” is not the answer!
Secure management of the systems
  secure password update
  secure storage in databases
Scalable security from small enterprise to large Telco environments
Security should be firewall friendly


## Slide 14: “Historic” Evolution of H.235
1997
1998
1999
2000
1996
2001
2002
Initial Draft
Security Profiles
Annex D
Annex E
started
H.323V2
H.323V4
H.323V5?
H.235V2
Annex D
Annex E approved
Annex F
H.530
consent
H.235V1
approved
H.235V3 consent?
Core Security Framework Engineering
Consolidation
Improvement

1st Deployment

## Slide 15: H.235 – Security for H.323
“Security and Encryption for H.323 and other H.245-based multimedia terminals”
provides cryptographic protection of control protocols (RAS, H.225.0 and H.245) and audio/video media stream data
negotiation of cryptographic services, algorithms and capabilities
integrated key management functions / secure point-to-point and multipoint communications
interoperable security profiles
sophisticated security techniques (Elliptic curves, anti-spamming & AES)
may use existing Internet security packages and standards (IPSec, SSL/TLS)
Recommendation H.235 version 2 released in 11/2000

Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: H.235 - “H.323 Security“ Security Protocol Architecture
AV
Applications
Audio
G.711
G.722
G.723.1
G.729
Video
H.261
H.263
Encryption
RTCP
H.225.0
Terminal
to
Gatekeeper
Signaling
(RAS)
Terminal Control and Management
Data
Applications
Security
Capabilities
Security
Capabilities
T.124
T.125
Unreliable Transport / UDP, IPX
Reliable Transport / TCP, SPX
Network Layer / IP / IPSec
Link Layer /......
Physical Layer / .....
T.123
Scope of H.323
Scope of H.235
TLS/SSL
Multimedia Applications, User Interface
TLS/SSL
Authenti-
cation
RTP

Scope of T.120
H.225.0
Call
Signaling
(Q.931)
H.245
System
Control
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: H.530 The Security Problem of H.323 Mobility
Provide secure user and terminal mobility in distributed H.323 environments beyond interdomain interconnection and limited GK-zone mobility
Security issues:
  Mobile Terminal/User authentication and authorization in foreign visited domains
  Authentication of visited domain
  Secure key management
  Protection of signaling data between MT and visited domain


## Slide 18: Part III
Media Gateway Decomposition H.248 Security


## Slide 19: H.248 Security in decomposed Gateways
(interim AH) IPSEC AH/ESP
H.225.0/ H.245/ H.235
SCN/SS7
RTP/ H.235
TDM voice trunk
IKE

H.248
H.245 OLC/ H.235
H.235 RTP payload security
Media Gateway MG
IPSEC
IKE
H.235 Key Management
IPSEC
IKE
Media Gateway Controller MGC
Notes: <number>
<footer>
<header>
<date/time>
H.235 provides plenty of options, with no mandatory settings
RAS: 11, Call Signaling: 12, Call Control: 10, Media Stream Encryption: 4
SET, zBsp. IP Phone

## Slide 20: Part IV
H.320 Audio/Video Security


## Slide 21: Security for Multimedia Terminals on circuit-switched networks
H.233: “Confidentiality System for Audiovisual Services”
  point-to-point encryption of H.320 A/V payload data by ISO 9979 registered algorithms: FEAL, DES, IDEA, B-CRYPT or BARAS stream ciphers
H.234: “Key Management and Authentication System for Audiovisual Services”
  uses ISO 8732 manual key management
  uses extended Diffie-Hellman key distribution protocol
  RSA based user authentication with X.509-like certificates by 3-way X.509 protocol variant


## Slide 22: Part V
Security Aspects of Data Conferencing


## Slide 23: Security for Computer Supported Collaborative Work (CSCW)
CSCW scenarios:
  Users work in a virtual office (Teleworking/Telecommuting from home)
  collaboration of users in a tele-conference through a conference system
Security aspects:
  user authentication for granting access to the corporate environment
  telecommuting server can protect out-bound/VPN application data
  secure remote access and management to home office PC
  home office PCs deserve special security protection:
    against intruders, viruses
    against misuse of corporate services
    unauthorized access to local information though application sharing
  point-to-point security may not be optimal in a decentralized multi-party conference


## Slide 24: Security for Multimedia Conferencing T.120 and Security
T.120 has very weak information security available (unprotected passwords), common state of the art cryptographic mechanisms are not supported.
OS security features do not prevent against typical T.120 threats (especially T.128 application sharing vulnerabilities); this problem already arises in simple pt-2-pt scenarios.
Additional threats exist for group-based multipoint scenarios: insider threats, lack of access control, “write token” not protected, unsecured conference management ,…
  The T.120 “virtual conference room” needs integral and user friendly security protection: for authentication & role-based authorization, for confidentiality, for integrity, and security policy negotiation capabilities.


## Slide 25: Emergency Telecommunications services Security for Multimedia Applications and Systems
Security objectives:
  prevent theft of service and denial of service by unauthorized user
  support access control and authorization of ETS users
  ensure the confidentiality and integrity of calls
  provide rapid and user-friendly authentication of ETS users
H.SETS is the provisional title for a new work item under study within Q.G with the focus on the multimedia security aspects of ETS
Relationship identified with QoS, network issues, robustness and reliability,...


## Slide 26: Contacts
Pierre-André Probst
ITU-T Study Group 16 Chair
Swisscom
6, Chemin Isaac Machard
CH-1290 Versoix/Switzerland
T: + 41 22 950 05 07
F: + 41 22 950 05 06
M: + 41 79 229 96 56
E-mail: probst-pa@bluewin.ch
Dipl.-Inform. Martin Euchner
Rapporteur Q.G/16
Siemens AG, ICN M SR 3
Hofmannstr. 51
81359 Munich, Germany
Tel: +49 89 722 55790
Email: martin.euchner@icn.siemens.de