## Slide 1: Security Activities in IETF in support of Mobile IP
Semyon (Simon) Mizikovsky
Lucent Technologies, Inc.
Lucent Technologies
Bell Labs Innovations

## Slide 2: What is Mobile IP?
Mobile IP becomes front-end for AAA
FA
FA
AAA
Server
Broker
Network
Internet
Home AAA
Server
AAA
HA
First Visited Network
Next Visited Network
MIP
Tunnel

## Slide 3: Mobile IP and User Authentication
Challenge/Response authenticated with AAA infrastructure (RFC 3012bis)
FA
Visited AAA
Server
Broker
Network
Home AAA
Server
HA
MIP Advertisement (Challenge)
MIP Registration ReQuest (AUTHm)
AAA Authentication/Authorization Request
AAA Authorization Response (AUTHh)
MIP RRQ
MIP RRP
MN
MIP RRP (AUTHh)

## Slide 4: Mobile IP Keys
FA
Corporate
Network
HA
AAA
Server
Broker
Network
Internet
Dynamic MIP Tunnel
Protected by IPSec
MN
MN-FA Key
Home AAA
Server
FA-HA Key
MN-HA Key
MN-AAAh Key

## Slide 5: Mobile IP Keys Description
K1 = MN-AAAh_Key
  Pre-provisioned Long Term Root Key
K2 = MN-HA_key
  Supports dynamic allocation of HA, even in visited network. Intermediate Term.
  Used to authenticate subsequent registrations from different FAs during same session
K3 = FA-HA_key
  Used to authenticate control messages
  Could also protect bearer traffic
  Could be used as the key for IPSec
K4 = MN-FA_key
  Could be used as input for link-layer (Air Interface) security.

## Slide 6: Current IETF Mobile IP Drafts
Mobile IP Authentication
  RFC3012bis
    Mutual MN-AAAh Authentication
Mobile IP Key Distribution
  AAA Key Distribution Extensions to RFC3012
  http://www.ietf.org/internet-drafts/draft-ietf-mobileip-aaa-key-09.txt
    Not interlocked with Authentication
EAP-AKA
  http://www.ietf.org/internet-drafts/draft-arkko-pppext-eap-aka-00.txt
  Mutual MN-AAAh Authentication and Key Generation
    Requires maintaining states in FA, HA, and AAAh.

## Slide 7: EAP Shared Key Exchange (SKE) draft- salgarelli- pppext- eap- ske- 01. txt

## Slide 8: SKE – Abstract and Rationale
Combined Mutual Authentication and Key Generation scheme based on EAP.
  Applicable to 802.11, Cdma2000, UMTS, and other mobile technologies.
Optimized for efficiency to support roaming clients.
  Minimal number of messages exchanged between Mobile Node (Client) and Authenticator.
  Only 1 Round Trip Transaction to the AAAh required to complete authentication and session key generation.
  Supports evolution towards 1- pass authentication for Mobile- IP enabled clients.
Uses cryptographically strong MN-AAAh Key.
  Resistant to Dictionary Attacks.
SKE is cipher-suite - independent.
  The EAP Master Secret Key (K_ EMS) is derived as the result of successful process.
  All session keys can be derived from it depending on specific cipher application.

## Slide 9: EAP SKE Initiation

## Slide 10: EAP SKE Completion

## Slide 11: Mobile IP SKE Variant

## Slide 12: Mobile IP SKE Variant

## Slide 13: SKE Functions
Authentication Responses of MN (Am), AAAh (Ah), and FA (Af) are Secure MACs of pre-shared keys, respective Challenges (Nf, Nm, Nh), and MN Identity (NAI).
  Am = MAC (MN-AAAh_KEY | Nf | Nm | NAI)
  Ah = MAC (MN-AAAh_KEY | Nm | Nf | NAI)
  Af = MAC (FA-HA_Key | Nf | Nh | NAI)
EAP Master Secret Key (K_EMS) is a Secure Pseudo-Random Function of MN-AAAh_Key, AAAh Challenge (Nh), and Auth response of the AAAh (Ah).
  K_EMS = PRF (MN-AAAh_KEY | Nh | Ah)
Other keys are generated from K_EMS.
  MN-FA_Key = PRF (K_EMS|Nm|Nf)
  MN-HA_Key = PRF (K_EMS|Nm|Nh)
  FA-HA_Key = PRF (K_EMS|Nf|Nh)
Standard Key-Explosion functions can be used
  HMAC-SHA1, PRF-SHA1, HMAC-MD5, etc.

## Slide 14: SKE Properties
Secrecy and Authenticity
  Home AAA and MN Authenticate each-other.
  EAP Master Secret Key (K_EMS) guaranteed to be fresh, random, and unique (Derived from Nf, Nm, and Nh),
  Key Generation interlocked with Authentication.
Forward secrecy
  Compromise of K-EMS preserves security of past and future sessions and secrecy of the root key (MN-AAAh_Key).
Efficiency
  Minimum number of Air Interface messages.
  Only 1 Round Trip Transaction with AAAh.
Provably Secure
Stateless protocol (as opposed to EAP-AKA)

## Slide 15: Summary
Even though Mobile IP Authentication is Mandatory, the Key Generation and Distribution is not.
There are few Key Generation and Key Distribution schemes – neither is adopted by IETF yet. All require change in AAA operation.
RADIUS specs are closed, DIAMETER specs are not mature.
SKE is an example of efficient and secure Authentication & Key Generation Protocol optimized for mobile environment, including 802.x, 3GPP UMTS, 3GPP2 Cdma2000, etc.